## Slide 1: Chapter 10 Digital-to-Analogue Conversion
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Notes: <number>

## Slide 2: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Digital-to-Analogue Converter (DAC) introduction
DAC types
DAC’s characteristic parameters
DAC12 module:
  Features
  Operation
  Registers
Laboratory 6: Voltage ramp generator
Quiz

## Slide 3: Introduction (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The final stage in digital processing is to convert the digital output value to a signal that can be used by the real-world e.g. a voltage or current;
A Digital-to-Analogue converter (DAC) is an electronic device or circuit that converts a digital representation of a quantity to a discrete analogue value;
The inputs to a DAC are the digital value and a reference voltage VREF to set the analogue output level;

## Slide 4: Introduction (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Provides a continuous time output signal, mathematically often treated as discrete Dirac pulses into a zero-order hold and consisting of a series of fixed steps;
Filtering the discrete output signal can be used to approximate a continuous time signal, as well as:
  Increasing the resolution;
  Increasing the number of discrete levels and;
  Reducing the level size (reduces the quantization error).

## Slide 5: Introduction (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Ideal DAC output:
  A sequence of impulses filtered to construct a continuous time analogue signal;
  Precise reproduction of the sampled signal up to the Nyquist frequency.
Real DAC output: Reconstruction is not precise
  Filter has infinite phase delay;
  There will be quantization errors.
The digital data sequence is usually converted into an analogue voltage at a uniform update rate;
The clock signal latches the actual data of the digital input data sequence and the DAC holds the output analogue voltage until the next clock signal latches new data.

## Slide 6: DAC types (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Binary Weighted DAC:
  Contains one resistor (or current source) for each bit of the DAC connected to a common voltage source VREF;
  There are accuracy problems (high precision resistors are required);
R/2R Ladder DAC:
  Binary weighted DAC that uses a repeating cascaded structure of resistors of value R and 2R;
  The MSP430’s DAC12 module uses this architecture.

## Slide 7: DAC types (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R/2R Ladder DAC:
  Example: R/2R 4 bit DAC architecture:
  Switch current to negative input of Op-Amp which is a virtual ground

## Slide 8: DAC types (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Interpolating DACs:
  Use a pulse density conversion technique (see Chapter 9).
Pulse Width Modulator DAC:
  A stable voltage (or current) is switched into a low-pass (LP) filter during a time period representative of the digital input value.
Thermometer coded DAC:
  Equal resistor (or current source) for each value of DAC output;
  High precision and conversion speed;
  Expensive.

## Slide 9: DAC types (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Hybrid DAC:
  Combination of the previous techniques in a single converter;
Segmented DAC:
  Combination of the thermometer coded principle for the most significant bits (MSBs) and the binary weighted principle for the least significant bits (LSBs);
  Uses the best of both topologies.

## Slide 10: DAC characteristic parameters (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Resolution (n):
  Number of possible DAC output levels, 2n (n: n.º of bits);
  The Effective Number Of Bits (ENOB) is the actual resolution achieved by the DAC, taking into account errors like nonlinearity, signal-to noise ratio.
Integral Non-Linearity (INL):
  Deviation of a DAC's transfer function from a straight line.
Differential NonLinearity (DNL):
  Difference between an actual step height and the ideal value of 1 LSB;
  DNL < 1 LSB, the DAC is monotonic, that is, no loss of data.

## Slide 11: DAC characteristic parameters (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Offset error:
  Analogue output voltage when the digital input is zero.
Gain error:
  Difference between the ideal maximum output voltage and the actual maximum value of the transfer function, after subtracting the offset error.
Monotonicity:
  Ability of the analogue output of the DAC to increase with an increase in digital code or the converse.
Total Harmonic Distortion (THD):
  Distortion and noise introduced to the signal by the DAC.
Dynamic range:
  Difference between the largest and the smallest signals.

## Slide 12: DAC12 module
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The 12 bit DAC12 module is a voltage output DAC;
All the MSP430 hardware development tools contain this module;
The MSP430FG4618 device on the Experimenter’s board has two DAC12 modules, allowing them to be grouped together for synchronous update operation.

## Slide 13: DAC12 module
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DAC12 block diagram:

## Slide 14: DAC12 features
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
12 bit monotonic output;
8-bit or 12-bit voltage output resolution;
Programmable settling time vs. power consumption;
Internal or external reference selection;
Straight binary or Two’s complement data format;
Self-calibration option for offset correction;
Synchronized update capability for multiple DAC12s;
Direct Memory Access (DMA) enable.

## Slide 15: DAC12 operation (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DAC12 core:
  Dynamic range controlled by:
    DAC’s resolution: 8 bits or 12 bits (DAC12RES bit);
    Full-scale output: 1xVREF or 3xVREF (DAC12IR bit);
    Input data format: straight binary or two’s complement (DAC12DF bit).
  The output voltage (straight binary data format):

## Slide 16: DAC12 operation (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DAC12_xDAT Data Format:
  The data format modifies the full-scale output voltage:

## Slide 17: DAC12 operation (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Updating the DAC12 voltage output (DAC12_xDAT reg.):
  Configurable with the DAC12LSELx bits:
    DAC12LSELx = 0: Immediate when new data is written;
    DAC12LSELx = 1: Grouped (data is latched);
    DAC12LSELx = 2: Rising edge from the Timer_A CCR1;
    DAC12LSELx = 3: Rising edge from the Timer_B CCR2.

## Slide 18: DAC12 operation (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DAC12 Interrupts:
  The DAC12IV is shared with the DMA controller;
  This structure provides:
    Increased system flexibility;
    No code execution required;
    Lower power;
    Higher efficiency.

## Slide 19: DAC12 Registers (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DAC12_xCTL, DAC12 Control Register
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8
DAC12OPS | DAC12SREFx |  | DAC12RES | DAC12LSELx |  | DAC12CALON | DAC12IR
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
DAC12AMPx |  |  | DAC12DF | DAC12IE | DAC12IFG | DAC12ENC | DAC12GRP
Bit |  | Description
15 | DAC12OPS | DAC12 output: DAC12OPS = 0  DAC12_0 on P6.6, DAC12_1 on P6.7 DAC12OPS = 1  DAC12_0 on VeREF+, DAC12_1 on P5.1
14-13 | DAC12REFx | DAC12 reference voltage: DAC12REF1 DAC12REF0 = 00  VREF+ DAC12REF1 DAC12REF0 = 01  VREF+ DAC12REF1 DAC12REF0 = 10  VeREF+ DAC12REF1 DAC12REF0 = 11  VeREF+
12 | DAC12RES | DAC12 resolution: DAC12RES = 0  12 bit resolution DAC12RES = 1  8 bit resolution
11-10 | DAC12LSELx | DAC12 load: DAC12LSEL1 DAC12LSEL0 = 00 DAC12_xDAT written DAC12LSEL1 DAC12LSEL0 = 01 all grouped DAC12_xDAT written DAC12LSEL1 DAC12LSEL0 = 10 Rising edge of Timer_A.OUT1 (TA1) DAC12LSEL1 DAC12LSEL0 = 11 Rising edge of Timer_B.OUT2 (TB2)
9 | DAC12CALON | DAC12 calibration initialized or in progress when DAC12CALON = 1
8 | DAC12IR | DAC12 input range: DAC12IR = 0  DAC12 full-scale output: 3x reference voltage DAC12IR = 1  DAC12 full-scale output: 1x reference voltage

## Slide 20: DAC12 Registers (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DAC12_xCTL, DAC12 Control Register
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8
DAC12OPS | DAC12SREFx |  | DAC12RES | DAC12LSELx |  | DAC12CALON | DAC12IR
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
DAC12AMPx |  |  | DAC12DF | DAC12IE | DAC12IFG | DAC12ENC | DAC12GRP
Bit |  | Description |  | 
7-5 | DAC12AMPx | DAC12 amplifier setting: AMP2 AMP1 AMP0 = 000  AMP2 AMP1 AMP0 = 001  AMP2 AMP1 AMP0 = 010  AMP2 AMP1 AMP0 = 011  AMP2 AMP1 AMP0 = 100  AMP2 AMP1 AMP0 = 101  AMP2 AMP1 AMP0 = 110  AMP2 AMP1 AMP0 = 111  f: frequency (speed) I: current | Input buffer: Off Off Low f / I Low f / I Low f / I Medium f / I Medium f / I High f / I | Output buffer: DAC12 off (high Z) DAC12 off (0 V) Low f / I Medium f / I High f / I Medium f / I High f / I High f / I
4 | DAC12DF | DAC12 data format: DAC12DF = 0  Straight binary DAC12DF = 1  Two’s complement |  | 
3 | DAC12IE | DAC12 interrupt enable when DAC12IE = 1 |  | 
2 | DAC12IFG | DAC12 Interrupt flag DAC12IFG = 1 when interrupt pending |  | 
1 | DAC12ENC | DAC12 enable when DAC12ENC = 1 and DAC12LSELx>0. |  | 
0 | DAC12GRP | Groups DAC12_x with the next higher DAC12_x when DAC12GRP = 1 (exception for DAC12_1) |  | 

## Slide 21: DAC12 Registers (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DAC12_xDAT, DAC12 Data Register
  The four most significant bits (bits 15 – 12) are always zero;
  The twelve least significant bits store the DAC12 data (bits 11 – 0);
  The DAC12 data is right justified, but the MSB depends on:
    Resolution:
      8 bit: Bit 7;
      12 bit: Bit 11.
    Data format:
      Straight binary: MSB is data;
      Two’s complement: MSB is sign.

## Slide 22: Laboratory 6: Voltage ramp generator (1/16)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Overview:
  This laboratory implements a voltage ramp generator. The DAC module reference is obtained from the ADC module;
  The DAC is configured with 12-bit resolution in straight binary format;
  The value of the DAC output is updated once every 1 msec by Timer_A interrupt service routine (ISR);
  The buttons SW1 and SW2 are used to manually modify the output value of the DAC;
  When the microcontroller is not performing any tasks, it enters low power mode.

## Slide 23: Laboratory 6: Voltage ramp generator (2/16)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  The DAC12_0 (connected to P6.6) module uses VREF+ as the reference voltage. It is therefore necessary to activate this reference voltage in the ADC12 module;
  The output of the DAC is updated whenever Timer_A generates an interrupt. Timer_A is configured to generate an interrupt with a 1 msec time period;
  After refreshing the output of the DAC, the system returns to low power mode LPM3;
  The buttons SW1 and SW2 allow manual changes to be made to the DAC’s output value.

## Slide 24: Laboratory 6: Voltage ramp generator (3/16)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  The application starts by stopping the Watchdog Timer;
  Then, the reference voltage of the ADC12 is activated and set to 2.5 V;
  There is a delay time in order for the reference voltage to settle;
  During this time period, the device enters low power mode LPM0;
  The delay period is controlled by Timer_A, and when the period ends, it enables an interrupt (wakes the device).

## Slide 25: Laboratory 6: Voltage ramp generator (4/16)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization (cont):
  Timer_A is reconfigured to generate an interrupt once every 1 msec;
  This interrupt service routine (ISR) updates the output of the DAC;
  Ports P1.0 and P1.1 are connected to the buttons SW1 and SW2;
  They are configured as inputs with interrupt capability;
  The ISR decodes the interrupt source:
    When button SW1 is pressed, then the output of the DAC is increased;
    When button SW2 is pressed, then the output of the DAC is decreased.

## Slide 26: Laboratory 6: Voltage ramp generator (5/16)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  Reference voltage selection:
    The DAC uses VREF+ as the reference voltage;
    What is the value required to write to the configuration register in order to make the reference voltage available internally?
    ADC12CTL0 = ________________;

## Slide 27: Laboratory 6: Voltage ramp generator (6/16)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration (continued):
  DAC12 configuration:
    DAC12_0 output is on P6.6;
    DAC12_0 is configured with 12-bit resolution;
    The output is updated immediately when a new DAC12 data value is written in straight binary data format to the DAC12_0DAT register;
    The full-scale output must be equal to the VREF+ 2.5 V internal reference voltage;

## Slide 28: Laboratory 6: Voltage ramp generator (7/16)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration (continued):
  DAC12 configuration:
    Choose a compromise solution between the settling time and current consumption by selecting a medium frequency and current for both input and output buffers;
    Configure the following register in order to meet these requirements:
    DAC12_0CTL = ________________;

## Slide 29: Laboratory 6: Voltage ramp generator (8/16)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration (continued):
  Timer_A configuration:
    Configure Timer_A register to enable an interrupt with a period of 1 msec;
    Use the ACLK clock signal as the clock source;
    Timer_A is configured in count up mode in order to count until the TAR value reaches the TACCR0 value.
    TACCTL0 = ___________________;
    TACCR0 = ____________________;
    TACTL = _____________________;

## Slide 30: Laboratory 6: Voltage ramp generator (9/16)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration (continued):
  I/O Ports configuration:
    Port P1 uses the bits P1.0 and P1.2 to activate the ISR whenever the buttons SW1 and SW2 are activated (low-to-high transition).
    Configure these registers:
    P1SEL = _________________;
    P1DIR = _________________;
    P1IFG = _________________;
    P1IE = __________________;

## Slide 31: Laboratory 6: Voltage ramp generator (10/16)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Monitor the analogue signal with an oscilloscope:
    Connect an oscilloscope to pin 6 of Header 8.
  Measure the current drawn:
    Assign different values to the bits set in DAC12AMP0;
    Suspend the execution of the application and change the registers directly;
    Disable the DAC12EC bit. This bit must later be re-enabled.
    Please note the special cases relating to:
      DAC12 off;
      High impedance output and DAC12 off;
      Output: 0 V.

## Slide 32: Laboratory 6: Voltage ramp generator (11/16)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
FLL+ configuration:
FLL_CTL0 |= DCOPLUS | XCAP18PF; // DCO+ set,
// freq = xtal x D x N+1
SCFI0 |= FN_4; // x2 DCO freq,
// 8MHz nominal DCO
SCFQCTL = 121; // (121+1) x 32768 x 2 = 7.99 MHz
Reference voltage configuration:
ADC12CTL0 = REF2_5V | REFON; // Internal 2.5V ref on
MSP-EXP430FG4618 | SOLUTION
Using the MSP-EXP430FG4618 Development Tool and the MSP430FG4618 device, implement a ramp generator. | 

## Slide 33: Laboratory 6: Voltage ramp generator (12/16)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DAC12 configuration:
DAC12_0DAT = 0x00; // DAC_0 output 0V
DAC12_0CTL = DAC12IR | DAC12AMP_5 | DAC12ENC;
// DAC_0 -> P6.6,
// DAC_1 -> P6.7,
// DAC reference Vref,
// 12 bits resolution,
// Immediate load,
// DAC full scale output,
// Medium speed/current,
// Straight binary,
// Not grouped

## Slide 34: Laboratory 6: Voltage ramp generator (13/16)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Timer_A configuration:
// Before entering in LPM0:
TACTL = TACLR | MC_1 | TASSEL_2; // up mode, SMCLK
// Timer_A ISR:
TAR = 0; // TAR reset
TACCR0 = 13600; // Delay to allow Ref to settle
TACCTL0 |= CCIE; // Compare-mode interrupt
TACTL = TACLR | MC_1 | TASSEL_2; // up mode, SMCLK

## Slide 35: Laboratory 6: Voltage ramp generator (14/16)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Timer_A configuration:
// Before entering in LPM0:
TACTL = TACLR | MC_1 | TASSEL_2; // up mode, SMCLK
// Timer_A ISR:
TAR = 0; // TAR reset
TACCR0 = 13600; // Delay to allow Ref to settle
TACCTL0 |= CCIE; // Compare-mode interrupt
TACTL = TACLR | MC_1 | TASSEL_2; // up mode, SMCLK

## Slide 36: Laboratory 6: Voltage ramp generator (15/16)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
FLL+ configuration:
FLL_CTL0 |= DCOPLUS + XCAP18PF; // DCO+ set,
// freq = xtal x D x N+1
SCFI0 |= FN_4; // x2 DCO freq, 8MHz nominal DCO
SCFQCTL = 121; // (121+1)x32768x2 = 7.99 MHz
Reference voltage configuration:
ADC12CTL0 = REF2_5V + REFON; // Internal 2.5V ref on

## Slide 37: Laboratory 6: Voltage ramp generator (16/16)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Configuration of ports:
// SW1 and SW2 ports configuration
P1SEL &= ~0x03; // P1.0 and P1.1 I/O ports
P1DIR &= ~0x03; // P1.0 and P1.1 digital inputs
P1IFG = 0x00; // clear all interrupts pending
P1IE |= 0x03; // enable port interrupts
// P6.6 (DAC12_0 output)
// There is no need to configure P6.6 as a
// special function output since it was configured in the
// DAC12 configuration register (DAC12_0CTL) using
// DAC12OPS = 0

## Slide 38: Quiz (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
1. The DAC12 peripheral module included in MSP430 devices uses:
  (a) Binary Weighted DAC;
  (b) Interpolating DAC;
  (c) Thermometer coded DAC;
  (d) R/2R Ladder DAC.
2. In a R/2R Ladder DAC architecture, the equivalent resistance between VREF and ground is:
  (a) R/2;
  (b) R;
  (c) 2R;
  (d) 4R.

## Slide 39: Quiz (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
3. For a DAC with a Differential Non-Linearity of less than 1 LSB:
  (a) The transfer function deviates from a straight line;
  (b) The analogue output voltage value is zero when the digital input is zero;
  (c) The full-scale output voltage is equal to the maximum digital input;
  (d) No data is lost.
4. Filtering is important to DAC operation because it:
  (a) Increases resolution;
  (b) Reproduces a signal precisely up to the Nyquist frequency;
  (c) Can provide an approximate smooth continuous time signal;
  (d) Spreads noise over more frequencies.

## Slide 40: Quiz (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
5. To generate a DAC12 analogue output voltage of three times the reference voltage with 12-bit resolution:
  (a) DAC12RES = 0 and DAC12IR = 1;
  (b) DAC12RES = 0 and DAC12DF = 1;
  (c) DAC12IR = 1 and DAC12DF = 0;
  (d) DAC12RES = 1 and DAC12IR = 1.
6. To update the DAC12’s analogue output voltage on a rising edge of the Timer_A CCR1 output:
  (a) DAC12LSELx = 3;
  (b) DAC12LSELx = 2;
  (c) DAC12LSELx = 1;
  (d) DAC12LSELx = 0.

## Slide 41: Quiz (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Answers:
  1. (d) R/2R Ladder DAC.
  2. (b) R.
  3. (d) No data is lost.
  4. (c) Can provide an approximate smooth continuous time signal.
  5. (a) DAC12RES = 0 and DAC12IR = 1.
  6. (b) DAC12LSELx = 2.