## Slide 1: Chapter 11 Direct Memory Access (DMA)
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Notes: <number>

## Slide 2: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Direct Memory Access (DMA) capability
DMA configuration and operation:
  Block diagram
  Features
  System and DMA interrupts
  DMA transfers
DMA Registers
Laboratory 7: Direct Memory Access:
  Lab7A: Data Memory transfer triggered by software
  Lab7B: Sinusoidal waveform generator
Quiz

## Slide 3: DMA capability (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The MSP430 has been designed for applications requiring low power;
When the application requires data-handling, the direct memory access (DMA) capability included in some devices is useful:
  5xxx; FG4xx(x); F261x; F16x(x) and F15x;
  Among these: MSP430FG4618 (Experimenter’s board).
DMA automatically handles data;
DMA does not require CPU intervention;
DMA helps reduce the power consumption (CPU remains sleeping).

## Slide 4: DMA capability (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Concept of DMA: move functionality to peripherals:
  Peripherals use less current than the CPU;
  Delegating control to peripherals allows the CPU to shut down (saves power);
  “Intelligent” peripherals are more capable, providing a better opportunity for CPU shutoff;
  DMA can be enabled for repetitive data handling, increasing the throughput of peripheral modules;
  Minimal software requirements and CPU cycles.

## Slide 5: DMA capability (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The following TI Application Reports cover the use of the DMA controller for different applications, with the aim of lowering power consumption:
    Streamlining the mixed-signal path with the signal-chain-on-chip MSP430F169 <slyt078.pdf>
    Interfacing the MSP430 with MMC/SD Flash Memory Cards <slaa281b.pdf>
    Digital FIR Filter Design Using the MSP430F16x <slaa228.pdf>
    Using the USCI I2C Master <slaa382.pdf>

## Slide 6: DMA configuration and operation (1/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Block diagram:

## Slide 7: DMA configuration and operation (2/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMA controller features:
  Three independent transfer channels;
  Configurable (ROUNDROBIN bit) DMA channel priorities:
    Default: DMA0−DMA1−DMA2;
  DMA Transfer cycle time:
    Requires only two MCLK clock cycles per transfer;
    Each byte/word transfer requires:
      2 MCLK cycles after synchronization;
      1 MCKL cycle of wait time after transfer.

## Slide 8: DMA configuration and operation (3/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMA controller features:
  Block sizes up to 65535 bytes or words;
  Configurable edge/level-triggered transfer (DMALEVEL bit).
  Byte or word and mixed byte/word transfer capability:
    Byte-to-byte;
    Word-to-word;
    Byte-to-word (upper byte of the destination word is cleared);
    Word-to-byte (lower byte of the source word is transferred).

## Slide 9: DMA configuration and operation (4/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMA controller features:
  Four addressing modes for each DMA channel are independently configurable (DMASRCINCRx and DMADSTINCRx control bits):
    Fixed address to fixed address;
    Fixed address to block of addresses;
    Block of addresses to fixed address;
    Block of addresses to block of addresses.

## Slide 10: DMA configuration and operation (5/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMA controller features:
  Six transfer modes (each channel is individually configurable by the DMADTx bits):

## Slide 11: DMA configuration and operation (6/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
System interrupts:
  DMA transfers are not interruptible by system interrupts, but system ISRs can be interrupted by DMA transfers;
  Only NMI interrupts can be given priority over the DMA controller (ENNMI bit is set). If the ENNMI bit is not set, system interrupts remain pending until the completion of the transfer.
DMA controller interrupts:
  Each DMA channel has its own DMAIFG flag that is set when the corresponding DMAxSZ register counts to zero (all modes);
  If the corresponding DMAIE and GIE bits are set, an interrupt request is generated.

## Slide 12: DMA configuration and operation (7/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMA controller interrupts:
  The MSP430FG4618 implements the interrupt vector register DMAIV;
  All DMAIFG flags are prioritized and combined to source a single interrupt vector;
  DMAIV is used to determine which flag requested an interrupt.

## Slide 13: DMA configuration and operation (8/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMA transfers:
  USCI_B I2C module with DMA:
    Two trigger sources for the DMA controller;
    Triggers a transfer when new I2C data is received and when data is required for transmit.
  ADC12 with DMA:
    Automatically moves data from any ADC12MEMx register to another location.
  DAC12 with DMA:
    Automatically moves data to the DAC12_xDAT register.

## Slide 14: DMA configuration and operation (9/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMA transfers:
  DMA with flash memory:
    Automatically moves data to the Flash memory;
    Performs the data move data word/byte to the Flash;
    The write timing control is done by the Flash controller;
    Write transfers to the Flash memory succeed if the Flash controller set-up is done before the DMA transfer and if the Flash is not busy.
  All DMA transfers:
    Occur without CPU intervention;
    Operate independently of any low-power modes;
    Increase throughput of modules.

## Slide 15: DMA Registers (1/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMACTL0, DMA Control Register 0 (FG4618)
  All DMAxTSELx registers are the same.

## Slide 16: DMA Registers (2/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMACTL0, DMA Control Register 0 (FG4618) (continued)

## Slide 17: DMA Registers (3/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMACTL0, DMA Control Register 0 (FG4618) (continued)

## Slide 18: DMA Registers (4/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMACTL0, DMA Control Register 0 (FG4618) (continued)

## Slide 19: DMA Registers (5/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMACTL1, DMA Control Register 1 (FG4618)

## Slide 20: DMA Registers (6/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMAxCTL, DMA Channel x Control Register (FG4618)

## Slide 21: DMA Registers (7/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMAxCTL, DMA Channel x Control Register (FG4618) (continued)

## Slide 22: DMA Registers (8/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMAxCTL, DMA Channel x Control Register (FG4618) (continued)

## Slide 23: DMA Registers (9/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMAxCTL, DMA Channel x Control Register (FG4618) (continued)

## Slide 24: DMA Registers (10/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMAxSA, DMA Source Address Register (FG4618)
  32-bit register points to the DMA source address for single transfers or the first source address for block transfers.
DMAxDA, DMA Destination Address Register (FG4618)
  32-bit register points to the DMA destination address for single transfers or the first source address for block transfers.
  For both registers (DMAxSA and DMAxDA):
    Bits 31−20 are reserved and always read as zero;
    Reading or writing to bits 19-16 requires the use of extended instructions;
    When writing to DMAxSA or DMAxDA with word instructions, bits 19-16 are cleared.

## Slide 25: DMA Registers (11/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMAxSZ, DMA Size Address Register (FG4618)
  The 16-bit DMA size address register defines the number of bytes/words of data per block transfer:
    DMAxSZ decrements with each word or byte transfer;
    When DMAxSZ = 0, it is immediately and automatically reloaded with its previously initialized value.
DMAIV, DMA Interrupt Vector Register (FG4618)
  16 bit DMAIV value only uses bits 3 to 1 (other bits = 0);
  DMAIV content provides the interrupt source priority:
      DMAIV = 02h: DMA channel 0 (highest priority);
      DMAIV = 04h: DMA channel 1;
      DMAIV = 06h: DMA channel 2;
      …
      DMAIV = 0Eh: Reserved (lowest priority).

## Slide 26: Lab7: Direct Memory Access
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Objective:
  Configure the MSP430FG4618 device of the Experimenter’s board to implement applications to transfer data without using the CPU.
Details:
  Similar to the previous exercise (Lab6), this laboratory is composed of a series of sub-tasks.
  This laboratory has been developed for the Code Composer Essentials version 3 software development tool only.

## Slide 27: Lab7: Direct Memory Access Lab7A: Data Memory transfer triggered by software
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Project files:
  C source files: Chapter 11 > Lab7 > Lab7A_student.c
  Solution files: Chapter 11 > Lab7 > Lab7A_solution.c
Overview:
  During this laboratory, analysis is performed of the data transfer between two regions of memory. The transfer is carried out under the control of software.
A. Resources:
  The following resource is used in this laboratory:
    DMA controller.

## Slide 28: Lab7: Direct Memory Access Lab7A: Data Memory transfer triggered by software
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Organization of the software application:
  Disable the watchdog timer;
  Port P2.1 is set as an output at logic level low;
  Data vector memory addresses are passed to the source data address DMA0SA and destination address DMA0DA registers;
  The number of words to transfer is loaded into DMA0SZ;
  The DMA channel 0 is configured to trigger the data transfer by software (after each transfer, the destination and source addresses are incremented);
  Port P2.1 state is switched prior to initiating the data transfer.

## Slide 29: Lab7: Direct Memory Access Lab7A: Data Memory transfer triggered by software
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  DMA channel configuration:
  The source and destination addresses of the data must be loaded into their respective registers:
    DMA0SA = _________________;
  DMA0DA = _________________;
  To move a total of 32 words, what is the value to write to the size register?
  DMA0SZ = _________________;

## Slide 30: Lab7: Direct Memory Access Lab7A: Data Memory transfer triggered by software
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  DMA channel configuration:
  The DMA channel must be configured to transfer the word under the control of software;
  The source and destination addresses should be incremented immediately after each transfer.
      DMA0CTL = ________________;

## Slide 31: Lab7: Direct Memory Access Lab7A: Data Memory transfer triggered by software
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  In Memory window, the addresses of data vectors Tab_1 and Tab_2 are displayed. The contents of these addresses must be identified in memory;
  Add a breakpoint to line 57 of code, corresponding to the line of code that performs the port P2.1 state switch;
  Execute the application, and whenever the breakpoint is reached, the execution of the application will be suspended. Observe the data being gradually transferred from the source to the destination;
  The data transfer is suspended once the 32 elements of the source data vector have been transferred.

## Slide 32: Lab7: Direct Memory Access Lab7A: Data Memory transfer triggered by software
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMA channel configuration:
// Start block address:
DMA0SA = (void (*)( )) &tab_1;
// Destination block address:
DMA0DA = (void (*)( )) &tab_2;
DMA0SZ = 0x0020; // Block size
DMA0CTL=DMADT_0 | DMASRCINCR_3 | DMADSTINCR_3 | DMAEN;
// Single transfer, DMA source and destination
// addresses increment, Enable DMA0
MSP-EXP430FG4618 | SOLUTION
Using the DMA controller included in the MSP-EXP430FG4618 Development Tool, analyse the data transfer between two regions of memory. | 

## Slide 33: Lab7: Direct Memory Access Lab7B: Sinusoidal signal generator
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Project files:
  C source files: Chapter 11 > Lab7 > Lab7B_student.c
  Solution files: Chapter 11 > Lab7 > Lab7B_solution.c
Overview:
  This laboratory uses the DMA controller to automatically transfer data between data memory and the DAC12 data register. Thus, a sinusoidal signal is produced, without CPU intervention.
A. Resources:
  This laboratory uses the following peripherals:
    DMA controller;
    DAC;
    ADC (reference generator: VREF+);
    Timer_A;
    Low power mode.

## Slide 34: Lab7: Direct Memory Access Lab7B: Sinusoidal signal generator
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Organization of the software application:
  The successive samples needed to produce the sinusoidal waveform from the DAC are stored in the data vector Sin_tab, which has 32 points;
  The software begins by disabling the watchdog timer, followed by activating the internal reference voltage VREF+;
  The source and destination registers of the data to be transferred by the DMA channel are loaded with the data vector Sin_tab address and with the DAC12 data register address;
  There are 32 data values to transfer.

## Slide 35: Lab7: Direct Memory Access Lab7B: Sinusoidal signal generator
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Organization of the software application:
  The data transfer is initiated whenever the flag DAC12IFG is enabled;
  It is a condition that for the data transfer to occur, the DAC interrupt is not enabled;
  The DMA controller is configured to perform in repeat mode and to transfer a word whenever the previous event occurs;
  The data source address is set to increment after each transfer, while the destination address must remain constant.

## Slide 36: Lab7: Direct Memory Access Lab7B: Sinusoidal signal generator
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Organization of the software application:
  The timer is configured to generate the PWM signal through the capture/compare unit TACCR1;
  SMCLK is the clock signal that will be used to count up to the value in the TACCR0 register;
  Finally, the settings and interrupts are enabled and the device enters into low power mode LPM0.

## Slide 37: Lab7: Direct Memory Access Lab7B: Sinusoidal signal generator
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  DAC12 reference voltage activation:
  The DAC12 requires a reference voltage;
  One of the options is to use the internal voltage VREF+;
  Set the ADC12CTLO register to activate this voltage:
  ADC12CTL0 =____________________;

## Slide 38: Lab7: Direct Memory Access Lab7B: Sinusoidal signal generator
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  DMA Controller configuration:
  Configure the registers DMA0SA, DMA0DA and DMA0SZ to transfer 32 words between the vector Sin_tab and DAC12_0DAT data register:
  DMA0SA = ______________________;
  DMA0DA = ______________________;
  DMA0SZ = ______________________;
  Configure the register DMACTL0 to provide a data transfer whenever the flag DAC12IFG is set:
  DMACTL0 = _____________________;

## Slide 39: Lab7: Direct Memory Access Lab7B: Sinusoidal signal generator
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  DMA Controller configuration:
  Configure the register DMA0CTL to carry out a repeat simple transfer, incrementing the data source address:
  DMA0CTL = _____________________;

## Slide 40: Lab7: Direct Memory Access Lab7B: Sinusoidal signal generator
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  Setup DAC12:
  The DAC12 will update its output whenever there is activation of the signal TA1;
  The DAC full-scale should be 1x reference voltage;
  Choose a medium relationship between the current and average conversion speed of the DAC:
  DAC12_0CTL = __________________;

## Slide 41: Lab7: Direct Memory Access Lab7B: Sinusoidal signal generator
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  Timer_A configuration:
  The Timer_A is responsible for synchronizing data transfer between memory and DAC12;
  The Timer_A input receives as the SMCLK signal (1.048576 MHz) and must have a 30 msec counting period;
  What value needs to be written to TACCR0 in order to achieve this counting period:
  TACCR0 = _______________________;
  TACTL =_________________________;

## Slide 42: Lab7: Direct Memory Access Lab7B: Sinusoidal signal generator
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  Timer_A configuration:
  The capture/compare unit TACCR1 should generate a PWM signal in set/reset mode;
  Configure the unit appropriately:
  TACCTL1 = ______________________;
  TACCR1 = _______________________;

## Slide 43: Lab7: Direct Memory Access Lab7B: Sinusoidal signal generator
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation
  The verification of this laboratory is performed by using an oscilloscope to monitor the output of the DAC12 Channel 0, available on header 8 pin 6.

## Slide 44: Lab7: Direct Memory Access Lab7B: Sinusoidal signal generator
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMA Controller configuration:
// Source block address:
DMA0SA = (void (*)( ))&Sin_tab;
// Destination single address:
DMA0DA = (void (*)( ))&DAC12_0DAT;
// Block size:
DMA0SZ = 0x20;
// DMA control register 0:
DMACTL0 = DMA0TSEL_5; // DAC12IFG trigger
MSP-EXP430FG4618 | SOLUTION
Using the DMA controller included in the MSP-EXP430FG4618 Development Tool, transfer a sinusoidal waveform to the DAC. | 

## Slide 45: Lab7: Direct Memory Access Lab7B: Sinusoidal signal generator
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DMA Controller configuration:
DMA0CTL = DMADT_4 + DMASRCINCR_3 + DMAEN;
// Repeated single transfer,
// DMA source address increment,
// since DMASRCBYTE = 0, the source address
// increments by two (word-word)

## Slide 46: Lab7: Direct Memory Access Lab7B: Sinusoidal signal generator
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Setup DAC12:
DAC12_0CTL = DAC12LSEL_2 | DAC12IR | DAC12AMP_5 | DAC12IFG | DAC12ENC;
// Rising edge of Timer_A.OUT1 (TA1),
// DAC12 full-scale output: 1x reference voltage,
// Input and output buffers: Medium freq./current,
// Enable DAC12

## Slide 47: Lab7: Direct Memory Access Lab7B: Sinusoidal signal generator
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Timer_A configuration:
TACCR0 = 32-1; // Clock period of TACCR0
TACTL = TASSEL_2 | MC_1; // SMCLK, continuous mode
TACCTL1 = OUTMOD_3; // TACCR1 set/reset
TACCR1 = 20; // TACCR1 PWM Duty Cycle

## Slide 48: Quiz (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
1. The DMA controller allows the system to:
  (a) Move data from one location to another without CPU intervention;
  (b) Increase the throughput of peripheral modules;
  (c) Reduce system power consumption by allowing the CPU to remain in a low-power mode;
  (d) All of above.
2. The upper byte of a byte-to-word transfer:
  (a) Maintains the previous value;
  (b) Is cleared;
  (c) Is loaded with the same value as the lower byte;
  (d) None of above.

## Slide 49: Quiz (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
3. When the DMA transfer mode DMAxTSELx = 1 is selected:
  (a) Each transfer requires a trigger;
  (b) A complete block is transferred with one trigger;
  (c) CPU activity is interleaved with a block transfer;
  (d) None of above.
4. NMI interrupts can interrupt the DMA controller when:
  (a) GIE bit is set;
  (b) DMAIE is set;
  (c) ENNMI bit is set;
  (d) DMAEN is set.

## Slide 50: Quiz (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
5. The DMA destination address when the DMADSTBYTE = 1 and DMADSTINCRx = 3:
  (a) Remains unchanged;
  (b) Increments by two;
  (c) Decrements by two;
  (d) Increments by one.
6. For the default DMA channel priority (DMA0−DMA1−DMA2), if ROUNDROBIN is cleared after transferring DMA0, the next priority is:
  (a) DMA2 − DMA0 − DMA1;
  (b) DMA1 − DMA2 − DMA0;
  (c) DMA0 − DMA1 − DMA2;
  (d) DMA1 − DMA0 − DMA2.

## Slide 51: Quiz (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Answers:
  1. (d) All of above.
  2. (b) Is cleared.
  3. (b) A complete block is transferred with one trigger.
  4. (c) ENNMI bit is set.
  5. (d) Increments by one.
  6. (c) DMA0 − DMA1 − DMA2.