## Slide 1: Chapter 12 Hardware Multiplier
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Notes: <number>

## Slide 2: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Introduction
Hardware Multiplier structure:
  Block diagram
  Operands
Hardware Multiplier Registers
Laboratory 8: Multiplication operations analysis:
  Lab8a: Multiplication without hardware multiplier
  Lab8b: Multiplication with hardware multiplier
  Lab8c: RMS and active power calculation
Quiz

## Slide 3: Introduction (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Several devices in the MSP430 family contain a hardware multiplier peripheral module:
    54xx;
    FG46xx;
    FE42x(A);
    F47xx; F44X; F42x(A);
    F261x; F24x(x);
    F16x(x).
The MSP430FG4618 (Experimenter’s board) supports multiplications using the Hardware Multiplier module, without interfering with CPU activities.

## Slide 4: Introduction (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The hardware multiplier supports:
  Unsigned multiply (MPY);
  Signed multiply (MPYS);
  Unsigned multiply accumulate (MAC);
  Signed multiply accumulate (MACS).
The multiplication operation can be:
  16×16 bits;
  16×8 bits;
  8×16 bits;
  8×8 bits. Operands are written to two registers, each one with 8 bits or 16 bits.

## Slide 5: Introduction (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The result of an operation can be accessed by reading two or three registers:
  Result low 16-bit word (bits 15 .. 0) in register RESLO;
  Result high 16-bit word (bits 31 .. 16) in register RESHI;
  When used MAC or MACS: bit 32 in register SUMEXT.
The result is available three MCLK cycles after the operands have been loaded into the peripheral registers;
Detailed information:
  TI Application Report: The MSP430 Hardware Multiplier – Function and Applications <slaa042.pdf>.

## Slide 6: Hardware Multiplier structure (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Block diagram:

## Slide 7: Hardware Multiplier structure (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Two 16-bit operand registers:
  First operand register, OP1:
    Has four addresses used to select the multiply mode:
  Second operand register, OP2:
    Writing to the register initiates the multiply operation.

## Slide 8: Hardware Multiplier structure (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Three result registers, RESLO, RESHI, and SUMEXT:
  RESLO stores the low word of the result;
  RESHI stores the high word of the result:
    The contents of RESHI depend on the multiply operation:

## Slide 9: Hardware Multiplier structure (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Three result registers, RESLO, RESHI, and SUMEXT:
  SUMEXT contains information about the result:
    The contents of SUMEXT depend on the multiply operation:

## Slide 10: Hardware Multiplier Registers
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The hardware multiplier registers do not define the type of multiplication operation;
They simply contain the operands and the data result:

## Slide 11: Laboratory 8: Multiplication operations analysis
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
This laboratory evaluates the hardware multiplier peripheral;
The laboratory is composed of three exercises, each of which uses a different characteristic of the hardware multiplier peripheral:
  Measurement of multiplication execution time, with and without the hardware multiplier;
  Differences between the use of the “*”operator and a direct write to the hardware multiplier registers;
  Typical real-world task: calculation of the active power and the RMS value of an electrical signal.

## Slide 12: Lab8a: Multiplication without hardware multiplier (1/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Project files:
  C source file: Chapter 12 > Lab8 > Lab8a_student.c
Overview:
  This laboratory explores and analyses the MSP430 performance when it performs multiplication operations without the hardware multiplier;
  The execution time is measured with an oscilloscope.

## Slide 13: Lab8a: Multiplication without hardware multiplier (2/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  This laboratory only uses Port P2.1 connected to LED2 in order to measure the execution time of the multiplication operation when performed by a software routine.
  It uses the default configuration of the FLL+;
  All clock signals required for the operation of the components of the device take their default values.

## Slide 14: Lab8a: Multiplication without hardware multiplier (3/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
    The application starts by stopping the Watchdog Timer;
    Port P2.1 is configured as an output port at a low level;
    The variables a and b to be multiplied are initialized;
    The multiplication of a and b is performed between toggles of P2.1;
    This application ends with the device entering into LPM4.

## Slide 15: Lab8a: Multiplication without hardware multiplier (4/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  Go to Properties > TI Debug Settings and select the Target tab. Uncheck the automatically step over functions without debug information when source stepping in order to allow you to step into the multiplication routine;
  Go to Properties > C/C++ Build > Linker MSP430 Linker v3.0 > General options and choose the option None at the Link in hardware version of RTS mpy routine. With this linker option, the application will be built without the hardware multiplier and all multiplication operations will be performed by a software routine;
  Rebuild the project and download it to the target.

## Slide 16: Lab8a: Multiplication without hardware multiplier (5/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Software multiplication routine analysis:
    Connect the oscilloscope probe to port P2.1, which is available on Header 4 pin 2;
    Put the cursor at line 51 of code {c = a*b} and execute Run to line;
    Go to the Disassembly view and switch to mixed disassembly view in order to show both C and Assembly code;

## Slide 17: Lab8a: Multiplication without hardware multiplier (6/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Software multiplication routine analysis (continued):
    Observe that the variables a and b are passed to registers and the#__mpyi routine is called;
    Run the code step-by-step with the Disassembly view active. This action will take you to the software multiplication routine;
    As the software multiplication routine source code is not available, switch to Assembly view only.

## Slide 18: Lab8a: Multiplication without hardware multiplier (7/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Software multiplication routine analysis (continued):
    Run the application step-by-step until the RETA instruction;
    This multiplication is a time-consuming operation for the CPU.

## Slide 19: Lab8a: Multiplication without hardware multiplier (8/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation
  Measurement of the multiply operation execution time:
    Restart the application. It will run from the beginning;
    Put the cursor on line 56 of code {_BIS_SR(LPM4)} and Run to line;
    Measure the pulse width using an oscilloscope;
    This software multiply operation takes around 54 sec.

## Slide 20: Lab8b: Multiplication with hardware multiplier (1/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Project files:
  C source files: Chapter 12 > Lab8 > Lab8b_student.c
Overview:
  This laboratory explores and analyses the MSP430 performance when it performs multiplication operations using the hardware multiplier peripheral;
  Two different operations are analysed:
    Using the “*” operator;
    Accessing the hardware multiplier registers directly.
  The execution times are measured with an oscilloscope.

## Slide 21: Lab8b: Multiplication with hardware multiplier (2/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  This laboratory only uses Port P2.1 connected to LED2 in order to measure the execution time of the multiplication operation when it is performed by the hardware multiplier module;
  It uses the default configuration of the FLL+;
  All the clock signals required for the operation of the device take their default values.

## Slide 22: Lab8b: Multiplication with hardware multiplier (3/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  The application starts by stopping the Watchdog Timer;
  Port P2.1 is configured as an output with a low level;
  The code can be divided into two parts:
  First part:
    The first part of the multiplication is performed using the “*” operator;
    This task is performed between P2.1 toggles, in order to determine the time required to perform the multiplication.

## Slide 23: Lab8b: Multiplication with hardware multiplier (4/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization (continued):
  Second part:
    The second part of the code is separated from the first by some _NOP() operations;
    The software time delay allows measurement of the execution time using an oscilloscope;
    This part of the multiplication operation is performed by directly accessing the hardware multiplier registers;
    The multiplication of the variables is performed between toggle P2.1 instructions;
  The application ends with the device in LPM4.

## Slide 24: Lab8b: Multiplication with hardware multiplier (5/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  Go to Properties > TI Debug Settings and select the Target tab. Uncheck the automatically step over functions without debug information when source stepping in order to allow you to step into the multiplication routine;
  Go to Properties > C/C++ Build > Linker MSP430 Linker v3.0 > General options and choose the option 16 (default) at the Link in hardware version of RTS mpy routine. With this linker option, the application will be built with the 16-bit hardware multiplier peripheral in the Experimenter’s board;
  Rebuild the project and download to the target.

## Slide 25: Lab8b: Multiplication with hardware multiplier (6/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Hardware multiplication routine analysis with the “*”operator:
    Connect an oscilloscope probe to port P2.1, which is available on Header 4 pin 2;
    Put the cursor at line 55 of code {c = a*b} and Run to line;
    Go to Disassembly view and switch to mixed disassembly view in order to show both C and Assembly code.

## Slide 26: Lab8b: Multiplication with hardware multiplier (7/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Hardware multiplication routine analysis with the “*” operator (continued):
    Observe that the variables a and b are passed to registers and that the #__mpyi_hw routine is called;
    Run the code step-by-step with the Disassembly view active. This action will lead you to the multiplication operation performed by the hardware multiplier;
    As the hardware multiplication routine source code is not available, switch to Assembly view only.

## Slide 27: Lab8b: Multiplication with hardware multiplier (8/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Hardware multiplication routine analysis with the “*” operator (continued):
    The routine starts with a PUSH of the Status Register onto the stack and then disables the interrupts (this always occurs when using the hardware multiplier peripheral);
    The next line of code exchanges data with the HW;
    When the routine exits, the SR is popped (POP instruction) from the system stack, restoring the previous CPU status.
    The routine finishes with the RETA instruction.

## Slide 28: Lab8b: Multiplication with hardware multiplier (9/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Hardware multiplication operation analysis with direct registers access:
    Switch to the C view;
    Put the cursor at line 72 of code {MPY = a} and Run to line;
    The routine call operation, as shown in the Disassembly view, is not stepped through;
    This exemplifies an effective energy saving procedure because less clock cycles are performed.

## Slide 29: Lab8b: Multiplication with hardware multiplier (10/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Measurement of the multiply operation execution time:
    Restart the application. It will run from the beginning;
    Put the cursor on line 77 of code {_BIS_SR(LPM4)} and Run to line;
    Measure the width of the time pulses using the oscilloscope;
    The first time pulse corresponds to the hardware multiplication routine with the operator “*”, which generates a pulse width of 42 sec;

## Slide 30: Lab8b: Multiplication with hardware multiplier (11/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Measurement of the multiply operation execution time (continued):
    The second time pulse corresponds to the hardware multiplication operation, generating a pulse width of 19 sec;
    Comparing both time pulses with the time pulse obtained in Lab8a, it can be seen how use of the hardware multiplier can significantly reduce the time required for a multiply operation;
    Not only does the hardware multiplier save time compared with the software multiplier, it also allows the processor to go to sleep much faster, and therefore saves the battery, which his important in low-power applications.

## Slide 31: Lab8c: RMS and active power calculation (1/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Project files:
  C source files: Chapter 12 > Lab8 > Lab8c_student.c
Overview:
  This laboratory explores and analyses the MSP430 performance when it makes multiplication operations using the hardware multiplier peripheral;
  It performs the typical real-world task of calculating the active power and the RMS value of an electrical signal.
  The execution times are measured with an oscilloscope.

## Slide 32: Lab8c: RMS and active power calculation (2/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  This laboratory only uses Port P2.1 connected to LED2 in order to measure the execution time of the task;
  It uses the default configuration of the FLL+;
  All of the clock signals required for the operation of the components of the device assume their default values.

## Slide 33: Lab8c: RMS and active power calculation (3/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  The application starts by stopping the Watchdog Timer;
  Two _NOP() instructions are provided to associate breakpoints in order to read current and voltage samples (N = 200) from files;
  Power is computed applying the following formula:

## Slide 34: Lab8c: RMS and active power calculation (4/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization (continued):
  A signed multiply operation is performed by writing the first sample of current to MPYS and the first sample of voltage to OP2;
  The multiplication result is stored in the RESHI and RESLO registers;
  A loop is performed with a signed multiply and accumulate (MACS) operation;
  The final result is transferred from RESHI and RESLO registers to the long variable result;

## Slide 35: Lab8c: RMS and active power calculation (5/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization (continued):
  The power is computed by dividing the variable result by the number of samples (N);
  Port P2.1 is active between MACS operations;
  The RMS current and RMS voltage values are calculated from the following expressions:

## Slide 36: Lab8c: RMS and active power calculation (6/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization (continued):
  The computing procedure is similar, with the exception of the square root (sqrt) operation;
  P2.1 is active throughout the current RMS value calculation;
  The times to execute the sqrt and division operations are determined when the RMS voltage value is calculated;
  This application ends by entering into LPM4.

## Slide 37: Lab8c: RMS and active power calculation (7/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  Go to Properties > TI Debug Settings and select Target tab. Uncheck the automatically step over functions without debug information when source stepping in order to allow you to step into the multiplication routine.
  Go to Properties > C/C++ Build > Linker MSP430 Linker v3.0 > General options and choose the option 16 (default) at the Link in hardware version of RTS mpy routine. With this linker option, the application will be built with the 16-bit hardware multiplier in the Experimenter’s board.
  Rebuild the project and download to the target.

## Slide 38: Lab8c: RMS and active power calculation (8/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Loading samples from files:
    Insert a breakpoint at line 61 of code (first _NOP() operation);
    Edit Breakpoint Properties and choose the Read Data from file action;
    Fill all fields with the required data:
      File: i.txt;
      Wrap around: True;
      Start address: &I;
      Length: 200.

## Slide 39: Lab8c: RMS and active power calculation (9/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Loading samples from files (continued):
    Include a breakpoint at line 63 of code (second _NOP() operation);
    Edit Breakpoint Properties and choose the Read Data from file action;
    Fill all fields with the required data:
      File: u.txt;
      Wrap around: True;
      Start address: &u;
      Length: 200.

## Slide 40: Lab8c: RMS and active power calculation (10/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Loading samples from files (continued):
    Alternatively, import a breakpoint from the file Lab8c_breakpoint.bkpt;
    Put the cursor at line 67 of code and Run to line;
    In the Variables view, add global variables i and u;
    Verify the data inside these arrays.

## Slide 41: Lab8c: RMS and active power calculation (11/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Computing active power:
    Connect the oscilloscope probe to port P2.1, which is available on Header 4 pin 2;
    Put the cursor at line 88 of code and Run to line;
    In the Variables view, add the global variable P and format it to decimal;
    The active power is around 1204 W;
    The pulse width: 5.4 msec (200 MACS operations).

## Slide 42: Lab8c: RMS and active power calculation (12/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Compute RMS current value:
    Starting at the last step of the previous task, put the cursor on line 105 of code {MPYS = u[0]} and Run to line;
    Add a global variable I (RMS voltage);
    The value is 10;
    Pulse width: 12.6 msec (200 MACS operations, 1 division operation and 1 square root operation).

## Slide 43: Lab8c: RMS and active power calculation (13/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Compute RMS voltage value:
    Starting on the last step of the previous task, put the cursor on line 121 of code {_BIS_SR(LPM4)} and Run to line;
    Add a global variable U (RMS voltage);
    The value is 240;
    The pulse width: 6.8 msec (200 MACS operations).

## Slide 44: Quiz (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
1. The Hardware Multiplier peripheral module is implemented in the:
  (a) eZ430-F2013 hardware development tool;
  (b) eZ430-RF2500 hardware development tool;
  (c) Experimenter’s board;
  (d) None of above.
2. The Hardware Multiplier supports:
  (a) Unsigned and signed multiply;
  (b) Unsigned and signed multiply and accumulate;
  (c) 16×16 bits, 16×8 bits, 8×16 bits, 8×8 bits;
  (d) All of above.

## Slide 45: Quiz (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
3. The RESHI result register stores:
  (a) The low word of the result;
  (b) The high word of the result;
  (c) The extended sign of the result;
  (d) The carry of the result.
4. The MSB bit of RESHI register for the Signed multiply contains:
  (a) The sign of the result;
  (b) The MSB of the result;
  (c) The carry of the result;
  (d) None of above.

## Slide 46: Quiz (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
5. A SUMEXT = 0 in a MACS operation indicates a result:
  (a) Positive;
  (b) Zero;
  (c) All of above;
  (d) None of above.
6. The RESHI register contents for a signed multiplication operation are in which data format:
  (a) Straight binary;
  (b) Two’s complement;
  (c) One’s complement;
  (d) None of above.

## Slide 47: Quiz (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Answers:
  1. (c) Experimenter’s board.
  2. (d) All of above.
  3. (b) The high word of the result.
  4. (a) The sign of the result.
  5. (c) All of above.
  6. (b) Two’s complement.