## Slide 1: Chapter 13 Flash Programming
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Notes: <number>

## Slide 2: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Introduction
Flash memory operation and segmentation
Write/erase modes
Access during write/erase
Flash memory controller registers
Laboratory 9: Flash write/erase operations
Quiz

## Slide 3: Introduction (1/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Memory in general is broadly classified as read-only memory (ROM) or random-access memory (RAM);
Flash memory is a hybrid of ROM and RAM;
Flash memory is:
    Low cost;
    Electrically programmable;
    Fast to read from;
    High density;
    Reliable;
    Non-volatile.

## Slide 4: Introduction (2/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
MSP430Fxxx(x) flash memory structure is:
  Divided into segments;
  Allows bit-, byte- and word- addressing and programming;
  Must be erased in segments.
Flash memory controller:
  Controls programming and erase operations;
  Has 3 or 4 registers (see the device-specific data sheet);
  Has a timing generator:
    Sourced from ACLK, SMCLK, or MCLK;
    Flash timing generator operating frequency: ~257 kHz < f(FTG) < ~476 kHz (see device-specific data);
    The selected clock source should be divided using the FNx bits to meet the frequency requirements of f(FTG).

## Slide 5: Introduction (3/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Flash memory controller:
  Timing generator block diagram:
  Uses a voltage generator to supply programming and erase voltages. The output voltage must be stable.

## Slide 6: Introduction (4/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
An MSP430 flash device can be programmed via:
  JTAG interface (requires four signals, ground and optionally VCC and RST/NMI);
  Bootstrap Loader (using a UART serial interface);
  Custom solution (using one of the interfaces available and through user developed software).
Additional information (TI Application Notes & Reports ):
  MSP430 flash memory characteristics <slaa334a.pdf>
    Physics behind MSP430 data-sheet specifications;
    Recommendations for correct MSP430 flash handling.

## Slide 7: Introduction (5/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Additional information (TI Application Reports & Presentations):
  Understanding MSP430 flash data retention <slaa392.pdf>
    Data retention for the MSP430 flash memory;
    Major effect of high temperatures on flash data retention.
  Features of the MSP430 bootstrap loader <slaa089d.pdf>
    Specific entry sequence applied to specific device pins, followed by an additional sequence of commands to initiate the required function;
    The BSL code is stored in a special section of ROM (cannot be overwritten by other applications);
    Triggered by toggling the TCK pin on the JTAG port;
    It uses the UART communication protocol (9600 baud);
    Same functions as the JTAG interface, with the exception of the security fuse programming.

## Slide 8: Introduction (6/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Additional information (TI Application Reports & Presentations):
  Application of bootstrap loader in MSP430 with flash hardware and software proposal <slaa096.pdf>
    Simple and low-cost hardware and software (C code) solutions to access the bootstrap loader (BSL) functions via the serial port (RS-232) of a PC.
  Solid state voice recorder using MSP430 flash <slaa123.pdf>
    Development of a solid state voice recorder (analogue voice pattern conversion to digital data) with real-time storage;
    Flexibility of in-system programmable flash memory.

## Slide 9: Introduction (7/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Additional information (TI Application Reports & Presentations):
  Programming a flash-based MSP430 using the JTAG interface <slaa149d.pdf>
    Functions required to erase, program, and verify the MSP430’s flash memory module using the JTAG interface;
    Program the JTAG access security fuse;
    The security fuse is a one-time only burn (further flash memory writes and erasures are impossible);
    Prohibits flash programming and further JTAG access.
  A Flash monitor for the MSP430 <slaa341.pdf>
    Development of a flash monitor program to evaluate the device’s memory;
    Update the flash contents with new application code via a universal USART peripheral interface.

## Slide 10: Flash memory operation and segmentation (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
MSP430 flash memory block diagram:
  MSP430FG4618 (Experimenter’s board) has two flash memory arrays.

## Slide 11: Flash memory operation and segmentation (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The flash memory partitions (device-specific data):
    Main memory section (two or more 512-byte segments);
    Information memory section (two 128-byte segments), located at lower memory addresses, in the address space immediately following RAM.

## Slide 12: Flash memory operation and segmentation (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
2xx family: SegmentA (information A):
  eZ430-F2013;
  eZ430-RF2500.
  Partition of the information memory, can be locked to separate it from all other segments:
    LOCKA = 1:
      SegmentA cannot be written or erased;
      All information memory is protected from erasure during a mass erase or production programming.
    LOCKA = 0:
      SegmentA can be erased and written;
      All information memory is erased during a mass erase or production programming.

## Slide 13: Flash memory write/erase modes
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Default mode: read mode (memory operates like ROM):
  Flash memory is not being erased or written;
  Flash timing generator off;
  Voltage generator off.
The flash memory write/erase modes are selected with the BLKWRT, WRT, GMERAS, MERAS, and ERASE bits;
To stop any write or erase operation before its normal completion, set the EMEX bit. When EMEX = 1:
  All flash operations cease;
  The flash returns to read mode;
  All bits in the FCTL1 register are reset.

## Slide 14: Erase modes (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Erase modes:
  Initiated from within flash memory:
    All timing is controlled by the flash controller;
    CPU is held during the erase cycle (dummy write);
    CPU resumes code execution after the erase cycle finishes.
  Initiated from RAM:
    CPU is not held and can execute code from RAM;
    CPU can access any flash address again when BUSY = 0 (end of the erase cycle).

## Slide 15: Erase modes (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Erase modes:
1 This bit is only present in the MSP430FG461x devices
2 This bit is only present in the MSP430F2xxx devices

## Slide 16: Erase mode procedure (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Segment Erase:
    Check BUSY = 0 (FCTL3 register);
    LOCK = 0 (FCTL3 register);
    ERASE = 1 (FCTL1 register);
    Perform a dummy write to the segment to be erased (Any write, clear or logical operation);
    A segment erase requires approximately 5000 cycles of the timing generator (during this period BUSY = 1);
    Wait for BUSY = 0 (FCTL3 register).
    LOCK = 1 (FCTL3 register) to prevent accidental writes.

## Slide 17: Erase mode procedure (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Mass Erase (all main memory segments):
  Similar to Segment erase;
  Requires setting MERAS bit instead of ERASE bit in the FCTL1 register.
All Erase (all segments):
  Requires setting (GMERAS), MERAS and ERASE bits in the FCTL1 register.

## Slide 18: Erase mode procedure (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Segment and mass erase modes procedure:

## Slide 19: Write modes
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A byte/word write cycle can be initiated from within flash memory or from RAM;
A block write cycle cannot be initiated from within flash memory (only from RAM);
The block write can be used to accelerate the flash write process (twice as fast as byte/word mode), when many sequential bytes or words need to be programmed.

## Slide 20: Write modes procedure (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Byte/word write:
  Check BUSY = 0 (FCTL3 register);
  LOCK = 0 (FCTL3 register);
  WRT = 1 (FCTL1 register);
  Write the byte or word (element) to the appropriate address (starts the timing generator);
  To write an element requires 33 cycles of the timing generator (during this period BUSY = 1);
  Wait for BUSY = 0 (FCTL3 register);
  LOCK = 1 (FCTL3 register) to prevent accidental writes.

## Slide 21: Write modes procedure (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Byte/word write:

## Slide 22: Write modes procedure (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Write a block (successive write of 64 bytes in a block):
  Check BUSY = 0 (FCTL3 register);
  LOCK = 0 (FCTL3 register);
  WRT = 1 and BLKWRT = 1 (FCTL1 register);
  Write the element in the block to the appropriate address (starts the timing generator);
  Loop until WAIT = 1 (FCTL3 register);
  Repeat write next element until all have been written;
  Set WRT = 0 and BLKWRT = O (FCTL1 register);
  A block write requires 20 cycles Timing Generator/element, + overhead: 15 more cycles (during this period BUSY = 1);
  Wait for BUSY = 0 (FCTL3 register);
  LOCK = 1 (FCTL3 register) to prevent accidental writes.

## Slide 23: Write modes procedure (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Block (64-byte blocks) write:

## Slide 24: Flash memory access during write/erase
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
When BUSY = 1, any write or any erase operation initiated from RAM or from flash memory triggers the following conditions:
Flash operation | Flash access | Wait | Result
Any erase Byte/word write | Read | 0 | ACCVIFG = 0 Value read: 03FFFh
 | Write | 0 | ACCVIFG = 0 Write ignored
 | Instruction fetch | 0 | ACCVIFG = 0 CPU fetch: 03FFFh
Block write | Any | 0 | ACCVIFG = 1 LOCK = 1
 | Read | 1 | ACCVIFG = 0 Value read: 03FFFh
 | Write | 1 | ACCVIFG = 0 Flash written
 | Instruction fetch | 1 | ACCVIFG = 1 LOCK = 1

## Slide 25: Registers (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
FCTL1, Flash Memory Control Register (MSP430FG4618)
(1) MSP430F2xx(x) family devices. Not present on MSP430F2013.
(2) MSP430FG461x devices.

## Slide 26: Registers (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
FCTL2, Flash Memory Control Register (MSP430FG4618)

## Slide 27: Registers (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
FCTL3, Flash Memory Control Register (MSP430FG4618)
Bit |  | Description
7 | FAIL | Operation failure of the clock source, f(FTG), or a flash operation is aborted from an interrupt when EEIEX = 1 when FAIL = 1
6 | LOCKA(1) | Segment A locked and all information memory is protected from erasure during a mass erase when LOCKA = 1
5 | EMEX | Emergency exit when EMEX = 1
4 | LOCK | Locks the flash memory for writing or erasing when LOCK = 1
3 | WAIT | WAIT = 0  while flash memory is being written to WAIT = 1  when flash memory is ready for the next byte/word write
2 | ACCVIFG | Access violation interrupt flag ACCVIFG = 1 when interrupt is pending
1 | KEYV | Flash security key violation KEYV = 1 when FCTLx password was written incorrectly (not 0A5h)
0 | BUSY | Flash timing generator is busy when BUSY = 1

## Slide 28: Laboratory 9: Flash write/erase operations (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Objective:
  Using the MSP430FG4618 device of the Experimenter’s board provide flash write/erase operations.
Details:
  Like the previous exercise (Lab8), this laboratory is composed of some sub-tasks.
  This laboratory has been developed for the Code Composer Essentials version 3 software development tool only.

## Slide 29: Laboratory 9: Flash write/erase operations (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Overview:
  The TI MSP430 has internal flash memory that can be used for data storage;
  Two different methods of writing to the flash memory are studied in this laboratory;
  The first method requires the CPU execution of the code resident in flash memory. The consequences of this procedure are discussed;
  In the second part of the laboratory, the flash write and erase operations are conducted with the CPU executing the code resident in RAM. The important details are highlighted.

## Slide 30: Lab9a. Flash memory programming with the CPU executing the code in the flash memory
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Project files:
  C source files: Chapter 13>Lab9> Lab9a_student.c
  Chapter 13>Lab9> lnk_msp430fg4618.cmd
  Solution file: Chapter 13>Lab9> Lab9a_solution.c
A. Resources:
  This laboratory uses the flash memory controller. The operation of this device is analyzed using a digital output port (P2.1).
  The project must be compiled, including the files Lab9_student.c and lnk_msp430fg4618.cmd.
  The code is resident in the flash memory, so whenever a flash write or erase operation occurs, the CPU access to this memory space is automatically inhibited.

## Slide 31: Lab9a. Flash memory programming with the CPU executing the code in the flash memory
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  The software begins by disabling the Watchdog Timer. Port P2.1 is set as an output at logic low level;
  The flash memory controller is configured with the clock MCLK/3 (fFTG operating frequency is located within the specified limits from 257 kHz to 476 kHz);
  A set of routines are provided to erase, write and copy the contents of a segment. The main tasks related to the flash memory handling are presented using this set of routines.

## Slide 32: Lab9a. Flash memory programming with the CPU executing the code in the flash memory
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  The information Segments A and B are erased;
  Bytes are written to SegmentA;
  Words are written to SegmentB;
  The contents of the information memory SegmentA are copied to the information SegmentB, the values in the latter being overwritten.

## Slide 33: Lab9a. Flash memory programming with the CPU executing the code in the flash memory
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  Flash memory controller configuration:
    Configure the register FCTL2 to use the clock MCLK/3 divided by 3 (Do not forget to enter the password to access the register from now on).
    FCTL2 = ______________________;
  Segment erase routine:
    Configure the registers FCTL1 and FCTL3 in order to initiate the flash segment erase process by writing to an address belonging to the segment to be erased:
    FCTL1 = ______________________;
    FCTL3 = ______________________;

## Slide 34: Lab9a. Flash memory programming with the CPU executing the code in the flash memory
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  Segment erase routine:
    Use block flash write and erase operations after erasing the segment:
    FCTL3 = ______________________;
  Flash write routine:
    Configure the registers in order to start writing to the flash memory:
    FCTL1 = ______________________;
    FCTL3 = ______________________;
    Set up block write and erase operations and when the write is complete, disable further writes:
    FCTL1 = ______________________;
    FCTL3 = ______________________;

## Slide 35: Lab9a. Flash memory programming with the CPU executing the code in the flash memory
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Execution time for the information segments erase operation:
    Put the cursor on line 124 of code, located just after the second port P2.1 switching state;
    Execute the software until the cursor position is reached;
    The erase operation timing can be seen in an oscilloscope probe connected to pin 2 of Header 4.

## Slide 36: Lab9a. Flash memory programming with the CPU executing the code in the flash memory
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Bytes write in the information memory A:
    The routine write_char_flash allows writing a byte to flash memory (receives the memory address);
    Open the memory window, and add the address of the information memory A. Its contents become visible after rendering;
    Change the presentation of the memory contents:
      Choose the option Column Size 1, from the context menu of the memory window, through the option Format.
    Now with the the execution of the for loop, the flash contents are being written sequentially.

## Slide 37: Lab9a. Flash memory programming with the CPU executing the code in the flash memory
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Bytes write in the information B memory:
    This routine is similar to the previous one;
    Note that now the flash write address is increased by two since a word occupies two bytes of memory;
    The information is more readily observed when the memory contents display mode is restored to its initial state;
    Reset the default conditions in the option Format of the context menu.

## Slide 38: Lab9a. Flash memory programming with the CPU executing the code in the flash memory
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Copy the contents of the information A memory to information B memory:
    The output port P2.1 is enabled before the copy process begins;
    The copy routine receives the beginning of the source information segment and the beginning of the destination information segment;
    The information is then successively read and written from one segment to another;
    The port P2.1 is disabled at the end of the copy process;
    Measure the task execution time using an oscilloscope.

## Slide 39: Lab9a. Flash memory programming with the CPU executing the code in the flash memory
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Flash memory controller configuration:
  FCTL2 = FWKEY | FSSEL0 | FN1;
// MCLK/3 for Flash Timing Generator
Segment erase routine:
FCTL1 = FWKEY | ERASE; // Set Erase bit
FCTL3 = FWKEY; // Clear Lock bit
// Block flash write and erase operations after erasing
// the segment:
FCTL3 = FWKEY | LOCK; // Set LOCK bit
MSP-EXP430FG4618 | SOLUTION
Using the MSP-EXP430FG4618 Development Tool, implement flash memory programming with the CPU executing the code from the flash memory. | 

## Slide 40: Lab9a. Flash memory programming with the CPU executing the code in the flash memory
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Flash write routine:
  FCTL1 = FWKEY | ERASE; // Set Erase bit
  FCTL3 = FWKEY; // Clear Lock bit
  // Block the flash write and erase operations and
  // disable the writing bit after the writing process in
  // the segment:
  FCTL3 = FWKEY | LOCK; // Set LOCK bit

## Slide 41: Lab9b. Flash memory programming with the CPU executing the code from RAM
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Project files:
  C source files: Chapter 13 > Lab9 > Lab9b_student.c
  Chapter 13 > Lab9 >
  lnk_msp430fg4618_RAM.cmd
  Solution file: Chapter 13 > Lab9 > Lab9b_solution.c
A. Resources:
  The tasks developed in the previous laboratory are executed again in this exercise. The difference is that this time the software is running from RAM;
  This process requires special procedures during the project build phase;
  The routines to run from RAM must be correctly set up. (The application begins by copying the routines from flash to RAM).

## Slide 42: Lab9b. Flash memory programming with the CPU executing the code from RAM
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  The directive MEMORY determines the device's memory configuration;
  The memory can be organized in accordance with the system needs;
  This directive identifies the memory ranges that are physically present on the device;
  Each of these ranges has a set of features, such as:
    Name;
    Initial address;
    Length;
    Optional attributes set;
    Optional filling specifications.

## Slide 43: Lab9b. Flash memory programming with the CPU executing the code from RAM
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  The directive Memory is organized as described below:
  MEMORY
  {
  name 1 [(attr)] : origin = constant, length = constant [, fill = constant]
  .
  .
  name n [(attr)] : origin = constant, length = constant [, fill = constant]
  }

## Slide 44: Lab9b. Flash memory programming with the CPU executing the code from RAM
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  The directive SECTIONS controls how the sections are built and memory is reserved;
  The control is as follows:
    Describes how the input and output sections are related;
    Defines the output sections in the executable program;
    Defines where the output sections are placed in memory;
    Allows changing the name of the output sections.
  The directive SECTIONS is organized as described below.
  SECTIONS
  {
  name : [property [, property] [, property] . . . ]
  name : [property [, property] [, property] . . . ]
  name : [property [, property] [, property] . . . ]
  }

## Slide 45: Lab9b. Flash memory programming with the CPU executing the code from RAM
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  The following directives are possible;
  Reserve memory space to load the section:
  Syntax: load = allocation or
  Allocation or
  > allocation
  Define the memory space where the code belonging to the section will run:
  Syntax: run = allocation or
  run > allocation

## Slide 46: Lab9b. Flash memory programming with the CPU executing the code from RAM
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  In this project we wish to write the code in flash memory, but we want it to be executed from RAM;
  The Linker offers a very simple way to accomplish this task;
  The memory space where the code is stored is associated with another memory space, where the code will run;
  The application transfers the code to the memory space where it will be executed.

## Slide 47: Lab9b. Flash memory programming with the CPU executing the code from RAM
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  The memory spaces needed to store the routines are defined in the lnk_msp430fg4618_RAM.cmd file.
  RAM_MEM : origin = 0x1100, length = 0x0200
  FLASH_MEM : origin = 0x3100, length = 0x0200
  Also are defined the sections:
  .FLASHCODE : load = FLASH_MEM, run = RAM_MEM
  .RAMCODE : load = FLASH_MEM

## Slide 48: Lab9b. Flash memory programming with the CPU executing the code from RAM
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  The software for this laboratory has the same structure as the previous one;
  The directive #pragma CODE_SECTION (symbol, "section name") reserves space for the "symbol" in a section called "section name". Thus, the routines are stored in section ".FLASHCODE“;
  The routine copy_flash_to_RAM transfers the flash contents to RAM;
  The files Lab9_student.c and lnk_msp430fg4618_RAM.cmd must be used during the compilation.
  Now, the code is executed from RAM. Check, the state of the Wait bit of the register FCTL3, whenever appropriate.

## Slide 49: Lab9b. Flash memory programming with the CPU executing the code from RAM
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  Flash storage management routines:
    To store the flash management routines in the section ".FLASHCODE" complete the empty spaces:
  #pragma CODE_SECTION(______________,____________)
  void erase_segment(int address)
  #pragma CODE_SECTION(______________,____________)
  void write_char_flash(int address, char value)
  #pragma CODE_SECTION(______________,____________)
  void write_int_flash(int address, int value)
  #pragma CODE_SECTION(______________,____________)
  void copy_seg_flash(int address_source, int address_destination)

## Slide 50: Lab9b. Flash memory programming with the CPU executing the code from RAM
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  Check the flag wait:
    At software key points, and whenever writing or erasing the flash memory, perform a delay before proceeding with the data write;
    Complete the following line of code in order to suspend the program flow while the Wait flag is not enabled:
    while(_____________);

## Slide 51: Lab9b. Flash memory programming with the CPU executing the code from RAM
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Analyse the differences between the different versions of the routines;
  Note the successive delays used in the different versions to be executed from RAM.

## Slide 52: Lab9b. Flash memory programming with the CPU executing the code from RAM
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Flash management routines storage:
  #pragma CODE_SECTION(erase_segment,".FLASHCODE")
  void erase_segment(int address)
  #pragma CODE_SECTION(write_char_flash,".FLASHCODE")
  void write_char_flash(int address, char value)
  #pragma CODE_SECTION(write_int_flash,".FLASHCODE")
  void write_int_flash(int address, int value)
  #pragma CODE_SECTION(copy_seg_flash,".FLASHCODE")
  void copy_seg_flash(int address_source, int address_destination)
MSP-EXP430FG4618 | SOLUTION
Using the MSP-EXP430FG4618 Development Tool, implement flash memory programming with the CPU executing the code from RAM. | 

## Slide 53: Lab9b. Flash memory programming with the CPU executing the code from RAM
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Check the flag wait:
  while(FCTL3&BUSY); // Check BUSY flag
MSP-EXP430FG4618 | SOLUTION
Using the MSP-EXP430FG4618 Development Tool, implement flash memory programming with the CPU executing the code from RAM. | 

## Slide 54: Quiz (1/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
1. Features of flash memory are:
  (a) Low cost;
  (b) Fast to read from;
  (c) Non-volatile;
  (d) All of above.
2. The timing generator of the MSP430 flash memory can be sourced by:
  (a) ACLK;
  (b) SMCLK;
  (c) MCLK;
  (d) All of above.

## Slide 55: Quiz (2/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
3. An MSP430 flash device can be programmed via:
  (a) JTAG interface;
  (b) Bootstrap loader;
  (c) Custom software solution;
  (d) All of above.
4. Flash memory is partitioned into:
  (a) Two sections;
  (b) Three sections;
  (c) Four sections;
  (d) None of above.

## Slide 56: Quiz (3/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
5. When LOCKA is set:
  (a) SegmentA can be written and erased;
  (b) SegmentA cannot be written or erased;
  (c) All information memory is protected from erasure during a mass erase or production programming;
  (d) All information memory is erased during a mass erase or production programming.
6. When EMEX is set:
  (a) Write operation begins;
  (b) Erase operation begins;
  (c) All flash operations cease;
  (d) None of above.

## Slide 57: Quiz (4/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
7. An erase cycle can be initiated from:
  (a) Within flash memory;
  (b) From RAM;
  (c) Within flash memory or from RAM;
  (d) Simultaneously within flash memory and from RAM.
8. For the MSP430FG4618 when GMERAS and MERAS bits are set:
  (a) A segment is erased;
  (b) All main memory is erased – selected array;
  (c) All information memory is erased – selected array;
  (d) All flash memory is erased – both arrays.

## Slide 58: Quiz (5/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
9. When BLKWRT and WRT are set:
  (a) A byte/word write cycle is initiated within flash memory;
  (b) A block write cycle is initiated from RAM;
  (c) A block write cycle is initiated within flash memory;
  (d) A byte/word write cycle is initiated from RAM.
10. When reading within flash memory while BUSY = 1:
  (a) ACCVIFG = 1 and the value read is 03FFFh;
  (b) ACCVIFG = 0 and the value read is 03FFFh;
  (c) ACCVIFG = 1 and LOCK = 1;
  (d) None of above.

## Slide 59: Quiz (6/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
11. The 16 bit of the FCTL1 flash memory controller control register must have:
  (a) All its high-byte bits at 0;
  (b) A 0x096h password in the high-byte to read from flash memory and a 0x0A5h password must be written to the high byte to write to the flash memory;
  (c) A 0x05Ah password in the high-byte to read and write to the flash memory;
  (d) All its high-byte bits at 1.
12. When the FAIL bit of the control register is set:
  (a) The clock source has failed;
  (b) The flash operation was aborted;
  (c) An access violation occurred;
  (d) The flash security key was incorrect.

## Slide 60: Quiz (7/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Answers:
  1. (d) All of above.
  2. (d) All of above.
  3. (d) All of above.
  4. (a) Two sections.
  5. (b) SegmentA cannot be written or erased.
  6. (c) All flash operations cease.
  7. (c) Within flash memory or from RAM.
  8. (d) All flash memory is erased – both arrays.
  9. (b) A block write cycle is initiated from RAM.
  10. (a) ACCVIFG = 1 and the value read is 03FFFh.
  11. (b) A 0x096h password in the high-byte to read from flash memory and a 0x0A5h password must be written in the high byte to write to the flash memory.
  12. (a) The clock source has failed.