## Slide 1: Chapter 14 Communications USCI Module
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Notes: <number>

## Slide 2: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
MSP430 communications interfaces
USCI module introduction
USCI operation: UART mode
USCI operation: SPI mode
USCI operation: I2C mode
USCI registers: UART, SPI and I2C modes
Lab10b: USCI echo test
Quiz

## Slide 3: MSP430 communications interfaces (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Equipped with three serial communication interfaces:
  USART (Universal Synchronous/Asynchronous Receiver/Transmitter):
    UART mode;
    SPI mode;
    I2C (on ‘F15x/’F16x only).
  USCI (Universal Serial Communication Interface):
    UART with Lin/IrDA support;
    SPI (Master/Slave, 3 and 4 wire modes);
    I2C (Master/Slave, up to 400 kHz).
  USI (Universal Serial Interface):
    SPI (Master/Slave, 3 & 4 wire mode);
    I2C (Master/Slave, up to 400 kHz).

## Slide 4: MSP430 communications interfaces (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Comparison between the communication modules:
USART | USCI | USI
UART: - Only one modulator - n/a - n/a - n/a | UART: - Two modulators support n/16 timings - Auto baud rate detection - IrDA encoder & decoder - Simultaneous USCI_A and USCI_B (2 channels) | 
SPI: - Only one SPI available - Master and Slave Modes - 3 and 4 Wire Modes | SPI: - Two SPI (one on each USCI_A and USCI_B) - Master and Slave Modes - 3 and 4 Wire Modes | SPI: - Only one SPI available - Master and Slave Modes
I2C: (on ‘15x/’16x only) - Master and Slave Modes - up to 400kbps | I2C: - Simplified interrupt usage - Master and Slave Modes - up to 400kbps | I2C: - SW state machine needed - Master and Slave Modes

## Slide 5: USCI module introduction (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Although supporting UART, SPI and I2C, the USCI (Universal Serial Communication Interface) module is a communications interface specially designed to interconnect with high-speed industrial protocols:
  LIN (Local interconnect Network), used for low-cost modules in cars e.g. door modules, alarms, rain-sensors;
  IrDA (Infrared Data Association).
The USCI module is available in the following devices:
    MSP430F5xx;
    MSP430F4xx and MSP430FG41xx;
    MSP430F2xx.

## Slide 6: USCI module introduction (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The USCI module supports:
  Low power operating modes (with auto-start);
  Two individual blocks:
    USCI_A: UART and SPI;
    USCI_B: SPI and I2C.
  Double buffered TX/RX;
  Baud rate/bit clock generator:
    With auto-baud rate detect;
    Flexible clock source.
  RX glitch suppression;
  DMA enabled;
  Error detection.

## Slide 7: USCI module introduction (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
USCI block diagram:

## Slide 8: USCI operation: UART mode (1/17)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
In asynchronous mode, the USCI_Ax modules connect the MSP430 to an external system via two external pins, UCAxRXD and UCAxTXD;
UART mode is selected when the UCSYNC bit is cleared;
USCI transmits and receives characters asynchronously;
Timing for each character is based on the selected baud rate of the USCI;
Transmit and receive use the same clock frequency leading to the same baud rate;

## Slide 9: USCI operation: UART mode (2/17)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
USCI operation in UART mode block diagram:

## Slide 10: USCI operation: UART mode (3/17)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Recommended initialization/re-configuration process:
  Set UCSWRST (BIS.B #UCSWRST,&UCAxCTL1);
  Initialize all USCI registers with UCSWRST = 1 (including UCAxCTL1);
  Configure ports;
  Clear UCSWRST via software:
  (BIC.B #UCSWRST,&UCAxCTL1);
  Enable interrupts (optional) via UCAxRXIE and/or UCAxTXIE.

## Slide 11: USCI operation: UART mode (4/17)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Character format specified as follows:
  Start bit;
  Seven or eight data bits;
  Even/odd/no parity bit;
  Address bit (address-bit mode);
  One or two stop bits.
  The UCMSB bit controls the direction of the transfer and selects LSB (usual in UART communication) or MSB first.

## Slide 12: USCI operation: UART mode (5/17)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Asynchronous communication formats:
  Idle-line multiprocessor communication protocol (minimum of two devices):
    IDLE is detected after > 10 periods of continuous marks after the stop bit;
    The first character after IDLE is an address;
    Can be programmed to receive only address characters.

## Slide 13: USCI operation: UART mode (6/17)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Asynchronous communication formats (continued):
  Address-bit multiprocessor communication protocol (minimum of three devices):
    An extra bit in the received character marks an address character;
    UART can be programmed to receive only address characters.

## Slide 14: USCI operation: UART mode (7/17)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Automatic baud rate detection (UCMODEx = 11):
  Data frame is preceded by a synchronization sequence:
    Break: Detected when 11 or more continuous zeros (spaces) are received;
    Synch field: Data 055h inside a byte field.

## Slide 15: USCI operation: UART mode (8/17)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Automatic baud rate detection (UCMODEx = 11):
  The baud rate is calculated from a valid SYNC;
  Auto baud rate value stored in UxBR1, UxBR0 and UxMCTL (modulation pattern);
  BREAK time-out detect in hardware;
  Programmable delimiter time;

## Slide 16: USCI operation: UART mode (9/17)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
IrDA encoder and decoder (UCIREN = 1):

## Slide 17: USCI operation: UART mode (10/17)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
IrDA encoder and decoder (UCIREN = 1):
  IrDA encoding:
    Encoder sends a pulse for every zero bit in the transmit bit stream coming from the UART;
    Pulse duration (defined by UCIRTXPLx bits) specifies the number of half clock periods of the clock (UCIRTXCLK);
    Oversampling baud rate generator allows selection of IrDA standard 3/16 bit length.

## Slide 18: USCI operation: UART mode (11/17)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
IrDA encoder and decoder (UCIREN = 1):
  IrDA decoding:
  Programmable low or high pulse detection (UCIRRXPL) by the decoder;
  Programmable received pulse length filter adds noise filter capability as well as glitch detection.

## Slide 19: USCI operation: UART mode (12/17)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Automatic error detection:
  Glitch suppression prevents the USCI from being accidentally started;
  Any pulse on UCAxRXD shorter than the deglitch time (approximately 150 ns) will be ignored.
  Framing error UCFE: Set if the stop bit is missing from a received frame;
  Parity error UCPE: Set if there is a parity mismatch in a received frame;
  Receive overrun error UCOE: Set if UCAxRXBUF is overwritten;
  Break condition UCBRK:
    Set if all bits in the received frame = 0;
    Set the UCAxRXIFG if UCBRKIE bit is set.

## Slide 20: USCI operation: UART mode (13/17)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Enable the USCI receive enable bit URXEx:
  Clear UCSWRST;
  The falling edge of the start bit enables the baud rate generator;
  If a valid start bit is detected, a character will be received.
USCI transmit enable:
  Clear UCSWRST;
  Transmission is initiated by writing data to UCAxTXBUF;
  The baud rate generator is enabled;
  The data value in UCAxTXBUF is moved to the transmit shift register on the next BITCLK after the transmit shift register is empty;
  UCAxTXIFG is set when a new data value can be written into UCAxTXBUF.

## Slide 21: USCI operation: UART mode (14/17)
USCI baud rate generation:
  Standard baud rates from non-standard source frequencies;
  Two modes of operation (UCOS16 bit):
    Low-frequency baud rate;
    Oversampling baud rate.
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt

## Slide 22: USCI operation: UART mode (15/17)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Transmit bit timing:
  The timing for each character is the sum of the individual bit timings;
  A modulation feature of the baud rate generator reduces the cumulative bit error.
Two error sources for receive bit timing:
  Bit-to-bit timing error;
  Error between a start edge occurring and the start edge being accepted by the USCI module.

## Slide 23: USCI operation: UART mode (16/17)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
USCI interrupts:
  One interrupt vector for transmission and one interrupt vector for reception:
  USCI transmit interrupt operation:
    UCAxTXIFG interrupt flag is set by the transmitter to indicate that UCAxTXBUF is ready to accept another character;
    An interrupt request is generated if UCAxTXIE and GIE are also set;
    UCAxTXIFG is automatically reset if a character is written to UCAxTXBUF.

## Slide 24: USCI operation: UART mode (17/17)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
USCI interrupts (continued):
  USCI receive interrupt operation:
    UCAxRXIFG interrupt flag is set each time a character is received and loaded into UCAxRXBUF;
    An interrupt request is also generated if UCAxRXIE and GIE are set;
    UCAxRXIFG and UCAxRXIE are reset by a system reset PUC signal or when UCSWRST = 1;
    UCAxRXIFG is automatically reset when UCAxRXBUF is read.

## Slide 25: USCI operation: SPI mode (1/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Flexible interface:
  3- or 4-pin SPI;
  7- or 8-bit data length;
  Master or slave;
  LSB or MSB first.
S/W configurable clock phase and polarity;
Programmable SPI master clock;
Double buffered TX/RX;
Interrupt driven TX/RX (USCI_A and USCI_B share TX and RX vector);
Direct Memory Address ( DMA) enabled;
LPMx operation.

## Slide 26: USCI operation: SPI mode (2/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
USCI module: SPI mode block diagram:

## Slide 27: USCI operation: SPI mode (3/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
USCI module: SPI connections:

## Slide 28: USCI operation: SPI mode (4/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Serial data transmitted and received by multiple devices using a shared clock provided by the master;
Three or four signals are used for SPI data exchange:
  UCxSIMO: Slave in, master out;
  UCxSOMI: Slave out, master in;
  UCxCLK: USCI SPI clock;
  UCxSTE: Slave transmit enable:
    Enables a device to receive and transmit data and is controlled by the master;
    4 wire master, senses conflicts with other master(s);
    In 4 wire slave, externally controls TX and RX.

## Slide 29: USCI operation: SPI mode (5/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
USCI initialization/re-configuration process:
  Set UCSWRST (BIS.B #UCSWRST,&UCAxCTL1);
  Initialize all USCI registers with UCSWRST = 1 (including UCxCTL1);
  Configure ports;
  Clear UCSWRST via software (BIC.B #UCSWRST,&UCxCTL1);
  Enable interrupts (optional) via UCxRXIE and/or UCxTXIE.

## Slide 30: USCI operation: SPI mode (6/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Define the character format as presented earlier;
Define mode: Master or Slave;
Enable SPI transmit/receive clearing the UCSWRST bit;
Define serial clock control:
  UCxCLK is provided by the master on the SPI bus;
  Configure serial clock polarity and phase (UCCKPL and UCCKPH bits).

## Slide 31: USCI operation: SPI mode (7/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
USCI interrupts:
  One interrupt vector for transmission and one interrupt vector for reception:
  SPI transmit interrupt operation:
    UCxTXIFG interrupt flag is set by the transmitter to indicate that UCxTXBUF is ready to accept another character;
    An interrupt request is generated if UCxTXIE and GIE are also set;
    UCxTXIFG is automatically reset if the interrupt request is serviced or if a character is written to UCxTXBUF.

## Slide 32: USCI operation: SPI mode (8/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
USCI interrupts (continued):
  USCI receive interrupt operation:
    UCxRXIFG interrupt flag is set each time a character is received and loaded into UCxRXBUF;
    An interrupt request is also generated if UCxRXIE and GIE are set;
    UCxRXIFG and UCxRXIE are reset by a system reset PUC signal or when SWRST = 1;
    UCxRXIFG is automatically reset if the pending interrupt is serviced (when UCSWRST = 1) or when UCxRXBUF is read.

## Slide 33: USCI operation: SPI mode (9/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
USCI interrupts (continued):
  SPI TX interrupt: SPI RX interrupt:

## Slide 34: USCI operation: I2C mode (1/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The I2C mode supports any master or slave I2C-compatible device (Specification v2.1);
Each I2C device is recognized by a unique address and can operate as either a transmitter or a receiver, as well as either the master or the slave;
A master initiates a data transfer and generates the clock signal SCL;
Any device addressed by a master is considered a slave;
Communication using the bi-directional serial data (SDA) and serial clock (SCL) pins;

## Slide 35: USCI operation: I2C mode (2/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
I2C mode block diagram:

## Slide 36: USCI operation: I2C mode (3/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
I2C mode block diagram:

## Slide 37: USCI operation: I2C mode (4/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Initialized using the sequence given earlier;
I2C serial data:
  One clock pulse is generated by the master for each data bit transferred;
  Operates with byte data (MSB transferred first);
  The first byte after a START condition consists of a 7-bit slave address and the R/W bit:
    R/W = 0: Master transmits data to a slave;
    R/W = 1: Master receives data from a slave.
  The ACK bit is sent from the receiver after each byte on the 9th SCL clock.

## Slide 38: USCI operation: I2C mode (5/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
I2C addressing modes (7-bit and 10-bit addressing modes);
I2C module operating modes:
  Master transmitter;
  Master receiver;
  Slave transmitter;
  Slave receiver.
Arbitration procedure is invoked if two or more master transmitters simultaneously start a transmission on the bus;

## Slide 39: USCI operation: I2C mode (6/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
I2C Clock generation and synchronization:
  SCL is provided by the master on the I2C bus;
  Master mode: BITCLK is provided by the USCI bit clock generator;
  Slave mode: the bit clock generator is not used.

## Slide 40: USCI operation: I2C mode (7/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
I2C interrupts:
  One interrupt vector for transmission and one interrupt vector for reception;
  I2C transmit interrupt operation:
    UCBxTXIFG interrupt flag is set by the transmitter to indicate that UCBxTXBUF is ready to accept another character;
    An interrupt request is also generated if UCBxTXIE and GIE are set;
    UCBxTXIFG is automatically reset if a character is written to UCBxTXBUF or a NACK is received.

## Slide 41: USCI operation: I2C mode (8/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
I2C interrupts (continued):
  I2C receive interrupt operation:
    UCBxRXIFG interrupt flag is set each time a character is received and loaded into UCxRXBUF;
    An interrupt request is also generated if UCBxRXIE and GIE are set;
    UCBxRXIFG and UCBxRXIE are reset by a system reset PUC signal or when SWRST = 1;
    UCxRXIFG is automatically reset when UCBxRXBUF is read.

## Slide 42: USCI operation: I2C mode (9/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
I2C interrupts (continued):
  I2C transmit/receive interrupt operation:

## Slide 43: USCI operation: I2C mode (10/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
I2C interrupts (continued):
  I2C state change interrupt flags:
    Arbitration-lost, UCALIFG: Flag is set when two or more transmitters start a transmission simultaneously, or operates as master but is addressed as a slave by another master;
    Not-acknowledge interrupt, UCNACKIFG: Flag set when an acknowledge is expected but is not received;
    Start condition detected interrupt, UCSTTIFG: Flag set when the I2C module detects a START condition together with its own address while in slave mode;
    Stop condition detected interrupt, UCSTPIFG: Flag set when the I2C module detects a STOP condition while in slave mode.

## Slide 44: USCI operation: I2C mode (11/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
I2C interrupts (continued):
I2C TX interrupt: I2C RX interrupt:

## Slide 45: USCI registers (UART, SPI and I2C modes) (1/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UCAxCTL0, USCI_Ax Control Register 0 (UART, SPI)
UCBxCTL0, USCI_Bx Control Register 0 (SPI, I2C)
Mode | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
UART | UCPEN | UCPAR | UCMSB | UC7BIT | UCSPB | UCMODEx |  | UCSYNC=0
SPI | UCCKPH | UCCKPL | UCMSB | UC7BIT | UCMST | UCMODEx |  | UCSYNC=1
I2C | UCA10 | UCSLA10 | UCMM | Unused | UCMST | UCMODEx=11 |  | UCSYNC=1
Bit |  | UART mode description |  | SPI mode description |  | I2C mode description
7 | UCPEN | Parity enable when UCPEN = 1 | UCCKPH | Clock phase select: UCCKPH = 0  Data is changed on the 1st UCLK edge and captured on the next one. UCCKPH = 1  Data is captured on the 1st UCLK edge and changed on the next one. | UCA10 | Own addressing mode select: UCA10= 0  7-bit address UCA10= 1  10-bit address
6 | UCPAR | Parity select: UCPAR = 0  Odd parity UCPAR = 1  Even parity | UCCKPL | Clock polarity select. UCCKPL = 0  Inactive state: low. UCCKPL = 1  Inactive state: high. | UCSLA10 | Slave addressing mode select: UCSLA10= 0  7-bit address UCSLA10= 1  10-bit address
5 | UCMSB | MSB first select: UCMSB = 0  LSB first UCMSB = 1  MSB first | UCMSB | As UART mode | UCMM | Multi-master environment select: UCMM= 0  Single master UCMM= 1  Multi master

## Slide 46: USCI registers (UART, SPI and I2C modes) (2/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UCAxCTL0, USCI_Ax Control Register 0 (UART, SPI)
UCBxCTL0, USCI_Bx Control Register 0 (SPI, I2C)
Mode | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
UART | UCPEN | UCPAR | UCMSB | UC7BIT | UCSPB | UCMODEx |  | UCSYNC=0
SPI | UCCKPH | UCCKPL | UCMSB | UC7BIT | UCMST | UCMODEx |  | UCSYNC=1
I2C | UCA10 | UCSLA10 | UCMM | Unused | UCMST | UCMODEx=11 |  | UCSYNC=1
Bit |  | UART mode description |  | SPI mode description |  | I2C mode description
4 | UC7BIT | Character length: = 0  8-bit data = 1  7-bit data | UC7BIT | As UART mode | Unused | 
3 | UCSPB | Stop bit select: = 0  One stop bit = 1  Two stop bits | UCMST | Master mode: = 0  USART is slave = 1  USART is master | UCMST | Master mode select. = 0  Slave mode = 1  Master mode
2-1 | UCMODEx | USCI asynchronous mode: = 00  UART = 01  Idle-Line Multiproc. = 10  Address-Bit Multiproc. = 11  UART with ABR. | UCMODEx | USCI synchronous mode: = 00  3-Pin SPI = 01  4-Pin SPI (slave enabled when UCxSTE=1) = 10  4-Pin SPI (slave enabled when UCxSTE=0) = 11  I2C | UCMODEx=11 | USCI Mode: = 00  3-Pin SPI = 01  4-Pin SPI (master/slave enabled if STE = 1) = 10  4-Pin SPI (master/slave enabled if STE = 0) = 11  I2C
0 | UCSYNC=0 | Synchronous mode enable: = 0  Asynchronous = 1  Synchronous | UCSYNC=1 | As UART mode | UCSYNC=1 | As UART mode

## Slide 47: USCI registers (UART, SPI and I2C modes) (3/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UCAxCTL1, USCI_Ax Control Register 1 (UART, SPI)
UCBxCTL1, USCI_Bx Control Register 1 (SPI, I2C)
Mode | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
UART | UCSSELx |  | UCRXEIE | UCBRKIE | UCDORM | UCTXADDR | UCTXBRK | UCSWRST
SPI | UCSSELx |  | Unused | Unused | Unused | Unused | Unused | UCSWRST
I2C | UCSSELx |  | Unused | UCTR | UCTXNACK | UCTXSTP | UCTXSTT | UCSWRST
Bit |  | UART mode description |  | SPI mode description |  | I2C mode description
7-6 | UCSSELx | BRCLK source clock: = 00  UCLK = 01  ACLK = 10  SMCLK = 11  SMCLK | UCSSELx | BRCLK source clock: = 00  N/A = 01  ACLK = 10  SMCLK = 11  SMCLK | UCSSELx | BRCLK source clock: = 00  UCLKI = 01  ACLK = 10  SMCLK = 11  SMCLK
5 | UCRXEIE | Receive erroneous-character IE: = 0  Rejected (UCAxRXIFG not set) = 1  Received (UCAxRXIFG set) | Unused |  | Unused | Slave addressing mode select: UCSLA10= 0  7-bit address UCSLA10= 1  10-bit address
4 | UCBRKIE | Receive break character IE: = 0  Not set UCAxRXIFG. = 1  Set UCAxRXIFG. | Unused |  | UCTR | Transmitter/Receiver select: = 0  Receiver = 1  Transmitter

## Slide 48: USCI registers (UART, SPI and I2C modes) (4/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UCAxCTL1, USCI_Ax Control Register 1 (UART, SPI)
UCBxCTL1, USCI_Bx Control Register 1 (SPI, I2C)
Mode | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
UART | UCSSELx |  | UCRXEIE | UCBRKIE | UCDORM | UCTXADDR | UCTXBRK | UCSWRST
SPI | UCSSELx |  | Unused | Unused | Unused | Unused | Unused | UCSWRST
I2C | UCSSELx |  | Unused | UCTR | UCTXNACK | UCTXSTP | UCTXSTT | UCSWRST
Bit |  | UART mode description |  | SPI mode description |  | I2C mode description
3 | UCDORM | Dormant. Puts USCI into sleep mode: = 0  Not dormant = 1  Dormant | Unused |  | UCTXNACK | Transmit a NACK: = 0  Acknowledge normally = 1  Generate NACK
2 | UCTXADDR | Transmit address: = 0  Next frame transmitted is data = 1  Next frame transmitted is address | Unused |  | UCTXSTP | Transmit STOP condition in master mode: = 0  No STOP generated = 1  Generate STOP
1 | UCTXBRK | Transmit break: = 0  Next frame transmitted is not a break = 1  Next frame transmitted is a break or a break/synch | Unused |  | UCTXSTT | Transmit START condition in master mode: = 0  No START generated = 1  Generate START
0 | UCSWRST | Software reset enable =0  Disabled. USCI reset released for operation 1  Enabled. USCI logic held in reset state | UCSWRST | As UART mode | UCSWRST | As UART mode

## Slide 49: USCI registers (UART, SPI and I2C modes) (5/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UCAxBR0, USCI_Ax Baud Rate Control Register 0 (UART, SPI)
UCBxBR0, USCI_Bx Bit Rate Control Register 0 (SPI, I2C)
UCAxBR1, USCI_Ax Baud Rate Control Register 1 (UART, SPI)
UCBxBR1, USCI_Bx Bit Rate Control Register 1 (SPI, I2C)
Mode | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
UART / SPI / I2C | UCBRx – low byte |  |  |  |  |  |  | 
Mode | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
UART / SPI / I2C | UCBRx – high byte |  |  |  |  |  |  | 
Bit |  | UART mode description |  | SPI mode description |  | I2C mode description
7-6 | UCBRx | Clock prescaler setting of the baud rate generator: Prescaler value (16-bit value) = {UCAxBR0+UCAxBR1x256} | UCBRx | Bit clock prescaler setting: Prescaler value (16-bit value) = {UCAxBR0+UCAxBR1×256} | UCBRx | As SPI mode

## Slide 50: USCI registers (UART, SPI and I2C modes) (6/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UCAxSTAT, USCI_Ax Status Register (UART, SPI)
UCBxSTAT, USCI_Bx Status Register (SPI, I2C)
Mode | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
UART | UCLISTEN | UCFE | UCOE | UCPE | UCBRK | UCRXERR | UCADDR UCIDLE | UCBUSY
SPI | UCLISTEN | UCFE | UCOE | Unused | Unused | Unused | Unused | UCBUSY
I2C | Unused | UCSCLLOW | UCGC | UCBBUSY | UCNACKIFG | UCSTPIFG | UCSTTIFG | UCALIFG
Bit |  | UART mode description |  | SPI mode description |  | I2C mode description
7 | UCLISTEN | Listen enable: = 0  Disabled = 1  UCAxTXD is internally fed back to receiver | UCLISTEN | Listen enable: = 0  Disabled = 1  The transmitter output is internally fed back to receiver | Unused | 
6 | UCFE | Framing error flag: = 0  No error = 1  Character with low stop bit | UCFE | Framing error flag: = 0  No error = 1  Bus conflict (4w master) | UCSCLLOW | SCL low: = 0  SCL is not held low = 1  SCL is held low
5 | UCOE | Overrun error flag: = 0  No error = 1  Overrun error | UCOE | As UART mode | UCGC | General call address received: = 0  No general call address = 1  General call address

## Slide 51: USCI registers (UART, SPI and I2C modes) (7/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UCAxSTAT, USCI_Ax Status Register (UART, SPI)
UCBxSTAT, USCI_Bx Status Register (SPI, I2C)
Mode | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
UART | UCLISTEN | UCFE | UCOE | UCPE | UCBRK | UCRXERR | UCADDR UCIDLE | UCBUSY
SPI | UCLISTEN | UCFE | UCOE | Unused | Unused | Unused | Unused | UCBUSY
I2C | Unused | UCSCLLOW | UCGC | UCBBUSY | UCNACKIFG | UCSTPIFG | UCSTTIFG | UCALIFG
Bit |  | UART mode description |  | SPI mode description |  | I2C mode description
4 | UCPE | Parity error flag: = 0  No error = 1  Character with parity error | Unused |  | UCBBUSY | Bus busy: = 0  Bus inactive = 1  Bus busy
3 | UCBRK | Break detect flag: = 0  No break condition = 1  Break condition occurred | Unused |  | UCNACKIFG | NACK received interrupt flag: = 0  No interrupt pending = 1  Interrupt pending
2 | UCRXERR | Receive error flag. = 0  No receive errors detected = 1  Receive error detected | Unused |  | UCSTPIFG | Stop condition interrupt flag: = 0  No interrupt pending = 1  Interrupt pending
1 | UCADDR UCIDLE | Address-bit multiproc. mode: = 0  Received character is data = 1  Received character is an address Idle-line multiproc. mode: = 0  No idle line detected = 1  Idle line detected | Unused |  | UCSTTIFG | Start condition interrupt flag: = 0  No interrupt pending = 1  Interrupt pending
0 | UCBUSY | USCI busy: = 0  USCI inactive = 1  USCI transmit/receive | UCBUSY |  | UCALIFG | Arbitration lost interrupt flag: = 0  No interrupt pending = 1  Interrupt pending

## Slide 52: USCI registers (UART, SPI and I2C modes) (8/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UCAxRXBUF, USCI_Ax Receive Buffer Register (UART, SPI)
UCBxRXBUF, USCI_Bx Receive Buffer Register (SPI, I2C)
Mode | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
UART / SPI / I2C | UCRXBUFx |  |  |  |  |  |  | 
Bit |  | UART mode description |  | SPI mode description |  | I2C mode description
7-0 | UCRXBUFx | The receive-data buffer is user accessible and contains the last received character from the receive shift register. Reading UCxRXBUF resets receive-error bits, UCADDR/UCIDLE bit and UCAxRXIFG. In 7-bit data mode, UCAxRXBUF is LSB justified and the MSB is always cleared. | UCRXBUFx | As UART mode Reading UCxRXBUF resets the receive-error bits, and UCxRXIFG | UCRXBUFx | As SPI mode

## Slide 53: USCI registers (UART, SPI and I2C modes) (9/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UCAxTXBUF, USCI_Ax Transmit Buffer Register (UART, SPI)
UCBxTXBUF, USCI_Bx Transmit Buffer Register (SPI, I2C)
Mode | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
UART / SPI / I2C | UCTXBUFx |  |  |  |  |  |  | 
Bit |  | UART mode description |  | SPI mode description |  | I2C mode description
7-0 | UCTXBUFx | The transmit data buffer is user accessible and holds the data waiting to be moved into the transmit shift register and transmitted on UCAxTXD. Writing to the transmit data buffer clears UCAxTXIFG. | UCTXBUFx | The transmit data buffer is user accessible and holds the data waiting to be moved into the transmit shift register and transmitted. Writing to the transmit data buffer clears UCxTXIFG. | UCTXBUFx | As SPI mode

## Slide 54: USCI registers (UART, SPI and I2C modes) (10/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
IE2, Interrupt Enable Register 2 (UART, SPI, I2C)
Mode | 7 | 6 | 5 |  | 4 | 3 | 2 | 1 | 0
UART |  |  |  |  |  |  |  | UCA0TXIE | UCA0RXIE
SPI |  |  |  |  |  | UCB0TXIE | UCB0RXIE | UCA0TXIE | UCA0RXIE
I2C |  |  |  |  |  | UCB0TXIE | UCB0RXIE |  | 
Bit |  | UART mode description |  | SPI mode description |  | I2C mode description
3 |  |  | UCB0TXIE | USCI_B0 transmit interrupt enable: = 0  Disabled = 1  Enabled | UCB0TXIE | As SPI mode
2 |  |  | UCB0RXIE | USCI_B0 receive interrupt enable: = 0  Disabled = 1  Enabled | UCB0RXIE | As SPI mode
1 | UCA0TXIE | USCI_A0 transmit interrupt enable: = 0  Disabled = 1  Enabled | UCA0TXIE | As UART mode |  | 
0 | UCA0RXIE | USCI_A0 receive interrupt enable: = 0  Disabled = 1  Enabled | UCA0RXIE | As UART mode |  | 

## Slide 55: USCI registers (UART, SPI and I2C modes) (11/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
IFG2, Interrupt Flag Register 2 (UART, SPI, I2C)
Mode | 7 | 6 | 5 |  | 4 | 3 | 2 | 1 | 0
UART |  |  |  |  |  |  |  | UCA0TXIFG | UCA0RXIFG
SPI |  |  |  |  |  | UCB0TXIFG | UCB0RXIFG | UCA0TXIFG | UCA0RXIFG
I2C |  |  |  |  |  | UCB0TXIFG | UCB0RXIFG |  | 
Bit |  | UART mode description |  | SPI mode description |  | I2C mode description
3 |  |  | UCB0TXIFG | USCI_B0 transmit interrupt flag: = 0  No interrupt pending = 1  Interrupt pending | UCB0TXIFG | As SPI mode
2 |  |  | UCB0RXIFG | USCI_B0 receive interrupt flag: = 0  No interrupt pending = 1  Interrupt pending | UCB0RXIFG | As SPI mode
1 | UCA0TXIFG | USCI_A0 transmit interrupt flag: = 0  No interrupt pending = 1  Interrupt pending | UCA0TXIFG | As UART mode |  | 
0 | UCA0RXIFG | USCI_A0 receive interrupt flag: = 0  No interrupt pending = 1  Interrupt pending | UCA0RXIFG | As UART mode |  | 

## Slide 56: USCI registers (UART, SPI and I2C modes) (12/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UC1IE, USCI_A1 Interrupt Enable Register (UART, SPI)
UC1IE, USCI_B1 Interrupt Enable Register (SPI, I2C)
Mode | 7 | 6 | 5 |  | 4 | 3 | 2 | 1 | 0
UART | Unused | Unused | Unused | Unused |  |  |  | UCA1TXIE | UCA1RXIE
SPI | Unused | Unused | Unused | Unused |  | UCB1TXIE | UCB1RXIE | UCA1TXIE | UCA1RXIE
I2C | Unused | Unused | Unused | Unused |  | UCB1TXIE | UCB1RXIE |  | 
Bit |  | UART mode description |  | SPI mode description |  | I2C mode description
3 |  |  | UCB1TXIE | USCI_B1 transmit interrupt enable: UTXIE1 = 0  Disabled UTXIE1 = 1  Enabled | UCB1TXIE | As SPI mode
2 |  |  | UCB1RXIE | USCI_B1 receive interrupt enable: URXIE1 = 0  Disabled URXIE1 = 1  Enabled | UCB1RXIE | As SPI mode
1 | UCA1TXIE | USCI_A1 transmit interrupt enable: UTXIE1 = 0  Disabled UTXIE1 = 1  Enabled | UCA1TXIE | As UART mode |  | 
0 | UCA1RXIE | USCI_A1 receive interrupt enable: URXIE1 = 0  Disabled URXIE1 = 1  Enabled | UCA1RXIE | As UART mode |  | 

## Slide 57: USCI registers (UART, SPI and I2C modes) (13/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UC1IFG, USCI_A1 Interrupt Flag Register (UART, SPI)
UC1IFG, USCI_B1 Interrupt Flag Register (SPI, I2C)
Mode | 7 | 6 | 5 |  | 4 | 3 | 2 | 1 | 0
UART |  |  |  |  |  |  |  | UCA1TXIFG | UCA1RXIFG
SPI |  |  |  |  |  | UCB1TXIFG | UCB1RXIFG | UCA1TXIFG | UCA1RXIFG
I2C |  |  |  |  |  | UCB1TXIFG | UCB1RXIFG |  | 
Bit |  | UART mode description |  | SPI mode description |  | I2C mode description
3 |  |  | UCB1TXIFG | USCI_B1 transmit interrupt flag: = 0  No interrupt pending = 1  Interrupt pending | UCB1TXIFG | As SPI mode
2 |  |  | UCB1RXIFG | USCI_B1 receive interrupt flag: = 0  No interrupt pending = 1  Interrupt pending | UCB1RXIFG | As SPI mode
1 | UCA1TXIFG | USCI_A1 transmit interrupt flag: = 0  No interrupt pending = 1  Interrupt pending | UCA1TXIFG | As UART mode |  | 
0 | UCA1RXIFG | USCI_A1 receive interrupt flag: = 0  No interrupt pending = 1  Interrupt pending | UCA1RXIFG | As UART mode |  | 

## Slide 58: USCI registers (UART, SPI and I2C modes) (14/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UCAxMCTL, USCI_Ax Modulation Control Register (UART)
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
UCBRFx |  |  |  | UCBRSx |  |  | UCOS16
Bit |  | UART mode description
7-4 | UCBRFx | First modulation pattern for BITCLK16 when UCOS16 = 1 (See Table 19-3 of the MSP430x4xx User’s Guide)
3-1 | UCBRSx | Second modulation pattern for BITCLK (See Table 19-2 of the MSP430x4xx User’s Guide)
0 | UCOS16 | Oversampling mode enabled when UCOS16 = 1

## Slide 59: USCI registers (UART, SPI and I2C modes) (15/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UCAxIRTCTL, USCI_Ax IrDA Transmit Control Register (UART)
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
UCIRTXPLx |  |  |  |  |  | UCIRTXCLK | UCIREN
Bit |  | UART mode description
7-2 | UCIRTXPLx | Transmit pulse length: tPULSE = (UCIRTXPLx + 1) / (2 x fIRTXCLK)
1 | UCIRTXCLK | IrDA transmit pulse clock select: UCIRTXCLK = 0  BRCLK UCIRTXCLK = 1  BITCLK16, when UCOS16 = 1  BRCLK, otherwise
0 | UCIREN | IrDA encoder/decoder enable: UCIREN = 0  IrDA encoder/decoder disabled UCIREN = 1  IrDA encoder/decoder enabled

## Slide 60: USCI registers (UART, SPI and I2C modes) (16/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UCAxIRRCTL, USCI_Ax IrDA Receive Control Register (UART)
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
UCIRRXFLx |  |  |  |  |  | UCIRRXPL | UCIRRXFE
Bit |  | UART mode description
7-2 | UCIRRXFLx | Receive filter length (minimum pulse length): tMIN = (UCIRRXFLx + 4) / (2 × fIRTXCLK)
1 | UCIRRXPL | IrDA receive input UCAxRXD polarity. When a light pulse is seen: UCIRRXPL = 0  IrDA transceiver delivers a high pulse UCIRRXPL = 1  IrDA transceiver delivers a low pulse
0 | UCIRRXFE | IrDA receive filter enabled: UCIRRXFE = 0  Disabled UCIRRXFE = 1  Enabled

## Slide 61: USCI registers (UART, SPI and I2C modes) (17/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UCAxABCTL, USCI_Ax Auto Baud Rate Control Register (UART)
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Reserved |  | UCDELIMx |  | UCSTOE | UCBTOE | Reserved | UCABDEN
Bit |  | UART mode description
5-4 | UCDELIMx | Break/synch delimiter length: UCDELIM1 UCDELIM0 = 00  1 bit time UCDELIM1 UCDELIM0 = 01  2 bit times UCDELIM1 UCDELIM0 = 10  3 bit times UCDELIM1 UCDELIM0 = 11  4 bit times
3 | UCSTOE | Synch field time out error: UCSTOE = 0  No error UCSTOE = 1  Length of synch field exceeded measurable time
2 | UCBTOE | Break time out error: UCBTOE = 0  No error UCBTOE = 1  Length of break field exceeded 22 bit times.
0 | UCABDEN | Automatic baud rate detect enable: UCABDEN = 0  Baud rate detection disabled UCABDEN = 1  Baud rate detection enabled

## Slide 62: USCI registers (UART, SPI and I2C modes) (18/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UCBxI2COA, USCIBx I2C Own Address Register (I2C)
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8
UCGCEN | 0 | 0 | 0 | 0 | 0 | I2COAx | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
I2COAx |  |  |  |  |  |  | 
Bit |  | UART mode description
15 | UCGCEN | General call response enable: UCGCEN = 0  Do not respond to a general call UCGCEN = 1  Respond to a general call
9-0 | I2COAx | I2C own address (local address of the USCI_Bx I2C controller)  Right-justified address  7-bit address  Bit 6 is the MSB, Bits 9-7 are ignored.  10-bit address  Bit 9 is the MSB.

## Slide 63: USCI registers (UART, SPI and I2C modes) (19/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UCBxI2CSA, USCI_Bx I2C Slave Address Register (I2C)
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8
0 | 0 | 0 | 0 | 0 | 0 | I2CSAx | 
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
I2CSAx |  |  |  |  |  |  | 
Bit |  | UART mode description
9-0 | I2CSAx | I2C slave address (slave address of the external device to be addressed by the USCI_Bx module)  Only used in master mode  Right-justified address  7-bit address  Bit 6 is the MSB, Bits 9-7 are ignored.  10-bit address  Bit 9 is the MSB.

## Slide 64: USCI registers (UART, SPI and I2C modes) (20/20)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UCBxI2CIE, USCI_Bx I2C Interrupt Enable Register (I2C)
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Reserved |  |  |  | UCNACKIE | UCSTPIE | UCSTTIE | UCALIE
Bit |  | UART mode description
3 | UCNACKIE | Not-acknowledge interrupt enable: UCNACKIE = 0  Interrupt disabled UCNACKIE = 1  Interrupt enabled
2 | UCSTPIE | Stop condition interrupt enable: UCSTPIE = 0  Interrupt disabled UCSTPIE = 1  Interrupt enabled
1 | UCSTTIE | Start condition interrupt enable: UCSTTIE = 0  Interrupt disabled UCSTTIE = 1  Interrupt enabled
0 | UCALIE | Arbitration lost interrupt enable: UCALIE = 0  Interrupt disabled UCALIE = 1  Interrupt enabled

## Slide 65: Lab10a: USCI echo test using UART mode
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Project files:
  C source files: Chapter 14 > Lab10 > Lab10a_student.c
  Solution file: Chapter 14 > Lab10 > Lab10a_solution.c
Overview:
  This laboratory explores the USCI module in UART mode that will be connected to a CCE IO console;
  When the connection is established, the character sequence written at the keyboard to the console will be displayed again on the console.

## Slide 66: Lab10a: Echo test using USCI module: UART
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  This laboratory uses the USCI module in asynchronous mode;
  The RX interrupt activates the service routine that reads the incoming character and sends it again to the PC (computer), allowing the instantaneous display of the written character;
  The resources used are:
    USCI module;
    Interrupts;
    IO ports:
    System clock.
  Configures the FLL+ and selects the base frequency for the UART. In this example it will be 8 MHz.

## Slide 67: Lab10a: Echo test using USCI module: UART
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  Performs the required hardware configuration;
  ISR generated by the reception of a new character;
  System clock at a frequency of 8 MHz.

## Slide 68: Lab10a: Echo test using USCI module: UART
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  Control registers:
    The connection will operate in the following mode:
      Parity disabled;
      LSB first;
      8-bit data;
      One stop bit.
    The module will operate on the following mode:
      Asynchronous;
      SMCLK source clock;
      No Receive erroneous-character interrupt-enable;
      No Receive break character interrupt-enable.

## Slide 69: Lab10a: Echo test using USCI module: UART
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration (continued):
  Control registers:
    Configure the following control registers based on these characteristics:
  UCA0CTL0 = _______________;
  UCA0CTL1 = _______________;

## Slide 70: Lab10a: Echo test using USCI module: UART
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration (continued):
  Baud rate generation:
    The module has an 8 MHz clock source and the objective is to establish a connection at a communication rate of 9600 baud;
    It is necessary to set up the baud rate generation in oversampling mode;
    Configure the following registers:
  UCA0BR0 = _______________;
  UCA0BR1 = _______________;
  UCA0MCTL = _______________;

## Slide 71: Lab10a: Echo test using USCI module: UART
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration (continued):
  Configuration of Ports:
    In order to set the external interfaces of the USCI module, it is necessary to configure the I/O ports;
    Select the USCI peripheral in UART mode following the connections provided at the Experimenter’s board:
  P2SEL = __________________;

## Slide 72: Lab10a: Echo test using USCI module: UART
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration (continued):
  RX interrupt enable:
    To finish the module configuration, it is necessary to enable the receive interrupts:
    IE2 = ____________________;

## Slide 73: Lab10a: Echo test using USCI module: UART
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Once the USCI module is configured in accordance with the previous steps, to initiate the experiment, complete the file Lab10a_student.c, compile it and run it on the Experimenter’s board;
  The solution to the laboratory can be found in the file Lab10a_solution.c.
  For correct operation, there must be a connection between the Experimenter’s board and the PC:
    Enable CCE console: Window>Show View>Console;
    If necessary, configure the CCE console options in accordance to the connection details.

## Slide 74: Lab10a: Echo test using USCI module: UART
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Control registers:
  UCA0CTL0 = 0x00;
//UCPEN|UCPAR|UCMSB|UC7BIT|UCSPB|UCMODEx|UCSYNC|
//UCPEN (Parity) = 0b -> Parity disabled
//UCPAR (Parity select) = 0b -> Odd parity
//UCMSB (MSB first select) = 0b -> LSB first
//UC7BIT (Character length) = 0b -> 8-bit data
//UCSPB (Stop bit select) = 0b -> One stop bit
//UCMODEx (USCI mode) = 00b -> UART Mode
//UCSYNC = 0b -> Asynchronous mode
MSP-EXP430FG4618 | SOLUTION
Using USCI module in UART mode included in the MSP-EXP430FG4618 Development Tool, develop a procedure to connect it to a PC’s I/O console. When the connection is established, the character sequence written to the console by the keyboard will be displayed on the console. | 

## Slide 75: Lab10a: Echo test using USCI module: UART
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Control registers:
  UCA0CTL1 = 0x81;
  //UCSSELx|UCRXEIE|UCBRKIE|UCDORM|UCTXADDR|UCTXBRK|UCSWRST
  //UCSSELx (USCI clock source select) = 10b -> SMCLK
  //UCRXEIE = 0b -> Erroneous characters rejected
  //UCBRKIE = 0b -> Received break characters set
  //UCDORM = 0b -> Not dormant
  //UCTXADDR = 0b -> Next frame transmitted is data
  //UCTXBRK = 0b -> Next frame transmitted is no break
  //UCSWRST = 1b -> normally Set by a PUC

## Slide 76: Lab10a: Echo test using USCI module: UART
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Baud rate generation
UCA0BR0 = 0x34;
UCA0BR1 = 0x00;
//Prescaler = 8MHz/(16 x 9600) = 52 = 0x34
//9600 from 8MHz -> SMCLK
UCA0MCTL = 0x11;
//UCBRFx|UCBRSx|UCOS16|
//UCBRFx (1st modulation stage) = 0001b -> Table 19-4
//UCBRSx (2nd modulation stage) = 000b -> Table 19-4
//UCOS16 (Oversampling mode) = 1b -> Enabled

## Slide 77: Lab10a: Echo test using USCI module: UART
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Configuration of ports
P2SEL |= 0x30;
//P2.4,P2.5 = USCI_A0 TXD,RXD
RX interrupt enable
IE2 |= UCA0RXIE;
//Enable USCI_A0 RX interrupt

## Slide 78: Quiz (1/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
1. The USCI module has:
(a) One module;
(b) Two modules;
(c) Three modules;
(d) None.
2. The USCI module in UART mode supports:
(a) LIN;
(b) IrDA;
(c) All of above;
(d) None of above.

## Slide 79: Quiz (2/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
3. The UCMSB bit controls:
(a) The direction of the data transfer;
(b) Selects LSB or MSB first;
(c) All of above;
(d) None of above.
4. The automatic baud rate detection uses a “break” which is:
(a) Detected when 11 or more continuous “0”s are received;
(b) Detected when 4 or more continuous “0”s are received;
(c) Detected when 8 or more continuous “0”s are received;
(d) None.

## Slide 80: Quiz (3/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
5. The automatic baud rate detection uses a synch field which is represented by:
(a) Data 022h inside a byte field;
(b) Data 055h inside a byte field;
(c) Data 044h inside a byte field;
(d) None.
6. The USCI module in UART mode for IrDA decoding detects:
(a) Low pulse;
(b) High pulse;
(c) All of above;
(d) None.

## Slide 81: Quiz (4/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
7. The baud rate can be generated using:
(a) A low frequency;
(b) Oversampling;
(c) All of above;
(d) None of above.
8. In USCI I2C communication, the ACK bit is sent from the receiver after:
(a) Each bit on the 9th SCL clock;
(b) Each byte on the 2th SCL clock;
(c) Each bit on the 2th SCL clock;
(d) Each byte on the 9th SCL clock.

## Slide 82: Quiz (5/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
9. The operating modes provided by the I2C mode are:
(a) Master transmitter and Slave receiver;
(b) Slave transmitter and Master receiver;
(c) All of above;
(d) None of above.
10. The I2C state change interrupt flags are:
(a) Arbitration-lost and Not-acknowledge;
(b) Start and stop conditions;
(c) All of above;
(d) None of above.

## Slide 83: Quiz (6/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Answers:
  1. (b) Two modules.
  2. (c) All of above.
  3. (c) All of above.
  4. (a) Detected when 11 or more continuous “0”s are received.
  5. (b) Data 055h inside a byte field.
  6. (c) All of above.
  7. (c) All of above.
  8. (d) Each byte on the 9th SCL clock.
  9. (c) All of above.
  10. (c) All of above.