## Slide 1: Chapter 14 Communications USART Module
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Notes: <number>

## Slide 2: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
MSP430 communications interfaces
USART module introduction
USART operation: UART mode
USART operation: SPI mode
USART registers (UART and SPI modes)
Quiz

## Slide 3: MSP430 communications interfaces (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Equipped with three serial communication interfaces:
  USART (Universal Synchronous/Asynchronous Receiver/Transmitter):
    UART mode;
    SPI mode;
    I2C (on ‘F15x/’F16x only).
  USCI (Universal Serial Communication Interface):
    UART with Lin/IrDA support;
    SPI (Master/Slave, 3 and 4 wire modes);
    I2C (Master/Slave, up to 400 kHz).
  USI (Universal Serial Interface):
    SPI (Master/Slave, 3 & 4 wire mode);
    I2C (Master/Slave, up to 400 kHz).

## Slide 4: MSP430 communications interfaces (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Comparison between the communication modules:
USART | USCI | USI
UART: - Only one modulator - n/a - n/a - n/a | UART: - Two modulators support n/16 timings - Auto baud rate detection - IrDA encoder & decoder - Simultaneous USCI_A and USCI_B (2 channels) | 
SPI: - Only one SPI available - Master and Slave Modes - 3 and 4 Wire Modes | SPI: - Two SPI (one on each USCI_A and USCI_B) - Master and Slave Modes - 3 and 4 Wire Modes | SPI: - Only one SPI available - Master and Slave Modes
I2C: (on ‘15x/’16x only) - Master and Slave Modes - up to 400kbps | I2C: - Simplified interrupt usage - Master and Slave Modes - up to 400kbps | I2C: - SW state machine needed - Master and Slave Modes

## Slide 5: USART module introduction (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The USART (Universal Synchronous/Asynchronous Receiver/Transmitter) module is a base unit for serial communications, supporting asynchronous communications (RS232) and synchronous (SPI) communications.
The USART module is available on the 4xx series devices:
  MSP430x42x and MSP430x43x: One module;
  MSP430x44x and MSP430FG461x: Two modules.

## Slide 6: USART module introduction (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The USART supports:
    Low power operating modes (with auto-start);
    UART or SPI mode (I2C on ‘F15x/’F16x only);
    Double buffered TX/RX;
    Baud rate generator;
    DMA enabled;
    Error detection.

## Slide 7: USART operation: UART mode (1/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Transmits and receives characters asynchronously;
Timing for each character is based on the selected baud rate;
Transmit and receive use the same clock frequency leading to the same baud rate;

## Slide 8: USART operation: UART mode (2/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Recommended initialization/re-configuration process:
  Set SWRST (BIS.B #SWRST,&UxCTL);
  Initialize all USART registers with SWRST = 1 (including UxCTL);
  Enable USART module via the MEx SFRs (URXEx and/or UTXEx);
  Clear SWRST via software (BIC.B #SWRST,&UxCTL);
  Enable interrupts (optional) via the IEx SFRs (URXIEx and/or UTXIEx);

## Slide 9: USART operation: UART mode (3/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Character format can be specified as follows:
  Start bit;
  Seven or eight data bits;
  Even/odd/no parity bit;
  Address bit (address-bit mode);
  One or two stop bits.

## Slide 10: USART operation: UART mode (4/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Asynchronous communication formats:
  Idle-line multiprocessor communication protocol (minimum of two devices):
    IDLE is detected after > 10 periods of continuous marks after the stop bit;
    The first character after IDLE is an address;
    Can be programmed to receive only address characters.

## Slide 11: USART operation: UART mode (5/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Asynchronous communication formats:
  Address-bit multiprocessor communication protocol (minimum of three devices):
    An extra bit in the received character marks the character as an address;
    UART can be programmed to receive only address characters.

## Slide 12: USART operation: UART mode (6/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Automatic error detection:
  Glitch suppression prevents the USART from being accidentally started;
  Any pulse on UCxRXD shorter than the deglitch time (approximately 30 ns) will be ignored.
  Framing error FE: Set if the stop bit is missing from a received frame;
  Parity error PE: Set if there is parity mismatch in a received frame;
  Receive overrun error OE: Set if UxRXBUF is overwritten;
  Break condition BRK: Set if all bits in the received frame = 0;

## Slide 13: USART operation: UART mode (7/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Enable the USART receive enable bit URXEx:
  The receive-data buffer, UxRXBUF, contains the character moved from the RX shift register after the character is received.

## Slide 14: USART operation: UART mode (8/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Enable the USART transmit enable bit UTXEx:
  Transmission is initiated by writing the data to UxTXBUF;
  The data value is then moved to the transmit shift register on the next BITCLK after the TX shift register is empty, and transmission begins.

## Slide 15: USART operation: UART mode (9/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
USART baud rate generation:
  Standard baud rates from non-standard source frequencies;
  The USART module uses a prescaler/divider and a modulator;
  The timing bit (BITCLK) of this module is allowed to be smaller than a third of the clock signal, BRCLK.

## Slide 16: USART operation: UART mode (10/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
USART baud rate generation (continued):
  Timing bit:
    Implemented in two stages:
      For BRCLK, the division factor N is given by:
      Its integer part is the first phase of the bit time;
      Its fractional part of this factor is the modulator;
      The new definition of N is given by:

## Slide 17: USART operation: UART mode (11/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
USART interrupts:
  One interrupt vector for transmission and one interrupt vector for reception:
  UART transmit interrupt operation:
    UTXIFGx interrupt flag is set by the transmitter to indicate that UxTXBUF is ready to accept another character;
    An interrupt request is also generated if UTXIEx and GIE are set;
    UTXIFGx is automatically reset if the interrupt request is serviced or if a character is written to UxTXBUF.

## Slide 18: USART operation: UART mode (12/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
USART interrupts (continued):
  UART receive interrupt operation:
    URXIFGx interrupt flag is set each time a character is received and loaded into UxRXBUF;
    An interrupt request is also generated if URXIEx and GIE are set;
    URXIFGx and URXIEx are reset by a system reset PUC signal or when SWRST = 1;
    URXIFGx is automatically reset if the pending interrupt is serviced (when URXSE = 0) or when UxRXBUF is read.

## Slide 19: USART operation: UART mode (13/13)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Receive-start edge detect feature (URXSE bit). Should be used when:
  BRCLK is sourced by the DCO;
  DCO is off due to low-power mode operation.

## Slide 20: USART operation: SPI mode (1/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Serial data transmitted and received by multiple devices using a shared clock provided by the master;
Three or four signals are used for SPI data exchange:
  SIMO: Slave In, Master Out;
  SOMI Slave Out, Master In;
  UCLK USART SPI clock;
  STE slave transmit enable (controlled by the master).

## Slide 21: USART operation: SPI mode (2/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
USART initialization/re-configuration process:
  Set SWRST (BIS.B #SWRST,&UxCTL);
  Initialize all USART registers with SWRST = 1 (including UxCTL);
  Enable USART module via the MEx SFRs (URXEx and/or UTXEx);
  Clear SWRST via software (BIC.B #SWRST,&UxCTL);
  Enable interrupts (optional) via the IEx SFRs (URXIEx and/or UTXIEx);

## Slide 22: USART operation: SPI mode (3/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Define mode: Master or Slave;
Enable SPI transmit/receive, USPIEx;
  State diagram of transmit enable for SPI master mode:

## Slide 23: USART operation: SPI mode (4/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Enable SPI transmit/receive, USPIEx;
  State diagram of transmit enable for SPI slave mode:

## Slide 24: USART operation: SPI mode (5/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Enable SPI transmit/receive, USPIEx;
  State diagram of receive enable for SPI master mode:

## Slide 25: USART operation: SPI mode (6/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Enable SPI transmit/receive, USPIEx;
  State diagram of receive enable for SPI slave mode:

## Slide 26: USART operation: SPI mode (7/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Define serial clock control:
  UCLK is provided by the master on the SPI bus.
    MM = 1: BITCLK is provided by the USART baud rate generator on the UCLK;
    MM = 0: USART clock is provided on the UCLK pin by the master (baud rate generator disable);
    The SPI receiver and transmitter operate in parallel and use the same clock source for data transfer.
Define serial clock polarity (CKPL bit) and phase (CKPH bit);

## Slide 27: USART operation: SPI mode (8/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
USART interrupts:
  One interrupt vector for transmission and one interrupt vector for reception:
  UART transmit interrupt operation:
    UTXIFGx interrupt flag is set by the transmitter to indicate that UxTXBUF is ready to accept another character;
    An interrupt request is generated if UTXIEx and GIE are also set;
    UTXIFGx is automatically reset if the interrupt request is serviced or if a character is written to UxTXBUF.

## Slide 28: USART registers (UART and SPI modes) (1/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
In this section, the register bit definitions are provided for both USART peripheral interfaces:
  Asynchronous UART mode;
  Synchronous SPI mode.
The registers common to both modes are described simultaneously, taking into account that some of them are represented by the same mnemonic, only differentiated by the register number (“UART” for UART mode and “SPI” for SPI mode);
The registers used exclusively for one mode are presented separately.

## Slide 29: USART registers (UART and SPI modes) (2/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UxCTL, USART Control Register
Bit |  | UART mode description |  | SPI mode description
7 | PENA | Parity enable when PENA = 1 Parity bit is generated (UTXDx) and expected (URXDx). | U | Unused
6 | PEV | Parity select: PEV = 0  Odd parity PEV = 1  Even parity |  | Unused
5 | SPB | Stop bit select: SPB = 0  One stop bit SPB = 1  Two stop bits | I2C | I2C or SPI mode select when SYNC = 1. I2C = 0  SPI mode I2C = 1  I2C mode
4 | CHAR | Character length: CHAR = 0  7-bit data CHAR = 1  8-bit data | C | As UART mode
3 | LISTEN | Listen enable when LISTEN = 1. The transmit signal is internally fed back to the receiver. | L | As UART mode
2 | SYNC | Synchronous mode enable: SYNC = 0  UART mode SYNC = 1  SPI Mode | SNC | As UART mode
1 | MM | Multiprocessor mode select MM = 0  Idle-line multiprocessor protocol MM = 1  Address-bit multiprocessor protocol | MM | Master mode: MM = 0  USART is slave MM = 1  USART is master
0 | SWRST | Software reset enable: SWRST = 0  Disabled. USART reset released for operation SWRST = 1  Enabled. USART logic held in reset state | SWRST | As UART mode

## Slide 30: USART registers (UART and SPI modes) (3/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UxTCTL, USART Transmit Control Register
Mode | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
UART | Unused | CKPL | SSELx |  | URXSE | TXWAKE | Unused | TXEPT
SPI | CKPH | CKPL | SSELx |  | Unused | Unused | STC | TXEPT
Bit |  | UART mode description |  | SPI mode description
7 | Unused |  | CKPH | 
6 | CKPL | Clock polarity select: CKPL = 0  UCLKI = UCLK CKPL = 1  UCLKI = inverted UCLK | CKPL | Clock polarity select: CKPL = 0  UCLKI = The inactive state is low. CKPL = 1  UCLKI = The inactive state is high.
5-4 | SSELx | BRCLK source clock: SSEL1 SSEL0 = 00  UCLKI SSEL1 SSEL0 = 01  ACLK SSEL1 SSEL0 = 10  SMCLK SSEL1 SSEL0 = 11  SMCLK | SSELx | BRCLK source clock: SSEL1 SSEL0 = 00  External UCLK (slave mode only) SSEL1 SSEL0 = 01  ACLK (master mode only) SSEL1 SSEL0 = 10  SMCLK (master mode only) SSEL1 SSEL0 = 11  SMCLK (master mode only)
3 | URXSE | UART receive start-edge enable when URXSE = 1 | Unused | 
2 | TXWAKE | Transmitter wake: TXWAKE = 0  Next frame transmitted is data TXWAKE = 1  Next frame transmitted is an address | Unused | 
1 | Unused |  | STC | Slave transmit control: STC = 0  4-pin SPI mode: STE enabled. STC = 1  3-pin SPI mode: STE disabled.
0 | TXEPT | Transmitter empty flag: TXEPT = 0  UART is transmitting data and/or data is waiting in UxTXBUF TXEPT = 1  Transmitter shift register and UxTXBUF are empty or SWRST=1 | TXEPT | Transmitter empty flag: TXEPT = 0  UART is transmitting data and/or data is waiting in UxTXBUF TXEPT = 1  UxTXBUF and TX shift register are empty

## Slide 31: USART registers (UART and SPI modes) (4/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UxRCTL, USART Receive Control Register
Mode | 7 | 6 | 5 |  | 4 | 3 | 2 | 1 | 0
UART | FE | PE | OE | BRK |  | URXEIE | URXWIE | RXWAKE | RXERR
SPI | FE | Unused | OE | Unused |  | Unused | Unused | Unused | Unused
Bit |  | UART mode description |  | SPI mode description
7 | FE | Framing error flag: = 0  No error = 1  Character received with low stop bit | FE | Master mode framing error flag: (MM = 1, STC = 0) = 0  No conflict detected = 1  Bus conflict (STE’s negative edge)
6 | PE | Parity error flag: = 0  No error = 1  Character received with parity error | Unused | 
5 | OE | Overrun error flag: = 0  No error = 1  A character was transferred into UxRXBUF before the previous character was read. | OE | As UART mode
4 | BRK | Break detect flag: = 0  No break condition = 1  Break condition occurred | Unused | 
3 | URXEIE | Receive erroneous-character interrupt-enable: = 0  Err. characters rejected = 1  Err. characters received | Unused | 
2 | URXWIE | Receive wake-up interrupt-enable: = 0  All received characters set IFG = 1  Received address characters set IFG | Unused | 
1 | RXWAKE | Receive wake-up flag: = 0  Received character is data = 1  Received character is an address | Unused | 
0 | RXERR | Receive error flag: = 0  No receive errors detected = 1  Receive error detected | Unused | 

## Slide 32: USART registers (UART and SPI modes) (5/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UxBR0, USART Baud Rate Control Register 0
UxBR1, USART Baud Rate Control Register 1
Mode | 7 | 6 | 5 |  | 4 | 3 | 2 | 1 | 0
UART / SPI | 27 | 26 | 25 | 24 |  | 23 | 22 | 21 | 20
Mode | 7 | 6 | 5 |  | 4 | 3 | 2 | 1 | 0
UART / SPI | 215 | 214 | 213 | 212 |  | 211 | 210 | 29 | 28
Bit |  | UART mode description |  | SPI mode description
7 | UxBRx | The valid baud-rate control range is 3  UxBR < 0FFFFh, where UxBR = {UxBR1+UxBR0}. Unpredictable receive/transmit timing occurs if UxBR < 3. | UxBRx | The baud-rate generator uses the content of {UxBR1+UxBR0} to set the baud rate. Unpredictable SPI operation occurs if UxBR < 2.

## Slide 33: USART registers (UART and SPI modes) (6/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UxMCTL, USART Modulation Control Register
UxRXBUF, USART Receive Buffer Register
Mode | 7 | 6 | 5 |  | 4 | 3 | 2 | 1 | 0
UART / SPI | m7 | m6 | m5 | m4 |  | m3 | m2 | m1 | m0
Bit |  | UART mode description |  | SPI mode description
7 | UxMCTLx | Selects the modulation for BRCLK. | UxMCTLx | Not used in SPI mode and should be set to 00h.
Mode | 7 | 6 | 5 |  | 4 | 3 | 2 | 1 | 0
UART / SPI | 27 | 26 | 25 | 24 |  | 23 | 22 | 21 | 20
Bit |  | UART mode description |  | SPI mode description
7 | UxRXBUFx | The receive-data buffer is user accessible and contains the last received character from the receive shift register. Reading UxRXBUF resets the receive-error bits, the RXWAKE bit, and URXIFGx. In 7-bit data mode, UxRXBUF is LSB justified and the MSB is always cleared. | UxRXBUFx | The receive-data buffer is user accessible and contains the last received character from the receive shift register. Reading UxRXBUF resets the OE bit and URXIFGx flag. In 7-bit data mode, UxRXBUF is LSB justified and the MSB is always cleared.

## Slide 34: USART registers (UART and SPI modes) (7/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
UxTXBUF, USART Transmit Buffer Register
Mode | 7 | 6 | 5 |  | 4 | 3 | 2 | 1 | 0
UART / SPI | 27 | 26 | 25 | 24 |  | 23 | 22 | 21 | 20
Bit |  | UART mode description |  | SPI mode description
7 | UxTXBUFx | The transmit data buffer is user accessible and holds the data waiting to be moved into the transmit shift register and transmitted on UTXDx. Writing to the transmit data buffer clears UTXIFGx. The MSB of UxTXBUF is not used for 7-bit data and is cleared. | UxTXBUFx | The transmit data buffer is user accessible and contains current data to be transmitted. When seven-bit character-length is used, the data should be MSB justified before being moved into UxTXBUF. Data is transmitted MSB first. Writing to UxTXBUF clears UTXIFGx.

## Slide 35: USART registers (UART and SPI modes) (8/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ME1, Module Enable Register 1
ME2, Module Enable Register 2
Bit |  | UART mode description |  | SPI mode description
7 | UTXE0 | USART0 transmit enable: UTXE0 = 0  Module not enabled UTXE0 = 1  Module enabled |  | 
6 | URXE0 | USART0 receive enable: URXE0 = 0  Module not enabled URXE0 = 1  Module enabled | USPIE0 | USART0 SPI enable: USPIE0 = 0  Module not enabled USPIE0 = 1  Module enabled
Mode | 7 | 6 | 5 |  | 4 | 3 | 2 | 1 | 0
UART | UTXE0 | URXE0 |  |  |  |  |  |  | 
SPI |  | USPIE0 |  |  |  |  |  |  | 
Mode | 7 | 6 | 5 |  | 4 | 3 | 2 | 1 | 0
UART |  |  | UTXE1 | URXE1 |  |  |  |  | 
SPI |  |  |  | USPIE1 |  |  |  |  | 
Bit |  | UART mode description |  | SPI mode description
5 | UTXE1 | USART1 transmit enable: UTXE1 = 0  Module not enabled UTXE1 = 1  Module enabled |  | 
4 | URXE1 | USART1 receive enable: URXE1 = 0  Module not enabled URXE1 = 1  Module enabled | USPIE1 | USART1 SPI enable: USPIE1 = 0  Module not enabled USPIE1 = 1  Module enabled

## Slide 36: USART registers (UART and SPI modes) (9/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
IE1, Interrupt Enable Register 1
IE2, Interrupt Enable Register 2
Bit |  | UART mode description |  | SPI mode description
7 | UTXIE0 | USART0 UTXIFG0 transmit interrupt enable: UTXIE0 = 0  Interrupt not enabled UTXIE0 = 1  Interrupt enabled | UTXIE0 | As UART mode
6 | URXIE0 | USART0 URXIFG0 receive interrupt enable: URXIE0 = 0  Interrupt not enabled URXIE0 = 1  Interrupt enabled | URXIE0 | As UART mode
Mode | 7 | 6 | 5 |  | 4 | 3 | 2 | 1 | 0
UART / SPI | UTXIE0 | URXIE0 |  |  |  |  |  |  | 
Mode | 7 | 6 | 5 |  | 4 | 3 | 2 | 1 | 0
UART / SPI |  |  | UTXIE1 | URXIE1 |  |  |  |  | 
Bit |  | UART mode description |  | SPI mode description
7 | UTXIE1 | USART1 UTXIFG1 transmit interrupt enable: UTXIE1 = 0  Interrupt not enabled UTXIE1 = 1  Interrupt enabled | UTXIE1 | As UART mode
6 | URXIE1 | USART1 URXIFG1 receive interrupt enable: URXIE1 = 0  Interrupt not enabled URXIE1 = 1  Interrupt enabled | URXIE1 | As UART mode

## Slide 37: USART registers (UART and SPI modes) (10/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
IFG1, Interrupt Flag Register 1
Mode | 7 | 6 | 5 |  | 4 | 3 | 2 | 1 | 0
UART / SPI | UTXIFG0 | URXIFG0 |  |  |  |  |  |  | 
Bit |  | UART mode description |  | SPI mode description
7 | UTXIFG0 | USART0 transmit interrupt flag. UTXIFG0 is set when U0TXBUF is empty. UTXIFG0 = 0  No interrupt pending UTXIFG0 = 1  Interrupt pending | UTXIFG0 | As UART mode
6 | URXIFG0 | USART0 receive interrupt flag. URXIFG0 is set when U0RXBUF has received a complete character. URXIFG0 = 0  No interrupt pending URXIFG0 = 1  Interrupt pending | URXIFG0 | As UART mode

## Slide 38: USART registers (UART and SPI modes) (11/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
IFG2, Interrupt Flag Register 2
Mode | 7 | 6 | 5 |  | 4 | 3 | 2 | 1 | 0
UART / SPI |  |  | UTXIFG1 | URXIFG1 |  |  |  |  | 
Bit |  | UART mode description |  | SPI mode description
7 | UTXIFG1 | USART1 transmit interrupt flag. UTXIFG1 is set when U1TXBUF is empty. UTXIFG1 = 0  No interrupt pending UTXIFG1 = 1  Interrupt pending | UTXIFG1 | As UART mode
6 | URXIFG1 | USART1 receive interrupt flag. URXIFG1 is set when U1RXBUF has received a complete character. URXIFG1 = 0  No interrupt pending URXIFG1 = 1  Interrupt pending | URXIFG1 | As UART mode

## Slide 39: Quiz (1/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
1. The USART supports the following communication modes:
(a) UART and I2C;
(b) SPI and I2C;
(c) UART and SPI;
(d) None of above.
2. The USART module has:
(a) One SPI module;
(b) Two SPI modules;
(c) Three SPI modules;
(d) None of the above.

## Slide 40: Quiz (2/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
3. The USART:
(a) Transmits and receives characters synchronously;
(b) Transmits characters synchronously and receives characters asynchronously;
(c) Transmits characters asynchronously and receives characters synchronously;
(d) Transmits and receives characters asynchronously.
4. The USART character format is composed of:
(a) {Start bit, Seven data bits, Parity bit, Stop bit};
(b) {Start bit, Eight data bits, Parity bit, Stop bits};
(c) {Start bit, Seven data bits, Parity bit, Address bit; Stop bit};
(d) Each of the above is possible.

## Slide 41: Quiz (3/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
5. The asynchronous communication formats available to the USART module are:
(a) Idle-line multiprocessor communication protocol;
(b) Address bit multiprocessor communication protocol;
(c) All of above;
(d) None of above.
6. The automatic error detection recognizes:
(a) Framing, Parity, Receive Overrun and Break condition errors;
(b) Framing and Parity errors;
(c) Receive Overrun and Break condition errors;
(d) Framing, Parity, Receive Overrun errors.

## Slide 42: Quiz (4/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
7. The serial clock control in SPI mode when MM = 1 is provided by the:
(a) UCLK pin on the master;
(b) BITCLK USART baud rate generator on the UCLK;
(c) All of above;
(d) None of above.

## Slide 43: Quiz (5/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Answers
  1. (c) UART and SPI.
  2. (a) One SPI module.
  3. (d) Transmits and receives characters asynchronously.
  4. (d) Each of the above is possible.
  5. (c) All of above.
  6. (a) Framing, Parity, Receive Overrun and Break condition errors.
  7. (b) BITCLK USART baud rate generator on the UCLK.