## Slide 1: Chapter 14 Communications USI Module
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
<footer> Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt

## Slide 2: Contents
MSP430 communications interfaces
USI module introduction
USI operation: SPI mode
USI operation: I2C mode
USI registers (SPI and I2C modes)
Lab10b: Echo test using SPI
Lab10c: Echo test using I2C
Quiz

## Slide 3: MSP430 communications interfaces (1/2)
Equipped with three serial communication interfaces:
  USART (Universal Synchronous/Asynchronous Receiver/Transmitter):
    UART mode;
    SPI mode;
    I2C (on ‘F15x/’F16x only).
  USCI (Universal Serial Communication Interface):
    UART with Lin/IrDA support;
    SPI (Master/Slave, 3 and 4 wire modes);
    I2C (Master/Slave, up to 400 kHz).
  USI (Universal Serial Interface):
    SPI (Master/Slave, 3 & 4 wire mode);
    I2C (Master/Slave, up to 400 kHz).

## Slide 4: MSP430 communications interfaces (2/2)
Comparison between the communication modules:
USART | USCI | USI
UART: - Only one modulator - n/a - n/a - n/a | UART: - Two modulators support n/16 timings - Auto baud rate detection - IrDA encoder & decoder - Simultaneous USCI_A and USCI_B (2 channels) | 
SPI: - Only one SPI available - Master and Slave Modes - 3 and 4 Wire Modes | SPI: - Two SPI (one on each USCI_A and USCI_B) - Master and Slave Modes - 3 and 4 Wire Modes | SPI: - Only one SPI available - Master and Slave Modes
I2C: (on ‘15x/’16x only) - Master and Slave Modes - up to 400kbps | I2C: - Simplified interrupt usage - Master and Slave Modes - up to 400kbps | I2C: - SW state machine needed - Master and Slave Modes

## Slide 5: USI module introduction (1/2)
The USI (Universal Serial Interface) module supports basic SPI and I2C synchronous serial communications;
It is available in the MSP430x20xx family of devices;
The USI module supports:
  SPI or I2C modes;
  Interrupt driven;
  Reduces CPU load;
  Flexible clock source selection.

## Slide 6: USI module introduction (2/2)
USI block diagram:
  SPI mode:
    Programmable data length (8/16-bit shift register);
    MSB/LSB first.
  I2C mode:
    START/STOP detection;
    Arbitration lost detection.
  Interrupt driven;
  Reduces CPU load;
  Flexible clock source.

## Slide 7: USI operation: SPI and I2C modes (1/5)
Shift register and bit counter that include logic to support SPI and I2C communication;
USISR shift register (up to 16 bits supported):
  Directly accessible by software;
  Contains the data to be transmitted/received (simultaneously);
  MSB or LSB first.
Bit counter:
  Controls the number of bits transmitted/received;
  Counts the number of sampled bits;
  Sets USIIFG when the USICNTx = 0 (decrementing or writing zero to USICNTx bits);
  Writing USICNTx > 0 automatically clears USIIFG when USIIFGCC = 0 (automatically stops clocking after last bit).

## Slide 8: USI operation: SPI and I2C modes (2/5)
USI initialization:
  Reset USISWRST;
  Set USIPEx bits (USI function for the pin and maintains the PxIN and PxIFG functions for the pin):
    Port input levels can be read via the PxIN register by software;
    Incoming data stream can generate port interrupts on data transitions.

## Slide 9: USI operation: SPI and I2C modes (3/5)
Recommended USI initialization process:
  Set the USIPEx bits in the USI control register (USI function for the pin and set up the PxIN and PxIFG functions for the pin as well);
  Set the direction of the RX and TX shift register (MSB or LSB first) by USILSB bit;
  Select the mode (master or slave) by USIMTS bit;
  Enable or disable output data by USIOE bit;
  Enable USI interrupts by setting USIIE bit;
  Set up USI clock by configuring the USICKCTL control register;
  Enable USI by setting USISWRST bit;
  Read port input levels via the PxIN register by software;
  Incoming data stream will generate port interrupts on data transitions.

## Slide 10: USI operation: SPI and I2C modes (4/5)
USI clock generation:
  Clock selection multiplexer:
    Internal clocks ACLK or SMCLK;
    External clock SCLK;
    USISWCLK (software clock input bit);
    Timer_A CAP/COM outputs.
  Configurable divider;
  Auto-stop on interrupt: USIIFG;
  Selectable phase and polarity.

## Slide 11: USI operation: SPI and I2C modes (5/5)
USICKPL: Selects the inactive level of the SPI clock (data latching on rising or falling edge);
USICKPH: Selects the clock edge on which SDO is updated and SDI is sampled (idle high or low support).
USIIFG automatically cleared and set by USICNTx;
Clock stop on IFG: USIIFG and USISTTIFG.

## Slide 12: USI operation: SPI mode (1/2)
Configure SPI mode:
  SPI master:
    USIMST = 1;
    USII2C = 0;
    Select clock source;
    SCLK -> output.
  SPI slave:
    USIMST = 0;
    USII2C = 0;
    SCLK -> input;
    Receives the clock externally from the master.
USIPEx bits enable data and clock pins;
Port logic functions, including interrupts as normal;
Data output latched on shift clock.

## Slide 13: USI operation: SPI mode (2/2)
SPI interrupts:
  One interrupt vector associated with the USI module;
  One interrupt flag, USIIFG:
    Set when bit counter counts to zero;
    Generates an interrupt request when USIIE = 1;
    Cleared when USICNTx > 0 (USIIFGCC = 0), or directly by software;
    Stops clock when set.

## Slide 14: USI operation: I2C mode (1/10)
Configure USI module in I2C mode:
  USII2C =1;
  USICKPL = 1;
  USICKPH = 0;
I2C data compatibility:
  USILSB = 0;
  USI16B = 0;
Enable SCL and SDA
port functions:
  Set USIPE6 and USIPE7.

## Slide 15: USI operation: I2C mode (2/10)
I2C master:
  USIMST = 1 and USII2C = 1;
  Select clock source (output to SCL line while USIIFG = 0).
I2C slave:
  USIMST = 0;
  SCL is held low if USIIFG=1, USISTTIFG=1 or if USICNTx=0.

## Slide 16: USI operation: I2C mode (3/10)
I2C transmitter:
  Data value is first loaded into USISRL;
  USIOE= 1: Enable output and start transmission (writes 8 into USICNTx);
  Send Start (or repeated Start);
  Define address and set R/W;
  Slave ACK: (Data TX/RX + ACK for N bytes);
  SCL is generated in master mode or released from being held low in slave mode;
  USIIFG is set after the transmission of all 8 bits (stops clock signal on SCL in master mode or held low at the next low phase in slave mode);
  Stop (or repeated Start).

## Slide 17: USI operation: I2C mode (4/10)
I2C receiver:
  Clear USIOE (disable output);
  Enable reception by writing 8 into USICNTx (USIIFG = 0);
  SCL is generated in master mode or released from being held low in slave mode;
  USIIFG is set after 8 clocks (stops the clock signal on SCL in master mode or holds SCL low at the next low phase in slave mode).

## Slide 18: USI operation: I2C mode (5/10)
SDA configuration:
  Direction;
  Used for TX/RX, ACK/NACK handling and START/STOP generation;
  USIGE: Output latch control;
  USIOE: Data output enable.

## Slide 19: USI operation: I2C mode (6/10)
START condition:
(high-to-low transition on SDA while SCL is high);
  Clear MSB of the shift register;
  USISTTIFG set on start (Sources USI interrupt).

## Slide 20: USI operation: I2C mode (7/10)
STOP condition:
(low-to-high transition on SDA while SCL is high):
  Clear the MSB in the shift register and loads 1 into USICNTx (finishes the acknowledgment bit and pulls SDA low);
  USISTP set on stop (CPU-accessible flag).

## Slide 21: USI operation: I2C mode (8/10)
Receiver ACK/NACK generation:
  After address/data reception;
  SDA = output;
  Output 1 data bit: 0 = ACK, 1 = NACK.
Transmitter ACK/NACK Detection:
  After address/data transmission;
  SDA = input;
  Receive 1 data bit: 0 = ACK, 1 = NACK.
Arbitration procedure (in multi-master I2C systems);

## Slide 22: USI operation: I2C mode (9/10)
I2C Interrupts:
  One interrupt vector associated with the USI;
  Two interrupt flags, USIIFG and USISTTIFG;
  Each interrupt flag has its own interrupt enable bit, USIIE and USISTTIE;
  When an interrupt is enabled and the GIE bit is set, a set interrupt flag will generate an interrupt request;
  USIIFG is set (USICNTx = 0);
  USISTTIFG is set (START condition detection).

## Slide 23: USI operation: I2C mode (10/10)
Example:
  Procedure for I2C communication between a Master TX and a Slave RX.
Master TX | Slave RX
1: Send Start, Address and R/W bit | 1: Detect Start, receive address and R/W
2: Receive (N)ACK | 2: Transmit (N)ACK
3: Test (N)ACK and handle TX data | 3: Data RX
4: Receive (N)ACK | 4: Transmit (N)ACK
5: Test (N)ACK and prepare Stop | 5: Reset for next Start
6: Send Stop | 

## Slide 24: USI registers (SPI and I2C modes) (1/8)
USICTL0, USI Control Register 0

## Slide 25: USI registers (SPI and I2C modes) (2/8)
USICTL0, USI Control Register 0 (continued)

## Slide 26: USI registers (SPI and I2C modes) (3/8)
USICTL1, USI Control Register 1

## Slide 27: USI registers (SPI and I2C modes) (4/8)
USICTL1, USI Control Register 1 (continued)

## Slide 28: USI registers (SPI and I2C modes) (5/8)
USICKCTL, USI Clock Control Register

## Slide 29: USI registers (SPI and I2C modes) (6/8)
USICKCTL, USI Clock Control Register (continued)

## Slide 30: USI registers (SPI and I2C modes) (7/8)
USICNT, USI Bit Counter Register

## Slide 31: USI registers (SPI and I2C modes) (8/8)
USISRL, USI Low Byte Shift Register
USISRH, USI High Byte Shift Register

## Slide 32: Lab10b: Echo test using SPI mode (1/17)
Project files:
  C source files: Chapter 14 > Lab10 > Lab10b1_student.
  Chapter 14 > Lab10 > Lab10b2_student.c
  Solution files: Chapter 14 > Lab10 > Lab10b1_solution.c
Chapter 14 > Lab10 > Lab10b2_solution.c
Overview:
  This laboratory explores the USCI and USI communication interfaces in SPI mode;
  The MSP430 devices supported by the Experimenter’s board will exchange messages between themselves;

## Slide 33: Lab10b: Echo test using SPI mode (2/17)
Overview (continued):
  MSP430FG4618: Master reads the current state of the slave, and drives it to the new desired state;
  MSP430F2013: Slave commanded by the Master.
A. Resources:
  USCI module: MSP430FG4618;
  USI module: MSP430F2013;
  Both units operate in SPI mode;
  Basic Timer1 of the master device is programmed to switch the status of the slave device once every 2 seconds;
  The slave is notified of the arrival of information through the end of counting interrupt of the USI module.

## Slide 34: Lab10b: Echo test using SPI mode (3/17)
A. Resources (continued):
  The resources used are:
    USCI module;
    USI module;
    Basic Timer1;
    Interrupts;
    I/O ports.

## Slide 35: Lab10b: Echo test using SPI mode (4/17)
B. Software application organization:

## Slide 36: Lab10b: Echo test using SPI mode (5/17)
B. Software application organization:
  The master unit is composed of two software modules:
    The "Main master task" module contains the operational algorithm of the master unit;
    The "ISR Basic Timer" module wakes the "Main master task" with a rate of once every 2 seconds.
  Similarly, the slave unit is composed of two modules:
    The "Main slave task" module contains the operational algorithm of the slave unit;
    The "USI ISR" module reads the data received, prepares the USI module for reception of a new command and wakes the "Main slave task" to execute the algorithm associated with the reception of the new command.

## Slide 37: Lab10b: Echo test using SPI mode (6/17)
C. Configuration:
  Configure the control registers USCI_B (master):
    The SPI connection will operate as follows:
      Clock phase -> Data bits are sent on the first UCLK edge and captured on the following edge;
      Clock polarity -> the inactive state is low;
      MSB first;
      8-bit data;
      Master mode;
      3-Pin SPI;
      Source clock -> SMCLK.

## Slide 38: Lab10b: Echo test using SPI mode (7/17)
C. Configuration (continued):
  Configure the control registers USCI_B (master):
    Configure the following control registers based on these characteristics:
  UCB0CTL0 = _______________;
  UCB0CTL1 = _______________;

## Slide 39: Lab10b: Echo test using SPI mode (8/17)
C. Configuration (continued):
  Data rate USCI_B (master):
    The system clock is configured to operate with a frequency of ~ 1048 kHz from the DCO;
    This frequency will be the working base of the USCI module;
    The connection operates at a clock frequency of ~ 500 kHz. Configure the following registers:
  UCB0BR0= _______________;
  UCB0BR1= _______________;

## Slide 40: Lab10b: Echo test using SPI mode (9/17)
C. Configuration (continued):
  Ports configuration USCI_B (master):
    In order to set the external interfaces of the USCI module, it is necessary to configure the I/O ports;
    Select the USCI peripheral in SPI mode following the connections provided at the Experimenter’s board:
    P3SEL = __________________;

## Slide 41: Lab10b: Echo test using SPI mode (10/17)
C. Configuration (continued):
  Configure the control registers USI (slave):
    The SPI connection will operate in the following mode:
      MSB first;
      8-bit data;
      Slave mode;
      Clock phase -> Data bits are sent on the first SCLK edge and captured on the following edge;
      USI counter interrupt enable.

## Slide 42: Lab10b: Echo test using SPI mode (11/17)
C. Configuration (continued):
  Configure the control registers USI (slave):
    Configure the following control registers based on these characteristics:
    USICTL0 = _______________;
    USICTL1 = _______________;

## Slide 43: Lab10b: Echo test using SPI mode (12/17)
D. Analysis of operation:
  Once the USCI module is configured in accordance with the previous steps, to initiate the experiment, complete the files Lab10b1_student.c (master – MSP430FG4618) and Lab10b2_student.c (slave – MSP430F2013), compile them and run them on the Experimenter’s board;
  The finished solution can be found in the files Lab10b1_solution.c and Lab10b2_soluction.c.
  For this laboratory, the following jumper settings are required:
    PWR1/2, BATT, LCL1/2, JP2;
    SPI: H1- 1&2, 3&4, 5&6, 7&8.

## Slide 44: Lab10b: Echo test using SPI mode (13/17)
D. Analysis of operation:
  Verification:
    Once the program code is running in the two microcontrollers, monitor LED3 of the Experimenter’s board. It will blink at a rate of 4 flashes per second.

## Slide 45: Lab10b: Echo test using SPI mode (14/17)
Control registers USCI_B (master):
UCB0CTL0 = 0x29;
//UCB0CTL0 = UCCKPH|UCCKPL|UCMSB|UC7BIT|UCMST|UCMODEx|UCSYNC
//UCCKPH (Clock phase) = 0b -> Data is changed on the
// first UCLK edge and captured on the following edge.
//UCCKPL (Clock polarity) = 0b -> Inactive state is low
//UCMSB (MSB first select) = 1b -> MSB first
//UC7BIT (Character length) = 0b -> 8-bit data
//UCMST (Master mode) = 1b -> Master mode
//UCMODEx (USCI mode) = 00b -> 3-Pin SPI
//UCSYNC (Synch. mode enable) = 1b -> Synchronous mode
MSP-EXP430FG4618 (master) | SOLUTION
Using USCI module in SPI mode included in the FG4618 (configured as master) of the Experimenter’s board, establish a connection to the F2013 by its USI module in SPI mode. The data exchanged is displayed by the LED blinking. | 

## Slide 46: Lab10b: Echo test using SPI mode (15/17)
Control registers USCI_B (master):
UCB0CTL1 = 0x81;
//UCB0CTL1 = UCSSELx | Unused |UCSWRST|
//UCSSELx (USCI clock source select)= 10b -> SMCLK
//UCSWRST (Software reset) = 1b -> normally set by a PUC
Data rate USCI_B (master):
UCB0BR0 = 0x02;
UCB0BR1 = 0x00;
// Data rate = SMCLK/2 ~= 500kHz
// UCB0BR1 = 0x00 & UCB0BR0 = 0x02
Configure I/O ports:
P3SEL |= 0x0E;
// P3.1,P3.2,P3.3 option select

## Slide 47: Lab10b: Echo test using SPI mode (16/17)
USI (slave) control registers:
USICTL0 = 0xE3;
//USICTL0 = USIPE7|USIPE6|USIPE5|USILSB|USIMST|USIGE|USIOE|USISWRST
//USIPE7 (USI SDI/SDA port enable) = 1b -> USI enabled
//USIPE6 (USI SDO/SCL port enable) = 1b -> USI enabled
//USIPE5 (USI SCLK port enable) = 1b -> USI enabled
//USILSB (LSB first) = 0b -> MSB first
//USIMST (Master) = 0b -> Slave mode
//USIGE (Output latch control) = 0b -> Output latch enable
//USIOE (Serial data output enable) = 1b -> Output enabled
//USISWRST (USI software reset) = 1b -> Software reset
MSP-EXP430F2013 (slave) | SOLUTION
Using the USCI module in SPI mode included in the FG4618 (configured as master) of the Experimenter’s board, establish a connection to the F2013 by its USI module in SPI mode. The data exchanged is displayed by the LED blinking. | 

## Slide 48: Lab10b: Echo test using SPI mode (17/17)
USI (slave) control registers:
USICTL1 = 0x10;
//USICTL1= USICKPH|USII2C|USISTTIE|USIIE|USIAL|USISTP|USISTTIFG|USIIFG
//USICKPH (Clock phase select) = 0b -> Data is changed on the first
// SCLK edge and captured on the following edge
//USII2C (I2C mode enable) = 0b -> I2C mode disabled
//USISTTIE (START condition interrupt) = 0b -> Not used
//USIIE (USI counter) = 1b -> Interrupt enabled
//USIAL (Arbitration lost) = 0b -> Not used
//USISTP (STOP condition received) = 0b -> Not used
//USISTTIFG (START condition int. flag) = 0b -> Not used
//USIIFG (USI counter int. flag) = 0b -> No int. pending

## Slide 49: Lab10c: Echo test using I2C mode (1/21)
Project files:
  C source files: Chapter 14 > Lab10 > Lab10c1_student.c
  Chapter 14 > Lab10 > Lab10c2_student.c
  Solution files: Chapter 14 > Lab10 > Lab10c1_solution.c
  Chapter 14 > Lab10 > Lab10c2_solution.c
Overview:
  This laboratory explores the USCI and USI communication interfaces in I2C mode;
  It uses the two MSP430 devices included on the Experimenter’s board: MSP430FG4618 as the master and the MSP430F2013 as slave;
  The master receives a single byte from the slave as soon as a button connected to P1.0 is pressed.

## Slide 50: Lab10c: Echo test using I2C mode (2/21)
A. Resources:
  This laboratory uses the USCI module of the MSP430FG4618 device and the USI module included in the MSP430F2013. Both units operate in I2C mode;
  The interrupts on the slave unit are generated exclusively by the USI module. They are:
    START condition on the I2C bus;
    Data reception and transmission.
  The interrupts in the master unit are provided by the USCI module. They are:
    Data reception;
    Logic level change on Port1.

## Slide 51: Lab10c: Echo test using I2C mode (3/21)
A. Resources:
  The resources used are:
    USCI module;
    USI module;
    Interrupts;
    I/O ports.

## Slide 52: Lab10c: Echo test using I2C mode (4/21)
B. Software application organization:
  Software architecture:

## Slide 53: Lab10c: Echo test using I2C mode (5/21)
B. Software application organization:
  The master task is composed of two interrupt service routines:
    The S1 switch service routine is used to control the way the master receives a new data frame from the slave;
    The USCI module interrupt service routine ensures that the data sent by the slave is read by the master .
  A state machine has been implemented for the USI module of the slave unit;
  It is important to note that the states “RX Address” and “RX (N)ACK" are transient states that ensure the USI module is ready for the next activity.

## Slide 54: Lab10c: Echo test using I2C mode (6/21)
B. Software application organization:
  Slave state machine:

## Slide 55: Lab10c: Echo test using I2C mode (7/21)
C. Configuration:
  Configure the control registers USCI_B (master):
    The connection via I2C bus is to operate as follows:
      Address slave with 7-bit address;
      Master mode;
      Single master;
      USCI clock source is SMCLK.
    Configure the following control registers based on these characteristics:
    UCB0CTL0 = _______________;
    UCB0CTL1 = _______________;

## Slide 56: Lab10c: Echo test using I2C mode (8/21)
C. Configuration (continued):
  Data rate USCI_B (master):
    The system clock is configured to operate with a frequency of ~ 1048 kHz from the DCO;
    This frequency will be the working base for the USCI module;
    The connection operates at a clock frequency of ~ 95.3kHz. Configure the following registers:
    UCB0BR0= _______________;
    UCB0BR1= _______________;

## Slide 57: Lab10c: Echo test using I2C mode (9/21)
C. Configuration (continued):
  Ports configuration USCI_B (master):
    In order to set the external interfaces for the USCI module, it is necessary to configure the I/O ports;
    Select the USCI peripheral in I2C mode to be compatible with the connections on the Experimenter’s board:
    P3SEL = __________________;

## Slide 58: Lab10c: Echo test using I2C mode (10/21)
C. Configuration (continued):
  Configure the control registers USI (slave):
    The connection via I2C bus is to operate as follows:
      Slave mode;
      USI counter interrupt enable (RX and TX);
      START condition interrupt-enable;
      USIIFG is not cleared automatically.
    Configure the following control registers:
    USICTL0 = _______________;
    USICTL1 = _______________;
    USICNT = ________________;

## Slide 59: Lab10c: Echo test using I2C mode (11/21)
C. Configuration (continued):
  Configure the control registers USI (slave):
    The slave unit interrupt service routine is not yet complete. The portion related to the “I2C_TX” state needs to be completed:
      Configure the USI module as an output;
      Insert the value to transmit in the transmit register;
      Configure the bit counter.
    USICTL0 |=________________;
    USISRL =_________________;
    USICNT |=________________;

## Slide 60: Lab10c: Echo test using I2C mode (12/21)
D. Analysis of operation:
  Once the USCI module is configured in accordance with the previous steps, to initiate the experiment, complete the files:
    Lab10c1_student.c (master – MSP430FG4618)
    Lab10c2_student.c (slave – MSP430F2013)
    Compile them and run them on the Experimenter’s board;
  The completed solution can be found in the files Lab10c1_solution.c and Lab10c2_soluction.c.
  For this laboratory it is necessary to set up the following jumper settings:
    PWR1/2, BATT, LCL1/2, JP2;
    SPI: H1- 1&2, 3&4.

## Slide 61: Lab10c: Echo test using I2C mode (13/21)
D. Analysis of operation:
  Verification:
    The slave data values are sent and incremented from 0x00 with each transmitted byte, and are verified by the Master;
    The LED is off for address/data Acknowledge and the LED turns on for address/data Not Acknowledge;
    The LED3 blinks at each data request:
      It is turned on by a START condition;
      It is turned off by the data transmit acknowledge by the slave;
      (Note: the I2C bus is not released by the master because the successive START conditions are interpreted as “repeated START”).

## Slide 62: Lab10c: Echo test using I2C mode (14/21)
D. Analysis of operation:
  Verification:
    Verify the value received by setting a breakpoint in the line of code “RxBuffer = UCB0RXBUF;” of the USCI interrupt.

## Slide 63: Lab10c: Echo test using I2C mode (15/21)
USCI (master) control registers:
UCB0CTL0 = 0x0F;
//UCB0CTL0 =
//UCA10|UCSLA10|UCMM|Unused|UCMST|UCMODEx|UCSYNC|
//UCA10 (Own address) = 0b -> Own address (7-bit)
//UCSLA10 (Slave address) = 0b -> 7-bit slave address
//UCMM (Multi-master) = 0b -> Single master
//Unused
//UCMST (Master mode) = 1b -> Master mode
//UCMODEx (USCI mode) = 11b -> I2C Mode
//UCSYNC (Synchronous mode enable) = 1b -> Synchronous
MSP-EXP430FG4618 (master) | SOLUTION
Using USCI module in I2C mode included in the FG4618 (configured as master) of the Experimenter’s board, establish a connection to the F2013 by its USI module in I2C mode. The master receives a single byte from the slave as soon as a button connected on P1.0 is pressed. | 

## Slide 64: Lab10c: Echo test using I2C mode (16/21)
USCI (master) control registers:
UCB0CTL1 = 0x81;
//UCB0CTL1 =
//UCSSELx|Unused|UCTR|UCTXNACK|UCTXSTP|UCTXSTT|UCSWRST|
//UCSSELx (USCI clock source select) = 10b -> SMCLK
//Unused
//UCTR (Transmitter/Receiver) = 0b -> Receiver
//UCTXNACK (Transmit a NACK) = 0b -> Ack normally
//UCTXSTP (Transmit STOP condition) = 0b -> No STOP
//UCTXSTT (Transmit START condition) = 0b -> No START
//UCSWRST (Software reset) = 1b -> Enabled

## Slide 65: Lab10c: Echo test using I2C mode (17/21)
Data rate:
// DATA RATE
// data rate -> fSCL = SMCLK/11 = 95.3 kHz
UCB0BR0 = 0x0B; // fSCL = SMCLK/11 = 95.3 kHz
UCB0BR1 = 0x00;
Configure ports:
P3SEL |=0x06; // Assign I2C pins to USCI_B0

## Slide 66: Lab10c: Echo test using I2C mode (18/21)
USI (slave) control registers:
USICTL0 = 0XC1;
//USICTL0 =|USIPE7|USIPE6|USIPE5|USILSB|USIMST|USIGE|USIOE|USISWRST|
//USIPE7 (USI SDI/SDA port enable) = 1b -> USI function enabled
//USIPE6 (USI SDO/SCL port enable) = 1b -> USI function enabled
//USIPE5 (USI SCLK port enable) = 0b -> USI function disable
//USILSB (LSB first) = 0b -> MSB first
//USIMST (Master) = 0b -> Slave mode
//USIGE (Output latch control) = 0b -> Depends on shift clock
//USIOE (Serial data output enable) = 0b -> Output enabled
//USISWRST (USI software reset) = 1b -> Software reset
MSP-EXP430F2013 (slave) | SOLUTION
Using USCI module in I2C mode included in the FG4618 (configured as master) of the Experimenter’s board, establish a connection to the F2013 by its USI module in I2C mode. The master receives a single byte from the slave as soon as a button connected on P1.0 is pressed. | 

## Slide 67: Lab10c: Echo test using I2C mode (19/21)
USI (slave) control registers:
USICTL1 = 0x70;
//USICTL1 =
//|USICKPH|USII2C|USISTTIE|USIIE|USIAL|USISTP|USISTTIFG|USIIFG|
//USICKPH (Clock phase select) = 0b -> Data is changed
// on the first SCLK edge and captured on the following edge.
//USII2C (I2C mode enable) = 1b -> I2C mode enabled
//USISTTIE = 1b -> Interrupt on START condition enabled
//USIIE = 1b -> USI counter interrupt enable
//USIAL (Arbitration lost) = 0b -> Not used
//USISTP (STOP condition received) = 0b -> Not used
//USISTTIFG (START condition int. flag) = 0b -> Not used
//USIIFG (USI counter int. flag) = 0b -> No int. pending

## Slide 68: Lab10c: Echo test using I2C mode (20/21)
USI Bit Counter Register:
USICNT |= 0x20;
//USICNT =
//USISCLREL| USI16B |USIIFGCC |USICNTx|
//USISCLREL (SCL release) = 0b -> SCL line is held low
// if USIIFG is set
//USI16B (16-bit shift register enable) = 0b -> 8-bit
// shift register mode
//USIIFGCC (USI int. flag clear control) = 1b -> USIIFG
// is not cleared automatically
//USICNTx (USI bit count) = 00000b (not relevant)

## Slide 69: Lab10c: Echo test using I2C mode (21/21)
I2C state machine:
USICTL0 |= USIOE; // SDA = output
USISRL = SlaveData; // Send data byte
USICNT |= 0x08; // Bit counter = 8, TX data

## Slide 70: Quiz (1/4)
1. The USI module has:
(a) A SPI interface;
(b) An I2C interface;
(c) All of above;
(d) None of above.
2. The internal USI clock generation can use:
(a) ACLK and SMCLK;
(b) ACLK and MCLK;
(c) SMCLK and MCLK;
(d) None of above.

## Slide 71: Quiz (2/4)
3. The USISR shift register supports:
(a) 8 bits;
(b) 16 bits;
(c) All of above;
(d) None of above.
4. The USIIFG is set when:
(a) Bit counter counts to 0xFF;
(b) Bit counter counts to 0x00;
(c) Bit counter counts to 0x80;
(d) Bit counter counts to 0x08.

## Slide 72: Quiz (3/4)
5. After address/data reception, the receiver ACK/NACK is:
(a) SDA = input: 0 = ACK, 1 = NACK;
(b) SDA = output: 0 = ACK, 1 = NACK;
(c) SDA = input: 1 = ACK, 0 = NACK;
(d) SDA = output: 1 = ACK, 0 = NACK.
6. After address/data transmission the transmitter ACK/NACK is:
(a) SDA = input: 0 = ACK, 1 = NACK;
(b) SDA = output: 0 = ACK, 1 = NACK;
(c) SDA = input: 1 = ACK, 0 = NACK;
(d) SDA = output: 1 = ACK, 0 = NACK.

## Slide 73: Quiz (4/4)
Answers:
  1. (c) All of above.
  2. (a) ACLK and SMCLK.
  3. (c) All of above.
  4. (b) Bit counter counts to 0x00.
  5. (b) SDA = output: 0 = ACK, 1 = NACK.
  6. (a) SDA = input: 0 = ACK, 1 = NACK.