## Slide 1: Chapter 14 Communications Introduction
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
<footer> Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt

## Slide 2: Contents
Introduction
Communications system model
Transmission mode
Serial communications
Synchronous and asynchronous serial communications
Peripheral Interface Serial (SPI) protocol
I2C (Inter-Integrated Circuit) protocol
MSP430 communications interfaces
Quiz

## Slide 3: Introduction
An important feature of modern microprocessor based systems is their communication capability, that is, their ability to exchange information with other systems in the surrounding environment;
At the low level, communications interfaces are used to download a firmware update or to set up local configurations (e.g. turn features on or off), amongst other tasks;
At a higher level, communication interfaces are used to exchange information in distributed applications.

## Slide 4: Communications system model (1/2)
Digital communication devices:
  Transmitter: Has the task of putting the information into the appropriate format for subsequent transmission;
  Receiver: Is responsible for collecting the message that has been sent and extracting the original information;
  Communication medium: The physical medium through which the information flows and is commonly implemented as:
    Twisted pair wire;
    Fibre optic cable;
    Radio frequency transmission.

## Slide 5: Communications system model (2/2)
Devices participating in a digital communication system:
  DTE: Data Terminal Equipment;
  DCE: Data Communications Equipment.

## Slide 6: Transmission mode (1/5)
Communications between digital devices can be divided into two types :
  Parallel communications;
  Serial communications.
Parallel communications:
  The physical transmission medium has independent signal lines in numbers equal to the transmitted digital word bits;
  The information transmitted at any given instant is the data word formed by the logical levels on the various signal lines.

## Slide 7: Transmission mode (2/5)
Parallel communications:
  Example: Character ASCII “W” parallel transmission.
Information flow

## Slide 8: Transmission mode (3/5)
Serial communications:
  Physical transmission medium needs only one signal line;
  The information transmitted is provided by the transmitter as a sequence of bits, sent at the rate established between the transmitter and the receiver;
  Additional information is needed to enable the synchronization between the receiver and transmitter:
    Start bit: Added to the beginning of the information transmitted, so that the receiver can identify the beginning of a new transmission;
    Stop bit(s): Added to the end of the information transmitted to indicate that the data value is complete.

## Slide 9: Transmission mode (4/5)
Serial communications:
  Example: Character ASCII “W” serial transmission:

## Slide 10: Transmission mode (5/5)
Advantages and disadvantages of parallel and serial communication:
Characteristic | Parallel | Serial
Bus line | One line per bit | One line
Sequence | All bits of one word simultaneously | Sequence of bits
Transmission rate | High | Low
Bus length | Short distances | Short and long distances
Cost | High | Low
Critical characteristics | Synchronisation between the different bits is demanding | Asynchronous transmission needs start and stop bits Synchronous transmission needs some other synchronisation

## Slide 11: Serial communications (1/3)
The start bit identifies the beginning of a data transfer and is generated by a high-to-low transition on the bus;
Following the start bit are the data bits. In this example, the ASCII code for the text transfer uses seven data bits;
The error-checking bit (parity bit) is sent after the data bits;
To terminate the transmission, one or two stop bits are issued;
Using seven data bits, the complete message can use one or two stop bits. Using eight data bits, only one stop bit is available for transmission.

## Slide 12: Serial communications (2/3)
Parity bit:
  Used to verify the integrity of information transmitted;
  The bit is added by the transmitter and indicates whether the total sum of the numbers "1" in the message data is odd or even;
  The transmissions can be configured for odd or even parity.

## Slide 13: Serial communications (3/3)
Baud rate example:
  The transmission of “W”:
    Character uses seven data bits;
    Four bits are used for control, making a total of 11 bits.
    This corresponds to 11 baud;
    If the characters are transmitted at a rate of 10 characters per second, the baud rate will be:
    10x11 = 1100 baud/s.

## Slide 14: Synchronous and asynchronous serial communications (1/2)
Serial communications may be:
  Asynchronous: where the transmission rate (baud rate) is fixed by the transmitter and the receiver works at the same baud rate, using the transmitted start bit to synchronize the start of a new message;
  Synchronous: where there is a separate synchronization clock signal connected between the receiver and the transmitter.
Synchronous communications:
  Normally one unit assumes the role of master and one or more of the other units take the role of slaves;
  The clock signal generated by the master is used by the slave units to transfer data in/out of the TX and RX registers;
  It is possible for a device to transmit and receive simultaneously.

## Slide 15: Synchronous and asynchronous serial communications (2/2)
Asynchronous communications:
  Characterised by the absence of any synchronization clock signal between the units;
  The transmission in this mode does not allow simultaneous transmission and reception, that is, when one device transmits the other devices just listen.

## Slide 16: Serial Peripheral Interface (SPI) protocol (1/2)
The Serial Peripheral Interface ( SPI) bus is a standard form of synchronous serial communication;
Developed by Motorola;
Operates in full duplex mode;
Master/Slave relationship;
Communications are always
initiated by the master.
Low cost.

## Slide 17: Peripheral Interface Serial (SPI) protocol (2/2)
Supports only one master;
Can support more than a slave;
Short distance between devices, e.g. on a printed circuit boards (PCBs);
Special attention needs to be observed to the polarity and phase of the clock signal;
The master sends data on one edge of clock and reads data on the other edge. Therefore, it can send/receive at the same time.

## Slide 18: I2C (Inter-Integrated Circuit) protocol (1/3)
Multi-master synchronous serial computer bus;
Invented by Philips Semiconductors;
Developed with the main objective of establishing links between integrated circuits and to connect low-speed peripherals;
Based on a two bi-directional open-drain lines pulled up with resistors:
    SDA: Serial Data;
    SCL: Serial clock.
Typical voltages used are +5.0 V or +3.3 V, although systems with other voltages are possible.

## Slide 19: I2C (Inter-Integrated Circuit) protocol (2/3)
Communications is always initiated and completed by the master, which is responsible for generating the clock signal;
In more complex applications, I2C can operate in multi-master mode;
The slave selection by the master is made using the seven-bit address of the target slave;
The master (in transmit mode) sends:
  Start bit;
  7-bit address of the slave it wishes to communicate with;
  A single bit representing whether it wishes to write (0) to or read (1) from the slave;
  The target slave will acknowledge its address.

## Slide 20: I2C (Inter-Integrated Circuit) protocol (3/3)
Example of an I2C communication system:

## Slide 21: MSP430 communications interfaces (1/2)
Equipped with three serial communication interfaces:
  USART (Universal Synchronous/Asynchronous Receiver/Transmitter):
    UART mode;
    SPI mode;
    I2C (on ‘F15x/’F16x only).
  USCI (Universal Serial Communication Interface):
    UART with Lin/IrDA support;
    SPI (Master/Slave, 3 and 4 wire modes);
    I2C (Master/Slave, up to 400 kHz).
  USI (Universal Serial Interface):
    SPI (Master/Slave, 3 & 4 wire mode);
    I2C (Master/Slave, up to 400 kHz).

## Slide 22: MSP430 communications interfaces (2/2)
Comparison between the communication modules:
USART | USCI | USI
UART: - Only one modulator - n/a - n/a - n/a | UART: - Two modulators support n/16 timings - Auto baud rate detection - IrDA encoder & decoder - Simultaneous USCI_A and USCI_B (2 channels) | 
SPI: - Only one SPI available - Master and Slave Modes - 3 and 4 Wire Modes | SPI: - Two SPI (one on each USCI_A and USCI_B) - Master and Slave Modes - 3 and 4 Wire Modes | SPI: - Only one SPI available - Master and Slave Modes
I2C: (on ‘15x/’16x only) - Master and Slave Modes - up to 400kbps | I2C: - Simplified interrupt usage - Master and Slave Modes - up to 400kbps | I2C: - SW state machine needed - Master and Slave Modes

## Slide 23: Quiz (1/6)
1. In the parallel communication transmission mode:
(a) The data is transferred more slowly;
(b) Each bit of the data has its own line;
(c) All of above;
(d) None of above.
2. In the serial communication transmission mode:
(a) The data bits arrive sequentially;
(b) The digital data is transferred faster;
(c) All of above;
(d) None of above.

## Slide 24: Quiz (2/6)
3. The serial transmission mode is the most popular digital data communications method because:
(a) Higher bit transfer rates are achieved;
(b) It is cheaper to implement than parallel transmission mode;
(c) All of above;
(d) None of above.
4. In asynchronous serial transmission communications, the frame must include:
(a) Start and stop bits.
(b) Parity bit.
(c) All of above;
(d) None of above.

## Slide 25: Quiz (3/6)
5. Even parity means that an additional bit is:
(a) Added to the data to make the sum of the “1” bits even;
(b) Subtracted from the data to make the sum of the “1” bits even;
(c) All of above;
(d) None of above.
6. A USART is used:
(a) Only for asynchronous transmissions;
(b) Only for synchronous transmissions;
(c) In parallel transmission communications;
(d) In serial transmission communications.

## Slide 26: Quiz (4/6)
7. Synchronous communication performed between two USART requires:
(a) A common clock either in the transmitter or the receiver;
(b) No common clock;
(c) An independent clock in the transmitter;
(d) An independent clock in the receiver.
8. Asynchronous communication between two USARTs requires:
(a) A common clock in the transmitter and the receiver;
(b) An independent clock in the transmitter and the receiver;
(c) A common clock in the transmitter or the receiver;
(d) An independent clock in the transmitter or the receiver.

## Slide 27: Quiz (5/6)
9. I2C is a bus:
(a) Synchronous with a master and a slave where both can be the transmitter or receiver;
(b) Where the master generates the clock;
(c) All of above;
(d) None of above.

## Slide 28: Quiz (6/6)
Answers:
  1. (b) Each bit of the data has its own line.
  2. (a) The data bits arrive sequentially.
  3. (c) All of above.
  4. (c) All of above.
  5. (a) Added to the data to make the sum of the “1” bits even.
  6. (d) In serial transmission communications.
  7. (a) A common clock either in the transmitter or the receiver.
  8. (b) An independent clock in the transmitter and the receiver.
  9. (d) None of above.