## Slide 1: Chapter 15 Advanced Laboratories RF link using the eZ430-RF2500
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Notes: <number>

## Slide 2: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Introduction
The application
The hardware
The software
Configuration
Algorithms
New challenges

## Slide 3: Introduction (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
This laboratory demonstrates the operation of a small wireless communication application;
The purpose of this laboratory is to send and receive text messages, making use of RF links between the central unit (base unit) and the various peripheral units (remote units).
It is an integrated application, using some peripherals of the MSP430, in particular, the USCIx communication modules;
Additionally, it uses the CC2500 radio transceiver as an interface to external devices;
Even though the application is simple, it is motivating to the user because the IO console allows easy interaction with the system;

## Slide 4: Introduction (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
This laboratory has the following objectives:
  To demonstrate the importance of software organization as a fundamental part of an embedded systems project:
    To approach the problem using a top-down approach, applying the necessary abstraction to organize the software into functional layers.
  To give an example of the management of a complex project, integrating together more than one functional module:
    To develop a modular structure so that several functional modules co-exist together within a single software project.

## Slide 5: Introduction (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
This laboratory has the following objectives (continued):
  Make use of the wireless communications capability of the MSP430, demonstrating its practical advantages;
  Consolidate knowledge acquired during the previous laboratories, namely:
    From the MSP430 communications interfaces laboratories:
      SPI mode to access the transceiver CC2500;
      UART mode to interface with the IO console.

## Slide 6: The application (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
This laboratory establishes communications between various RF units;
The stations are identified by an ID, i.e., the address for presentation to the network. When a station wants to communicate with another station, it must use the address of the target station in the message;
The CC2500 has several ways to communicate, which determine the size of the messages exchanged;
In order to simplify the communication process, fixed-size address and data have been used (maximum message size 64 bytes). This corresponds to the size of the CC2500 FIFO.

## Slide 7: The application (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
CC2500 packages format:

## Slide 8: The application (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
This laboratory has two units with distinct functional differences:
  The code differs between the two units:
  One unit contains the base station functionality:
    Receives messages from all peripheral units;
    Works as a radio beacon;
    Sends to to all remote stations;
    Acknowledges messages received.
  The other unit acts as a remote station.

## Slide 9: The application (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Block Diagram of the Application:

## Slide 10: The hardware (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The application is ready to run on the eZ430-RF2500 hardware development kit (see Chapter 3 for details). The devices used are the:
    CC2500 radio transceiver;
    MSP430F2274;
    RS232 interface, accessed through the USB interface, which is available for development.

## Slide 11: The hardware (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The CC2500 is a radio frequency transceiver operating in the widely used ISM/SRD (Industrial-Scientific-Medical /Short-Range-Devices) 2.4 GHz frequency band;
It is a low-cost device with low power consumption, designed for consumer electronics applications.

## Slide 12: The hardware (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The communications protocol uses very little data formatting. It is up to the user to define the communications protocol that best suits their application and implement their own software;
The CC2500 is a low pin-out device, because it integrates all the radio functions, except the antenna;
This device is not sufficiently independent that it can operate without the aid of a microcontroller;
When coupled to the MSP430, connection is made between:
    Access to internal registers: SPI interface belongs to the USCIB0 unit;
    Status pins: GDO0 and GDO2 (P2.6 and P2.7).

## Slide 13: The hardware (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
CC250 RF transceiver:

## Slide 14: The software (1/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Internal structure:
  Structured in layers:
    Base layer: Hardware abstraction layer. Responsible for separating the higher layers of software from the hardware;
    Middle SPI layer: Ensures the communication functions for the correct operation of CC2500;
    UART layer: Provides connection to the PC via RS232;
    CC2500 layer: Access and control functions controlling the CC2500 (SPI and the GPIO);
    Application layer: Uses the features offered by layers at a lower level to implement the tasks necessary for the correct operation of the application.

## Slide 15: The software (2/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Software structure:

## Slide 16: The software (3/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Each layer has different functional responsibilities:
  Hardware definition layer:
File | Description
TI_CC_CC1100-CC2500.h | Definitions specific to the CC1100/2500 devices (Chipcon’s/TI SmartRF Studio software can assist in generating register contents)
TI_CC_MSP430.h | Definitions specific to the MSP430 device
TI_CC_hardware_board.h | Definitions specific to the board (connections between MSP430 and CCxxxx)

## Slide 17: The software (4/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
  SPI layer:
  CC2500 layer:
File | Description
TI_CC_spi.h | Function declarations for hal_spi.c
TI_CC_spi.c | Functions for accessing CC1100/CC2500 registers via SPI from MSP430
File | Description
cc1100-CC2500.c | Initialization of messages, transmission and reception functions.
TI_CC_CC1100-CC2500.h | Function declarations for cc1100-CC2500.c

## Slide 18: The software (5/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
  UART layer:
File |  | Description
hal_uart.c | Initialization of messages and transmission functions via RS232. | 
hal_uart.h | Function declarations for hal_uart.c | 

## Slide 19: Configuration (1/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Clearly defined start-up of the multiple hardware modules and the various software modules;
Important: The unit’s address needs to be changed during compilation, to allocate a unique address.

## Slide 20: Configuration (2/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Base station code:
  Two interrupt service routines (ISR) and two buffers:

## Slide 21: Configuration (3/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Base station code:
    Port2 ISR:
      Enabled by GDO0, which causes a L-H transition when it receives a valid Sync_Word;
      H-L transition at the end of a message reception;
      The contents of the received messages are sent to the IO console via the RS232 connection;
    The Timer_A service routine is used to send a message to check for correct reception from the remote stations (maximum of 15);
    The two buffers are used to hold the messages:
      The transmit buffer is used to build the message for later transmission;
      The receive buffer is used to hold the data read from the CC2500 FIFO when a message is received.

## Slide 22: Configuration (4/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Remote station code:
  Composed of two interrupt service routines (ISR) and two buffers:

## Slide 23: Configuration (5/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Remote station code:
    Port2 ISR:
      Enabled by the GDO0, which causes a L-H transition when it receives a valid Sync_Word;
      H-L transition at the end of a message reception;
      Received message contents to IO console (RS232).
    Port1 ISR: Generated when the button is pressed, sending the signal announcing the presence of the remote station;
    Two buffers used to hold the messages:
      Transmit buffer is used to build the message for later transmission;
      The receive buffer is used to hold the data read from the CC2500 FIFO after receiving a message.

## Slide 24: Algorithms (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Transmission algorithm implemented by Port1 ISR:

## Slide 25: Algorithms (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Reception algorithm used by the Port2 ISR in both stations:

## Slide 26: New challenges
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
This laboratory has brought together the range of ideas and concepts taught in the CDROM. It can also be used as the basis for other and more exciting new challenges;
Using the present laboratory as a starting point, develop an application to exchange written messages between a series of stations scattered inside a room, a kind of "wireless messenger“;
The messages typed into the IO console for a particular address would be sent by wireless support to the console addressed.

## Slide 27: New challenges
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
To achieve this objective, it is useful to define a small set of user-defined commands, such as:
    Address allocation at the local station;
    Address allocation at the remote station;
    Sending a message;
    Neighbourhood screening of possible talking partners;
    Among others…