## Slide 1: Chapter 15 Advanced Laboratories MSP430 assembly language tutorial: MSP430X CPU
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Notes: <number>

## Slide 2: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Exploring the addressing modes of the MSP430X architecture:
  Main features of the MSP430X CPU architecture
  Organization of the MSP430X CPU
  MSP430X CPU registers
  Instruction format in the MSP430X CPU
  Exceptions to the representation of the extended Format II instructions
  Extended emulated instructions
  MSP430X address instructions
  MSP430X CPU addressing modes

## Slide 3: Exploring the addressing modes of the MSP430X architecture (1/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Main features of the MSP430X CPU architecture:
  The MSP430X CPU extends the addressing capabilities of the MSP430 family beyond 64 kB to 1 MB;
  To achieve this, some changes have been made to the addressing modes and two new types of instructions have been added;
  One instruction type allows access to the entire address space, and the other is designed for address calculations;
  The MSP430X CPU address bus has 20 bits, although the data bus still has 16 bits. Memory accesses to 8-bit, 16-bit and 20-bit data are supported;
  Despite these changes, the MSP430X CPU remains compatible with the MSP430 CPU, having a similar number of registers.

## Slide 4: Exploring the addressing modes of the MSP430 architecture (2/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Organization of the MSP430X CPU:
  Although the MSP430X CPU structure is similar to that of the MSP430 CPU, there are some differences that will now be highlighted;
  All the MSP430X registers have 20 bits, with the exception of the Status Register (SR) which has 16 bits;
  The MSP430X CPU can now process 20-bit or 16-bit data.

## Slide 5: Exploring the addressing modes of the MSP430 architecture (3/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The MSP430X CPU has 16 registers, some of which have special use:
R0 (PC) Program Counter:
  Has the same function as the MSP430 CPU, although now it has 20 bits.
R1 (SP) Stack Pointer:
  Has the same function as the MSP430 CPU, although now it has 20 bits.
R2 (SR) Status Register:
  Has the same function as the MSP430 CPU, but it still has 16 bits.

## Slide 6: Exploring the addressing modes of the MSP430 architecture (4/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R2 (SR) Status Register:
  Description of the SR bits:

## Slide 7: Exploring the addressing modes of the MSP430 architecture (5/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R2 (SR/CG1) and R3 (CG2) Constant Generators:
  Registers R2 and R3 can be used to generate six different constants commonly used in programming, without adding an additional 16-bit word to the instruction;
  The constants are fixed and are selected by the (As) bits of the instruction. (As) selects the addressing mode;
  Values of constants
  generated:

## Slide 8: Exploring the addressing modes of the MSP430 architecture (6/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R2 (SR/CG1) and R3 (CG2) Constant Generators:
  Whenever the operand is one of the six constants, the registers are selected automatically;
  Therefore, when used in constant mode, registers R2 and R3 cannot be used as source registers.
R4-R15 – General-purpose registers:
  Have the same function as in the MSP430 CPU, although they now have 20 bits;
  These registers can process 8-bit, 16-bit or 20-bit data;
  If a byte is written to one of these registers it takes bits 7:0, the bits 19:8 are filled with zeroes;
  If a word is written to one of these registers it takes bits 15:0, the bits 19:16 are filled with zeroes.

## Slide 9: Exploring the addressing modes of the MSP430 architecture (7/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R4-R15 – General-purpose registers:
  Handling byte data (8 bits) using the suffix .B:

## Slide 10: Exploring the addressing modes of the MSP430 architecture (8/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R4-R15 – General-purpose registers:
  Handling word data (16 bits) using the suffix .W:

## Slide 11: Exploring the addressing modes of the MSP430 architecture (9/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R4-R15 – General-purpose registers:
  Manipulation of a 20-bit address using the suffix .A:

## Slide 12: Instruction format in the MSP430X CPU (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
There are three possibilities to choose between the instructions of the MSP430 CPU and MSP430X CPU:
    Use only the MSP430 CPU instructions. The following rules must be followed, with the exception of the instructions CALLA/RETA, BRA:
      Put all the data in memory below 64 kB and access the data using 16-bit pointers;
      Place the routines at an address within the range PC 32 kB;
      No 20-bits data.
    Use only the MSP430X CPU instructions. This causes a reduction in the application execution speed and an increase in the memory space occupied by the program;
    Use an appropriate selection of the instruction types.

## Slide 13: Instruction format in the MSP430X CPU (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The MSP430X CPU supports all functions of the MSP430 CPU;
It also offers a set of instructions that provide full access to the 20-bit addressing space;
An additional op-code word is added to some of the instructions. Therefore all addresses, indexes and immediate numbers have 20 bits.

## Slide 14: Extension word for register addressing mode (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
In register mode, the extension word of an instruction of format type I (two operands) or format type II (single operand) is coded as:
The description of each field:

## Slide 15: Extension word for register addressing mode (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Unlike the MSP430, the MSP430X CPU supports the repeated execution of the same instruction, provided that the operands are of the register type;
The repetition is set by placing the repeat RPT instruction before the instruction to be executed;
The assembler incorporates information in the extension word in the fields # (bit 7) and in the repetition counter (bits 3:0);
An example of this feature will be provided later.

## Slide 16: Extension word for the other addressing modes
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
In a non-register addressing mode, the extension word of an instruction, whether format I (double operands) or format II (single operand), is coded as:
The description of each field:

## Slide 17: Extended format I -Double operand- instructions
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
There are twelve extended instructions that use two operands:

## Slide 18: Examples: Extended double operand instructions (1/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of register R5 to register R4:
MOVX R5,R4
  Instruction code: 0x1840 – 0x4504
  This instruction uses 2 words;
  The instruction coding specifies that the CPU must perform the 16-bit data function MOVX, using the contents of the source register R5 and the destination register R4.
0 | 0 | 0 | 1 | 1 | 0 | 0 | ZC | # | A/L | 0 | 0 | n-1/Rn
0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 0 0 0
Op-code |  |  |  | S-reg |  |  |  | Ad | B/W | As |  | D-reg
0 1 0 0 |  |  |  | 0 1 0 1 |  |  |  | 0 | 0 | 0 0 |  | 0 1 0 0
MOVX |  |  |  | R5 |  |  |  | Register | 16-bit | Register |  | R4

## Slide 19: Examples: Extended double operand instructions (2/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of the register R5 to the memory address TONI:
MOVX R5,TONI
  Instruction code: 0x184F – 0x4580
  This instruction uses 3 words;
0 | 0 | 0 | 1 | 1 | src 19:16 |  | A/L | 0 | 0 | dst 19:16
0 | 0 | 0 | 1 | 1 | 0 0 0 0 |  | 1 | 0 | 0 | 1 1 1 1
Op-code |  |  |  | S-reg |  | Ad | B/W | As |  | D-reg
0 1 0 0 |  |  |  | 0 1 0 1 |  | 1 | 0 | 0 0 |  | 0 0 0 0
MOVX |  |  |  | R5 |  | Symbolic | 16-bits | Register |  | PC

## Slide 20: Examples: Extended double operand instructions (3/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of the register R5 to the memory address TONI (continued):
MOVX R5,TONI
  The instruction coding specifies that the CPU must perform the 16-bit data function MOVX, the source being the contents of register R5 and the destination being the memory address pointed to by (dst 19:16: X1 + PC);
  The bits dst 19:16 is stored in the extension word and the value X1 is stored in the word following.
0 | 0 | 0 | 1 | 1 | src 19:16 |  | A/L | 0 | 0 | dst 19:16
0 | 0 | 0 | 1 | 1 | 0 0 0 0 |  | 1 | 0 | 0 | 1 1 1 1
Op-code |  |  |  | S-reg |  | Ad | B/W | As |  | D-reg
0 1 0 0 |  |  |  | 0 1 0 1 |  | 1 | 0 | 0 0 |  | 0 0 0 0
MOVX |  |  |  | R5 |  | Symbolic | 16-bits | Register |  | PC

## Slide 21: Examples: Extended double operand instructions (4/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of the memory address TONI to register R5:
MOVX TONI,R5
  Instruction code: 0x1FC0 – 0x4015
  This instruction uses 3 words;
0 | 0 | 0 | 1 | 1 | src 19:16 |  | A/L | 0 | 0 | dst 19:16
0 | 0 | 0 | 1 | 1 | 1 1 1 1 |  | 1 | 0 | 0 | 0 0 0 0
Op-code |  |  |  | S-reg |  | Ad | B/W | As |  | D-reg
0 1 0 0 |  |  |  | 0 0 0 0 |  | 0 | 0 | 0 1 |  | 0 1 0 1
MOVX |  |  |  | PC |  | Register | 16-bit | Symbolic |  | R5

## Slide 22: Examples: Extended double operand instructions (5/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of the memory address TONI to register R5 (continued):
MOVX TONI,R5
  The coding specifies that the CPU must perform the 16-bit data function MOVX, the source being the contents of memory address pointed to by (src 19:16: X1 + PC) and the destination being register R5;
  The bits dst 19:16 are stored in the extension word and the value X1 is stored in the word following.
0 | 0 | 0 | 1 | 1 | src 19:16 |  | A/L | 0 | 0 | dst 19:16
0 | 0 | 0 | 1 | 1 | 1 1 1 1 |  | 1 | 0 | 0 | 0 0 0 0
Op-code |  |  |  | S-reg |  | Ad | B/W | As |  | D-reg
0 1 0 0 |  |  |  | 0 0 0 0 |  | 0 | 0 | 0 1 |  | 0 1 0 1
MOVX |  |  |  | PC |  | Register | 16-bit | Symbolic |  | R5

## Slide 23: Examples: Extended double operand instructions (6/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of the memory address TONI to the memory address EDEN:
MOVX TONI,EDEN
  Instruction code: 0x1FCF – 0x4090
  This instruction uses 4 words;
0 | 0 | 0 | 1 | 1 | src 19:16 |  | A/L | 0 | 0 | dst 19:16
0 | 0 | 0 | 1 | 1 | 1 1 1 1 |  | 1 | 0 | 0 | 1 1 1 1
Op-code |  |  |  | S-reg |  | Ad | B/W | As |  | D-reg
0 1 0 0 |  |  |  | 0 0 0 0 |  | 1 | 0 | 0 1 |  | 0 0 0 0
MOVX |  |  |  | PC |  | Symbolic | 16-Bit | Symbolic |  | PC

## Slide 24: Examples: Extended double operand instructions (7/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of the memory address TONI to the address memory EDEN:
MOVX TONI,EDEN
  The coding specifies that the CPU must perform the 16-bit data function MOVX, the source being the contents of the memory address pointed to by (src 19:16: X1 + PC) and the destination being the contents of the memory address pointed to by (dst 19:16: X2 + PC);
  The bits src 19:16 and dst 19:16 are stored in the extension word and the words X1 and X2 are stored in the words following.
0 | 0 | 0 | 1 | 1 | src 19:16 |  | A/L | 0 | 0 | dst 19:16
0 | 0 | 0 | 1 | 1 | 1 1 1 1 |  | 1 | 0 | 0 | 1 1 1 1
Op-code |  |  |  | S-reg |  | Ad | B/W | As |  | D-reg
0 1 0 0 |  |  |  | 0 0 0 0 |  | 1 | 0 | 0 1 |  | 0 0 0 0
MOVX |  |  |  | PC |  | Symbolic | 16-Bit | Symbolic |  | PC

## Slide 25: Extended format II - single operand- instructions (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Extended instructions using format II are:

## Slide 26: Extended format II - single operand- instructions (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The MSP430X CPU has some additional capabilities in addition to those of the MSP430 CPU:
  The ability to push/pop several registers on/off the data stack using only a single instruction;
  The ability to rotate the contents of a register several times during the execution of a single instruction.

## Slide 27: Examples: Extended single operand instructions (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Rotate right the 20-bit contents of register R5 with the carry flag:
RRCX.A R5
  Instruction code: 0x1800 – 0x1045
  This instruction uses 2 words;
  The coding specifies that the CPU must perform the function RRCX using the 20-bit data contents of register R5.
0 | 0 | 0 | 1 | 1 | 0 | 0 | ZC | # | A/L | 0 | 0 | n-1/Rn
0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 0 0 0
Op-code |  |  |  |  |  |  |  |  | B/W | Ad |  | D/S-reg
0 0 0 1 0 0 0 0 0 |  |  |  |  |  |  |  |  | 1 | 0 0 |  | 0 1 0 1
RRCX |  |  |  |  |  |  |  |  | 20-bit | Register |  | R5

## Slide 28: Examples: Extended single operand instructions (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Rotate right the 20-bit contents of the memory address TONI with carry flag:
RRCX.A TONI
  Instruction code: 0x180F – 0x1050
  This instruction uses 3 words;
  The coding specifies that the CPU must perform the function RRCX using the 20-bit data contents of the memory address pointed to by (dst 19:16: X1 + PC);
0 | 0 | 0 | 1 | 1 | src 19:16 | A/L | 0 | 0 | dst 19:16
0 | 0 | 0 | 1 | 1 | 0 0 0 0 | 0 | 0 | 0 | 1 1 1 1
Op-code |  |  |  |  |  | B/W | Ad |  | D/S-reg
0 0 0 1 0 0 0 0 0 |  |  |  |  |  | 1 | 0 1 |  | 0 0 0 0
RRCX |  |  |  |  |  | 20-bit | Symbolic |  | PC

## Slide 29: Examples: Extended single operand instructions (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Rotate right the 20-bit contents of the memory address TONI with carry flag (continued):
RRCX.A TONI
  Instruction code: 0x180F – 0x1050
  The bits dst 19:16 are stored in the extension word and the value X1 is stored in the word following;
0 | 0 | 0 | 1 | 1 | src 19:16 | A/L | 0 | 0 | dst 19:16
0 | 0 | 0 | 1 | 1 | 0 0 0 0 | 0 | 0 | 0 | 1 1 1 1
Op-code |  |  |  |  |  | B/W | Ad |  | D/S-reg
0 0 0 1 0 0 0 0 0 |  |  |  |  |  | 1 | 0 1 |  | 0 0 0 0
RRCX |  |  |  |  |  | 20-bit | Symbolic |  | PC

## Slide 30: Examples: Extended single operand instructions (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Rotate right the 20-bit contents of the memory address TONI with carry flag (continued):
RRCX.A TONI
  Because the instruction operand is located in memory rather than in a CPU register, two words are used to store the operand. The format is shown in the figure below:

## Slide 31: Exceptions to the representation of the extended Format II instructions (1/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Store the 20-bit registers R10, R9, R8:
PUSHM.A #3,R10
  The instructions PUSHM and POPM are coded according to the structure given in the figure below:
  Instruction code: 0x142A
  This instruction uses 1 word;
  The coding specifies that the CPU must perform the function PUSHM of the 20-bit registers R10 to R8.
Op-code | n - 1 | D-reg
0 0 0 1 0 1 0 0 | 0 0 1 0 | 1 0 1 0
PUSHM.A | #3 | R10

## Slide 32: Exceptions to the representation of the extended Format II instructions (2/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Rotate right three times the contents of the 20-bit register R5 with the carry flag:
RRCM.A #3,R5
  The instructions RRCM, RRAM, RRUM and RLAM are coded according to the structure given in the figure below:

## Slide 33: Exceptions to the representation of the extended Format II instructions (3/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Rotate right three times the content of the 20-bit register R5 with the carry flag (continued):
RRCM.A #3,R5
  Instruction code: 0x0845
  This instruction uses 1 word;
  The coding specifies that the CPU must perform the function RRCM using the contents of the 20-bit register R5 a total of 3 times.
C | n-1 | Op-code | R-reg
0 0 0 0 | 1 0 | 0 0 0 1 0 0 | 0 1 0 1
 | #3 | RRCM | R5

## Slide 34: Exceptions to the representation of the extended Format II instructions (4/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Perform a branch in the program flow:
BRA R5
  This type of instruction can be coded in three different formats, as shown in the figure below:

## Slide 35: Exceptions to the representation of the extended Format II instructions (5/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Perform a branch in the program flow (continued):
BRA R5
  Instruction code: 0x05C0
  This instruction uses 1 word;
  The coding specifies that the PC must be loaded with the value in register R5.
C | R-reg | Op-code | 0(PC)
0 0 0 0 | 0 1 0 1 | 1 1 0 0 | 0 0 0 0
 | R5 | BRA | PC

## Slide 36: Exceptions to the representation of the extended Format II instructions (6/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Call a routine:
CALLA R5
  This type of instruction can be coded in three different formats, as shown in the figure below:

## Slide 37: Exceptions to the representation of the extended Format II instructions (7/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Call a routine (continued):
CALLA R5
  Instruction code: 0x1345
  This instruction uses 1 word;
  The coding specifies that the PC must be loaded with the value in register R5;
  The execution of this instruction saves the PC on the data stack, so the function can return at the end of execution of the routine.
Op-code | D-reg
0 0 0 1 0 0 1 1 0 1 0 0 | 0 1 0 1
CALLA | R5

## Slide 38: Extended emulated instructions
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The constant generator provide a set of extended emulated instructions, as shown in the following table:

## Slide 39: MSP430X address instructions
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Address instructions support 20-bit operands, but they have restrictions on the addressing modes they can use;
List of extended address instructions:

## Slide 40: MSP430X CPU addressing modes
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
As with the MSP430 CPU, the MSP430X CPU supports seven addressing modes for the source operand and four addressing modes for the destination operand;
Both the MSP430 CPU and MSP430X CPU instructions can be used throughout the 1 MB address space;
In the following sections we will explore the different addressing modes available to the MSP430X CPU.

## Slide 41: Register mode (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
This addressing mode is identical to that of the MSP430 CPU;
There are three different types of access to the registers:
  8-bit access (Byte operation);
  16-bit access (Word operation);
  20-bit access (Address-word).
The instruction SXT is the only exception, as the sign of the value is extended to the other bits of the register.

## Slide 42: Register mode (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the 20-bit contents of register R5 to register R4:
MOVX.A R5,R4
  Instruction code: 0x1800 – 0x4544
  The instruction uses 2 words.
  The 20-bit contents (B/W = 1 and A/L = 0) of register R5 (S-reg = 0101) is transferred to register R4 (D-reg = 0100);
0 | 0 | 0 | 1 | 1 | 0 | 0 | ZC | # | A/L | 0 | 0 | n-1/Rn
0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 0 0 0
Op-code |  |  |  | S-reg |  |  |  | Ad | B/W | As |  | D-reg
0 1 0 0 |  |  |  | 0 1 0 1 |  |  |  | 0 | 1 | 0 0 |  | 0 1 0 0
MOVX |  |  |  | R5 |  |  |  | Register | 20-bit | Register |  | R4

## Slide 43: Register mode (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the 20-bit contents of register R5 to register R4 (continued):
MOVX.A R5,R4
  After the execution of the instruction, the PC is incremented by 4 and pointed to the next instruction;
  The addressing mode used for the source and destination operands is specified by Ad = 0 (Register mode) and As = 00 (Register mode).

## Slide 44: Indexed mode
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Indexed mode can be used in three different situations:
  Indexed mode in the memory address space below 64 kB;
  Indexed mode in the memory address space above 64 kB;
  Indexed mode using a MSP430X CPU instruction.

## Slide 45: Indexed mode: below 64 kB (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Indexed mode in the memory address space below 64 kB:
  If the CPU register Rn points to a memory address located below 64 kB, the address resulting from the sum of the index and the register Rn has the value zero in bits 19:16.
  This ensures that the address is always located in memory below 64 kB.

## Slide 46: Indexed mode: below 64 kB (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by (R5 – 0x30) to the word pointed to by (R4 + 2):
  MOV 0XFFD0(R5),2(R4)
  Instruction code: 0x4594
  This instruction uses 3 words;
  The instruction coding specifies that the word (B/W = 0) pointed to by the sum of register R5 contents (S-reg = 0101) and the word X1 should be moved to the memory address pointed to by the sum of the register R4 contents (D-reg = 0100) and the word X2;
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 1 0 1 | 1 | 0 | 0 1 | 0 1 0 0
MOV | R5 | Indexed | 16-bit | Indexed | R4

## Slide 47: Indexed mode: below 64 kB (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by (R5 – 0x30) to the word pointed to by (R4 + 2) (continued):
  MOV 0XFFD0(R5),2(R4)
  The words X1 and X2 are located in the memory addresses following the instruction;
  The addressing mode used for the source and destination operands is specified by the bits Ad = 1 (Indexed mode) and As = 01 (Indexed mode), because D-reg = 0100 and S-reg = 0101 respectively;
  In this example, bits 19:16 are set to zero when the operand addresses are calculated.

## Slide 48: Indexed mode: below 64 kB (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by (R5 – 0x30) to the word pointed to by (R4 + 2) (continued):
  MOV 0XFFD0(R5),2(R4)

## Slide 49: Indexed mode: above 64 kB (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Indexed mode in the memory address space above 64 kB:
  If the CPU register Rn points to a memory address above 64 kB, bits 19:16 are used to calculate the operand of the address;
  A prerequisite is that the operand must be located in the range Rn  32KB, because the index is a signed 16-bit value;
  Outside this range, the operand address can overflow or underflow the memory address space below or above the 64 kB.
  If the registers now point to a memory address space above 64 kB, bits 19:16 are used to determine the address in the operands.

## Slide 50: Indexed mode: above 64 kB (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Indexed mode in the memory address space above 64 kB (continued):

## Slide 51: Indexed mode: MSP430X CPU (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Indexed mode using a MSP430X CPU instruction:
  When a MSP430X CPU instruction is used in indexed mode, the operand can reside anywhere in the range of addresses Rn  19 bits;
  The operand address is calculated from the sum of the 20-bit contents of the register Rn and the signed 20-bit index.

## Slide 52: Indexed mode: MSP430X (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by (R5 – 0x30) to the word pointed to by (R4 + 2):
MOVX 0xFFFD0(R5),2(R4)
  Instruction code: 0x1FC0 – 0x4594
  This instruction uses 4 words;
0 | 0 | 0 | 1 | 1 | src 19:16 | A/L | 0 | 0 | dst 19:16
0 | 0 | 0 | 1 | 1 | 1 1 1 1 | 1 | 0 | 0 | 0 0 0 0
Op-code |  |  | S-reg |  | Ad | B/W | As |  | D-reg
1 0 0 0 |  |  | 0 1 0 1 |  | 1 | 0 | 0 1 |  | 0 1 0 0
MOVX |  |  | R5 |  | Indexed | 16-bit | Indexed |  | R4

## Slide 53: Indexed mode: MSP430X CPU (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by (R5 – 0x30) to the word pointed to by (R4 + 2) (continued):
MOVX 0xFFFD0(R5),2(R4)
  The instruction coding specifies that the word (B/W = 0 and A/L = 1) pointed to by the sum of register R5 contents (S-reg = 0101) and the word X1 should be moved to the memory address pointed to by the sum of the register R4 contents (D-reg = 0100) and the word X2;
  The four MSB indices are placed in the extension word of the instruction and the other 16 bits are placed in the words following the instruction;
  The addressing mode used for the source and destination operands is specified by the bits Ad = 1 (Indexed mode) and As = 01 (Indexed mode), because D-reg = 0100 and S-reg = 0101 respectively.

## Slide 54: Indexed mode: MSP430X CPU (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by (R5 – 0x30) to the word pointed to by (R4 + 2) (continued):
MOVX 0xFFFD0(R5),2(R4)

## Slide 55: Symbolic mode
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The symbolic addressing mode uses the register PC to determine the location of the operand based on an index;
Similar to the previous addressing mode, there are three different ways to use symbolic mode with the MSP30X CPU.
  Symbolic mode in the memory address space below 64 kB;
  Symbolic mode in the memory address space above 64 kB;
  Symbolic mode using a MSP430X CPU instruction.

## Slide 56: Symbolic mode: below 64 kB (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
As in the indexed addressing mode, if the PC register points to a memory address below 64 kB, the bits 19:16 of the address calculated from the sum of the PC register and the signed 16-bit index are set to zero.
Move the contents of the address EDEN located at 0x00200 to the address TONI located at 0x00202:
MOV EDEN,TONI
  Instruction code: 0x4090
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 0 0 0 | 1 | 0 | 0 1 | 0 0 0 0
MOV | PC | Symbolic | 16-bit | Symbolic | PC

## Slide 57: Symbolic mode: below 64 kB (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of the address EDEN located at 0x00200 to the address TONI located at 0x00202 (cont.):
MOV EDEN,TONI
  This instruction uses 3 words;
  The instruction decoding specifies that the word (B/W = 0) pointed to by the sum of the register PC contents (S-reg = 0000) and the word X1 should be moved to the memory address pointed to by the sum of the register PC contents (D-reg = 0000) and the word X2;
  The words X1 and X2 are stored in the memory addresses following the instruction;
  The addressing mode used for the source and destination operands is specified by the bits Ad = 1 (Symbolic mode) and As = 01 (Symbolic mode), because D-reg = 0000 and S-reg = 0000, respectively.

## Slide 58: Symbolic mode: below 64 kB (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of address the EDEN located at 0x00200 to the address TONI located at 0x00202 (cont.):
MOV EDEN,TONI

## Slide 59: Symbolic mode: above 64 kB (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
If the PC register points to a memory address above 64 kB, bits 19:16 of the PC are used to calculate the operand address;
The operand must be located in the memory range PC  32 kB, because the index is a signed 16-bit value;
If outside this range, there may be an overflow or underflow in the address space corresponding to memory below 64 kB.

## Slide 60: Symbolic mode: above 64 kB (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of the address EDEN located at 0x10200 to register R5:
MOV EDEN,R5
  Instruction code: 0x4015
  This instruction uses 2 words;
  The instruction coding specifies that the word (B/W = 0) pointed to by the sum of the register PC contents (S-reg = 0000) and the word X1 should be moved to the register R5 (D-reg = 0101);
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 0 0 0 | 0 | 0 | 0 1 | 0 1 0 1
MOV | PC | Register | 16-bit | Symbolic | R5

## Slide 61: Symbolic mode: above 64 kB (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of the address EDEN located at 0x10200 to register R5 (continued):
MOV EDEN,R5
  The word X1 is in the memory address following the instruction;
  The addressing mode used for the source and destination operands is specified by the bits Ad = 0 (Register mode) and As = 01 (Symbolic mode), because D-reg = 0101 and S-reg = 0000, respectively.

## Slide 62: Symbolic mode: above 64 kB (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of the address EDEN located at 0x10200 to register R5 (continued):
MOV EDEN,R5

## Slide 63: Symbolic mode: MSP430X CPU (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
When a MSP430X CPU instruction is used in symbolic mode, the operand can be located anywhere in the range of the addresses PC  19 bits;
The operand address is calculated from the sum of the 20-bit contents of the PC register and the signed 20-bit index.

## Slide 64: Symbolic mode: MSP430X CPU (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of the address EDEN located at 0x00200 to register R5:
MOVX EDEN,R5
  Instruction code: 0x1FC0 – 0x4015
  This instruction uses 3 words;
0 | 0 | 0 | 1 | 1 | src 19:16 | A/L | 0 | 0 | dst 19:16
0 | 0 | 0 | 1 | 1 | 1 1 1 1 | 1 | 0 | 0 | 0 0 0 0
Op-code |  |  |  | S-reg | Ad | B/W | As |  | D-reg
0 1 0 0 |  |  |  | 0 0 0 0 | 0 | 0 | 0 1 |  | 0 1 0 1
MOVX |  |  |  | PC | Register | 16-bit | Symbolic |  | R5

## Slide 65: Symbolic mode: MSP430X CPU (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of the address EDEN located at 0x00200 to register R5 (continued):
MOVX EDEN,R5
  The instruction coding specifies that the CPU must perform the function MOVX of the 16-bit data (B/W = 0 and A/L = 1), from the memory address contents pointed to by (src 19:16:X1 + PC) to register R5;
  The bits (src 19:16) are stored in the extension word and the word X1 is stored in the word following the instruction;
  The addressing mode used for the source and destination operands is specified by the bits Ad = 0 (Register mode) and As = 01 (Symbolic mode), because D-reg = 0000 and S-reg = 0101, respectively.

## Slide 66: Symbolic mode: MSP430X CPU (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of the address EDEN located at 0x00200 to register R5 (continued):
MOVX EDEN,R5

## Slide 67: Absolute mode
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Absolute mode uses the word contents following the instruction as the operand address;
There are two different ways to use absolute mode with the MSP30X CPU.
  Absolute mode in the memory address space below 64 kB:
    In memory space below 64 kB, this instruction operates in the same way as the MSP430 CPU.
  Absolute mode using a MSP430X CPU instruction.

## Slide 68: Absolute mode: MSP430X CPU (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
If a MSP430X CPU instruction is used with an address in absolute mode, the 20-bit absolute address of the operand is used with an index of zero (generated by the constant generators) to point to the operand;
The four MSBs of the indices are placed in the extension word of the instruction and the other 16 bits are placed in the words following the instruction.

## Slide 69: Absolute mode: MSP430X CPU (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of the address EDEN located at 0x00200 to the address TONI located at 0x00202:
MOVX &EDEN,&TONI
  Instruction code: 0x1840 – 0x4292
  This instruction uses 4 words;
0 | 0 | 0 | 1 | 1 | src 19:16 | A/L | 0 | 0 | dst 19:16
0 | 0 | 0 | 1 | 1 | 0 0 0 0 | 1 | 0 | 0 | 0 0 0 0
Op-code |  |  |  | S-reg | Ad | B/W | As |  | D-reg
0 1 0 0 |  |  |  | 0 0 1 0 | 1 | 0 | 0 1 |  | 0 0 1 0
MOVX |  |  |  | SR/CG1 | Absolute | 16-bit | Absolute |  | SR/CG1

## Slide 70: Absolute mode MSP430X CPU (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of the address EDEN located at 0x00200 to the address TONI located at 0x00202 (cont.):
MOVX &EDEN,&TONI
  The instruction coding specifies that the CPU must perform the function MOVX of 16-bit data (B/W = 0 and A/L = 1) from the memory address contents pointed to by (src 19:16:X1) to the memory address contents pointed to by (dst 19:16:X2);
  The bits src 19:16 and dst 19:16 are stored in the extension word;
  The words X1 and X2 are stored following the instruction;
  The addressing mode used for the source and destination operands is specified by the bits Ad = 1 (Absolute mode) and As = 01 (Absolute mode), because D-reg = 0010 and S-reg = 0010, respectively.

## Slide 71: Absolute mode: MSP430X CPU (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of the address EDEN located at 0x00200 to the address TONI located at 0x00202 (cont.):
MOVX &EDEN,&TONI

## Slide 72: Indirect register mode (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Indirect addressing mode uses the contents of register Rn to point to the 20-bit operand;
It can only be used to point to the source operand.
Move the operand pointed to by the contents of register R5 to the memory address TONI located at 0x00202:
MOVX @R5,&TONI
  Instruction code: 0x1840 – 0x45A2
0 | 0 | 0 | 1 | 1 | src 19:16 | A/L | 0 | 0 | dst 19:16
0 | 0 | 0 | 1 | 1 | 0 0 0 0 | 1 | 0 | 0 | 0 0 0 0
Op-code |  |  |  | S-reg | Ad | B/W | As |  | D-reg
0 1 0 0 |  |  |  | 0 1 0 1 | 1 | 0 | 1 0 |  | 0 0 1 0
MOVX |  |  |  | R5 | Absolute | 16-bit | Indirect |  | SR/CG1

## Slide 73: Indirect register mode (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the operand pointed to by the contents of register R5 to the memory address TONI located at 0x00202:
MOVX @R5,&TONI
  This instruction uses 3 words;
  The instruction coding specifies that the CPU must perform the function MOVX of 16-bit data (B/W = 0 and A/L = 1), from the memory address contents pointed to by the register R5 to the memory address contents pointed to by (dst 19:16:X1);
  The bits dst 19:16 are stored in the extension word;
  The words X1 is stored following the instruction;
  The addressing mode used for the source and destination operands is specified by the bits Ad = 1 (Absolute mode) and As = 10 (Indirect mode), because D-reg = 0010 and S-reg = 0101, respectively.

## Slide 74: Indirect register mode (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the operand pointed to by the contents of register R5 to the memory address TONI located at 0x00202:
MOVX @R5,&TONI

## Slide 75: Indirect auto-increment mode (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
This addressing mode uses the contents of register Rn to point to the 20-bit source operand;
The register Rn is automatically incremented by 1 for a byte operand, by 2 for a word operand and by 4 for an address operand.

## Slide 76: Indirect auto-increment mode (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by register R5 to the memory address TONI located at 0x00202:
MOVX @R5+,&TONI
  Instruction code: 0x1840 – 0x45B2
  This instruction uses 3 words;
0 | 0 | 0 | 1 | 1 | src 19:16 | A/L | 0 | 0 | dst 19:16
0 | 0 | 0 | 1 | 1 | 0 0 0 0 | 1 | 0 | 0 | 0 0 0 0
Op-code |  |  |  | S-reg | Ad | B/W | As |  | D-reg
0 1 0 0 |  |  |  | 0 1 0 1 | 1 | 0 | 1 1 |  | 0 0 1 0
MOVX |  |  |  | R5 | Absolute | 16-bit | Ind. aut. inc. |  | SR/CG1

## Slide 77: Indirect auto-increment mode (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by register R5 to the memory address TONI located at 0x00202 (continued):
MOVX @R5+,&TONI
  The instruction coding specifies that the CPU must perform the function MOVX of the 16-bit data (B/W = 0 and A/L = 1), from the memory address contents pointed to by the register R5 to the memory address contents pointed to by (dst 19:16:X1);
  The bits dst 19:16 are stored in the extension word;
  The word X1 is stored following the instruction;
  The addressing modes used for the source and destination operands are specified by the bits Ad = 1 (Absolute mode) and As = 11 (Indirect auto-increment mode), because D-reg = 0010 and S-reg = 0101, respectively.

## Slide 78: Indirect auto-increment mode (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by register R5 to the memory address TONI located at 0x00202 (continued):
MOVX @R5+,&TONI

## Slide 79: Immediate mode
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The immediate addressing mode allows constants to be placed after the instruction and use them as source operands;
There are two ways to use immediate mode:
  A 8-bit or 16-bit constant with a MSP430 CPU instruction:
    The operation in this situation is similar to that of the MSP430 CPU.
  A 20-bit constant with a MSP430X CPU instruction:
    If a MSP430X CPU instruction is used in immediate addressing mode, the constant has a 20-bit value;
    The bits 19:16 are stored in the extension word and the remaining bits are stored following the instruction.

## Slide 80: Immediate mode: MSP430X CPU (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the constant #0x12345 to register R5:
MOVX.A #0x12345,R5
  Instruction code: 0x1880 – 0x4075
  This instruction uses 3 words;
0 | 0 | 0 | 1 | 1 | src 19:16 | A/L | 0 | 0 | dst 19:16
0 | 0 | 0 | 1 | 1 | 0 0 0 1 | 0 | 0 | 0 | 0 0 0 0
Op-code |  |  |  | S-reg | Ad | B/W | As |  | D-reg
0 1 0 0 |  |  |  | 0 0 0 0 | 0 | 1 | 1 1 |  | 0 1 0 1
MOVX |  |  |  | PC | Register | 20-bit | Immediate |  | R5

## Slide 81: Immediate mode: MSP430X CPU (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the constant #0x12345 to register R5 (continued):
MOV.A #0x12345,R5
  The instruction coding specifies that the CPU must perform the function MOVX using 20-bit data (B/W = 1 and A/L = 0), from the location src 19:16:X1 to register R5;
  The bits src 19:16 are stored in the extension word;
  The word X1 is stored following the instruction;
  The addressing mode used for the source and destination operands is specified by the bits Ad = 0 (Register mode) and As = 11 (Immediate mode), because D-reg = 0101 and S-reg = 0000, respectively.

## Slide 82: Immediate mode: MSP430X CPU (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the constant #0x12345 to register R5 (continued):
MOV #0x12345,R5