## Slide 1: Chapter 15 Advanced Laboratories MSP430 assembly language tutorial: Creating an assembly project with CCE
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Notes: <number>

## Slide 2: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Introduction
Key assembly directives
Project example: square root extraction:
  Algorithm presentation
  Code implementation and analysis
  Testing the project

## Slide 3: Introduction (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The creation of an Assembly language project follows a sequence of steps very similar to a C/C++ project;
Tasks sequence:
    In File > New Project choose Managed Make C/ASM Project (Recommended);
    Assign a name to the project in Project Name, e.g., SQRT;
    Choose Project Type: MSP430 Executable;
    In Additional Project Setting, do not choose any connection with other projects;

## Slide 4: Introduction (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Tasks sequence (continued):
    In the Device Selection page, select the target device: MSP430FG4618. Do not forget to select the configuration option: Assembly only Project;
    At the end of this sequence of operations, a project named SQRT is opened in the work environment;
    Assign a new source code file to the project. In the option Menu > File > Source File and create a new file called SQRT.asm;

## Slide 5: Introduction (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Tasks sequence (continued):
    In the project properties menu, set the entry point as identified by the label BEGIN;
    This option is found on page Build C/C++ build > MSP430 Linker V3.0 > Symbol Management > Specify the program entry point for the output model (- entry point).

## Slide 6: Key assembly directives (1/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The MSP430 assembler translates the source code you have written into machine language;
The source files may contain the following elements:
  Assembly directives;
  Macro directives;
  Assembly language instructions.
For more detailed information on each element, please refer to the MSP430 Assembly Language Tools User’s Guide (slau131b.pdf);
Some of the most relevant aspects of the assembly language for the MSP430 will now be introduced;

## Slide 7: Key assembly directives (2/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The assembly programming tool processes the source code, producing an object file, and a descriptive listing of the entire process;
This process is completely controlled by macros, allowing conditional execution;
A options list can be found in the document MSP430 Assembly Language Tools User’s Guide (slau131b.pdf);
The MPS430 source code programs contains sequences of statements that have:
  Assembly directives;
  Assembly instructions;
  Macros, and;
  Comments.

## Slide 8: Key assembly directives (3/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A line can have four fields (label, mnemonic, operand list, and comment). The general syntax is:
[label[:]] mnemonic [operand list] [;comment]
Some line examples are:
.sect ".sysmem" ; Data Space
var1 .word 2 ; variable var1 declaration
.text ; Program Space
Label1: MOV.W R4,R5 ; move R4 contents to R5

## Slide 9: Key assembly directives (4/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The general guidelines for writing the code are:
  All statements must begin with a label, a blank, an asterisk, or a semicolon;
  Labels are optional. If used, they must begin in column 1;
  One or more blanks must separate each field. Tab and space characters are classed as blanks. You must separate the operand list from the preceding field with a blank;
  Comments are optional. Comments that begin in column 1 can begin with an asterisk or a semicolon (* or ;), but comments that begin in any other column must begin with a semicolon;
  A mnemonic cannot begin in column 1 or it will be interpreted as a label.

## Slide 10: Key assembly directives (5/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The assembler supports several formats for constants:
  Binary integer: 1111 0000b  0xF8
  Octal integer: 226  0x96
  Decimal integer: 25  0x19
  Hexadecimal integer  0x78
  Character  ‘a’
  Assembly time  value1 .set 3

## Slide 11: Key assembly directives (6/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Symbols are used as labels, constants, and substitution symbols;
A symbol name is a string of up to 200 alphanumeric characters (A-Z, a-z, 0-9, $, and _);
The first character in a symbol cannot be a number, and symbols cannot contain embedded blanks;
The symbols you define are case sensitive;
Symbols used as labels become symbolic addresses that are associated with locations in the program;
Labels used locally within a file must be unique.

## Slide 12: Key assembly directives (7/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Local labels are special labels whose scope and effect are temporary;
A local label can be defined in two ways:
  $n, where n is a decimal digit in the range 0-9.
    For example, $4 and $1 are valid local labels;
  name?, where name is any legal symbol name as described above.
    The assembler replaces the question mark with a period followed by a unique number;
    When the source code is expanded, you will not see the unique number in the listing file.

## Slide 13: Key assembly directives (8/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Normal labels must be unique;
Local labels, however, can be undefined and redefined again;
The smallest unit of an object file is called a section;
A section is a block of code or data that occupies contiguous space in the memory map with other sections;
Each section of an object file is separate and distinct.

## Slide 14: Key assembly directives (9/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Object files usually contain three default sections:
  .text section usually contains executable code;
  .data section usually contains initialized data;
  .bss section usually reserves space for uninitialized variables.
There are two basic types of sections:
  Initialized sections;
  Uninitialized sections.

## Slide 15: Key assembly directives (10/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Types of sections:
  Initialized sections:
    Contain data or code;
    The .text and .data sections are initialized with values;
    Named sections created with the .sect assembler directive are also initialized;
  Uninitialized sections:
    Reserve space in the memory map for uninitialized data;
    The .bss section is uninitialized;
    Named sections created with the .usect assembler directive are also uninitialized.

## Slide 16: Key assembly directives (11/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A line in a listing file has four fields:
  Field 1: contains the source code line counter;
  Field 2: contains the section program counter;
  Field 3: contains the object code;
  Field 4: contains the original source statement.

## Slide 17: Key assembly directives (12/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Example: Using sections directives:

## Slide 18: Key assembly directives (13/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Example: process of linking two files together:

## Slide 19: Key assembly directives (14/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Assembler directives supply data to the program and control the assembly process;
Assembler directives enable you to do the following:
  Assemble code and data into specified sections;
  Reserve space in memory for uninitialized variables;
  Control the appearance of listings;
  Initialize memory;
  Assemble conditional blocks;
  Define global variables;
  Specify libraries from which the assembler can obtain macros;
  Examine symbolic debugging information.

## Slide 20: Key assembly directives (15/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Assembler directives:
  Directives that define sections:

## Slide 21: Key assembly directives (16/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Assembler directives (continued):
  Directives that initialize constants (Data and Memory):

## Slide 22: Key assembly directives (17/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Assembler directives (continued):
  Directives that perform alignment and reserve space:

## Slide 23: Key assembly directives (18/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Assembler directives (continued):
  Directives that format the output listing:

## Slide 24: Key assembly directives (19/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Assembler directives (continued):
  Directives that reference other files:

## Slide 25: Key assembly directives (20/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Assembler directives (continued):
  Directives that enable conditional assembly:

## Slide 26: Key assembly directives (21/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Assembler directives (continued):
  Directives that define structures:
  Directives that define symbols at assembly time:

## Slide 27: Key assembly directives (22/22)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Assembler directives (continued):
  Directives that perform miscellaneous functions:

## Slide 28: Project example: square root extraction (1/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Algorithm presentation:
  The routine to perform the calculation of a square root should provide the result in a speedy manner and without needing a starting point, as in Newton's iterative method;
  The first step in the manual method of calculating the square root of a number is to partition the number into bit pairs, starting with the least significant bit;
  Begin with the most significant pair of digits, subtract 01 and proceed as follows:
    If the result of the subtraction is positive, enter a bit with value 1 in the square root result;
    If the result of the subtraction is negative, enter a bit with value 0 in the square root result.

## Slide 29: Project example: square root extraction (2/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Algorithm presentation (continued):
  The second step consists of adding to the subtraction result the following bit pair of the number;
  The next operation is now selected as follows:
    If the entered bit value in the square root result was 1, add 01 to the square root result and subtract this value;
    If the entered bit value in the square root result was 0, add 11 to the square root result and add this value;
    Proceed until the end of the calculation.

## Slide 30: Project example: square root extraction (3/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Algorithm presentation (continued):
  Example: Calculate the square root of 01 01 11 11 00b = 380d:
  The result is equal to 10011b = 19d which is the integer part of the square root of 380d.

## Slide 31: Project example: square root extraction (4/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Algorithm presentation (continued):
  Example: If instead of using
  01 01 11 11 00b, the following fractional number had been used:
  01 01 11 11 00, 00 00 00b
  The result would be:
  The process is identical to the previous one;
  The value of the square root with n fractional elements can be calculated by adding to the binary number with 2*n fractional elements.

## Slide 32: Project example: square root extraction (5/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Code implementation and analysis:
  The algorithm described above is used to build the SQRT_FUNCTION routine;
  The project for the CCE v3.0 can be found in Chapt15 > Lab11c;
  The program body starts by loading the file msp430xG46x.h, providing the C/C++ mnemonics;
  At addressing space ".sysmem" is reserved space for the variable number (type word) (UQ16), initialized with the value 50;
  The square root extraction procedure places the result in the variable sqrt (type word) (UQ8.8);

## Slide 33: Project example: square root extraction (6/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Code implementation and analysis (continued):
  The number of cycles to determine the solution is given by the variable count (type byte) initialized with 0x15, allowing 8 fractional part bits.
;************************************************************;
;************************************************************* .cdecls C,LIST, "msp430xG46x.h" ; load C file Headers
;-------------------------------------------------------------
.sect ".sysmem" ; Data Space
;-------------------------------------------------------------
number .word 50 ; reserve space for one word
sqrt .word 0 ; reserve space for one word
count .char 0x0F ; reserve space for one byte

## Slide 34: Project example: square root extraction (7/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Code implementation and analysis (continued):
  The program code is placed in the section ".text";
  After setting the entry point BEGIN, start to write the code;
  The first task in the code is to set up the stack pointer and to stop the watchdog timer;
  Next comes loading the data necessary to execute the routine in the stack using the PUSH instruction;
  The routine is then called. Note that it uses the CALL instruction, so the routine must reside in the address space below 64 kB. Therefore, only bits 15:0 of the register PC are placed on the stack;

## Slide 35: Project example: square root extraction (8/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Code implementation and analysis (continued):
  After running the routine, adding the value 6 to register SP (corresponding to the space occupied by the routine input data), restores the stack pointer.
;-------------------------------------------------------------
.text ; Program Space
;-------------------------------------------------------------
.global BEGIN ; entry point
BEGIN:
mov.w #0A00h,SP ; initialize stack pointer
mov.w #WDTPW+WDTHOLD,&WDTCTL ; stop WDT
push.w #number ; push data in to stack
push.w #sqrt
push.w count
call #SQRT_FUNCTION ; call function
ADD #0x6,SP ; restore SP
ret ; exit

## Slide 36: Project example: square root extraction (9/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Code implementation and analysis (continued):
  At the beginning of the routine, the machine context is stored. Therefore, all the registers used by the routine are placed on the stack;
  Also reserved is space for two temporary variables: temp1 and temp2, initialized with the values 0x00 and 0x01, respectively;

## Slide 37: Project example: square root extraction (10/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Code implementation and analysis (continued):
  The following figure shows the stack organization:

## Slide 38: Project example: square root extraction (11/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Code implementation and analysis (continued):
;--------------------------------------------------------------
; Square root function
;--------------------------------------------------------------
SQRT_FUNCTION:
push.w SR ; save context
push.w R4
push.w R5
push.w R6
push.w #00 ; define temp1
push.w #01 ; define temp2
mov.w 18(SP),R4 ; R4 point to number
mov.w 16(SP),R5 ; R5 point to sqrt

## Slide 39: Project example: square root extraction (12/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Code implementation and analysis (continued):
  The square root calculation begins at the label SQRT_LOOP1 and the loop is executed 16 times;
  The process begins by removing the 2 most significant bits of the variable number pointed by R4, and placing them in the least significant part of the variable temp1.

## Slide 40: Project example: square root extraction (13/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Code implementation and analysis (continued):
SQRT_LOOP1:
mov.w @R4,R6 ; take 1º MSB from number
rla.w R6
mov.w R6,0(R4)
mov.w 2(SP),R6 ; put it in temp1
rlc.w R6
mov.w R6,2(SP)
mov.w @R4,R6 ; take 2º MSB from number
rla.w R6
mov.w R6,0(R4)
mov.w 2(SP),R6 ; put it in temp1
rlc.w R6

## Slide 41: Project example: square root extraction (14/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Code implementation and analysis (continued):
  The value of variable temp1 is then compared with zero;
  If the result is negative, then the execution continues at the label SQRT_ADD;
  Otherwise, variable temp1 is subtracted from the value of variable temp2;
  After this procedure, the execution continues at the label SQRT_S1.

## Slide 42: Project example: square root extraction (15/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Code implementation and analysis (continued):
cmp #00,R6
jn SQRT_ADD ; if temp1 < 0 go SQRT_ADD
SQRT_SUB: ; temp1 = temp1 - temp2
sub.w 0(SP),R6
jmp SQRT_S1
SQRT_ADD: ; temp1 = temp1 + temp2
add.w 0(SP),R6
mov.w R6,2(SP)

## Slide 43: Project example: square root extraction (16/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Code implementation and analysis (continued):
  At this point, depending on the result with the previous operation, a bit of value 0 or 1 is entered in the sqrt result;
  If a (1) one (SQRT_PRE_SUB) was entered in the result, the bit pair 01 is added to variable temp2;
  If a (0) zero (SQRT_PRE_ADD) was entered in the result, the bit pair 11 is added to variable temp2;
  In both cases, the number of cycles is tested;
  If this value is less than zero, the execution continues at the label SQRT_END, otherwise it restarts the procedure at the label SQRT_LOOP1.

## Slide 44: Project example: square root extraction (17/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Code implementation and analysis (continued):
SQRT_S1:
cmp #00,R6
jn SQRT_PRE_ADD

## Slide 45: Project example: square root extraction (18/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Code implementation and analysis (continued):
SQRT_PRE_SUB:
mov.w R6,2(SP) ; save temp1 on stack
mov.w @R5,R6 ; insert 1 in sqrt
setc
rlc R6
mov R6,0(R5) ; save sqrt
rla.w R6
rla.w R6
add #1,R6 ; append 01b
mov.w R6,0(SP) ; save temp2
mov 14(SP),R6 ; test count
dec R6
mov R6,14(SP)
cmp #00,R6
jge SQRT_LOOP1
jmp SQRT_END

## Slide 46: Project example: square root extraction (19/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Code implementation and analysis (continued):
SQRT_PRE_ADD:
mov.w R6,2(SP) ; save temp1 on stack
mov.w @R5,R6 ; insert 0 in sqrt
clrc
rlc R6
mov R6,0(R5) ; save sqrt
rla.w R6
rla.w R6
add #3,R6 ; append 11b
mov.w R6,0(SP) ; save temp2
mov 14(SP),R6 ; test count
dec R6
mov R6,14(SP)
cmp #00,R6
jge SQRT_LOOP1

## Slide 47: Project example: square root extraction (20/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Code implementation and analysis (continued):
  Before ending the execution of the routine, it is necessary to restore the system state;
  The data values are removed from the stack;
  The execution of the routine ends with the instruction RET.
SQRT_END:
pop R6 ; restore context
pop R6
pop R6
pop R5
pop R4
pop SR
ret ; exit

## Slide 48: Project example: square root extraction (21/21)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Testing the project:
  After the project is built and configured, it is possible to start the debugging process;
  In the memory panel, introduce the addresses of the variables number, sqrt and count;
  Make a note of the stack value then run the program and verify the result;
  It should be noted that after using this routine, the stack should be returned to its previous state;
  The square root of the value (50d) is 0x712, which is the value 7.07 in format UQ8.8.