## Slide 1: Chapter 15 Advanced Laboratories MSP430 assembly language tutorial: MSP430 CPU
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Notes: <number>

## Slide 2: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Exploring the addressing modes of the MSP430 architecture:
  Instruction format:
    Instruction format I: Double operand
    Instruction format II: Single operand
    Jump instructions format
    Emulated instructions
  Addressing modes:
    Register mode
    Indexed mode
    Symbolic mode
    Absolute mode
    Indirect register mode
    Indirect auto-increment mode
    Immediate mode

## Slide 3: Exploring the addressing modes of the MSP430 architecture (1/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The MSP430 architecture:
  The MSP430 CPU incorporates features specifically designed to allow the use of modern programming techniques, such as:
    The computation of jump addresses;
    Data processing in tables;
    The use of high-level languages such as C.
  The whole memory space can be addressed by the MSP430 CPU, without needing paging, using seven different addressing modes.
  The MSP430 CPU has a set of 27 instructions that can be used with any of the addressing modes.

## Slide 4: Exploring the addressing modes of the MSP430 architecture (2/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Organization of the MSP430 CPU:
  16-bit address bus (MAB) and 16-bit data bus (MDB).
  Both registers and memory can be accessed either in word format or in byte format.
  Allows the direct transfer of data between memory, without passing through the registers.
  The 16-bit registers can be accessed directly through the instructions, some of which run in a single clock cycle.
  Some of the constants most used in programming can be obtained from the constant generator.

## Slide 5: Exploring the addressing modes of the MSP430 architecture (3/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Organization of the MSP430 CPU (continued):
  The architecture has a 16 bit Arithmetic Logic Unit (ALU).
  Carrying out operations affects the state of the following flags:
    Zero (Z);
    Carry (C);
    Overflow (V);
    Negative (N).
  The MCLK (Master) clock signal drives the CPU.

## Slide 6: Exploring the addressing modes of the MSP430 architecture (4/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The MSP430 CPU has 16 registers, some of which are dedicated to special use:
R0 (PC) (Program Counter):
  This register always points to the next instruction to be fetched;
  Each instruction occupies an even number of bytes. Therefore, the least significant bit (LSB) of the PC register is always zero;
  After fetch of an instruction, the PC register is incremented to point to the next instruction.

## Slide 7: Exploring the addressing modes of the MSP430 architecture (5/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R1 (SP) Stack Pointer:
  This register is used by the MSP430 CPU to store the return address of routines or interrupts;
  Each time the data stack is accessed, the SP is incremented or decremented automatically;
  The user should be careful to initialise the SP register with the valid address of the data stack in RAM;
  The stack pointer SP always points to an even address, so its LSB is always zero.

## Slide 8: Exploring the addressing modes of the MSP430 architecture (6/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R2 – SR/CG1 & R3 – CG2 (Status Register):
  The status of the MSP430 CPU is defined by a set of bits contained in register R2 (SR) (status register);
  This register can only be accessed through register addressing mode;
  All other addressing modes are reserved to support the constants generator;
  The organization of the individual bits of register R2 is shown in the following figure:

## Slide 9: Exploring the addressing modes of the MSP430 architecture (7/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R2 – SR/CG1 & R3 – CG2 (Status Register):
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Reserved for CG1 |  |  |  |  |  |  | V | SCG1 | SCG0 | OSCOFF | CPUOFF | GIE | N | Z | C
Bit |  | Description
8 | V | Overflow bit. V = 1  Result of an arithmetic operation overflows the signed-variable range.
7 | SCG1 | System clock generator 1. SCG1 = 1  DCO generator is turned off – if not used for MCLK or SMCLK
6 | SCG0 | System clock generator 0. SCG0 = 1  FLL+ loop control is turned off
5 | OSCOFF | Oscillator Off. OSCOFF = 1  turns off LFXT1 when it is not used for MCLK or SMCLK
4 | CPUOFF | CPU off. CPUOFF = 1  disable CPU core.
3 | GIE | General Interrupt Enable. GIE = 1  enables maskable interrupts.
2 | N | Negative flag. N = 1  result of a byte or word operation is negative.
1 | Z | Zero flag. Z = 1  result of a byte or word operation is 0.
0 | C | Carry flag. C = 1  result of a byte or word operation produced a carry.

## Slide 10: Exploring the addressing modes of the MSP430 architecture (8/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R2 – SR/CG1 & R3 – CG2 (Constant Generators):
  Six different constants commonly used in programming can be generated using the registers R2 and R3, without the need to add a 16-bit word of code to the instruction;
  The constants are fixed and are selected by the instruction bits (As). These control the addressing mode.
Register | As | Constant | Remarks
R2 | 00 | - | Register mode
R2 | 01 | (0) | Absolute mode
R2 | 10 | 00004h | +4, bit processing
R2 | 11 | 00008h | +8, bit processing
R3 | 00 | 00000h | 0, word processing
R3 | 01 | 00001h | +1
R3 | 10 | 00002h | +2, bit processing
R3 | 11 | 0FFFFh | -1, word processing

## Slide 11: Exploring the addressing modes of the MSP430 architecture (9/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R4-R15: General-purpose registers:
  The general purpose registers R4 to R15 can be used as data registers, data pointers and indices. They can be accessed either as a byte or as a word;
  These registers support operations on words or bytes;
  In the example to the right, the contents of the least significant byte of register R5 (0x8F) is added to the contents of the memory address pointed to by the register R6 (0x12h);

## Slide 12: Exploring the addressing modes of the MSP430 architecture (10/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R4-R15: General-purpose registers:
  The contents of the memory address is updated with the result of the operation (0xA1);
  The status flags of the CPU in the SR are updated after the execution of the instruction.

## Slide 13: Exploring the addressing modes of the MSP430 architecture (11/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R4-R15: General-purpose registers:
  The contents of the memory address pointed to by R6 (0x5F) is added to the contents of the least significant byte of register R5 (0x02);
  The result of the operation (0x61) is stored in the least significant byte of register R5;
  Meanwhile, the most significant byte of register R5 is set to zero;
  The system flags in SR are updated in accordance with the result.

## Slide 14: Instructions format (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
In addition to the 27 instructions of the CPU there are 24 emulated instructions;
The CPU coding is unique;
The emulated instructions make reading and writing code more easy, but do not have their own op-codes;
Emulated instructions are replaced automatically by instructions from the CPU;
There are no penalties for using emulated instructions.
There are three formats used to encode instructions for processing by the CPU core:
  Double operand;
  Single operand;
  Jumps.

## Slide 15: Instructions format (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The instructions for double and single operands, depend on the suffix used, (.W) word or (.B) byte.
These suffixes allow word or byte data access;
If the suffix is ignored, the instruction processes word data by default.

## Slide 16: Instructions format (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The source and destination of the data operated by an instruction are defined by the following fields:
  src: source operand address, as defined in As and S-reg;
  dst: destination operand address, as defined in Ad and D-reg;
  As: addressing bits used to define the addressing mode used by the source operand;
  S-reg: register used by the source operand;
  Ad: Addressing bits used to define the addressing mode used by the destination operand;
  D-reg: register used by the destination operand;
  B/W: word or byte access definition bit.

## Slide 17: Instructions format (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
While all addresses within the address space are valid, it is the responsibility of the user to check that the type of access is valid.
Example: the contents of the flash memory can be used as a source operand, but can only be written to in certain conditions.

## Slide 18: Instruction format I: Double operand
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Organization of instructions with two operands:
Double operand instructions:
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Op-code |  |  |  | S-Reg |  |  |  | Ad | B/W | As |  | D-Reg |  |  | 
Mnemonic | Operation | Description
Arithmetic instructions |  | 
ADD(.B or .W) src,dst | src+dstdst | Add source to destination
ADDC(.B or .W) src,dst | src+dst+Cdst | Add source and carry to destination
DADD(.B or .W) src,dst | src+dst+Cdst (dec) | Decimal add source and carry to destination
SUB(.B or .W) src,dst | dst+.not.src+1dst | Subtract source from destination
SUBC(.B or .W) src,dst | dst+.not.src+Cdst | Subtract source and not carry from destination
Logical and register control instructions |  | 
AND(.B or .W) src,dst | src.and.dstdst | AND source with destination
BIC(.B or .W) src,dst | .not.src.and.dstdst | Clear bits in destination
BIS(.B or .W) src,dst | src.or.dstdst | Set bits in destination
BIT(.B or .W) src,dst | src.and.dst | Test bits in destination
XOR(.B or .W) src,dst | src.xor.dstdst | XOR source with destination
Data instructions |  | 
CMP(.B or .W) src,dst | dst-src | Compare source to destination
MOV(.B or .W) src,dst | srcdst | Move source to destination

## Slide 19: Examples: double operand (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of register R5 to register R4:
  MOV R5,R4
  Instruction code: 0x4504
  This instruction uses 1 word;
  The instruction coding specifies that the CPU must perform a 16-bit data MOV instruction, with the contents of register R5 as the source and with register R4 as the destination.
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 1 0 1 | 0 | 0 | 0 0 | 0 1 0 0
MOV | R5 | Register | 16-Bits | Register | R4

## Slide 20: Examples: double operand (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of register R5 to the address in memory TONI:
MOV R5,TONI
  Instruction code: 0x4580
  This instruction uses 2 words;
  The instruction coding specifies that the CPU must perform a 16-bit data MOV instruction using the contents of register R5 to the memory address pointed to by X1 + PC;
  The word X1 is stored in the word following the instruction.
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 1 0 1 | 1 | 0 | 0 0 | 0 0 0 0
MOV | R5 | Symbolic | 16 Bits | Register | PC

## Slide 21: Examples: double operand (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents between the memory addresses EDEN and TONI:
MOV EDEN,TONI
  Instruction code: 0x4090
  This instruction uses 3 words;
  The instruction coding specifies that the CPU must perform a 16-bit data MOV instruction using the contents of the EDEN memory address pointed to by X1 + PC to the TONI memory address pointed to by X2 + PC;
  The word X1 followed by the word X2 are stored after the instruction.
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 0 0 0 | 1 | 0 | 0 1 | 0 0 0 0
MOV | PC | Symbolic | 16-Bits | Symbolic | PC

## Slide 22: Instruction format II: Single operand
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The instructions with one operand are coded using the following structure:
Single operand instructions:
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Op-code |  |  |  |  |  |  |  |  | B/W | Ad |  | D/S-Reg |  |  | 
Mnemonic | Operation | Description
Logical and register control instructions |  | 
RRA(.B or .W) dst | MSBMSB…LSBC | Roll destination right
RRC(.B or .W) dst | CMSB…LSBC | Roll destination right through (from) carry
SWPB( or .W) dst | Swap bytes | Swap bytes in destination
SXT dst | bit 7bit 8…bit 15 | Sign extend destination
PUSH(.B or .W) src | SP-2SP, src@SP | Push source on stack
Program flow control instructions |  | 
CALL(.B or .W) dst | SP-2SP, PC+2@SP dstPC | Subroutine call to destination
RETI | TOSSR, SP+2SP TOSPC, SP+2SP | Return from interrupt

## Slide 23: Examples: single operand (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of register R5 to the right with carry flag:
RRC R5
  Instruction code: 0x1005
  This instruction uses 1 word;
  The instruction coding specifies that the CPU must perform a 16-bit data RRC instruction using the contents of register R5.
Op-code | B/W | Ad | D-reg
0 0 0 1 0 0 0 0 0 | 0 | 0 0 | 0 1 0 1
RRC | 16 bits | Register | R5

## Slide 24: Examples: single operand (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Rotate the contents of memory TONI to the right with carry flag:
RRC TONI
  Instruction code: 0x1010
  This instruction uses 2 words;
  The instruction coding specifies that the CPU must perform a 16-bit data RRC instruction pointed to by X1 + PC;
  Word X1 is stored in the word following the instruction.
Op-code | B/W | Ad | D-reg
0 0 0 1 0 0 0 0 0 | 0 | 0 1 | 0 0 0 0
RRC | 16 bits | Symbolic | PC

## Slide 25: Jump instructions format (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
These instructions are used to direct program flow to another part of the program.
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Op-code |  |  | C |  |  | 10 bit PC offset |  |  |  |  |  |  |  |  | 
Mnemonic | Description
Program flow control instructions | 
JEQ/JZ label | Jump to label if zero flag is set
JNE/JNZ label | Jump to label if zero flag is reset
JC label | Jump to label if carry flag is set
JNC label | Jump to label if carry flag is reset
JN label | Jump to label if negative flag is set
JGE label | Jump to label if greater than or equal
JL label | Jump to label if less than
JMP label | Jump to label unconditionally

## Slide 26: Jump instructions format (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The op-code always takes the value 001b, indicating that it is a jump instruction;
The condition on which a jump occurs depends on the C field consisting of 3 bits, and may take the following values:
  000b: jump if not equal;
  001b: jump if equal;
  010b: jump if carry flag equal to zero;
  011b: jump if carry flag equal to one;
  100b: jump if negative (N = 1);
  101b: jump if greater than or equal (N=V or (N OR V=0));
  110b: jump if lower (N! = V or (V XOR N = 1));
  111b: unconditional jump.

## Slide 27: Jump instructions format (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The jumps are executed based on the PC contents, are controlled by the status bits, but do not affect the status bits;
The jump off-set is represented by a signed 10-bit value:
The range of the jump can be between -511 to +512 words, in relation to the PC position.

## Slide 28: Examples: jump format (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Continue execution at the label main if the carry flag is active:
JC main
  Instruction code: 0x2FE4
  This instruction uses 1 word;
  The instruction coding specifies that the PC must be loaded with the value resulting from the offset - 0x1C being applied to the previous expression.
Op-code | C | 10-Bit PC offset
0 0 1 | 0 1 1 | 1 1 1 1 1 0 0 1 0 0
JC | Carry = 1 | – 0x1C

## Slide 29: Examples: jump format (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Continue to unconditionally execute code at the label main:
JMP main
  Instruction code: 0x3FE3
  This instruction uses 1 word;
  The instruction coding specifies that the PC must be loaded with the value resulting from the offset - 0x1D being applied to the previous expression.
Op-code | C | 10-Bit PC offset
0 0 1 | 1 1 1 | 1 1 1 1 1 0 0 0 1 1
JMP | unconditional | – 0x1D

## Slide 30: Emulated instructions (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
In addition to the 27 CPU instructions, the following 24 emulated instructions can also be used:
Mnemonic | Operation | Emulation |  | Description
Arithmetic instructions |  |  |  | 
ADC(.B or .W) dst | dst+Cdst | ADDC(.B or .W) #0,dst | Add carry to destination | 
DADC(.B or .W) dst | dst+Cdst (decimally) | DADD(.B or .W) #0,dst | Decimal add carry to destination | 
DEC(.B or .W) dst | dst-1dst | SUB(.B or .W) #1,dst | Decrement destination | 
DECD(.B or .W) dst | dst-2dst | SUB(.B or .W) #2,dst | Decrement destination twice | 
INC(.B or .W) dst | dst+1dst | ADD(.B or .W) #1,dst | Increment destination | 
INCD(.B or .W) dst | dst+2dst | ADD(.B or .W) #2,dst | Increment destination twice | 
SBC(.B or .W) dst | dst+0FFFFh+Cdst dst+0FFhdst | SUBC(.B or .W) #0,dst | Subtract source and borrow /.NOT. carry from dest. | 

## Slide 31: Emulated instructions (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
In addition to the 27 CPU instructions, the following 24 emulated instructions can also be used (continued):
Mnemonic | Operation | Emulation |  | Description
Logical and register control instructions |  |  |  | 
INV(.B or .W) dst | .NOT.dstdst | XOR(.B or .W) #0(FF)FFh,dst | Invert bits in destination | 
RLA(.B or .W) dst | CMSBMSB-1…LSB+1LSB0 | ADD(.B or .W) dst,dst | Rotate left arithmetically | 
RLC(.B or .W) dst | CMSBMSB-1…LSB+1LSBC | ADDC(.B or .W) dst,dst | Rotate left through carry | 
Program flow control |  |  | 
BR dst | dstPC | MOV dst,PC | Branch to destination
DINT | 0GIE | BIC #8,SR | Disable (general) interrupts
EINT | 1GIE | BIS #8,SR | Enable (general) interrupts
NOP | None | MOV #0,R3 | No operation
RET | @SPPC SP+2SP | MOV @SP+,PC | Return from subroutine

## Slide 32: Emulated instructions (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
In addition to the 27 CPU instructions, the following 24 emulated instructions can also be used (continued):
Mnemonic | Operation | Emulation |  | Description
Data instructions |  |  |  | 
CLR(.B or .W) dst | 0dst | MOV(.B or .W) #0,dst | Clear destination | 
CLRC | 0C | BIC #1,SR | Clear carry flag | 
CLRN | 0N | BIC #4,SR | Clear negative flag | 
CLRZ | 0Z | BIC #2,SR | Clear zero flag | 
POP(.B or .W) dst | @SPtemp SP+2SP tempdst | MOV(.B or .W) @SP+,dst | Pop byte/word from stack to destination | 
SETC | 1C | BIS #1,SR | Set carry flag | 
SETN | 1N | BIS #4,SR | Set negative flag | 
SETZ | 1Z | BIS #2,SR | Set zero flag | 
TST(.B or .W) dst | dst + 0FFFFh + 1 dst + 0FFh + 1 | CMP(.B or .W) #0,dst | Test destination | 

## Slide 33: Examples: Emulated instructions (1/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Clear the contents of register R5:
CLR R5
  Instruction code: 0x4305
  This instruction is equivalent to using MOV R3, R5 where R3 takes the value #0.
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 0 1 1 | 0 | 0 | 0 0 | 0 1 0 1
MOV | R3 | Register | 16 Bits | Register | R5

## Slide 34: Examples: Emulated instructions (2/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Increment the content of register R5:
INC R5
  Instruction code: 0x5315
  This instruction is equivalent to having ADD 0(R3),R5 where R3 takes the value #1.
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 1 | 0 0 1 1 | 0 | 0 | 0 1 | 0 1 0 1
ADD | R3 | Register | 16 Bits | Indexed | R5

## Slide 35: Examples: Emulated instructions (3/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Decrement the contents of register R5:
DEC R5
  Instruction code: 0x8315
  This instruction is equivalent to using SUB 0(R3),R5 where R3 takes the value #1.
Op-code | S-reg | Ad | B/W | As | D-reg
1 0 0 0 | 0 0 1 1 | 0 | 0 | 0 1 | 0 1 0 1
SUB | R3 | Register | 16 Bits | Indexed | R5

## Slide 36: Examples: Emulated instructions (4/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Decrement by two the contents of register R5:
DECD R5
  Instruction code: 0x8325
  This instruction is equivalent to using SUB @R3,R5 where R3 points to the value #2.
Op-code | S-reg | Ad | B/W | As | D-reg
1 0 0 0 | 0 0 1 1 | 0 | 0 | 1 0 | 0 1 0 1
SUB | R3 | Register | 16 Bits | Indirect | R5

## Slide 37: Examples: Emulated instructions (5/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Do not carry out any operation:
NOP
  Instruction code: 0x4303
  This instruction is equivalent to using MOV R3,R3 and therefore the contents of R3 are moved to itself.
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 0 1 1 | 0 | 0 | 0 0 | 0 0 1 1
MOV | R3 | Register | 16 Bits | Register | R5

## Slide 38: Examples: Emulated instructions (6/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Add the carry flag to the register R5:
ADC R5
  Instruction code: 0x6305
  This instruction is equivalent to using ADDC R3,R5 where R3 takes the value #0.
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 1 0 | 0 0 1 1 | 0 | 0 | 0 0 | 0 1 0 1
ADDC | R3 | Register | 16 Bits | Register | R5

## Slide 39: Addressing modes (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
There are seven addressing modes that take a source operand and four of these addressing modes also take a destination operand;
The operands can be located in any memory space address, but the user needs to be aware of the effects that their accesses may have;
The addressing modes are selected by the As and Ad fields that make up the instruction;
The following table summarizes the seven addressing modes:

## Slide 40: Addressing modes (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Operands (single-operand instructions) Source operands (double-operand instructions) |  |  | Destination operands (double-operand instructions) |  | 
Addressing mode | As | S-reg | Addressing mode | Ad | D-reg
Register mode | 0 0 | 0 0 0 0 to 1 1 1 1 | Register mode | 0 | 0 0 0 0 to 1 1 1 1
Indexed mode | 0 1 | 0 0 0 1, 0 0 1 1 to 1 1 1 1 | Indexed mode | 1 | 0 0 0 1, 0 0 1 1 to 1 1 1 1
Symbolic mode | 0 1 | 0 0 0 0 | Symbolic mode | 1 | 0 0 0 0
Absolute mode | 0 1 | 0 0 1 0 | Absolute mode | 1 | 0 0 1 0
Indirect register mode | 1 0 | 0 0 0 0 to 1 1 1 1 |  |  | 
Indirect auto increment mode | 1 1 | 0 0 0 1 to 1 1 1 1 |  |  | 
Immediate mode | 1 1 | 0 0 0 0 |  |  | 

## Slide 41: Register mode (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
In Register addressing mode, the contents of a register is used as the operand;
This type of addressing mode can be used both with source and destination operands.
Move the contents of register R5 to register R4:
MOV R5,R4
  Instruction code: 0x4504
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 1 0 1 | 0 | 0 | 0 0 | 0 1 0 0
MOV | R5 | Register | 16-bit | Register | R4

## Slide 42: Register mode (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of register R5 to register R4
MOV R5,R4
  Instruction code: 0x4504
  The 16-bit contents (B/W = 0) of register R5 (S-reg) are transferred to the register R4 (D-reg);
  After the instruction fetch, the PC is incremented by 2 and points to the next instruction to be executed;
  The addressing mode used for the source and destination operands is determined by As = 00 (Register mode) and Ad = 0 (Register mode), respectively.
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 1 0 1 | 0 | 0 | 0 0 | 0 1 0 0
MOV | R5 | Register | 16-bit | Register | R4

## Slide 43: Register mode (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the contents of register R5 to register R4 (cont.): MOV R5,R4
  Instruction code: 0x4504
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 1 0 1 | 0 | 0 | 0 0 | 0 1 0 0
MOV | R5 | Register | 16-bit | Register | R4

## Slide 44: Indexed mode (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
In indexed mode, whether used to indicate the source address or the destination address, the sum of the register contents and the signed offset point to the location in memory;
The offset value is stored in the word following the instruction;
After the execution of the instruction, the contents of registers are not affected and the PC is incremented to point to the next instruction to be executed;
This addressing mode is useful to access data stored in tables. Apart from the registers PC and SR, all other registers can be used as an index in indexed mode.

## Slide 45: Indexed mode (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the byte pointed to by (R5 + 4) to the byte pointed to by (R4 + 1):
MOV.B 4(R5),1(R4)
  Instruction code: 0x45D4
  The instruction coding specifies that the byte (B/W = 1) pointed to by the sum of the contents of register R5 (S-reg = 0101) and the word X1 should be moved to the memory address pointed to by the sum of register R4 (D-reg = 0100) and the contents of the word X2;
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 1 0 1 | 1 | 1 | 0 1 | 0 1 0 0
MOV | R5 | Indexed | 8-bit | Indexed | R4

## Slide 46: Indexed mode (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the byte pointed to by (R5 + 4) to the byte pointed to by (R4 + 1) (continued):
MOV.B 4(R5),1(R4)
  Instruction code: 0x45D4
  The words X1 and X2 are located in the memory addresses following the instruction;
  The addressing mode used for the source and destination operands is controlled by the bits Ad = 1 (Indexed mode) and As = 01 (Indexed mode), because (D-reg = 0100) and (S-reg = 0101) respectively.
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 1 0 1 | 1 | 1 | 0 1 | 0 1 0 0
MOV | R5 | Indexed | 8-bit | Indexed | R4

## Slide 47: Indexed mode (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the byte pointed to by (R5 + 4) to the byte pointed to by (R4 + 1) (continued):
MOV.B 4(R5),1(R4)

## Slide 48: Symbolic mode (1/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
In symbolic addressing mode, for either the source or destination operands, the memory address is determined by adding an offset to the program counter (PC) register;
The offset value is obtained by determining the code position in the memory, then calculating the difference between the offset address and the memory position that should be achieved;
The assembler determines the offset value and puts it in the word following to the instruction;
After the execution of the instruction, the program counter (PC) register is incremented in order to point to the next instruction.

## Slide 49: Symbolic mode (2/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Although this mode of address is similar to register mode it request more cycles, but in this case, the program counter (PC) is used to point to the data;
This addressing mode can be used to determine either the source or the destination of the data.

## Slide 50: Symbolic mode (3/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by EDEN to the word pointed to by TONI:
MOV EDEN,TONI
  Instruction code: 0x4090
  The instruction coding specifies that the value pointed to by the sum of the PC register contents (S-reg = 0) and the word X1 should be moved to the memory address pointed to by the sum of register PC contents (D-reg = 0) and the word X2;
  The words X1 and X2 are stored in the memory addresses following the instruction.
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 0 0 0 | 1 | 0 | 0 1 | 0 0 0 0
MOV | PC | Symbolic | 16-bit | Symbolic | PC

## Slide 51: Symbolic mode (4/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by EDEN to the word pointed to by TONI (continued):
MOV EDEN,TONI
  Instruction code: 0x4090
  The addressing mode used for the source and destination operands is controlled by the bits Ad = 1 (Symbolic mode) and As = 01 (Symbolic mode) because (D-reg = 0000) and (S-reg = 0000), respectively.
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 0 0 0 | 1 | 0 | 0 1 | 0 0 0 0
MOV | PC | Symbolic | 16-bit | Symbolic | PC

## Slide 52: Symbolic mode (5/5)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by EDEN to the word pointed to by TONI:
MOV EDEN,TONI

## Slide 53: Absolute mode (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
In Absolute mode, the data memory address is placed after the instruction;
The difference between this addressing mode and Indexed mode is that the register R2 is now used as an index, using the constants generator to generate the value zero;
This addressing mode can be used to define either the source address or the destination address.

## Slide 54: Absolute mode (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by EDEN to the word pointed to by TONI:
MOV &EDEN,&TONI
  Instruction code: 0x4292
  From the instruction coding it can be seen that the register R2 has (S-reg = 0010) and (D-reg = 0010). Register R2 is used as an addresses index, in which the constant generator loads the value zero;
  When the contents of this register is added to the offset value X1 or X2, the source and destination addresses are obtained;
  The words X1 and X2 are stored in the memory addresses following the instruction.
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 0 1 0 | 1 | 0 | 0 1 | 0 0 1 0
MOV | R2/CG1 | Absolute | 16-bit | Absolute | R2/CG1

## Slide 55: Absolute mode (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by EDEN to the word pointed to by TONI (continued):
MOV &EDEN,&TONI
  Instruction code: 0x4292
  The addressing mode used for the source and destination operands is specified by the bits Ad = 1 (Absolute mode) and As = 01 (Absolute mode) because (D-reg = 0010) and (S-reg = 0010), respectively.
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 0 1 0 | 1 | 0 | 0 1 | 0 0 1 0
MOV | R2/CG1 | Absolute | 16-bit | Absolute | R2/CG1

## Slide 56: Absolute mode (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by EDEN to the word pointed to by TONI (continued):
MOV &EDEN,&TONI

## Slide 57: Indirect register mode (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
In Indirect register mode, any of the 16 CPU registers can be used. If R2 or R3 are used then a constant value is used as an operand, #0x04 for R2 and #0x2 for R3;
A restriction arises from the fact that this addressing mode can only be used to specify the source operand address in dual-operand instructions;
An alternative way to avoid this restriction is to use indexed mode to specify the destination operand address, with a zero offset.

## Slide 58: Indirect register mode (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by R5 to the word pointed to by R4:
MOV @R5,0(R4)
  Instruction code: 0x45A4
  The instruction coding specifies that register R5 (S-reg = 0101) uses the source address (As = 10);
  The destination address is pointed to in Indexed mode (Ad = 1) by R4 (D-reg = 0100), using a zero value offset.
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 1 0 1 | 1 | 0 | 1 0 | 0 1 0 0
MOV | R5 | Indexed | 16-bit | Indirect | R4

## Slide 59: Indirect register mode (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by R5 to the word pointed to by R4 (continued):
MOV @R5,0(R4)

## Slide 60: Indirect auto-increment mode (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
This addressing mode is similar to the previous one;
The contents of source register is incremented according to the data type processed;
If the data value is byte, the source register is incremented by 1;
If the data value is a word, the source register is incremented by 2;
Note that this addressing mode can only be used to specify the source operand in dual-operand instructions.

## Slide 61: Indirect auto-increment mode (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by R5 to the word pointed to by R4, and increment the source pointer:
MOV @R5+,0(R4)
  Instruction code: 0x45B4
  The instruction coding specifies that the register R5 (S-reg = 0101) contains the source address (As = 11);
  The destination address is pointed to in indexed mode by R4 (D-reg = 0100), using a zero value offset;
  The execution of the instruction increments the contents of register R5 by 2.
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 1 0 1 | 1 | 0 | 1 1 | 0 1 0 0
MOV | R5 | Indexed | 16-bit | Ind. aut. inc. | R4

## Slide 62: Indirect auto-increment mode (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the word pointed to by R5 to the word pointed to by R4, and increment the source pointer (continued):
MOV @R5+,0(R4)

## Slide 63: Immediate mode (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The Immediate addressing mode allows values to be loaded directly into registers or memory addresses. It can only be used with source operands.
Move the value 0x0200 to R5:
MOV #0x0200,R5
  Instruction code: 0x4035
  The instruction coding specifies that the register PC (S-reg = 0000) is used to define the address of the word in memory that loads the register R5 (D-reg = 0101) with (Ad = 11).
Op-code | S-reg | Ad | B/W | As | D-reg
0 1 0 0 | 0 0 0 0 | 0 | 0 | 1 1 | 0 1 0 1
MOV | PC | Register | 16-bit | Immediate | R5

## Slide 64: Immediate mode (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Move the value 0x0200 to R5 (continued):
MOV 0x0200,R5