## Slide 1: Chapter 2 Software Development tools Code Composer Essentials v3: Code Debugging
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
MSP430 Teaching Materials
<footer> Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt

## Slide 2: Contents
Code Composer v3: Code debugging:
  Debugging steps
  EEM - Enhanced Emulation Module
  Breakpoints types
  Predefined breakpoint set
  Variables view
  Expressions view
  Memory view
  Expanding CCE capabilities with Eclipse JDT and PDE
<footer>>> Contents

## Slide 3: Introduction to CCE (1/25) Code debugging
TI’s debugger generates an output file as a result of building the project;
Debugging steps:
  Select an active project, or click Run > Debug Active Project or select the icon ;
  It resets and suspends the execution of code on the device;
  The contents of all status registers are modified to their power-up state defaults, in accordance with the device specifications;
  The reset command is enabled by > Reset CPU;

## Slide 4: Introduction to CCE (2/25) Code debugging
Debugging steps (continued):
  To start program execution, once it has been loaded into the device memory, select the option Run > Run (F8), or click on the button ;
  Execution will take place until the program finds a breakpoint;
  Program execution may be suspended at any time by using the command Run > Halt, or by clicking the button ;
  To re-start the execution of the application, use the command Run > Restart, or click :
    Does not modify the execution state of the device;
    Restores the PC to the starting point of the application .

## Slide 5: Introduction to CCE (3/25) Code debugging
Debugging steps (continued):
  The Set PC to Cursor feature moves the execution of the application to a particular point in the program memory;
  The execution of this command only modifies the contents of the PC register;
  No instructions will be executed in order to reach this particular point in program memory.

## Slide 6: Introduction to CCE (4/25) Code debugging
Debugging steps (continued):
  There are several ways to run the code until a specific point in the code:
    Use a breakpoint to stop the program execution when the specific point in code has been reached;
    Use the command Run > Run to Line, to run the code until the specified location;
    A special case is to run the code until the main function is reached :
      Set a temporary breakpoint at the start of main;
      Start the execution of the application;
      Once the temporary breakpoint is reached, the breakpoint is removed and execution suspended.

## Slide 7: Introduction to CCE (5/25) Code debugging
Debugging steps (continued):
  The stepping commands execute each instruction one at a time;
  When a function is reached, the code execution can continue:
    Into the function (Step Into);
    Perform the function and pass to the following instruction (Step Over);
    Once inside a function, the user can continue to execute each instruction individually, or run the rest of the function code until it ends (Step Out);

## Slide 8: Introduction to CCE (6/25) Code debugging
Debugging steps (continued):
  The next instruction execution is performed through Run > Step Into (F5), or by clicking the icon ;
  The next instruction is processed when this command is executed;
  If the following statement is a function call, the debugger passes the execution to the first instruction of the function, and suspends execution at that point;
  When the execution point is at the start of a function call, the step over operation can be used by selecting the Run > Step Over (F6) or by clicking the icon .

## Slide 9: Introduction to CCE (7/25) Code debugging
Debugging steps (continued):
  The debugger performs the function and suspends the execution when it returns;
  A breakpoint in a function suspends the execution;
  If the Step Over is used on an instruction that is not a function call, it will work as a Step Into command;
  It is possible to force the return of a function through the command Run > Step Return (F7), or by clicking the button ;
  The debugger will execute the rest of the function code and return the call point to suspend the execution;
  The command Terminate allows the debugging session to finish immediately.

## Slide 10: Introduction to CCE (8/25) Code debugging
EEM - Enhanced Emulation Module:
  Non-intrusive monitoring of the operation of the device ;
  Does not use processor resources;
  Facilitates the development of the application through the verification of the operation.

## Slide 11: Introduction to CCE (9/25) Code debugging
EEM - Enhanced Emulation Module:
  Features:
    Supports up to 8 hardware breakpoints;
    Operates at all frequencies and with all clock sources;
    Ability to set complex breakpoints (associate triggers);
    Suspend the execution of the application (program or data bus access);
    Access protection (data and program memory areas);
    All timers and counters can be inhibited (depending on the device);
    Inhibits generation of PWM signals when the application suspends;
    Allows real-time execution of the application in the following modes: single step, step into, run to cursor, step over;
    Supports all low power modes.

## Slide 12: Introduction to CCE (10/25) Code debugging
Events inside the device generate triggers;
These triggers can be classified as events that cause:
    Access to addressing and data busses;
    Access to CPU registers.
Depending on the device, it is possible to associate two or more of these triggers. This allows complex event detectors to be built that help locate the point of incorrect operation of the application;
Generally, a trigger can be used to control the following functional blocks of the EEM: breakpoints, trace and sequencer;
The activation of a trigger is conditional on access to the data and program busses or access to CPU registers.

## Slide 13: Introduction to CCE (11/25) Code debugging
Breakpoints types:
  Software breakpoint: implemented through the insertion of code in the application, in a way transparent to the user.
  Hardware breakpoint: implemented internally by the device hardware.
While the software breakpoints are not limited, the hardware breakpoints depend on the device and have a limit of 2 to 4 breakpoints;
An active breakpoint is identified by the symbol in the sidebar of the code window;
The symbol will identify a hardware breakpoint;
A disabled breakpoint will be identified by the symbol .

## Slide 14: Introduction to CCE (12/25) Code debugging
A breakpoint is set through one or more triggers;
Through these triggers it is possible to set up the following types of breakpoints:
    Address (simple) breakpoint;
    Data breakpoint;
    Register Breakpoint;
    Mask Register;
    Range breakpoint.
Address (simple) breakpoint:
  Defined using a trigger associated with an instruction read operation by the CPU;
  Specifies the instruction address where the trigger should occur.

## Slide 15: Introduction to CCE (13/25) Code debugging
Data Breakpoint:
  One of the triggers is used to detect the occurrence of a particular address in the address bus;
  The other is used to detect the occurrence of a read or write operation at that address;
  It is possible to force the suspension of the execution of the application when there is a match between the value written or read and the one specified.
Register Breakpoint:
  Uses a trigger to detect the access to a register.
Mask Register:
  Used when the register is composed of several fields, since it can apply a mask to only use specific bits.

## Slide 16: Introduction to CCE (14/25) Code debugging
Range breakpoint:
  Suspends the execution of the application on the occurrence of a:
    Write to flash;
    Invalid access to memory;
    Access to an instruction in invalid program space;
    Access to data on invalid space data.
Hardware breakpoints properties:
  Are established through different fields;
  The action to perform when all triggers are true can be defined in the Action option of the Hardware Configuration field:
    Halt;
    Trigger storage;
    Halt and trigger storage.

## Slide 17: Introduction to CCE (15/25) Code debugging
Hardware breakpoints properties (continued):
  In the Trigger field, specify through the available options, the check condition for a trigger true. The trigger can be:
    Memory Address bus:
      Location: Address of the program code line (e.g.: aes.c, line 30) or data memory address (e.g.: &a);
      Mask: the information introduced in this field is used in a logic AND operation with the content;
      Operator: Logic operation with the data (==, <=, >=, !=);
      Access: Memory access type.

## Slide 18: Introduction to CCE (16/25) Code debugging
Hardware breakpoints properties (continued):
  In the Trigger field, specify through various options, the check condition for a true trigger. The trigger can be:
    Memory Data bus:
      Value: A mask will be applied to the data on the data bus and to value added by the value and compared, to determine if the trigger is true;
      Mask: the information introduced in this field is used in a logic AND operation with the content;
      Operator: Logic operation with the data (==, <=, >=, !=);
      Access: Memory access type (like in Memory Address Bus).

## Slide 19: Introduction to CCE (17/25) Code debugging
Hardware breakpoints properties (continued):
  In the Trigger field, specify through various options, the check condition for a true trigger. The trigger can be:
    Miscellaneous:
      Group: Group to which the breakpoint belongs;
      Name: Name assigned to the breakpoint.

## Slide 20: Introduction to CCE (18/25) Code debugging
Predefined breakpoint set:
  Break in program range:
    Suspends execution of the application in a range of program memory addresses;
    Uses two triggers that define the range of addresses.
  Break in DMA transfer:
    Suspends the execution of the application, whenever a DMA read or write operation at the specified programme address occurs;
    Implemented using only one trigger.
  Break in DMA transfer range:
    Suspends execution of the application, whenever a DMA read or write operation at the specified address range occurs;
    Implemented using two triggers.

## Slide 21: Introduction to CCE (19/25) Code debugging
Predefined breakpoint set:
  Break in stack overflow:
    Suspends execution of application, whenever the stack pointer (SP) register value assumes a lower value than the one specified;
    Uses only one trigger.
  Breakpoint:
    Suspends execution of application, whenever the memory bus address takes the specified value;
    Implemented using only one trigger.
  Hardware breakpoint:
    Suspends execution of the application, whenever the memory bus address takes the specified value;
    Uses only one trigger.

## Slide 22: Introduction to CCE (20/25) Code debugging
Predefined breakpoint set:
  Watch on data address range:
    Suspends execution of the application, whenever the specified data memory addresses range is accessed;
    Uses two triggers to define the range of addresses.
  Watchpoint:
    Suspends execution of the application, whenever a specified data memory address is accessed;
    Uses a trigger to generate the watchpoint.
  Watchpoint with data:
    Suspends execution of the application, whenever a specified data memory address is accessed and the value of the address is equal to specified value;
    Two triggers are used to implement this watchpoint.

## Slide 23: Introduction to CCE (21/25) Code debugging
Procedure:
  Place the cursor at a particular line of code and then use the command to activate a breakpoint;
  The command enables or disables a breakpoint at the cursor location;
  An alternative method is to use the context menu with the option toggle breakpoint;
  The application debugging process often requires access to the current values of the variables.

## Slide 24: Introduction to CCE (22/25) Code debugging
Variables view:
  Monitors the local and global variables of the application ;
  In this view, CCE automatically displays the names and contents of the local variables of the function that is being executed;
  It is also possible to add the name of other local variables or global variables to be monitored in the debugging process;
  The values of local variables can be modified;
  The values of the variables that have been changed during the last instruction execution are displayed in red;
  Variable names cannot be modified.

## Slide 25: Introduction to CCE (23/25) Code debugging
Variables view:
  The representation format of a variable can be:
    Natural;
    Decimal;
    Hex.
  The variables that contain more than one element, such as arrays, structures, or pointers are presented with a (+) sign immediately after their name;
  The (+) sign means that the variable has elements that can be seen through the expansion of the (+) sign. The (-) sign allows the structure to be collapsed;
  Local variables can not be added or removed (only disabled - freeze value);
  Global variables can be added or removed.

## Slide 26: Introduction to CCE (24/25) Code debugging
Expressions view:
  Accepts the entry of expressions to evaluate them as the program is executed;
  These expressions are written in a syntax similar to that used by the C programming language;
  The available commands allows to:
    Specify the number of array elements to be displayed;
    Display the pointer/array elements (Display as Array);
    Return an expanded variable back to its original state (Remove Array Expansion);
    Change the value of a variable (Change value);
    Promote to a different type of variable (Cast to type);
    Restore the expression’s original data type (Restore Original Type).

## Slide 27: Introduction to CCE (25/25) Code debugging
Memory view:
  Monitor and modify the memory of the device ;
  The memory can be examined with a series of Memory Monitors;
  Each monitor represents a section of memory specified by location (base address);
  Each memory monitor may be presented in different data formats (Memory renderings):
    Hex (default);
    Ascii;
    Integer signed;
    Unsigned integer.

## Slide 28: Introduction to CCE Expanding CCE capabilities with Eclipse JDT and PDE
CCE can be expanded beyond its default capabilities;
There is a set of Eclipse plug-ins that can be used;
Features can be installed to allow Java programming and the development of Eclipse plug-ins;
These updates should be made only in when the features are needed. Alternatively, they can always co-exist in the same system, one CCE installation and another from Eclipse.
The CCE is based on the Eclipse’s release 3.2;
All plug-ins installed must be compatible with this version;
The installation of plug-ins is extremely easy. Just unpack the releases into the correct directories.