## Slide 1: Chapter 2 Software Development tools Code Composer Essentials v3: Creating a project
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
MSP430 Teaching Materials
<footer> Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt

## Slide 2: Contents
Code Composer Essentials v3:
  Introduction to CCE: Creating a project
    First steps
    C/C++ Project Information Indexing functionality
    Device selection
    Editing code
    Content wizard
    New model creation
    File history
    Import and Export functions
    Project configuration details
<footer>>> Contents

## Slide 3: Introduction to CCE (1/39) Creating a project
Select the option File> New > Managed Make C\ASM Project (recommended) to create a project:

## Slide 4: Introduction to CCE (2/39) Creating a project
Insert the name of the project ;
By default, all the project files are stored in a folder (with the name of the project), in the directory chosen for the workspace.

## Slide 5: Introduction to CCE (3/39) Creating a project
Additional settings are made to the project in creation, such as whether there are any dependencies of this project with another;
If this condition is true, the dependency should be established.

## Slide 6: Introduction to CCE (4/39) Creating a project
C/C++ Project Information Indexing functionality:
  Uses a parser to create a database of the contents of the project files;
  Used during the information search, project navigation, and in the content assistant;
  Is performed in the background and reacts to changes in content such as:
    C/C++ project creation or deletion;
    File creation or deletion;
    File import;
    Content files changes.

## Slide 7: Introduction to CCE (5/39) Creating a project
Information Indexing operation:
  Without Project contents indexing (No Indexer);
  Fast C/C++;
  Full Indexer (C/C++ Indexer).

## Slide 8: Introduction to CCE (6/39) Creating a project
Device selection:
  A compatible linker command file and supporting libraries are selected automatically.

## Slide 9: Introduction to CCE (7/39) Creating a project
Complete the creation of the project by selecting the option Finish;
At any time, it is possible to go back to previous windows by selecting the option Back.
Add the source code file to the project. Choose File > New > Source File.

## Slide 10: Introduction to CCE (8/39) Creating a project
Insert the file name;
Do not forget to add the file extension, e.g. lab1.c to denote a C language file.

## Slide 11: Introduction to CCE (9/39) Creating a project
The project is automatically selected as the default project;
Although the workspace allows several projects to be opened simultaneously, it allows only one project to be active;
To select an active project, the name of the project must be selected with the right mouse button in C/C++ Project view, in order to show the context menu;
Select option set as active project;
It will appear the expression [Active-Debug].

## Slide 12: Introduction to CCE (10/39) Creating a project
Start editing the source code for the project :
  Add the existing file lab1.c using the option add file to project.
  Find the file in Project > add file to project, as in the context menu of the view C/C++ Projects.
  The file lab1.c can be removed from the project by selecting it in the window and selecting the option delete;
  When the file is removed, it will be cleared from the directory.

## Slide 13: Introduction to CCE (11/39) Creating a project
Code Editor:
  Versatile and very effective tool helping the editing task.

## Slide 14: Introduction to CCE (12/39) Creating a project
Code Editor:
  Text Editor: Set of features set to speed up the code editing process.
  Icons:
    Bookmark:
    Breakpoint:
    Add a task:
    Search:
    Error mark:
    Warning:
    Information:

## Slide 15: Introduction to CCE (13/39) Creating a project
Code Editing:
  Editing of code is greatly facilitated using features such as search and replace: Select Edit > Find/Replace;
  The option Search > File allows the use of more elaborate expressions, such as global replacement in all the files of a particular directory;
  The search and replace tasks can be found on the drop-list;
  The CCE can regularly save the opened files. Select Windows > Preferences > General > Workspace and specify the time interval.

## Slide 16: Introduction to CCE (14/39) Creating a project
Content wizard:
  An effective tool to support the writing of code;
  To automatically insert a code structure model:
    Write the first letters of the structure name in the editor;
    Press Ctrl + Space keys to display a list of models;
    Options in the list can be reduced by continuing writing;
    Arrow Up and Arrow Down keys to select the model;
    Esc key allows use without the content wizard.

## Slide 17: Introduction to CCE (15/39) Creating a project
Content wizard:
  Configured in Window > Preferences.

## Slide 18: Introduction to CCE (16/39) Creating a project
Content wizard:
  The suggestions search range can be:
    Restricted to the editing files (Search current file and included files) only;
    In the whole project (Search current project).
  Automatic model insertion (as long as it is the only one in the options list, Insert single proposals automatically);
  List suggestions in alphabetical order (Present proposals in alphabetical order);
  Delay time (msec) to suggest a list (delay);
  Validity of suggestion (Content Assist Parsing timeout).

## Slide 19: Introduction to CCE (17/39) Creating a project
New model creation:
  Expand the C/C++ perspective in Window > Preferences and select Editor > Templates;
  Select the option New to create a new model.

## Slide 20: Introduction to CCE (18/39) Creating a project
New model creation:
  Enter a name for the new model;
  Add a description of the model in the Description field;
  The model itself is defined in the Pattern field;
  To insert a variable use the Insert Variable option.

## Slide 21: Introduction to CCE (19/39) Creating a project
File history:
  Comparisons between two files or previous versions of it;
  Select the file to compare with the one from local history in the navigation view;
  Select the Compare With > Local history option;
  The Compare With Local History window will open;
  Choose a previous state presented in the Local History list;
  The text comparison editor will then open;
  Navigation between changes is made through the Select Next Change and Select Previous Change buttons.

## Slide 22: Introduction to CCE (20/39) Creating a project
File history:
  To recover a project resource that has been cleared from the workspace:
    Select the project to restore a previous build state in the navigation view;
    Select the Restore from Local History... option in the context menu;
    The Restore From Local History window will open on the right hand side of the screen, with the files that were previously part of the project;
    The last state, or any of the previous states can be recovered fully by choosing it in the Local History list.
    Click Restore to restore the project.

## Slide 23: Introduction to CCE (21/39) Creating a project
Import and Export functions:
  Import/export different
  types of information;
  Activate the import
  process selecting the
  option Import in
  the context menu
  of the view
  C/C++ Projects.

## Slide 24: Introduction to CCE (22/39) Creating a project
Import and Export functions:
  Import/export resources:
    Archive File: Files stored in a compressed file;
    Import Breakpoints: Breakpoints scenario previously defined in another project or in the same project;
    Existing Project into Workspace: Project into the current workspace;
    File System: Files;
    Preferences: CCE configuration preferences;
    Etc...

## Slide 25: Introduction to CCE (23/39) Creating a project
Project configuration details:
  The project configuration defines a set of options to build it;
  The options defined at this level are applied to all the files of the project;
  The CCE allows setting different options for building at different stages of the project;
  Building a project is a process that generates new features starting from the existing ones, or updates them if they already exist.

## Slide 26: Introduction to CCE (24/39) Creating a project
Project configuration details:
  Can be invoked for different builds for different types of projects, or for different stages of development;
  The different build process types are:
    Incremental Build uses a build held earlier. From a past build state, the necessary changes are applied to the resources that have been changed;
    Clean Build ignores all previous builds as well as problems or mistakes that led to them. This type of build will convert all resources in accordance with the rules set in the project build configuration.

## Slide 27: Introduction to CCE (25/39) Creating a project
Project configuration details:
  Building a project can follow two different procedures:
  The behaviour of the configuration is defined in Window > Preferences > General > Workspace:
    Automatic builds:
      Always incremental;
      Carried out throughout the workspace;
      Whenever there is resource alteration, will initiate a build process.
    Manual build:
      Always triggered by the user;
      Can be clean or incremental;
      Can be applied to the files of a project or to the whole workspace.

## Slide 28: Introduction to CCE (26/39) Creating a project
Project configuration details:
  The order in which the build is processed is configurable;
  If the project contains references to another project, the CDT must first build the other project;
  The order in which the build takes place may be selected in Window > Preferences > General > Workspace > Build Order.

## Slide 29: Introduction to CCE (27/39) Creating a project
Project configuration details:
  Configure the compile, link and debug settings;
  Select the option Properties (view C/C++ Project).

## Slide 30: Introduction to CCE (28/39) Creating a project
Project configuration details:
  The management of the build files is held under the option C/C++ Build, accessed via the Manage button:
  Specify whether the compiler should Stop On Error or Keep Going On Error.

## Slide 31: Introduction to CCE (29/39) Creating a project
Project configuration details (MSP430X):
  The MSP430X devices allow data to be located anywhere in the 20-bit address space;
  For large projects, the compiler will use longer instructions that use more memory space for their storage;
  The memory space needed by the generated program will therefore be greater;
  Options:
    --large_memory_model in the compile option –vmspx;
    RTS libraries: rts430xl.lib and rts430xl_eh.lib.

## Slide 32: Introduction to CCE (30/39) Creating a project
Project configuration details:
  Linking:
    Multiplication using routines that use the hardware multiplier option (--use_hw_mpy);
    The length of the device multiplier must be specified:
      16 bit hardware multiplier (in most devices);
      32 bit multiplier module (F4xx and F5xx families).
  Initialization of static variables in the C program:
    None;
    Link using ROM autoinitialization model (--rom_model)
    Link using RAM autoinitialization model (--ram_model).

## Slide 33: Introduction to CCE (31/39) Creating a project
Project configuration details:
  Memory space configuration for:
    Arguments passed by the C routines (--arg_size);
    Dynamic allocation of memory by the program (--heap_size);
    System stack size (--stack_size).

## Slide 34: Introduction to CCE (32/39) Creating a project
Project configuration details:
  C/C++ Build:

## Slide 35: Introduction to CCE (33/39) Creating a project
Project configuration details:
  Configure the device in Properties> TI Build Setting:

## Slide 36: Introduction to CCE (34/39) Creating a project
Project configuration details:
  Configure the device in Properties> TI Debug Setting:
  Setup tab, option connection, establish the connecting method to the device, either parallel port or USB port;
  In Debugger tab specify whether to:
    Load the entire application (Load program);
    Just load the project’s symbols (Load symbols only);
    This last option is valid when the development environment cannot load the software, as in the case of software running in ROM;

## Slide 37: Introduction to CCE (35/39) Creating a project
Project configuration details:
  Configure the device in Properties> TI Debug Setting:
    Using the Target tab it is possible to define various aspects of the device:
      Enable the use of IO functions in Enable CIO functions use;
      Establish the starting point for execution of the code when a reset occurs or a program is loaded;
    The supply voltage and the breakpoints types (software or hardware) can be specified at the MSP430 properties. The memory storage process will also be defined with this tab.

## Slide 38: Introduction to CCE (36/39) Creating a project
Project configuration details:
  Configure the device in Properties> TI Debug Setting:

## Slide 39: Introduction to CCE (37/39) Creating a project
<number>
Copyright 2008 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Project configuration details:
  Configure the device in Properties> TI Build Setting:

## Slide 40: Introduction to CCE (38/39) Creating a project
Project configuration details:
  The project is built for the first time by selecting the Project > Build All option;
  The level of success in building the project can be examined in the Console and Problems windows;
  After successfully building a project:
    It can be automatically downloaded into the device;
    It can be built at the beginning of the debug session. The option Debug Active Project will recompile it and launch the debugger, using the device information defined in the project’s options.
  Note that an attempt to update the firmware can occur when the debugger is initialized for the first time, after a SR has been installed or a new USB interface is used.

## Slide 41: Introduction to CCE (39/39) Creating a project
Project configuration details:
  Switch to the Debug perspective;
  This operation can be carried out in two ways :
    With the perspective selection, or;
    By selecting Window > Open Perspective > Debug.
  When the project is debugged:
    Errors are identified as red marks on the right hand side;
    Problems are identified with white marks;
    Lines with errors have a mark on the left hand side.
  When the project is made (make option), the resources can be accessed on Properties > C/C++ Build > MSP430 Linker V3.0 > Linker Output in the option Produce list of input and output sections.