## Slide 1: Chapter 2 Software Development tools IAR Embedded Workbench™
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
MSP430 Teaching Materials
<footer> Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt

## Slide 2: Contents
IAR Embedded Workbench™
Setting up a new project:
  Step 1: Creating a workspace window
  Step 2: Creating the new project
  Step 3: Adding files to the project
  Step 4: Setting project options
  Step 5: Compiling and linking
  Step 6: Debugging the application
Summary

## Slide 3: IAR Embedded Workbench™ (1/2)
Kickstart Version (Free):
  4KB Limit on C code size for 430 devices;
  8KB Limit on C code size for 430X devices;
  Unlimited assembly language code size;
  Available from MSP430 web page;
  Supported by TI PIC;
  Able to use SimpliciTI libraries in project.
Baseline Version (~$995):
  12KB Limit on C code size;
  Unlimited assembler code size;
  Available and supported by IAR.
Full Version (~$2695):
  Unlimited code size;
  Available and supported by IAR.
All versions support all available MSP430 devices

## Slide 4: IAR Embedded Workbench™ (2/2)
Available for a range of P and C (8, 16 and 32 bits);
Integrated tools in this IDE are:
  Compiler IAR MSP430 C/C++;
  Assembler IAR MSP430;
  IAR XLINK Linker™;
  The IAR XAR Library Builder™;
  Text editor;
  Project management;
  Command lines utility;
  IAR C-SPY™ debugger.
Gives the user:
  A highly efficient IDE;
  Functional workspace methodology;
  Reduced development time.

## Slide 5: Setting up a new project
The IDE uses a methodology based on a workspace concept;
Modules can contain one or more projects;
The projects are made up of one or more source code files used to generate the binary file for simulation and/or programming;
Before creating a project, a workspace must first be created;
When IAR EWB starts for the first time, it creates a default workspace.

## Slide 6: Setting up a new project (1/2) Step 1: Creating a workspace window
Choose File > New > Workspace;
Pressing OK will display a window with an empty workspace.

## Slide 7: Setting up a new project (2/2) Step 1: Creating a workspace window
Save workspace: Choose File > Save Workspace;
Specify where the workspace file should be saved;
Name: HelloWorld in File name > Save to create the new workspace (file extension: .eww).

## Slide 8: Setting up a new project (1/3) Step 2: Creating the new project
Choose Project > Create New Project;
The Create New Project dialogue box allows a new project to be based on a project template;
Select the project template Empty project (creates an empty project that uses default project settings).

## Slide 9: Setting up a new project (2/3) Step 2: Creating the new project
The Tool chain must be set to MSP430, and click OK.

## Slide 10: Setting up a new project (3/3) Step 2: Creating the new project
In the Save As dialog box specify the location of the project file (newly created projects directory);
Name Project1 in the File name box, and click Save to create the new project;
The project will appear in the
workspace window.

## Slide 11: Setting up a new project Step 3: Adding files to the project
In the Workspace window, select the destination to which you want to add a source file (directly to the project);
To create new source files, choose
File>New and select Source/Text;
Choose Project>Add Files;
Locate the file in the CD’s
Chapter 2 > Lab1_IAR and click
Open to add it to the Project1.

## Slide 12: Setting up a new project Integrated Development Enviromnent
3 windows:
  Workspace: Project and associates files;
  Text editor: Source code file(s);
  Debug Log: Compilation information.

## Slide 13: Setting up a new project (1/4) Step 4: Setting project options
Select the project folder icon Project1 - Debug in the Workspace window and choose Project > Options;
The Target options page in the General Options category is displayed;
Settings:
  MSP430 device: MSP430FG4618;
  Output file: Executable;
  Library: CLIB.

## Slide 14: Setting up a new project (2/4) Step 4: Setting project options
Select C/C++ Compiler in the Category list to display the compiler option pages:
    Language: Details specifications for the C language interpretation;
    Code: Code optimization options configuration;
    Output: Output files type configuration;
    List: List files configuration created by the compiler.

## Slide 15: Setting up a new project (3/4) Step 4: Setting project options

## Slide 16: Setting up a new project (4/4) Step 4: Setting project options
Select Debugger in the Category list to display the debugger the option pages:
  Simulate in the PC: Setup -> Simulator;
  Testing the application on the C: Setup -> FET Debugger;
  After choosing one of the options, click OK.

## Slide 17: Setting up a new project (1/2) Step 5: Compiling and linking
To compile the file Lab1.c, select it in the Workspace window.
Choose Project>Compile.
The progress will be displayed in the Build messages window.

## Slide 18: Setting up a new project (2/2) Step 5: Compiling and linking
Creation of new directories at the Debug directory has been created containing the directories List, Obj, and Exe:
  List: destination directory for the list files (.lst);
  Obj: destination directory for the object files (.r43) from the compiler and the assembler (input to the IAR Linker);
  Exe: destination directory for the
  executable file (.d43) that will be
  used as an input to the IAR Debugger.

## Slide 19: Setting up a new project (1/2) Step 6: Debugging the application
Choose Project > Debug;
Workspace configuration is changed to the project execution mode.

## Slide 20: Setting up a new project (2/2) Step 6: Debugging the application
Workspace configuration for inspection (View >) of the windows of interest to the user:
    Disassembly: Hexadecimal format of the memory content interleaved with the C source code;
    Memory: Memory mapping with several data inspection options;
    Register: Monitor CPU and SFRs registers in the RAM;
    Watch: Inspect expressions or variables;
    Locals: Local variables inside a routine or function;
    Live Watch: Expressions or real-time monitoring of variables;
    Call Stack: Stack contents;
    Terminal I/O: Monitoring the I/O ports state.

## Slide 21: Summary
Brief presentation of the IAR EWB IDE;
Initial overview how to create a project;
Recommendation:
  Read and do the tutorials included in the manual “MSP430 IAR Embedded Workbench™ - IDE User Guide for Texas Instruments’ MSP430 Microcontroller Family” for a detailed description of the IAR IDE.