## Slide 1: Chapter 4 MSP430 Architecture
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Notes: <number>

## Slide 2: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
MSP430 architecture:
  Main characteristics
  Architecture topology
  Address space
  Interrupt vector table
  Central Processing Unit (MSP430 CPU)
  Central Processing Unit (MSP430X CPU)
  Addressing modes
  Instructions set
Quiz

## Slide 3: Introduction
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A comprehensive description of the MSP430 architecture, covering its:
  Main characteristics;
  Device architecture;
  Address space;
  Interrupt vector table;
  Central Processing Unit (MSP430 CPU and MSP430X CPU);
  7 seven addressing modes and instruction set composed of:
    27 base opcodes;
    24 emulated instructions.

## Slide 4: Microcontroller characteristics
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Integration: Able to implement a whole design onto a single chip.
Cost: Are usually low-cost devices (a few $ each);
Clock frequency: Compared with other devices (microprocessors and DSPs), MCUs use a low clock frequency:
  MCUs today run up to 100 MHz/100 MIPS (Million Instructions Per Second).
Power consumption: Low power (battery operation);
Bits: 4 bits (older devices) to 32 bits devices;
Memory: Limited available memory, usually less than 1 MByte;
Input/Output (I/O): Low to high (8 to 150) pin-out count.

## Slide 5: MSP430 main characteristics (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Low power consumption:
  0.1 A for RAM data retention;
  0.8 A for real-time clock mode operation;
  250 A/MIPS during active operation.
Low operation voltage (from 1.8 V to 3.6 V);
< 1 s clock start-up;
< 50 nA port leakage;
Zero-power Brown-Out Reset (BOR).

## Slide 6: MSP430 main characteristics (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
On-chip analogue features:
  10/12/16-bit Analogue-to-Digital Converter (ADC);
  12-bit dual Digital-to-Analogue Converter (DAC);
  Comparator-gated timers;
  Operational Amplifiers (Op Amps);
  Supply Voltage Supervisor (SVS).
16 bit RISC CPU:
  Compact core design reduces power consumption and cost;
  16-bit data bus;
  27 core instructions;
  7 addressing modes;
  Extensive vectored-interrupt capability.

## Slide 7: MSP430 main characteristics (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Flexibility:
  Up to 256 kByte Flash;
  Up to 100 pins;
  USART, I2C, Timers;
  LCD driver;
  Embedded emulation;
  And many more peripherals modules…
Microcontroller performance:
  Instruction processing on either bits, bytes or words
  Reduced instructions set;
  Compiler efficient;
  Wide range of peripherals;
  Flexible clock system.

## Slide 8: MSP430 Architecture
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Block diagram:

## Slide 9: Address Space
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Mapped into a single, contiguous address space:
  All memory, including RAM, Flash/ROM, information memory, special function registers (SFRs), and peripheral registers.
  Memory Map:

## Slide 10: Interrupt vector table
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Mapped at the very end of memory space (upper 16 words of Flash/ROM): 0FFE0h - 0FFFEh (4xx devices);
Priority of the interrupt vector increases with the word address.

## Slide 11: Central Processing Unit (MSP430 CPU) (1/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
RISC (Reduced Instructions Set Computing) architecture:
  Instructions are reduced to the basic ones (short set):
    27 physical instructions;
    24 emulated instructions.
  This provides simpler and faster instruction decoding;
  Interconnect by a using a common memory address bus (MAB) and memory data bus (MDB) - Von Neumann architecture:
    Makes use of only one storage structure for data and instructions sets.
    The separation of the storage processing unit is implicit;
    Instructions are treated as data (programmable).

## Slide 12: Central Processing Unit (MSP430 CPU) (2/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
RISC (Reduced Instructions Set Computing) type architecture:
  Uses a 3-stage instruction pipeline containing:
    Instruction decoding;
    16 bit ALU;
    4 dedicated-use registers;
    12 working registers.
Address bus has 16 bit so it can address 65 kB (including RAM + Flash + Registers);
Arithmetic Logic Unit (ALU):
  Addition, subtraction, comparison and logical (AND, OR, XOR) operations;
  Operations can affect the overflow, zero, negative, and carry flags of the SR (Status Register).

## Slide 13: Central Processing Unit (MSP430 CPU) (3/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Incorporates sixteen 16-bit registers:
    4 registers (R0, R1, R2 and R3) have dedicated functions;
    12 register are working registers (R4 to R15) for general use.
R0: Program Counter (PC):
  Points to the next instruction to be read from memory and executed by the CPU.
R1: Stack Pointer (SP):
  1st: stack can be used by user to store data for later use (instructions: store by PUSH, retrieve by POP);
  2nd: stack can be used by user or by compiler for subroutine parameters (PUSH, POP in calling routine; addressed via offset calculation on stack pointer (SP) in called subroutine);

## Slide 14: Central Processing Unit (MSP430 CPU) (4/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R1: Stack Pointer (SP) (continued):
  3rd: used by subroutine calls to store the program counter value for return at subroutine's end (RET);
  4th: used by interrupt - system stores the actual PC value first, then the actual status register content (on top of stack) on return from interrupt (RETI) the system get the same status as just before the interrupt happened (as long as none has changed the value on TOS) and the same program counter value from stack.

## Slide 15: Central Processing Unit (MSP430 CPU) (5/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R2: Status Register (SR):
  Stores status and control bits;
  System flags are changed automatically by the CPU;
  Reserved bits are used to support the constant generator.
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Reserved for CG1 |  |  |  |  |  |  | V | SCG1 | SCG0 | OSCOFF | CPUOFF | GIE | N | Z | C
Bit |  | Description
8 | V | Overflow bit. V = 1  Result of an arithmetic operation overflows the signed-variable range.
7 | SCG1 | System clock generator 0. SCG1 = 1  DCO generator is turned off – if not used for MCLK or SMCLK
6 | SCG0 | System clock generator 1. SCG0 = 1  FLL+ loop control is turned off
5 | OSCOFF | Oscillator Off. OSCOFF = 1  turns off LFXT1 when it is not used for MCLK or SMCLK
4 | CPUOFF | CPU off. CPUOFF = 1  disable CPU core.
3 | GIE | General interrupt enable. GIE = 1  enables maskable interrupts.
2 | N | Negative flag. N = 1  result of a byte or word operation is negative.
1 | Z | Zero flag. Z = 1  result of a byte or word operation is 0.
0 | C | Carry flag. C = 1  result of a byte or word operation produced a carry.

## Slide 16: Central Processing Unit (MSP430 CPU) (6/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
<number>
Copyright 2008 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R2/R3: Constant Generator Registers (CG1/CG2):
  Depending of the source-register addressing modes (As) value, six constants can be generated without code word or code memory access to retrieve them.
  This is a very powerful feature which allows the implementation of emulated instructions, for example, instead of implement a core instruction for an increment the constant generator is used.
Register | As | Constant | Remarks
R2 | 00 | - | Register mode
R2 | 01 | (0) | Absolute mode
R2 | 10 | 00004h | +4, bit processing
R2 | 11 | 00008h | +8, bit processing
R3 | 00 | 00000h | 0, word processing
R3 | 01 | 00001h | +1
R3 | 10 | 00002h | +2, bit processing
R3 | 11 | 0FFFFh | -1, word processing

## Slide 17: Central Processing Unit (MSP430 CPU) (7/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
<number>
Copyright 2008 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R4 - R15: General–Purpose Registers:
  These general-purpose registers are adequate to store data registers, address pointers, or index values and can be accessed with byte or word instructions.

## Slide 18: Central Processing Unit (MSP430X CPU) (1/10)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Main features of the MSP430X CPU architecture:
  The MSP430X CPU extends the addressing capabilities of the MSP430 family beyond 64 kB to 1 MB;
  To achieve this, some changes have been made to the addressing modes and two new types of instructions have been added;
  One instruction type allows access to the entire address space, and the other is designed for address calculations;
  The MSP430X CPU address bus has 20 bits, although the data bus still has 16 bits. Memory accesses to 8-bit, 16-bit and 20-bit data are supported;
  Despite these changes, the MSP430X CPU remains compatible with the MSP430 CPU, having a similar number of registers.

## Slide 19: Central Processing Unit (MSP430X CPU) (2/10)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Organization of the MSP430X CPU:
  Although the MSP430X CPU structure is similar to that of the MSP430 CPU, there are some differences that will now be highlighted;
  With the exception of the status register SR, all MSP430X registers are 20 bits;
  The CPU can now process 20-bit or 16-bit data.

## Slide 20: Central Processing Unit (MSP430X CPU) (3/10)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The MSP430X CPU has 16 registers, some of which have special use:
R0 (PC) Program Counter:
  Has the same function as the MSP430 CPU, although now it has 20 bits.
R1 (SP) Stack Pointer:
  Has the same function as the MSP430 CPU, although now it has 20 bits.
R2 (SR) Status Register:
  Has the same function as the MSP430 CPU, but it still has 16 bits.

## Slide 21: Central Processing Unit (MSP430X CPU) (4/10)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R2 (SR) Status Register:
  Description of the SR bits:

## Slide 22: Central Processing Unit (MSP430X CPU) (5/10)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R2 (SR/CG1) and R3 (CG2) Constant Generators:
  Registers R2 and R3 can be used to generate six different constants commonly used in programming, without adding an additional 16-bit word to the instruction;
  The constants are fixed and are selected by the (As) bits of the instruction. (As) selects the addressing mode.
  Values of constants
  generated:

## Slide 23: Central Processing Unit (MSP430X CPU) (6/10)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R2 (SR/CG1) and R3 (CG2) Constant Generators:
  Whenever the operand is one of the six constants, the registers are selected automatically;
  Therefore, when used in constant mode, registers R2 and R3 cannot be used as source registers.
R4-R15 – General-purpose registers:
  Have the same function as in the MSP430 CPU, although they now have 20 bits;
  These registers can process 8-bit, 16-bit or 20-bit data;
  If a byte is written to one of these registers it takes bits 7:0, the bits 19:8 are filled with zeroes. If a word is written to one of these registers it takes bits 15:0, the bits 19:16 are filled with zeroes.

## Slide 24: Central Processing Unit (MSP430X CPU) (7/10)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R4-R15 – General-purpose registers:
  Handling byte data (8 bits) using the suffix .B:

## Slide 25: Central Processing Unit (MSP430X CPU) (8/10)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R4-R15 – General-purpose registers:
  Handling word data (16 bits) using the suffix .W:

## Slide 26: Central Processing Unit (MSP430X CPU) (9/10)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
R4-R15 – General-purpose registers:
  Manipulation of a 20-bit address using the suffix .A:

## Slide 27: Central Processing Unit (MSP430X CPU) (10/10)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
All other differences in the addressing modes, instruction set and other details for the CPUX architecture present in MSP430 devices which have over 64kB of on chip memory are described in much greater depth is section 15.3.2.

## Slide 28: Addressing modes
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
7 addressing modes for the source operand:
4 addressing modes for the destination operand:
  Register mode; Indexed mode; Symbolic mode; Absolute mode.
For the destination operand, two additional addressing modes can be emulated.

## Slide 29: Instruction set
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
27 core instructions;
24 emulated instructions;
The instruction set is orthogonal;
The core instructions have unique opcodes decoded by the CPU, while the emulated ones need assemblers and compilers for their mnemonics;
There are three core-instruction formats:
  Double operand;
  Single operand;
  Program flow control - Jump.

## Slide 30: Quiz (1/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
1. The number and types of instructions used by the MSP430 CPU are:
(a) 27 core instructions;
(b) 20 core instructions and 14 emulated ones;
(c) 27 core instructions and 24 emulated ones;
(d) 24 core instructions.
2. The MSP430 RISC type CPU is:
(a) Based on a reduced instruction set;
(b) Based on pure pattern matching and absence of instructions;
(c) Based on a complex instruction set;
(d) A CPU without peripherals connections.

## Slide 31: Quiz (2/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
3. The von Neumann architecture used for the MSP430:
(a) Has the data storage entirely contained within the data processing unit;
(b) Has physically separate storage and signal pathways for instructions and data;
(c) Has a separate bus just for peripherals;
(d) Has program, data memory and peripherals all sharing a common bus structure.

## Slide 32: Quiz (3/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
4. The ALU in the MSP430 CPU handles:
(a) Addition, subtraction, multiplication and division operations;
(b) Addition, subtraction, comparison and logical (AND, OR, XOR) operations;
(c) Addition, subtraction, multiplication and comparison operations;
(d) Addition, subtraction, multiplication and logical (AND, OR, XOR) operations.

## Slide 33: Quiz (4/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
5. The MSP430 CPU incorporates:
(a) 14 registers (2 for dedicated functions and 12 for work);
(b) 16 registers (6 for dedicated functions and 10 for work);
(c) 18 registers (4 for dedicated functions and 14 for work);
(d) 16 registers (4 for dedicated functions and 12 for work).
6. The Program Counter (PC):
(a) Stores the return addresses of subroutine calls and interrupts;
(b) Points to the next instruction to be read from memory and executed by CPU;
(c) Stores state and control bits;
(d) Points to the next instruction to be written in memory.

## Slide 34: Quiz (5/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
7. The result of the Status Register SR = 0x0104 indicates:
(a) Arithmetic operation result overflows the signed-variable range and produced a carry;
(b) Arithmetic operation result overflows the signed-variable range which result is negative, when maskable interrupts are enabled;
(c) Arithmetic operation result is negative and produced a carry;
(d) CPU is disabled and the maskable interrupts are enabled.
8. The MSP430 Status Register (SR) bit:
(a) V is set when the result of a byte or word operation overflows;
(b) Z is set when the result of a byte or word operation is zero;
(c) all of the above;
(d) none of the above.

## Slide 35: Quiz (6/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
9. The MSP430 supports on two-address-instructions:
(a) Seven addressing modes for the source operand and three addressing modes for the destination operand;
(b) Six addressing modes for the source operand and four addressing modes for the destination operand;
(c) Seven addressing modes for the source operand and four addressing modes for the destination operand;
(d) Six addressing modes for the source operand and three addressing modes for the destination operand.

## Slide 36: Quiz (7/7)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Answers
  1. (c) 27 core instructions and 24 emulated instructions.
  2. (a) Based on a reduced instruction set.
  3. (d) has program, data memory and peripherals all sharing a common bus structure.
  4. (b) Addition, subtraction, comparison and logical (OR, AND, XOR) operations.
  5. (d) 16 registers (4: dedicated functions and 12 working).
  6. (b) Points to the next instruction to be read from memory and executed by the CPU.
  7. (b) Arithmetic operation result overflows the signed-variable range when result is negative, when maskable interrupts are enabled.
  8. (c) all of the above.
  9. (c) Seven for the source operand and four addressing modes for the destination operand.