## Slide 1: Chapter 5 Device Systems and Operating Modes
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
<footer> Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt

## Slide 2: Contents
Introduction
Internal system resets
System clocks
Interrupt management
Watchdog Timer
Supervisory voltage system
Low-power operating modes
Quiz

## Slide 3: Introduction
Description of the internal devices and systems of the MSP430;
It includes descriptions of the:
  Internal system reset;
  Clock sources;
  Interrupt management;
  Low-power operating modes.
Quiz.

## Slide 4: System reset (1/5)
The MSP430 families make use of two independent reset signals:
  Hardware reset signal - POR (Power On Reset);
  Software reset signal – PUC (Power Up Clear).
Different events determine which one of the reset signals is generated;
Sources that can generate a POR:
  Initial device power up;
  Low signal at the reset pin (RST/NMI) when this is configured in reset mode;
  Low signal at the supervisory voltage system (SVS) when the register bit PORON is high.

## Slide 5: System reset (2/5)
Sources that can generate a PUC:
  Active POR signal;
  Watchdog timer (WDT) expired when it is configured in supervision mode;
  Flash memory access control registers security key violation.

## Slide 6: System reset (3/5)
Conditions:
  Hardware reset signal (POR) is active then:
    SR is reset;
    PC is loaded with the address in location 0FFFEh;
    Peripheral registers all enter their power up state.
  Software reset signal (PUC) is active then:
    SR is reset;
    PC is loaded with either the reset vector (0FFFEh), or the PUC source interrupt vector;
    Only some peripheral registers are reset by PUC.

## Slide 7: System reset (4/5)
All 2xx and 4xx MSP430 devices possess a reset circuit by power source disturbance identified by Brown Out Reset (BOR);
This circuit is an enhanced POR system:
  Includes a hysteresis circuit;
  Device stays in reset mode until voltage is higher than the upper threshold (VB_IT+):
    BOR takes 2 msec to be inactive and allow the program execution by CPU;
  When voltage falls below the lower threshold (VB_IT-):
    BOR circuit will generate a reset signal;
    Suspends processor operation until the voltage rises up above the lower threshold inferior value.

## Slide 8: System reset (5/5)
Brownout timing:

## Slide 9: System clocks (1/24)
Allows the CPU and peripherals to operate from different clock sources;
The system clocks depend on the device in the MSP430 family:
  MSP430x2xx:
    The Basic Clock Module+ (BCM+);
      One or two oscillators (depending on the device);
      Capable of working with external crystals or resonators;
      Internal digitally controlled oscillator (DCO);
      Working frequency to up 16 MHz;
      Lower power consumption;
      Lower internal oscillator start-up time.

## Slide 10: System clocks (2/24)
  MSP430x2xx:
    Basic Clock+:

## Slide 11: System clocks (3/24)
  MSP430x4xx:
    Frequency Locked Loop (FLL+):
      One or two oscillators (depending on the device);
      Capable of working with external crystals or resonators;
      Internal digitally controlled oscillator (DCO), adjusted and controlled by hardware;
      Synchronized to a high-frequency internal clock from a low frequency external oscillator.

## Slide 12: System clocks (4/24)
  MSP430x4xx:
    FLL+:

## Slide 13: System clocks (5/24)
The clock sources from these oscillators can be selected to generate different clock signals:
  Master clock (MCLK):
    Generated by DCO (but can also be fed by the crystal oscillator);
    Activate and stable in less than 6 sec;
    Used by the CPU and high-speed peripherals.
  Subsystem main clock (SMCLK):
    Used as alternative clock source for peripherals.
  Auxiliary clock (ACLK):
    RTC self wake-up function from low power modes (32.768 kHz);
    Always fed by the crystal oscillator.
  Each clock can be internally divided by a factor of 1, 2, 4 or 8.

## Slide 14: System clocks (6/24)
Low/High frequency oscillator (LFXT1):
  Implemented in all MSP430 devices;
  Used with either:
    Low-frequency 32.768 kHz watch crystals (RTC);
    Standard crystals, resonators, or external clock sources in range 450 kHz to 8 MHz (16 MHz in 2xx family).
  The operating mode selection (one bit):
    (=0) -> LF clock;
    (=1) -> HF clock.
    XTS: located at the BCSCTL1 register (2xx family);
    XTS_FLL: located at the FLL_CTL0 register (4xx family).

## Slide 15: System clocks (7/24)
Second crystal oscillator (XT2):
  Sources of XT2CLK and its characteristics are identical to LFXT1 in HF mode (range 450 kHz to 8 MHz, or 16 MHz in the 2xx family);
  Load capacitance for the high frequency crystal or resonator must be provided externally;
  This oscillator can be disabled by the XT2OFF bit:
    BCSCTL1 register in 2xx family;
    FLL_CTL1 register in 4xx family (if XT2CLK is unused for source the MCLK and SMCLK clock signals).

## Slide 16: System clocks (8/24)
Digitally-controlled oscillator (DCO):
  Integrated ring oscillator with RC-type characteristics;
  Provide a wide, software-controllable frequency range;
  DCO frequency is synchronized to the FLL;
  Frequency modulation method provided by FLL functionality:
    2xx family:
      Does not have full FLL functionality;
      The DCO generates an internal signal (DCOCLK):
        Programmed internally or externally (DCOR bit);
        Controlled by a resistor connected to the ROSC and VCC pins.

## Slide 17: System clocks (9/24)
    2xx family:
      The DCO control bits:
        RSELx: fDCO range selection;
        DCOx: fDCO defined by the RSEL bits. The step size is defined by the parameter SDCO;
        MODx: Modulation bits select how often fDCO(RSEL, DCO+1) is used within the period of 32 DCOCLK cycles.
        The frequency fDCO(RSEL, DCO) is used for the remaining cycles.
      Specific frequency ranges and values vary by device:

## Slide 18: System clocks (10/24)
    2xx family:
      Basic Clock Module+ (BCM+) registers configuration:
        DCOCTL: DCO Control Register
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
DCOx |  |  | MODx |  |  |  | 
Bit |  | Description
7-5 | DCOx | Discrete DCO frequency selection step (depends on RSELx bits).
4-0 | MODx | Modulator selection.

## Slide 19: System clocks (11/24)
    2xx family:
      Basic Clock Module+ (BCM+) registers configuration:
        BCSCTL1: Basic Clock System Control Reg. 1
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
XT2OF | XTS | DIVAx |  | RSELx |  |  | 
Bit |  | Description
7 | XT2OF | XT2 oscillator fault: XT2OF = 0  XT2 normal operation XT2OF = 1  XT2 fault condition
6 | XTS | LFXT1 oscillator operating mode: XTS = 0  LF mode (low frequency) XTS = 1  HF mode (high frequency)
5-4 | DIVAx | ACLK frequency divider: DIVA1 DIVA0 = 0 0  /1 DIVA1 DIVA0 = 0 1  /2 DIVA1 DIVA0 = 1 0  /4 DIVA1 DIVA0 = 1 1  /8
3-0 | RSELx | Range select. Sixteen different frequency ranges are available.

## Slide 20: System clocks (12/24)
    2xx family:
      Basic Clock Module+ (BCM+) registers configuration:
        BCSCTL2: Basic Clock System Control Reg. 2
7 | 6 | 5 | 4 |  | 3 | 2 | 1 | 0
SELMx |  | DIVMx |  | SELS |  | DIVSx |  | DCOR
Bit |  | Description
7-6 | SELMx | MCLK source: SELM1 SELM0 = 0 0  DCO SELM1 SELM0 = 0 1  DCO SELM1 SELM0 = 1 0  XT2 SELM1 SELM0 = 1 1  LFXT1
5-4 | DIVMx | MCLK frequency divider: DIVM1 DIVM0 = 0 0  /1 DIVM1 DIVM0 = 0 1  /2 DIVM1 DIVM0 = 1 0  /4 DIVM1 DIVM0 = 1 1  /8
3 | SELS | SMCLK source: SELS = 0  DCO SELS = 1  XT2
2-1 | DIVSx | SMCLK frequency divider: DIVS1 DIVS0 = 0 0  /1 DIVS1 DIVS0 = 0 1  /2 DIVS1 DIVS0 = 1 0  /4 DIVS1 DIVS0 = 1 1  /8
0 | DCOR | DCO resistor selector DCOR = 0  Internal resistor DCOR = 1  External resistor

## Slide 21: System clocks (13/24)
    2xx family:
      Basic Clock Module+ (BCM+) registers configuration:
        BCSCTL3: Basic Clock System Control Reg. 3
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
XT2Sx |  | LFXT1Sx |  | XCAPx |  | XT2OFF | LFXT1OF
Bit |  | Description
7-6 | XT2Sx | XT2 range select: XT2S1 XT2S0 = 0 0  0.4 – 1 MHz XT2S1 XT2S0 = 0 1  1 – 3 MHz XT2S1 XT2S0 = 1 0  3 – 16 MHz XT2S1 XT2S0 = 1 1  0.4 – 16-MHz (Digital external)
5-4 | LFXT1Sx | Low-frequency clock select and LFXT1 range select: XTS=0: XTS=1: LFXT1S1 LFXT1S0 = 0 0  32768 Hz 0.4 - 1-MHz LFXT1S1 LFXT1S0 = 0 1  Reserved 1 - 3-MHz LFXT1S1 LFXT1S0 = 1 0  VLOCLK 3 - 16-MHz LFXT1S1 LFXT1S0 = 1 1  External 0.4 - 16-MHz
3-2 | XCAPx | Oscillator capacitor selection: XCAP1 XCAP0 = 0 0  ~1 pF XCAP1 XCAP0 = 0 1  ~6 pF XCAP1 XCAP0 = 1 0  ~10 pF XCAP1 XCAP0 = 1 1  ~12.5 pF
1 | XT2OFF | XT2 oscillator fault: XT2OFF = 0  No fault condition XT2OFF = 1  Fault condition
0 | LFXT1OF | LFXT1OF oscillator fault: LFXT1OF = 0  No fault condition LFXT1OF = 1  Fault condition

## Slide 22: System clocks (14/24)
    4xx family:
      The DCO generates the signal: (fDCOCLK)=ACLK x D x (N+1).
      The DCOPLUS bit sets the fDCOCLK frequency to:
        fDCO;
        fDCO/D: The FLLDx bits configure D=1, 2, 4 or 8.
      By default, DCOPLUS = 0, D = 2 providing:
        fDCO/2 on fDCOCLK;
        The multiplier (N+1) and D set the fDCOCLK.
      DCOPLUS = 0: fDCOCLK = (N + 1) x fACLK
      DCOPLUS = 1: fDCOCLK = D x (N + 1) x fACLK
      fDCO range selected by FNx bits (register SCFI0).

## Slide 23: System clocks (15/24)
Frequency Locked Loop (FLL) - 4xx family:
  Automatically modulates the DCO frequency;
  Greater precision and control;
  Mixes the programmed fDCO with the next higher fDCO.
  Operation:
    The DCO signal is divided by D and divided by N+1;
    The signal obtained is continuously applied to the count down input of a 10-bit up/down counter (frequency integrator);
    ACLK (LFXT1) is applied to the count up input of the counter;
    The counter output is fed back to the DCO modulator, correcting and synchronizing the operating frequency;
    The output of the frequency integrator can be read in SCFI1 and SCFI0 registers;
    The count is adjusted by +1 each ACLK (xtal) period, by -1 each period of the divided DCO signal.

## Slide 24: System clocks (16/24)
Frequency Locked Loop (FLL) - 4xx family:
  29 fDCO taps are set by 5 of the integrator bits, SCFI1 bits 7 to 3 (28, 29, 30, and 31 are equivalent);
  Each tap is approximately 10% higher than the previous;
  The modulator mixes two adjacent DCO frequencies to produce fractional taps;
  SCFI1 register bits 2 to 0 and SCFI0 register bits 1 to 0 are used for the digital modulator;
  The method of FLL can be described as switching between the two most close neighbour frequencies to our frequency asked for to achieve the frequency requested as a time-weighted average of both frequencies.

## Slide 25: System clocks (17/24)
Frequency Locked Loop (FLL) - 4xx family:
  FLL+ clock module configuration:
    SCFQCTL: System Clock Control Register
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
SCFQ_M | N |  |  |  |  |  | 
Bit |  | Description
7 | SCFQ_M | Modulation control: SCFQ_M = 0  FLL modulation enable SCFQ_M = 1  FLL modulation disable
6-0 | N | DCO frequency multiplier factor: DCOPLUS = 0  fDCOCLK = (N +1) fcrystal DCOPLUS = 1  fDCOCLK = D (N +1) fcrystal

## Slide 26: System clocks (18/24)
Frequency Locked Loop (FLL) - 4xx family:
  FLL+ clock module configuration:
    SCFI0: System Clock Frequency Integrator Reg. 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
FLLDx |  | FN_x |  |  |  | MODx (LSBs) | 
Bit |  | Description
7-6 | FLLDx | FLL+ feedback loop fDCOCLK divider: FLLD1 FLLD0 = 0 0  /1 FLLD1 FLLD0 = 0 1  /2 FLLD1 FLLD0 = 1 0  /4 FLLD1 FLLD0 = 1 1  /8
5-2 | FN_x | fDCO operating range: 0000  0.65 – 6.1 MHz 0001  1.3 – 12.1 MHz 001x  2.0 – 17.9 MHz 01xx  2.8 – 26.6 MHz 1xxx  4.2 – 46.0 MHz
1-0 | MODx | LSB modulator bits modified by the FLL+.

## Slide 27: System clocks (19/24)
Frequency Locked Loop (FLL) - 4xx family:
  FLL+ clock module configuration:
    SCFI1: System Clock Frequency Integrator Reg. 1
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
DCOx |  |  |  |  | MODx (MSBs) |  | 
Bit |  | Description
7-3 | DCOx | DCO tap selection modified by the FLL+.
2-0 | MODx | MSB modulator bits modified by the FLL+.

## Slide 28: System clocks (20/24)
Frequency Locked Loop (FLL) - 4xx family:
  FLL+ clock module configuration:
    FLL_CTL0: FLL+ Control Register 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
DCOPLUS | XTS_FLL | XCAPxPF |  | XT2OF | XT1OF | LFOF | DCOF
Bit |  | Description
7 | DCOPLUS | DCO output pre-divider: DCOPLUS = 0  Divider enable DCOPLUS = 1  Divider disable
6 | XTS_FLL | LFXT1 oscillator operating mode: XTS_FLL = 0  LF mode (low frequency) XTS_FLL = 1  HF mode (high frequency)
5-4 | XCAPxPF | LFXT1 oscillator load capacitance: XCAP1PF XCAP0PF = 0 0   1 pF XCAP1PF XCAP0PF = 0 1   6 pF XCAP1PF XCAP0PF = 1 0   8 pF XCAP1PF XCAP0PF = 1 1   10 pF
3 | XT2OF | XT2 oscillator fault: XT2OF = 0  XT2 normal operation XT2OF = 1  XT2 fault condition
2 | XT1OF | HF mode LFXT1 oscillator fault: XT1OF = 0  LFXT1 normal operation XT1OF = 1  LFXT1 fault condition
1 | LFOF | LF mode LFXT1 oscillator fault: LFOF = 0  LFXT1 normal operation LFOF = 1  LFXT1 fault condition
0 | DCOF | DCO oscillator fault: DCOF = 0  DCO normal operation DCOF = 1  DCO fault condition

## Slide 29: System clocks (21/24)
Frequency Locked Loop (FLL) - 4xx family:
  FLL+ clock module configuration:
    FLL_CTL1: FLL+ Control Register 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
- | SMCLKOFF | XT2OFF | SELMx |  | SELS | FLL_DIVx | 
Bit |  | Description
6 | SMCLKOFF | SMCLK disable: SMCLKOFF = 0  SMCLK enable SMCLKOFF = 1  SMCLK disable
5 | XT2OFF | XT2 disable: XT2OFF = 0  XT2 enable XT2OFF = 1  XT2 disable
4-3 | SELMx | MCLK source: SELM1 SELM0 = 0 0  DCO SELM1 SELM0 = 0 1  DCO SELM1 SELM0 = 1 0  XT2 SELM1 SELM0 = 1 1  LFXT1
2 | SELS | SMCLK source: SELS = 0  DCO SELS = 1  XT2
1-0 | FLL_DIVx | ACLK frequency divider: FLL_DIV_0 = 0 0  /1 FLL_DIV_1 = 0 1  /2 FLL_DIV_2 = 1 0  /4 FLL_DIV_3 = 1 1  /8

## Slide 30: System clocks (22/24)
Internal clock signals:
  In 2xx family clock system = the basic clock module+:
    Support for a 32768 Hz watch crystal oscillator;
    Internal very-low-power low-frequency oscillator;
    Internal digitally-controlled oscillator (DCO) stable <1 μs.
  The BCM+ provides the following clock signals:
      Auxiliary clock (ACLK), sourced either from:
        32768 Hz watch crystal;
        Internal oscillator LFXT1CLK in LF mode with an internal load capacitance of 6 pF.
      Main clock (MCLK), the system clock used by the CPU;
      Sub-Main clock (SMCLK), the sub-system clock used by the peripheral modules.

## Slide 31: System clocks (23/24)
Internal clock signals:
  Both MCLK and SMCLK are sourced from DCOCLK at ~1.1 MHz but can be sourced up to 16 MHz;
  2xx DCO calibration data (in flash info memory segment A).
DCO frequency | Calibration register | Size | Address
1 MHz | CALBC1_1MHZ CALBC0_1MHZ | Byte Byte | 010FFh 010FEh
8 MHz | CALBC1_8MHZ CALBC0_8MHZ | Byte Byte | 010FDh 010FCh
12 MHz | CALBC1_12MHZ CALBC0_12MHZ | Byte Byte | 010FBh 010FAh
16 MHz | CALBC1_16MHZ CALBC0_16MHZ | Byte Byte | 010F9h 010F8h

## Slide 32: System clocks (24/24)
Internal clock signals:
  Electrical characteristics vary over the recommended supply voltage range of between 2.2 V and 3.6 V. Higher DCO frequencies require higher supply voltages.
  Typical characteristics in active mode supply current for the (2xx family):

## Slide 33: Interrupt management (1/8)
<number>
Copyright 2008 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Interrupts:
  Are events applied to the application program that force a detour in program flow;
  Cause CPU subprogram execution (ISR);
  When Interrupt Service Routine (ISR) ends, the program flow returns to the previous state.
  There are three classes of interrupts:
    Reset;
    Interrupts not maskable by GIE;
    Interrupts maskable by GIE.

## Slide 34: Interrupt management (2/8)
<number>
Copyright 2008 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The interrupts are used to:
  Allow a CPU fast response to a specific event;
  Avoiding continuous polling for rare events;
  Minimal disruption to the processing of other tasks.
In GIE-maskable interrupts, if both peripheral interrupt enable bit and GIE are set, when an interrupt is requested, it calls the ISR;
The interrupt latency time:
  t between the event beginning and the ISR execution;
  Interrupt latency time starts with acceptance of IR and counting until starting of first instruction of ISR.

## Slide 35: Interrupt management (3/8)
During an interrupt event:
  PC of the next instruction and the SR are pushed onto the stack;
  Afterwards, the SR is cleared with exception of SCG0, along with the appropriate interrupt, disabling interrupts (reset the GIE flag);
  Other ISRs will not be called.
The RETI instruction at the end of the ISR will return to the original program flow, automatically popping the SR and PC;
Ensure that:
  The ISR processing time is less than the interrupt’s request time interval;
  To avoid stack overflow -> application program collapse.

## Slide 36: Interrupt management (4/8)
Types of interrupts (internal and external):
  Reset;
  Interrupts not maskable by GIE: (non)-maskable interrupts (NMI);
  Interrupts maskable by GIE.
  Interrupts priority (The nearer a module is to the CPU/NMIRS, the higher the priority).

## Slide 37: Interrupt management (5/8)
Types of interrupts (internal and external):
  Main differences between non-maskable and maskable interrupts:
    Non-maskable interrupts cannot be disabled by the GIE bit of the SR. Used for high priority events e.g. emergency shutdown;
    Maskable interrupts are recognized by the CPU’s interrupt control, so the GIE bit must be set. Can be switched off by software.
  The system reset interrupts (Oscillator/Flash and the Hard Reset) are treated as highest priority non-maskable interrupts, with their own interrupt vectors.

## Slide 38: Interrupt management (6/8)
Types of interrupts (internal and external):
  Non Maskable Interrupts:
    Not masked by GIE;
    Enabled by individual interrupt enable bits;
    Depend on the event source:
      NMIIE: Non-Maskable Interrupts Interrupt Enable:
        RST/NMI is configured in NMI mode;
        WDTNMIES bit generates an NMI;
        The RST/NMI flag NMIIFG is also set.
      ACCVIE: ACCess Violation to the flash memory Interrupt Enable:
        The flash ACCVIFG flag is set.
      OFIE: Oscillator Fault Interrupt Enable:
        This signal can be triggered by a PUC signal.

## Slide 39: Interrupt management (7/8)
Types of interrupts (internal and external):
  Non Maskable Interrupts:
    Example: ACCVIE (2xx family).
    ACCV=1  ACCVIFG=1
    ACCVIFG=1 and ACCVIE=1 (set by software)  NMIRS=1

## Slide 40: Interrupt management (8/8)
Types of interrupts (internal and external):
  (by GIE) Maskable Interrupts:
    Peripherals with interrupt capability or the watchdog timer overflow in interval timer mode;
    Individual enable/disable flag, located in peripheral registers or in the individual module;
    Can be disabled by resetting the GIE bit in SR, either by software or by hardware/interrupt.

## Slide 41: Watchdog timer (WDT and WDT+) (1/4)
The 16-bit WDT module can be used in:
  Supervision mode:
    Ensure the correct working of the software application;
    Perform a PUC;
    Generate an interrupt request after the counter overflows.
  Interval timer:
    Independent interval timer to perform a “standard” interrupt upon counter overflow periodically;
    Upper counter (WDTCNT) is not directly accessible by software;
    Control and the interval time selecting WDTCTL register;
    WDTCNT: clock signal ACLK or SMCLK (WDTSSEL bit).

## Slide 42: Watchdog timer (WDT and WDT+) (2/4)
The WDT control is performed through the:
  WDTCTL, Watchdog Timer Control Register, WDTCTL
    Eight MSBs (WDTPW): Password function, read as 0x69h, write as 0x5Ah unless the user want to force a PUC from software.
15 |  |  |  |  |  |  | 8
Read with the value 0x69h, WDTPW write with the value 0x5Ah |  |  |  |  |  |  | 

## Slide 43: Watchdog timer (WDT and WDT+) (3/4)
The WDT control is performed through the:
  WDTCTL, Watchdog Timer Control Register, WDTCTL
    Eight LSBs: WDT configuration
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
WDTHOLD | WDTNMIES | WDTNMI | WDTTMSEL | WDTCNTCL | WDTSSEL | WDTIS1 | WDTIS0
Bit |  | Description
7 | WDTHOLD | WDT hold when WDTHOLD = 1. Useful for energy economy.
6 | WDTNMIES | Select the NMI interrupt edge when WDTNMI = 1 WDTNMIES = 0  NMI on rising edge WDTNMIES = 1  NMI on falling edge
5 | WDTNMI | Select the RST/NMI pin function WDTNMI = 0  Reset function WDTNMI = 1  NMI function
4 | WDTTMSEL | Select the WDT mode: WDTTMSEL = 0  Supervision mode WDTTMSEL = 1  Interval timer mode
3 | WDTCNTCL | WDT counter clear: WDTCNTCL = 0  No action WDTCNTCL = 1  Counter initialization at 0x0000h
2 | WDTSSEL | Select the WDT clock signal: WDTSSEL = 0  SMCLK WDTSSEL = 1  ACLK
1-0 | WDTISx | Select the WDT timer interval: WDTIS1 WDTIS0 = 0 0  Clock signal / 32768 WDTIS1 WDTIS0 = 0 1  Clock signal / 8192 WDTIS1 WDTIS0 = 1 0  Clock signal / 512 WDTIS1 WDTIS0 = 1 1  Clock signal / 64

## Slide 44: Watchdog timer (WDT and WDT+) (4/4)
The WDT uses two bits in the Special Function Registers (SFRs) for interrupt control:
    WDTIE: WDT interrupt enable (IE1.0):
      Enables the WDTIFG interrupt for interval timer mode when WDTIE=1.
    WDTIFG: WDT interrupt flag (IFG1.0):
      Supervision mode:
        WDTIFG sources a reset vector interrupt.
        If WDTIFG=1, the WDT initiates the reset condition (detectable reset source).
      Interval mode:
        WDTIFG set after the selected time interval and requests a WDT interval timer interrupt;
        WDTIE and GIE bits set;
        WDTIFG reset automatically (also can be reset by software).

## Slide 45: Supervisory Voltage System (SVS) (1/2)
Used to monitor:
  AVCC supply voltage;
  External voltage (located at the SVSIN input).
When AVCC or SVSIN drops below selected threshold:
  Sets a flag generating an interrupt;
  Generates a system reset (POR).
Is disabled after a BOR to conserve current consumption;
SVS features:
    Output of SVS comparator accessible by software;
    Low-voltage condition latched (accessible by software);
    14 selectable threshold levels;
    External channel to monitor external voltage.

## Slide 46: Supervisory Voltage System (SVS) (2/2)
SVS control performed by:
  SVSCTL, SVS Control Register
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
VLDx |  |  |  | PORON | SVSON | SVSOP | SVSFG
Bit |  | Description
7-4 | VLDx | Voltage level detect. VLD3 VLD2 VLD1 VLD0 = 0000  SVS is off VLD3 VLD2 VLD1 VLD0 = 0001  1.9 V VLD3 VLD2 VLD1 VLD0 = 0010  2.1 V . . . VLD3 VLD2 VLD1 VLD0 = 1101  3.5 V VLD3 VLD2 VLD1 VLD0 = 1110  3.7 V VLD3 VLD2 VLD1 VLD0 = 1111  SVSIN to 1.25V
3 | PORON | When PORON = 1 enables the SVSFG flag to cause a POR device reset
2 | SVSON | This bit reflects the status of SVS operation, being set (SVSON=1) when the SVS is on
1 | SVSOP | This bit reflects the output value of the SVS comparator: SVSOP = 0  SVS comparator output is low SVSOP = 1  SVS comparator output is high
0 | SVSFG | When SVSFG=1 a low voltage condition occurs

## Slide 47: Low power operating modes (1/11)
One of the main features of the MSP430 families:
  Low power consumption (about 1 mW/MIPS or less);
  Important in battery operated embedded systems.
Low power consumption is only accomplished:
  Using low power operating modes design;
  Depends on several factors such as:
    Clock frequency;
    Ambient temperature;
    Supply voltage;
    Peripheral selection;
    Input/output usage;
    Memory type;
    ...

## Slide 48: Low power operating modes (2/11)
Low power modes (LPM):
  6 operating modes;
  Configured by the SR bits: CPUOFF, OSCOFF, SCG1, SCG0.
  Active mode (AM) - highest power consumption:
    Configured by disabling the SR bits described above;
    CPU is active;
    All enabled clocks are active;
    Current consumption: 250 A.
  Software selection up to 5 LPM of operation;
  Operation:
    An interrupt event can wake up the CPU from any LPM;
    Service the interrupt request;
    Restore back to the LPM.

## Slide 49: Low power operating modes (3/11)
Low power modes (LPM):
  Example: Typical current consumption (41x family).

## Slide 50: Low power operating modes (4/11)
Low power modes (LPM):
Mode | Current | SR bits configuration |  |  |  | Clock signals |  |  | Oscillator | 
 |  [A] | CPUOFF | OSCOFF | SCG1 | SCG0 | ACLK | SMCLK | MCLK | DCO | DC gen.
Low-power mode 0 (LPM0) | 35 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1
Low-power mode 1 (LPM1) | 44 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 1*
Low-power mode 2 (LPM2) | 19 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1
Low-power mode 3 (LPM3) | 0.8 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0
Low-power mode 4 (LPM4) | 0.1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
*DCO’s DC generator is enabled if it is used by peripherals.

## Slide 51: Low power operating modes (5/11)
Low power modes (LPM) characteristics:
  LPM0 to LPM3:
    Periodic processing based on a timer interrupt;
    LPM0: Both DCO source signal and DCO’s DC gen.;
    LPM0 and LPM1: Main difference between them is the condition of enable/disable the DCO’s DC generator;
    LPM2: DCO’s DC generator is active and DCO is disabled;
    LPM3: Only the ACLK is active (< 2 μA).
  LPM4:
    Externally generated interrupts;
    No clocks are active and available for peripherals.
    Reduced current consumption (0.1 μA).

## Slide 52: Low power operating modes (6/11)
Program flow steps:
  Enter Low-power mode:
    Enable/disable CPUOFF, OSCOFF, SCG0, SCG1 bits in SR;
    LPM is active after writing to SR;
    CPU will suspend the program execution;
    Disabled peripherals:
      Operating with any disabled clock;
      Individual control register settings.
    All I/O port pins and RAM/registers are unchanged;
    Wake up is possible through any enabled interrupt.

## Slide 53: Low power operating modes (7/11)
Program flow steps:
  An enabled interrupt event wakes the MSP430;
  Enter ISR:
    The operating mode is saved on the stack during ISR;
    The PC and SR are stored on the stack;
    Interrupt vector is moved to the PC;
    The CPUOFF, SCG1, and OSCOFF bits are automatically reset, enabling normal CPU operation;
    IFG flag cleared on single source flags.
  Returning from the ISR:
    The original SR is popped from the stack, restoring the previous operating mode;
    The SR bits stored in the stack are modified returning to a different operating mode after RETI instruction.

## Slide 54: Low power operating modes (8/11)
Examples of applications development using the MSP430 with and without low power modes consideration:
Example | Without low power mode | With low power mode
Toggling the bit 0 of port 1 (P1.0) periodically | Endless loop (100 % CPU load) | LPM0 Watchdog timer interrupt
UART to transmit the received message at a 9600 baud rate | Polling UART receive (100 % CPU load) | UART receive interrupt (0.1 % CPU load)
Set/reset during a time interval, periodically, of the peripheral connected to the bit 2 of port 1 (P1.2) | Endless loop (100 % CPU load) | Setup output unit (Zero CPU load)
Power manage external devices like Op-Amp | Putting the OPA Quiescent (Average current: 1 A) | Shutdown the Op-Amp between data acquisition (Average current: 0.06 A)
Power manage internal devices like Comparator A | Always active (Average typical current: 35 A) | Disable Comparator A between data acquisition
Respond to button-press interrupt in P1.0 and toggle LED on P2.1 | Endless loop (100 % CPU load) | Using LPMs while the LED is switch off: LPM3: 1.4 A LPM4: 0.3 A Configure unused ports in output direction P1 interrupt service routine

## Slide 55: Low power operating modes (9/11)
Rules of thumb for the configuration of LP applications:
  Extended ultra-low power standby mode. Maximize LPM3;
  Minimum active duty cycle;
  Performance on-demand;
  Use interrupts to control program flow;
  Replace software with on chip peripherals;
  Manage the power of external devices;
  Configure unused pins properly, setting them as outputs to avoid floating gate current.

## Slide 56: Low power operating modes (10/11)
Rules of thumb for LP applications configuration:
  Low-power efficient coding techniques:
    Optimize program flow;
    Use CPU registers for calculations and dedicated variables;
    Same code size for word or byte;
    Use word operations whenever possible;
    Use the optimizer to reduce code size and cycles;
    Use local variable (CPU registers) instead of global variables (RAM);
    Use bit mask instead of bit fields;

## Slide 57: Low power operating modes (11/11)
Rules of thumb for LP applications configuration:
  Low-power efficient coding techniques:
    Use unsigned data types where possible;
    Use pointers to access structures and unions;
    Use “static const” class to avoid run-time copying of structures, unions, and arrays;
    Avoid modulo;
    Avoid floating point operations;
    Count down “for” loops;
    Use short ISRs.

## Slide 58: Quiz (1/4)
1. The operating mode of the MSP430 is:
  (a) Determined by the program counter (PC) register;
  (b) Determined by the state of the CPU;
  (c) Determined by four control bits in the status register (SR);
  (d) All of above.
2. The MSP430 clock system control registers of the 2xx family hardware development tools (eZ430-F2013 and eZ430-RF2500) are:
  (a) Registers R4 to R9;
  (b) Register BCSCTL1, BCSCTL2 and DCOCTL;
  (c) Registers SCFQCTL, SCFI0, SCFI1 and FLL_CTL0;
  (d) Registers R13, R14 and R15.

## Slide 59: Quiz (2/4)
3. If the XTS bit in the BCSCTL1 control register is enabled:
  (a) The LFXT1 oscillator in the clock system can operate with a high-frequency crystal;
  (b) The LFXT1 oscillator is OFF;
  (c) The LFXT1 oscillator in the clock system can operate with a low-frequency crystal;
  (d) The XT2 oscillator is enabled.
4. When the SELS bit in the FLL_CTL1 control register of the MSP430FG4618 is reset:
  (a) The DCOCLK is OFF;
  (b) The SMCLK is divided by 8;
  (c) The source for the SMCLK clock is LFXT1 oscillator;
  (d) The source for the SMCLK clock is DCOCLK.

## Slide 60: Quiz (3/4)
5. In the MSP430, when the watchdog timer control bit WDTTMSEL is set:
  (a) The watchdog timer is an interval timer;
  (b) The watchdog timer is inactive;
  (c) Clears the watchdog timer counter;
  (d) Restarts the watchdog timer.
6. The 16 bit WDTCTL control register must have:
  (a) All its high byte bits at 0;
  (b) A 0x069h value in the high byte when WDTCTL is read and a 0x05Ah password must be written in the high byte to write to WDTCL;
  (c) A 0x05Ah password in the high byte to read and write to WDTCL;
  (d) All its bits of the high byte are 1.

## Slide 61: Quiz (4/4)
Answers:
  1. (c) Determined by four control bits in the status register (SR).
  2. (b) Register BCSCTL1, BCSCTL2 and DCOCTL.
  3. (a) The LFXT1 oscillator in the clock system can operate with a high-frequency crystal.
  4. (d) The source for the SMCLK clock is DCOCLK.
  5. (a) The watchdog timer is an interval timer.
  6. (b) A 0x069h value in the high byte when WDTCTL is read and a 0x05Ah password must be written in the high byte to write to WDTCL.