## Slide 1: Chapter 7 Timers Description of clock signals
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
<footer> Copyright 2008 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt

## Slide 2: Contents
Introduction to timers
Clock signals available on the hardware development kits
Basic Timer1
Timer_A and Timer_B:
  Operating modes
  Reset
  Registers
  Cap/Com blocks
  Output modes
  Timer_A Cap/Com registers
  Interrupts
  Timer_B special features
  Timer_B register special bits
Quiz

## Slide 3: Introduction (1/3)
Correct system timing is a fundamental requirement for the proper operation of a real-time application;
If the timing is incorrect, the input data may be processed after the output was updated;
The clock implementations vary among devices in the MSP430 family;
Each device provides different clock sources, controls and uses;
This chapter discusses the clock controls provided by the various MSP430 hardware platforms.

## Slide 4: Introduction (2/3)
MSP430x4xx family:
  Two general purpose 16-bit or 8-bit counters and event timers: Timer_A, Timer_B;
  Basic Timer 1 (MSP430x4xx devices).
MSP430x2xx family:
  Also has Timer_A and Timer_B, as above;
  Basic Clock Module+.
The timers may be driven from an internal or external clock;
Timer_A and Timer_B also include multiple independent capture and compare blocks, with interrupt capabilities;
The capture and compare blocks are suited to applications such as:
  Time events;
  Pulse Width Modulator (PWM).

## Slide 5: Introduction (3/3)
The system timing is fundamental to nearly every embedded application;
The main applications of timers are to:
    Generate events of fixed time-period;
    Allow periodic wakeup from sleep of the device;
    Count transitional signal edges;
    Replacing delay loops with timer calls allows the CPU to sleep between operations, thus consuming less power.

## Slide 6: Clock signals
The clock signals are controlled by two sets of registers (4xx family):
  The first set of registers configures the low-frequency signals for use by peripheral modules:
    Basic Timer Control Register (BTCTL);
    Basic Timer Counter 1 (BTCNT1);
    Basic Timer Counter 2 (BTCNT2).
  The second set of registers is dedicated to the configuration of general-purpose system clocks:
    System Clock Control (SCFQCTL);
    System Clock Frequency Integrator 0 (SCFI0);
    System Clock Frequency Integrator 1 (SCFI1);
    Frequency Locked Loop control registers (FLL+CTL0, FLL+CTL1).

## Slide 7: Basic Timer1 (1/5)
The Basic Timer 1 module consists of two independent 8-bit timers:
  Basic Timer 1 Counter 1 (BTCNT1);
  Basic Timer 1 Counter 2 (BTCNT2).
These can be used in cascade to form a 16-bit timer (software selectable by BTCTL register configuration);
The main characteristics of this module are:
    Clock for a Liquid Crystal Display (LCD) module;
    Suitable for a Real-Time Clock (RTC) implementation;
    Basic interval timer;
    Simple interrupt capability.

## Slide 8: Basic Timer1 (2/5)
The control registers determine the operation of the Basic Timer 1 module:
    BTCNT1 (Read/write 8 bit register) - Generate the fLCD:
      Clock source: ACLK;
      Frame frequency selectable by software (BTFRFQx):
      fLCD = ACLK/x.
    BTCNT2 (Read/write 8-bit register) - Programmable frequency divider to provide periodic CPU interrupts and/or a RTC system.
      3 possible clock sources:
        ACLK
        SMCLK
        ACLK/256 - cascaded with BTCNT1 (BTSSEL and BTDIV bits in the BTCTL register);
      Sources the Basic Timer1 interrupt, BTIFG, with interval selected by BTIPx bits.

## Slide 9: Basic Timer1 (3/5)
Block diagram:

## Slide 10: Basic Timer1 (4/5)
Registers:
  BTCTL, Basic Timer 1 Control Register
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
BTSSEL | BTHOLD | BTDIV | BTFRFQ1 | BTFRFQ0 | BTIP2 | BTIP1 | BTIP0
Bit |  | Description
7 | BTSSEL | BTCNT2 clock select (together with the BTDIV bit)
6 | BTHOLD | Basic Timer 1 hold: BTHOLD = 0  BTCNT1 and BTCNT2 active BTHOLD = 1  BTCNT1 hold, if BTDIV = 1 BTHOLD = 1  BTCNT1 and BTCNT2 hold
5 | BTDIV | Basic Timer 1 clock divider: BTSSEL BTDIV = 0 0  ACLK BTSSEL BTDIV = 0 1  ACLK/256 BTSSEL BTDIV = 1 0  SMCLK BTSSEL BTDIV = 1 1  ACLK/256
4-3 | BTFRFFQx | LCD frame frequency: BTFRFQ1 BTFRFQ0 = 0 0  fACLK/32 BTFRFQ1 BTFRFQ0 = 0 1  fACLK/64 BTFRFQ1 BTFRFQ0 = 1 0  fACLK/128 BTFRFQ1 BTFRFQ0 = 1 1  fACLK/256
2-0 | BTIPX | Basic Timer 1 interrupt interval: BTIP2 BTIP1 BTIP0 = 0 0 0  fCLK2 / 2 BTIP2 BTIP1 BTIP0 = 0 0 1  fCLK2 / 4 BTIP2 BTIP1 BTIP0 = 0 1 0  fCLK2 / 8 BTIP2 BTIP1 BTIP0 = 0 1 1  fCLK2 / 16 BTIP2 BTIP1 BTIP0 = 1 0 0  fCLK2 / 32 BTIP2 BTIP1 BTIP0 = 1 0 1  fCLK2 / 64 BTIP2 BTIP1 BTIP0 = 1 1 0  fCLK2 / 128 BTIP2 BTIP1 BTIP0 = 1 1 1  fCLK2 / 256

## Slide 11: Basic Timer1 (5/5)
Registers:
  IE2, Interrupt Enable Register 2
  IFG2, Interrupt Flag Register 2
7 |  |  |  |  |  |  | 0
BTIE |  |  |  |  |  |  | 
Bit |  | Description
7 | BTIE | Basic Timer 1 interrupt enable when BTIE = 1
7 |  |  |  |  |  |  | 0
BTIFG |  |  |  |  |  |  | 
Bit |  | Description
7 | BTIFG | Basic Timer 1 interrupt flag BTIFG = 1 when interrupt pending

## Slide 12: Timer_A and Timer_B Introduction (1/6)
Timer A and B are two general-purpose 16-bit counter/event timers;
There are slight differences between the two timers;
Features common to both timers include:
  Asynchronous 16-bit timer/counter with four operating modes:
    Timer_A length: 16 bits;
    Timer_B length: programmable: 8, 10, 12, or 16 bits.
    Timer/counter register, TAR (Timer_A) or TBR (Timer_B) -from now on described as TxR- increments or decrements (depending on mode of operation) with each rising edge of the clock signal;
    The timer can generate an interrupt when it overflows;
    Wide interrupt interval range: 1/MCLK to 32 seconds.

## Slide 13: Timer_A and Timer_B Introduction (2/6)
  Choice of selectable and configurable clock source:
    ACLK;
    SMCLK;
    External - via TACLK or INCLK (TASSELx bits);
    The selected clock source may additionally be divided by 2, 4, or 8 (IDx bits configuration).
  Configurable capture/compare registers:
    Timer_A has 3 or 5 capture/compare registers;
    Timer_B has 3 or 7 capture/compare registers;
    Timer_B capture/compare registers can be grouped.

## Slide 14: Timer_A and Timer_B Introduction (3/6)
  Configurable outputs and internal connections to several other modules:
    Faster response;
    No cycles are wasted while the Interrupt Service Routine ( ISR) loads/executes;
    Avoids CPU wakeup;
    Saves power.
    Outputs capability: Pulse Width Modulation (PWM);
    Comparator_A;
    Direct Memory Access (DMA);
    Digital-to-Analogue Converter (DAC12).

## Slide 15: Timer_A and Timer_B Introduction (4/6)
  Asynchronous input and output latching:
    Timer_A Capture/Compare (Cap/Com) registers are not buffered, being updated immediately when written to;
    Timer_B Cap/Com registers are double-buffered with synchronized loading.
  Interrupt vector register for fast decoding of all Timer_A and Timer_B interrupts:
    TACCR0 (or TBCCR0) interrupt vector for TACCR0 (or TBCCCR0) CCIFG;
    TAIV (or TBIV) interrupt vector for the remaining CCIFG flags and TAIFG (or TBIFG).

## Slide 16: Timer_A and Timer_B Introduction (5/6)
  Block diagram (Timer_A):

## Slide 17: Timer_A and Timer_B Introduction (6/6)
  Timers have four modes of operation:
    MCx bits (Timer_A or Timer_B Control Register)
MCx | Mode | Description
0 0 | Stop | The timer is halted
0 1 | Up | Up counting mode (from 0x0000 to the value in the TACCR0 or TBCCR0 register)
1 0 | Continuous | Continuous counting mode (from 0x0000 to 0xFFFF)
1 1 | Up/down | Up/down counting mode (from 0x0000 to the value in the TACCR0 or TBCCR0 register and back down to zero)

## Slide 18: Timer_A and Timer_B operating modes (1/3)
Up mode:
  TxR counts up till it reaches the value in the TxCCR0 register;
  TxR->TxCCR0: TACCR0 interrupt flag, CCIFG, is set;
  TxR=TxCCR0: EQU0 = 1 (restarts counting in TxR);
  TxCCR0->0: TxIFG interrupt flag is set:
    Interrupt period:
    tINT = 1/[fCLK/Prescaler/(TxCCR0+1)].

## Slide 19: Timer_A and Timer_B operating modes (2/3)
Continuous mode:
  TxR counts up till it reaches 0xFFFF (65536 counts);
  TxR=0xFFFF: TxR counting from zero (next clock pulse);
  0xFFFF->0: TxIFG interrupt flag is set:
    Interrupt period: tINT = 1/[fCLK/Prescaler/65536];
  (Correct only for TAR; for TBR 4 different end values. See User’s Guide for additional details).

## Slide 20: Timer_A and Timer_B operating modes (3/3)
Up/down mode:
  TxR counts up till it reaches the value in the TxCCR0 register;
  TxCCR0-1 -> TxCCR0: Interrupt flag, CCIFG, is set;
  TxR=TxCCR0: Counting is inverted;
  0x0001->0x0000: Interrupt flag TxIFG is set:
    Interrupt period: tINT = 1/[fCLK/Prescaler/(TxCCR02];

## Slide 21: Timer_A and Timer_B reset
The timers can be reset by the following actions:
  Writing 0 in the TxR register;
  Writing 0 in the TxCCR0 register, provided that the timer is not in continuous mode;
  Setting the TxCLR bit in the Timer Control Register (TxCTL).

## Slide 22: Timer_A and Timer_B registers
TACTL, Timer_A Control Register
15 |  |  |  |  | 10 | 9 | 8
Unused |  |  |  |  |  | TASSEL1 | TASSEL0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
ID1 | ID0 | MC1 | MC0 | Unused | TACLR | TAIE | TAIFG
Bit |  | Description
9-8 | TASSELx | Timer_A clock source: TASSEL1 TASSEL0 = 0 0  TACLK TASSEL1 TASSEL0 = 0 1  ACLK TASSEL1 TASSEL0 = 1 0  SMCLK TASSEL1 TASSEL0 = 1 1  INCLK
7-6 | IDx | Clock signal divider: ID1 ID0 = 0 0  / 1 ID1 ID0 = 0 1  / 2 ID1 ID0 = 1 0  / 4 ID1 ID0 = 1 1  / 8
5-4 | MCx | Clock timer operating mode: MC1 MC0 = 0 0  Stop mode MC1 MC0 = 0 1  Up mode MC1 MC0 = 1 0  Continuous mode MC1 MC0 = 1 1  Up/down mode
2 | TACLR | Timer_A clear when TACLR = 1
1 | TAIE | Timer_A interrupt enable when TAIE = 1
0 | TAIFG | Timer_A interrupt pending when TAIFG = 1

## Slide 23: Timer_A and Timer_B Cap/Com blocks (1/5)
Timer_A (and Timer_B) contain independent capture and compare blocks, TACCRx (or TBCCRx);
These blocks may be used to capture timer register contents, as they are at the time of an event, or to generate an event when the timer register contents correspond to the capture/compare register contents, e.g. to generate time intervals;
The setting of capture/compare is selected by the mode bit CAP in the individual Capture/Compare Control registers, TACCTLx (or TBCCTLx)

## Slide 24: Timer_A and Timer_B Cap/Com blocks (2/5)
Capture mode:
  Used to measure the period of time events with minimal CPU intervention.
  Procedure:
    Set the CAP bit to select capture mode;
    Set the SCS bit to synchronize the capture with the next timer clock (recommended to avoid race conditions);
    The input signal is sampled by the CCIxA (or CCIxB) input, selected by the CCISx bits in the Capture/Compare Control Register, TACCTLx (or TBCCTLx);

## Slide 25: Timer_A and Timer_B Cap/Com blocks (3/5)
    The capture edge of the input signal (rising, falling, or both) is selected by the CMx bits;
    When a valid edge is detected on the selected input line, the value in the Timer register is latched into the TACCRx (or TBCCRx) register, providing a time mark for the event;
    The interrupt flag CCIFG is set;
    The bit COV (=1) controls an overflow event when a second capture is performed, before the value from the first capture is read.

## Slide 26: Timer_A and Timer_B Cap/Com blocks (4/5)
Compare mode:
  Used for pulse generation or generation of interrupts at specific time intervals (PWM output signals).
  Procedure:
    Reset the CAP bit to select compare mode;
    TxR counts up to the value programmed in the TxCCRx register;
    When the timer value is equal to the value in the TxCCRx register, an interrupt is generated:
      Interrupt flag CCIFG is set;
      Internal signal EQUx = 1 (where x is the number of the CCR channel).

## Slide 27: Timer_A and Timer_B Cap/Com blocks (5/5)
    EQUx affects the output compare signal OUTx according to the output mode (defined by the OUTMODx bits in the TxCCTL;
    The input signal CCI is latched into SCCI.
Output operating modes uses:
  Modes 2, 3, 6 and 7: PWM output signals;
  Mode 3: active PWM signal at low state;
  Mode 7: active PWM signal at high state;
  Modes 2 and 6: complementary PWM signals;
  Modes 1 and 5: single event generation;
  Mode 4: signal with 1/2 frequency of the timer signal.

## Slide 28: Timer_A and Timer_B Output modes (1/2)
Output operating modes (OUTMODx bits):
OUTMODx | Mode | Description
0 0 0 | Output | The output signal OUTx is defined by the bit OUTx
0 0 1 | Set | OUTx = 1  timer = TxCCRx OUTx = 0  timer = 0 or until another output mode is selected and affects the output
0 1 0 | Toggle/Reset | OUTx = toggle  timer = TxCCRx OUTx = 0  timer = TxCCR0
0 1 1 | Set/Reset | OUTx = 1  timer = TxCCRx OUTx = 0  timer = TxCCR0
1 0 0 | Toggle | OUTx = toggle  timer = TxCCRx The output period is double the timer period
1 0 1 | Reset | OUTx = 0  timer = TxCCRx OUTx = 1  another output mode is selected and affects the output
1 1 0 | Toggle/Set | OUTx = toggle  timer = TxCCRx OUTx = 1  timer = TxCCR0
1 1 1 | Reset/Set | OUTx = 0  timer = TxCCRx OUTx = 1  timer = TxCCR0

## Slide 29: Timer_A and Timer_B Output modes (2/2)
Output examples:

## Slide 30: Timer_A Cap/Com registers (1/2)
TACCTLx, Timer_A Cap/Com Control Register
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8
CM1 | CM0 | CCIS1 | CCIS0 | SCS | SCCI | Unused | CAP
Bit |  | Description
15-14 | CMx | Capture mode: CM1 CM0 = 0 0  No capture CM1 CM0 = 0 1  Capture on rising edge CM1 CM0 = 1 0  Capture on falling edge CM1 CM0 = 1 1  Capture on both edges
13-12 | CCISx | Capture/compare input select: CCIS1 CCIS0 = 0 0  CCIxA CCIS1 CCIS0 = 0 1  CCIxB CCIS1 CCIS0 = 1 0  GND CCIS1 CCIS0 = 1 1  Vcc
11 | SCS | Synchronize capture input signal with timer clock: SCS = 0  Asynchronous capture SCS = 1  Synchronous capture
10 | SCCI | Synchronized capture/compare input
8 | CAP | Mode: Capture mode  CAP = 1 Compare mode  CAP = 0

## Slide 31: Timer_A Cap/Com registers (2/2)
TACCTLx, Timer_A Cap/Com Control Register
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OUTMOD2 | OUTMOD1 | OUTMOD0 | CCIE | CCI | OUT | COV | CCIFG
Bit |  | Description
7-5 | OUTMODx | Output mode: OUTMOD2 OUTMOD1 OUTMOD0 = 0 0 0  bit OUT OUTMOD2 OUTMOD1 OUTMOD0 = 0 0 1  Set OUTMOD2 OUTMOD1 OUTMOD0 = 0 1 0  Toggle/Reset OUTMOD2 OUTMOD1 OUTMOD0 = 0 1 1  Set / Reset OUTMOD2 OUTMOD1 OUTMOD0 = 1 0 0  Toggle OUTMOD2 OUTMOD1 OUTMOD0 = 1 0 1  Reset OUTMOD2 OUTMOD1 OUTMOD0 = 1 1 0  Toggle / Set OUTMOD2 OUTMOD1 OUTMOD0 = 1 1 1  Reset / Set
4 | CCIE | Capture/compare interrupt enable when CCIE = 1.
3 | CCI | Capture/compare input
2 | OUT | Output state
1 | COV | Capture overflow when COV = 1
0 | CCIFG | Capture/compare interrupt flag CCIFG = 1 when interrupt pending

## Slide 32: Timer_A and Timer_B Interrupts (1/3)
Interrupt characteristics:
  Capture mode:
    Any CCIFG flag is set when a timer value is captured in the associated TxCCRx register.
  Compare mode:
    Any CCIFG flag is set if TxR counts up to the TxCCRx value.
    Software may also set or clear a CCIFG flag;
    All CCIFG flags request an interrupt when their corresponding CCIE bit and GIE bit are set.

## Slide 33: Timer_A and Timer_B Interrupts (2/3)
Interrupt vectors associated with Timer_A:
  TACCR0 interrupt vector for TACCR0 CCIFG:
    TACCR0 CCIFG flag has the highest priority Timer_A interrupt;
    The TACCR0 CCIFG flag is automatically reset when the TACCR0 interrupt request is serviced.

## Slide 34: Timer_A and Timer_B Interrupts (3/3)
Interrupt vectors associated with Timer_A (continued):
  TAIV interrupt vector for TACCR1 CCIFG to TACCR4 CCIFG and TAIFG:
    Flags are given priority and combined to source a single interrupt vector (decreasing priority);
    TAIV determines which flag requests the interrupt;
    Disabling interrupts do not affect the value in TAIV;
    Any access (read/write) of TAIV automatically resets the highest pending interrupt flag;
    If another interrupt flag is set, another interrupt is immediately generated after servicing the initial interrupt.

## Slide 35: Timer_B special features (1/3)
Programmable length of the TBR register (equivalent to TAR in Timer_A) to be 8, 10, 12, or 16 bits:
  Configurable through selection of the CNTLx bits in TBCTL (equivalent to TACTL in Timer_A);
  The maximum count value, TBR(maximum), for the selectable lengths is 0FFh, 03FFh, 0FFFh, and 0FFFFh, respectively;
Three or seven capture/compare blocks TBCCRx;

## Slide 36: Timer_B special features (2/3)
Double-buffered compare latches with synchronized loading:
  In Timer_A, the signal generation in compare mode may cause noise during compare period updates because the TACRRx value is used directly to compare with the timer value;
  To avoid this condition, the compare latches TBCLx, buffered by TBCCRx, holds the data for the comparison to the timer value in compare mode;
  The CLLDx bits at the TBCCTLx register configure the timing of the transfer from TBCCRx to TBCLx.

## Slide 37: Timer_B special features (3/3)
Grouping channels capability:
  Multiple compare latches may be grouped together for simultaneous updates of the TBCLGRPx bits;
  Two conditions are required:
    All TBCCRx registers must be updated;
    The load event controlled by the CLLDx bits must occur.
All outputs can be put into a high-impedance state:
  TBOUTH = 1 puts Timer_B outputs into a high-impedance state, allowing higher security and lower delay time responding to failures.
The SCCI bit function is not implemented.

## Slide 38: Timer_B registers special bits (1/2)
TBCTL, Timer_B Control Register
15 | 14 |  | 13 | 12 | 11 | 10 | 9 | 8
Unused | TBCLGRP1 | TBCLGRP0 |  | CNTL1 | CNTL0 | Unused | TBSSEL1 | TBSSEL0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
ID1 | ID0 | MC1 | MC0 | Unused | TBCLR | TBIE | TBIFG
Bit |  | Description
14-13 | TBCLGRPx | TBCLx group: TBCLGRP1 TBCLGRP0 = 0 0  Each TBCLx latch loads independently TBCLGRP1 TBCLGRP0 = 0 1  TBCL1+TBCL2 (update control: TBCCR1 CLLDx)  TBCL3+TBCL4 (update control: TBCCR3 CLLDx)  TBCL5+TBCL6 (update control: TBCCR5 CLLDx)  TBCL0 independent TBCLGRP1 TBCLGRP0 = 1 0  TBCL1+TBCL2+TBCL3 (update control: TBCCR1 CLLDx)  TBCL4+TBCL5+TBCL6 (update control: TBCCR4 CLLDx)  TBCL0 independent TBCLGRP1 TBCLGRP0 = 1 1  TBCL0+TBCL1+TBCL2+TBCL3+TBCL4+TBCL5+TBCL6 (update control: TBCCR1 CLLDx)
12-11 | CNTLx | Counter Length: CNTL1 CNTL0 = 0 0  16-bit, TBR(max) = 0FFFFh CNTL1 CNTL0 = 0 1  12-bit, TBR(max) = 0FFFh CNTL1 CNTL0 = 1 0  10-bit, TBR(max) = 03FFh CNTL1 CNTL0 = 1 1  8-bit, TBR(max) = 0FFh

## Slide 39: Timer_B registers special bits (2/2)
TBCCTLx, Timer_B Capture/Compare Control Register
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8
CM1 | CM0 | CCIS1 | CCIS0 | SCS | CLLD1 | CLLD0 | CAP
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OUTMOD2 | OUTMOD1 | OUTMOD0 | CCIE | CCI | OUT | COV | CCIFG
Bit |  | Description
10-9 | CLLDx | Compare latch load: CLLD1 CLLD0 = 0 0  TBCLx loads on write to TBCCRx CLLD1 CLLD0 = 0 1  TBCLx loads when TBR counts to 0 CLLD1 CLLD0 = 1 0  TBCLx loads when TBR counts: - to 0 (up/continuous mode); - to TBCL0 or to 0 (up/down mode) CLLD1 CLLD0 = 1 1  TBCLx loads when TBR counts: - to TBCLx

## Slide 40: Quiz (1/4)
1. The timer/counter suitable for LCD controller frame frequency generation in the MSP430FG4618 is:
  (a) Timer_A;
  (b) BTCNT2;
  (c) Timer_B;
  (d) BTCNT1.
2. To set Timer_A to repeatedly count from 0x000 to 0xFFFF, the operating mode selected must be:
  (a) Up/Down mode (MCx = 3);
  (b) Up mode (MCx = 1);
  (c) Continuous (MCx = 2);
  (d) Stop (MCx = 0).

## Slide 41: Quiz (2/4)
3. The Timer_A configured in continuous operating mode is reset with:
  (a) Write 0xFFFF to TAR register;
  (b) Reset TACCR0;
  (c) Set TACLR bit in the TACTL register;
  (d) None of the above.
4. When TASSELx = 1, the timer (Timer_A or Timer_B) is sourced by:
  (a) ACLK;
  (b) TACLK;
  (c) INCLK;
  (d) SMCLK.

## Slide 42: Quiz (3/4)
5. To generate a PWM signal with an active high state it is necessary to configure the output operating mode as:
  (a) Mode 2;
  (b) Mode 3;
  (c) Mode 6;
  (d) Mode 7.
6. In the case where Timer_A is sourced by the ACLK (32768 Hz) and is configured in compare mode, the value in TACCR0 register to enable interrupts once every second must be:
  (a) 32768;
  (b) 32767;
  (c) 16384;
  (d) 65536.

## Slide 43: Quiz (4/4)
Answers
  1. (d) BTCNT1.
  2. (c) Continuous (MCx = 2).
  3. (c) Set TACLR bit in the TACTL register.
  4. (a) ACLK.
  5. (d) Mode 7.
  6. (b) 32767.