## Slide 1: Chapter 8 LCD Controller
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
<footer> Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt

## Slide 2: Contents
LCD Controller Introduction
LCD_A Controller Operation
LCD modes
LCD_A Controller Registers
Laboratory 4: LCD Message Display
Quiz

## Slide 3: Introduction (1/3)
Both the ’3xx and ’4xx families provide controllers for liquid crystal displays (LCDs):
  LCD_A controller: MSP430x42x0 and MSP430FG461x;
  LCD controller: All MSP430x4xx.
Example of LCD_A controller: Experimenter’s board;
Features:
  Display memory;
  Automatic signal generation;
  Configurable frame frequency;
  Blinking capability;
  Support for 4 types of LCDs:
    Static;
    2-mux, 1/2 bias (or 1/3 bias);
    3-mux, 1/3 bias (or 1/2 bias);
    4-mux, 1/3 bias (or 1/2 bias).

## Slide 4: Introduction (2/3)
Main differences between LCD and LCD_A controllers:
  LCD controller:
    Requires external circuitry (a resistor-divider network) to generate the 4 externally supplied voltage levels (R03, R13, R23 and R33) that supply the voltage generator;
    Uses the timing generator derived from Basic Timer 1.
  LCD_A controller:
    Similar features as LCD controller, but in addition:
      Regulated charge pump and contrast control by software;
      Fractional LCD biasing voltages (sourced internally or externally);
      Uses the ACLK to generate the timing for common and segment lines.

## Slide 5: Introduction (3/3)
LCD_A controller block diagram:

## Slide 6: LCD_A Controller Operation (1/7)
Can be configured to:
  Use external circuitry to generate the 4 externally supplied voltage levels (R03, R13, R23 and R33), which supply the voltage generator;
  Use the internal LCD Bias Generator to generate the fractional LCD biasing voltages, V2 − V5 independent of the source for VLCD:
      R33  V1: full-scale voltage (VLCD);
      R23  V2: 2/3 of full scale;
      V3: 1/2 of full scale;
      R13  V4: 1/3 of full scale;
      R03  V5: ground.

## Slide 7: LCD_A Controller Operation (2/7)
LCD_A voltage and bias generation:
  Both the peak output waveform voltage V1, as well as the fractional LCD biasing voltages V2 − V5 can be sourced externally:
    OSCOFF = 0: Oscillator sourcing ACLK off;
    LCDON = 0: LCD_A module in inactive;
  To use the internal voltage generation:
    OSCOFF = 1: Oscillator sourcing ACLK set;
    LCDON = 1: LCD_A module active;
    VLCD may be sourced internally from AVCC or by an internal charge pump.

## Slide 8: LCD_A Controller Operation (3/7)
LCD voltage and biasing characteristics LCD_A controller:
The LCD_A controller uses the ACLK (32768 Hz) prescaler selected using the LCDFREQx bits;
LCD frequency, fLCD, depends on:
  Framing frequency, fframe;
  Multiplex rate, mux (defined on the LCD specifications).
LCD frequency: fLCD = 2 × mux × fframe

## Slide 9: LCD_A Controller Operation (4/7)
LCD_A voltage selection:
  VLCD source:
    AVCC requires:
      VLCDEXT = 0;
      VLCDx = 0;
      VREFx = 0.
    Internal charge pump sourced from DVCC requires:
      VLCDEXT = 0;
      VLCDPEN = 1;
      VLCDx > 0 (software selectable LCD voltage from 2.60 V to 3.44 V (typical) independent of DVCC);
      Connect a 4.7 F capacitor between LCDCAP pin and ground.

## Slide 10: LCD_A Controller Operation (5/7)
LCD_A Bias Generation block diagram:

## Slide 11: LCD_A Controller Operation (6/7)
LCD_A Bias Generation:
  External fractional LCD biasing voltages, V2 − V5:
    REXT = 1;
    External equally weighted resistor divider (100 k to 1 M);
    VLCDEXT = 0:
      The VLCD voltage is sourced from the internal charge pump, with R33 providing a switched-VLCD output;
      Otherwise (VLCDEXT = 1), R33 provides a VLCD input.
    R03EXT = 1: V5 is sourced externally.

## Slide 12: LCD_A Controller Operation (7/7)
LCD_A Bias Generation:
  Internal bias generator:
    When LCD2B = 1, supports 1/2 bias LCDs;
    When LCD2B = 0, supports 1/3 bias LCDs in 2-mux, 3-mux, and 4-mux modes. In static mode, the internal divider network is disabled;
    For LCD devices that share the LCDCAP, R33, and R23 functions, the charge pump cannot be used with an external resistor divider using 1/3 biasing;
    When R03 is not available externally, V5 is always set to AVSS.

## Slide 13: LCD Modes (1/6)
LCD_A controller supports 4 types of LCDs:
  Static:
    Each MSP430 segment pin drives:
      One LCD segment.
    One common line driven by COM0.
    Capacity to drive 32 segments.
  2-mux, 1/2 bias (or 1/3 bias):
    Each MSP430 segment pin drives:
      Two LCD segments;
    Two common lines driven by COM0 and COM1.
    Capacity to drive 64 segments.

## Slide 14: LCD Modes (2/6)
LCD_A controller supports 4 types of LCDs:
  3-mux, 1/3 bias (or 1/2 bias):
    Each MSP430 segment pin drives:
      Three LCD segments;
    Three common lines driven by COM0, COM1, and COM2.
    Capacity to drive 90 segments.
  4-mux, 1/3 bias (or 1/2 bias):
    Each MSP430 segment pin drives:
      Four LCD segments;
    Four common lines driven by COM0, COM1, COM2, and COM3.
    Capacity to drive 120 segments.

## Slide 15: LCD Modes (3/6)
Static LCD:
  One pin for each segment;
  One pin for the backplane.
  Features:
    High contrast ratio;
    Large number of pins.

## Slide 16: LCD Modes (4/6)
2-mux LCD:
  Reduced pin count;
  LCD segments multiplexed:
    Matrix of segments;
    Two common pins (COM0 and COM1).
  Example: 2-mux;

## Slide 17: LCD Modes (5/6)
3-mux LCD
  1 segment pin to drive:
    3 LCD segments;
    3 common lines (COM0 to COM2).
  Example: 3-mux, 1/3 bias.

## Slide 18: LCD Modes (6/6)
4-mux LCD
  1 segment pin to drive:
    4 LCD segments;
    4 common lines (COM0 to COM3).
  Example: 4-mux, 1/3 bias.

## Slide 19: LCD_A Controller Registers (1/4)
LCDACTL, LCD_A Control Register

## Slide 20: LCD_A Controller Registers (2/4)
LCDAPCTL1, LCD_A Port Control Register 1
LCDAPCTL0, LCD_A Port Control Register 0
Bit |  | Description
7 | LCDS28 | LCD Segment 28 to 31 Enable.
6 | LCDS24 | LCD Segment 24 to 27 Enable.
5 | LCDS20 | LCD Segment 20 to 23 Enable.
4 | LCDS16 | LCD Segment 16 to 19 Enable.
3 | LCDS12 | LCD Segment 12 to 15 Enable.
2 | LCDS8 | LCD Segment 8 to 11 Enable.
1 | LCDS4 | LCD Segment 4 to 7 Enable.
0 | LCDS0 | LCD Segment 0 to 3 Enable.

## Slide 21: LCD_A Controller Registers (3/4)
LCDAVCTL0, LCD_A Voltage Control Register 0

## Slide 22: LCD_A Controller Registers (4/4)
LCDAVCTL1, LCD_A Voltage Control Register 1
Bit |  | Description
4 - 1 | VLCDx | Charge pump voltage select: VLCD3 VLCD2 VLCD1 VLCD0 = 0000  Disable. VLCD3 VLCD2 VLCD1 VLCD0 = 0001  VLCD = 2.60 V. VLCD3 VLCD2 VLCD1 VLCD0 = 0010  VLCD = 2.66 V. VLCD3 VLCD2 VLCD1 VLCD0 = 0011  VLCD = 2.72 V. VLCD3 VLCD2 VLCD1 VLCD0 = 0100  VLCD = 2.78 V. VLCD3 VLCD2 VLCD1 VLCD0 = 0101  VLCD = 2.84 V. VLCD3 VLCD2 VLCD1 VLCD0 = 0110  VLCD = 2.90 V. VLCD3 VLCD2 VLCD1 VLCD0 = 0111  VLCD = 2.96 V. VLCD3 VLCD2 VLCD1 VLCD0 = 1000  VLCD = 3.02 V. VLCD3 VLCD2 VLCD1 VLCD0 = 1001  VLCD = 3.08 V. VLCD3 VLCD2 VLCD1 VLCD0 = 1010  VLCD = 3.14 V. VLCD3 VLCD2 VLCD1 VLCD0 = 1011  VLCD = 3.20 V. VLCD3 VLCD2 VLCD1 VLCD0 = 1100  VLCD = 3.26 V. VLCD3 VLCD2 VLCD1 VLCD0 = 1101  VLCD = 3.32 V. VLCD3 VLCD2 VLCD1 VLCD0 = 1110  VLCD = 3.38 V. VLCD3 VLCD2 VLCD1 VLCD0 = 1111  VLCD = 3.44 V.

## Slide 23: Laboratory 4: LCD Message Display (1/18)
Summary:
  This laboratory utilises the MSP430FG4618 LCD_A controller supplied with the Experimenter’s board;
  This application performs a demonstration of the LCD, activating the various LCD segments.
A. Resources:
  The LCD display on the Experimenter’s board does not have its own LCD controller;
  This operation is provided by MSP430FG4618;
  The interface between these two components is described in the Experimenter’s Board datasheet.

## Slide 24: Laboratory 4: LCD Message Display (2/18)
A. Resources (continued):
  Connections between the MSP430FG4618 and the Softbaugh LCD SBLCDA4.

## Slide 25: Laboratory 4: LCD Message Display (3/18)
A. Resources (continued):
  Softbaugh LCD SBLCDA4 segments description.

## Slide 26: Laboratory 4: LCD Message Display (4/18)
A. Resources (continued):
  Softbaugh LCD SBLCDA4 segments display.

## Slide 27: Laboratory 4: LCD Message Display (5/18)
A. Resources (continued):
  Use the LCD in 4-mux mode;
  Use the charge pump;
  The segments shared with the I/O function are not used by the LCD, being made by the connection to the S4 to S25 segments;
  The four lines COM1, COM2, and COM3 are shared by ports P5.2, P5.3 and, P5.4, respectively. The COM0 line is also used;
  The pins R03, R13, R23 and LCDCAP/R33 are used to provide the V5, V4, V3, V2 and V1 (VLCD) voltages using an external resistors network and are available at Header H5.

## Slide 28: Laboratory 4: LCD Message Display (6/18)
A. Resources (continued):
  Use low power mode 3 (LPM3);
  Timer_A together with the TACCR0 unit are used to generate an interrupt once per second;
  The LED1 and LED2 are switched at each Timer_A interrupt;
  The button SW1 is used to change the value of voltage generated by the charge pump;
  The button SW2 is used to change the LCD frequency.

## Slide 29: Laboratory 4: LCD Message Display (7/18)
B. Software application organization:
  The application starts by configuring the Ports P5.2, P5.3 and P5.4 to the special function COM1, COM2 and COM3, respectively;
  The function COM0 is not shared with the digital I/O functions;
  Pins with multiplexed functions are selected to perform the control of the LCD segments;
  The LCD_A control register and the voltage configuration register are also configured.

## Slide 30: Laboratory 4: LCD Message Display (8/18)
B. Software application organization (continued):
  Execute the LCD clear routine LCD_all_off();
  Timer_A TACCRO unit is configured to generate an interrupt once every second;
  This ISR supplies the memory clock with msec, sec and min, and also connects/disconnects the remaining LCD symbols;
  The port pins P2.1 and P2.2 monitor the condition of LED2 and LED1, respectively;
  These ports are configured as digital outputs.

## Slide 31: Laboratory 4: LCD Message Display (9/18)
B. Software application organization (continued):
  The SW1 and SW2 buttons are configured to generate an interrupt when a change of state occurs at ports P1.0 and P1.2 respectively;
  This ISR modifies the LCD operation frequency or modifies the VLCD voltage, depending on the ISR source;
  Finally, all interrupts are activated and the system enters low power mode LPM3.

## Slide 32: Laboratory 4: LCD Message Display (10/18)
C. System configuration:
  LCD_A interface for LCD configuration:
    Select the function COM1, COM2 and COM3;
    What is the value to be written to these registers?
    P5DIR | = _______________;
    P5SEL | =________________;
    The LCD segments are controlled by the S4 to S25 LCD memory segments;
    Activate these segments by writing the correct value to the register:
    LCDAPCTL0 = _____________;

## Slide 33: Laboratory 4: LCD Message Display (11/18)
C. System configuration (continued):
  LCD operation frequency:
    In 4-mux mode, the LCD is refreshed by a signal with a frequency between 30 Hz to 100 Hz;
    The following expression is used to determine the LCD operation frequency, fLCD:
    fLCD = 2 x mux x fframe
    Choose the frequency that provides the best power savings.

## Slide 34: Laboratory 4: LCD Message Display (12/18)
C. System configuration (continued):
  LCD_A configuration:
    The LCD_A module is activated with the refresh frequency just described;
    What value should be written to the register?
    LCDACTL = ________________________;
    Use the charge pump to internally generate the voltages necessary for the operation of the LCD, using a 1/3 bias. What is the value to be written to the register?
    LCDAVCTL0 = ______________________;
    The charge pump is required to generate a LCD voltage of 3.44 V. Configure the register:
    LCDAVCTL1 = ______________________;

## Slide 35: Laboratory 4: LCD Message Display (13/18)
C. System configuration (continued):
  Timer_A configuration:
    The Timer_A generates an interrupt once every second. It uses the TACCR0 unit;
    Configure the following registers:
    TACCTL0 = ________________________;
    TACCR0 = _________________________;
    TACTL = __________________________;
  Output ports configuration:
    Configure the ports connected to LED1 and LED2 in order that at system start up, one port is active and the other is inactive:
    P2DIR | = _______________________;
    P2OUT | = _______________________;

## Slide 36: Laboratory 4: LCD Message Display (14/18)
C. System configuration (continued):
  Input ports configuration:
    The buttons SW1 and SW2 generate an interrupt on a low-to-high transition;
    Configure the registers as required:
    P1DIR |= _______________________;
    P1IES = ________________________;
    P1IE |= ________________________;

## Slide 37: Laboratory 4: LCD message presentation (15/18)
<number>
Copyright 2008 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Operation analysis:
  Compile the project, load it into microcontroller’s memory and execute the application;
  For each value of the operating frequency and voltage generated by the charge pump, measure the electrical current consumption;
  Draw a graph of these results and draw conclusions concerning the energy consumption.

## Slide 38: Laboratory 4: LCD Message Display (16/18)
<number>
Copyright 2008 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
LCD_A interface with the LCD configuration:
  P5DIR |= 0x1E; // Ports P5.2, P5.3, P5.4 as outputs
  P5SEL |= 0x1E; // Ports P5.2, P5.3 and P5.4 as
  // special function (COM1, COM2, COM3)
  LCDAPCTL0 = LCDS24|LCDS20|LCDS16|LCDS12|LCDS8|LCDS4;
  // Enable S4 to S25
MSP-EXP430FG4618 | SOLUTION
Configure the LCD_A controller of the MSP430FG4618 device of the Experimenter’s board to display a message in the display. | 

## Slide 39: Laboratory 4: LCD Message Display (17/18)
<number>
Copyright 2008 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
LCD operation frequency:
  LCDACTL = LCDFREQ_192 | LCD4MUX; // (ACLK = 32768)/192
  // 4-mux LCD
LCD_A configuration:
  LCDACTL |= LCDSON | LCDON; // LCD_A on
  // Segments on
  LCDAVCTL0 = LCDCPEN; // Charge pump enable
  LCDAVCTL1 = VLCD_3_44; // VLCD = 3.44 V
Timer_A configuration:
  TACCTL0 = CCIE; // TACCR0 interrupt enabled
  TACCR0 = 3268; // this count correspond to 1 msec
  TACTL = TASSEL_1 + MC_1 + ID_0; // ACLK, up mode

## Slide 40: Laboratory 4: LCD Message Display (18/18)
<number>
Copyright 2008 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Output ports configuration:
  P2DIR |= 0x06; // P2.1 and P2.2 as output
  P2OUT |= 0x04; // LED2 off and LED1 on
Input ports configuration:
  P1DIR &= ~0x03; // P1.0 and P1.1 digital inputs
  P1IES |= 0x03; // low-to-high transition interrupts
  P1IE |= 0x03; // enable port interrupts

## Slide 41: Quiz (1/4)
1. The fractional LCD biasing voltage V2, corresponds to which of the following fractions of full scale voltage:
  (a) 1;
  (b) 1/2;
  (c) 2/3;
  (d) 1/3.
2. To blink the LCD, the following LCD_A control register bit must be set:
  (a) LCDON;
  (b) LCDSON;
  (c) LCDCPEN;
  (d) LCD2B.

## Slide 42: Quiz (2/4)
3. To source the fractional LCD biasing voltages externally:
  (a) Reset OSCOFF and LCDON bits;
  (b) Set OSCOFF bit;
  (c) Reset LCDON bit;
  (d) Set OSCOFF and LCDON bit.
4. To configure a LCD refresh frequency to approximately once every 10 milliseconds:
  (a) LCDMXx = 1;
  (b) LCD2B = 1;
  (c) LCDFREQx = 3;
  (d) LCDFREQx = 7.

## Slide 43: Quiz (3/4)
5. An LCD with 3-mux, 1/3 bias configuration requires that:
  (a) LCDMXx = 2 and COM = 3;
  (b) LCD2B = 0;
  (c) All of the above;
  (d) None of the above.
6. An LCD with 3-mux, 1/2 bias is able to control:
  (a) 90 segments;
  (b) 160 segments;
  (c) 140 segments;
  (d) 64 segments.

## Slide 44: Quiz (4/4)
Solution
  (c) 2/3.
  2. (b) LCDSON.
  3. (a) Reset OSCOFF and LCDON bits.
  4. (d) LCDFREQx = 7.
  5. (c) All of the above.
  6. (a) 90 segments.