## Slide 1: Chapter 9 Data Acquisition A/D Conversion Introduction
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Notes: <number>

## Slide 2: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Introduction to Analogue-to-Digital Conversion
ADC Specifications
  DC performance
  AC performance
ADC Architectures
Quiz

## Slide 3: Analogue-to-Digital Conversion (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The analogue world (the real one) interfaces with digital systems through ADCs;
The ADC takes the voltage from the acquisition system (after signal conditioning) and converts it to an equivalent digital code;
The ADC ideal transfer function
for a 3 bit ADC is given by:
The digital code can be displayed, processed, stored or transmitted.

## Slide 4: Analogue-to-Digital Conversion (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
There are sufficient analogue peripherals in a number of MSP430 family devices to realize a complete signal chain;
Analogue class of applications:
  Is more or less defined by bandwidth range;
  Require an established resolution range.

## Slide 5: ADC Specifications (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Resolution, R:
  The smallest change to the analogue voltage that can be converted into a digital code;
  The Least Significant Bit (LSB):
  The resolution only specifies the width of the digital output word, not the performance;
  Most MSP430 devices offer a high-precision ADC:
      Slope;
      10, 12 or 14 Bit SAR;
      16 Bit Sigma-Delta.

## Slide 6: ADC Specifications (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Accuracy:
  Degree of conformity of a digital code representing the analogue voltage to its actual (true) value;
  Can express as the “degree of truth”.

## Slide 7: ADC Specifications (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Performance:
  Depends on the following specifications:
    Speed;
    Accuracy, also depends on the circuitry type:
      DC:
        Differential Non-Linearity (DNL);
        Integral Non-Linearity (INL);
        Offset error,
        Gain error…
      AC:
        Signal-to-noise ratio (SNR);
        Signal-to-noise and distortion ratio (SINAD);
        Total harmonic distortion (THD);
        Spurious-free dynamic range (SFDR)…

## Slide 8: ADC Specifications – DC performance (1/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Differential Non-Linearity (DNL):
  Determines how far an output code is from a neighbouring output code. The distance is measured as a VIN converted to LSBs;
  No DNL error requires that:
    as the VIN is swept over its
    range, all output code
    combinations will appear
    at the converter output;
  DNL error < ± 1 LSB
    ensures no missing codes.

## Slide 9: ADC Specifications – DC performance (2/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Integral Non-Linearity (INL):
  Is the integral of the DNL errors;
  Represents the difference between the measured converter result and the ideal transfer-function value.

## Slide 10: ADC Specifications – DC performance (3/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DNL, INL and noise impact on the dynamic range:
  INL, DNL and Noise errors cover the entire range;
  Impact on the Effective Number of Bits (ENOB);
  Not easily calibrated or corrected;
  Affects accuracy.

## Slide 11: ADC Specifications – DC performance (4/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Offset error:
  In bipolar systems, the offset error shifts the transfer function but does not reduce the number of available codes.

## Slide 12: ADC Specifications – DC performance (5/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Gain error:
  Full-scale error minus the offset error, measured at the last ADC transition on the transfer-function curve and compared with the ideal ADC transfer function;
  May (or not) include errors in the voltage reference of the ADC.

## Slide 13: ADC Specifications – DC performance (6/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Offset and gain errors impact on the dynamic range:

## Slide 14: ADC Specifications – DC performance (7/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Offset (a) and gain (b) errors calibration:
  Bipolar systems:
    Shift the analogue input (x) and digital output (y) axes of the transfer function so that the negative full-scale point aligns with the zero point:
    y = a + (1+b) x
    Apply zero volts to the ADC input and perform a conversion. The conversion result represents the bipolar zero offset error. Perform a gain adjustment.

## Slide 15: ADC Specifications – DC performance (8/9)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Offset (a) and gain (b) errors calibration:
  Unipolar systems:
    Previous methodology is applicable if the offset is positive;
    Gain error can be corrected by software considering a linear function in terms of the ideal transfer function slope (m1) and measured (m2):
    y = (m1/m2) x
Both offset and gain errors reduction techniques will imply partial loss of the ADC range.

## Slide 16: ADC Specifications – DC performance (9/9)
<number>
Copyright 2008 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Code-Edge Noise: Amount of noise that appears right at a code transition of the transfer function;
Voltage Reference (internal or external): Besides the settling time, the source of the reference voltage errors is related to the following specifications:
  Temperature drift: Affects the performance of an ADC converter based on resolution;
  Voltage noise: Specified as either an RMS value or a peak-to-peak value;
  Load regulation: Current drawn by other components will affect the voltage reference;
  Temperature effects (offset drift and gain drift).

## Slide 17: ADC Specifications – AC performance (1/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
AC parameters:
  Harmonics occur at multiples of the input frequency:

## Slide 18: ADC Specifications – AC performance (2/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Signal-to-noise ratio (SNR):
  Signal-to-noise ratio without distortion components;
  Determines where the average noise floor of the converter is, setting an ADC performance limit for noise.

## Slide 19: ADC Specifications – AC performance (3/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Signal-to-noise ratio (SNR):
  For an n bit ADC sine wave input is given by:
  Can be improved with oversampling:
    Lowers the average noise floor of the ADC;
    Spreads the noise over more frequencies (equalise total noise).

## Slide 20: ADC Specifications – AC performance (4/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Signal-to-noise ratio (SNR):
  Oversampling an ADC is a common principle to increase resolution;
  It reduces the noise at any one frequency point.
  A 2x oversampling reduces the noise floor by 3 dB, which corresponds to a ½ bit resolution increase;
  Oversampling by k times provides a SNR given by:

## Slide 21: ADC Specifications – AC performance (5/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Signal-to-noise and distortion ratio (SINAD):
  Similar to SNR;
  Includes the harmonic content [total harmonic distortion], from DC to the Nyquist frequency;
  Is defined as the ratio of the RMS value of an input sine wave to the RMS value of the noise of the converter;
  Writing the equation in terms of n, provides the number of bits that are obtained as a function of the RMS noise (effective number of bits, ENOB):

## Slide 22: ADC Specifications – AC performance (6/6)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Total harmonic distortion (THD):
  Gets increasingly worse as the input frequency increases;
  Primary reason for ENOB degradation with frequency is that SINAD decreases as the frequency increases toward the Nyquist limit, SINAD decreases.
Spurious-free dynamic range (SFDR):
  Defined as the ratio of the RMS value of an input sine wave to the RMS value of the largest trace observed in the frequency domain using a FFT plot;
  If the distortion component is much larger than the signal of interest, the ADC will not convert small input signals, thus limiting its dynamic range.

## Slide 23: ADC Architectures (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
There are many different ADC architectures:
  Successive Approximation (SAR);
  Sigma Delta (SD or );
  Slope or Dual Slope;
  Pipeline;
  Flash...as in quick, not memory.

## Slide 24: ADC Architectures (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The selection of an MSP430 ADC will depend on:
  Voltage range to be measured;
  Maximum frequency for AIN;
  Minimum resolution needed vs. analogue input variation;
  The need for differential inputs;
  Voltage reference range;
  The need for multiple channels for different analogue inputs.

## Slide 25: ADC Architectures (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC architectures included in the MSP430 devices populated in the hardware development tools:
  10 Bit SAR: MSP430F2274  eZ430-RF2500;
  12 Bit SAR: MSP430FG4618  Experimenter’s board;
  16 Bit Sigma-Delta: MSP430F2013  eZ430-F2013 and Experimenter’s board.

## Slide 26: ADC Architectures (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Further information concerning ADC fundamentals and applications can found on the TI website:
  Introduction to MSP430 ADCs <slap115.pdf>
  Understanding Data Converters <slaa013.pdf>
  A Glossary of Analogue-to-Digital Specifications and Performance Characteristics <sbaa147a.pdf>
  Optimized Digital Filtering for the MSP430 <slap108.pdf>
  Efficient MSP430 Code Synthesis for an FIR Filter <slaa357.pdf>
  Working with ADCs, OAs and the MSP430 <slap123.pdf>
  Hands-On: Using MSP430 Embedded Op Amps <slap118.pdf>
  Oversampling the ADC12 for Higher Resolution <slaa323.pdf>
  Hands-on Realizing the MSP430 Signal Chain through ADPCM <slap122.pdf>
  Amplifiers and Bits: An Introduction to Selecting Amplifiers for Data Converters <sloa035b.pdf>

## Slide 27: Quiz (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
9. The performance of an ADC is expressed by which specifications:
  (a) Speed, Accuracy, Signal-to-noise ratio (SNR) and distortion ratio (SINAD);
  (b) Offset and gain errors, and Signal-to-noise ratio (SNR);
  (c) Integral (INL) and Differential Non-Linearities (DNL) and Total harmonic distortion (THD);
  (d) All of the above.
10. Oversampling means:
  (a) An ADC performance parameter to limit noise;
  (b) Sampling at a rate much higher than the signal of interest;
  (c) To increase the resolution;
  (d) All of the above.

## Slide 28: Quiz (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
11. A low cost, low power consuming application that requires a 12 bit resolution with a 100 Hz output data rate should use an ADC with the architecture:
  (a) Slope;
  (b) Sigma-Delta;
  (c) SAR;
  (d) Flash.

## Slide 29: Quiz (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Answers:
  9. (d) All of the above.
  10. (d) All of the above.
  11. (a) Slope.