## Slide 1: Chapter 9 Data Acquisition Comparator-Based Slope ADC
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Notes: <number>

## Slide 2: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Comparator-Based Slope ADC:
  Single- and dual- slope ADC
  Resistive sensors measurements
  Voltage measurements

## Slide 3: Single and Dual Slope ADC (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Single Slope architecture:
  The simplest form of analogue-to-digital converter uses integration;
  Method:
    Integration of unknown input voltage;
    Value comparison with a known reference value;
    The time it takes for the two voltages to become equal is proportional to the unknown voltage.
  Drawbacks:
    The accuracy of this method is dependent on the tolerance of the passive elements (resistors and capacitors), which varies with the environment, resulting in low measurement repeatability.

## Slide 4: Single and Dual Slope ADC (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Dual Slope architecture:
  Overcomes the difficulties of the single slope method;
  Method:
    Unknown Vinput integration, for a fixed time, tint;
    Back-integration of known VREF for a variable time, tback_int.

## Slide 5: Single and Dual Slope ADC (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The dual slope method requires:
  Switch;
  Clock;
  Timer;
  Comparator.
Resolution: depends on the clock frequency and ramp duration;
Some MSP430 devices have no true ADC, but they do have analogue comparator module (comparator_A) that can be used to implement a low power slope ADC;
Comparator_A is present on the MSP430FG4618 (Experimenter’s board).

## Slide 6: Resistive Sensors Measurements (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Comparator_A can be used to measure resistive elements using single slope A/D conversion;
Thermistor: Resistor with RM varying according to T;
Schematic diagram of the measurement system:

## Slide 7: Resistive Sensors Measurements (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
MSP430 configuration:
  2 digital I/O pins (Px.x; Px.y): Charge and discharge CM;
  I/O set to output high (VCC) to charge CM, reset to discharge;
  I/O switched to high-Z input with CAPDx set when not in use;
  One output charges and discharges the capacitor via RREF;
  The other output discharges capacitor via RM;
  (+) terminal is connected to the + terminal of the capacitor;
  (–) terminal is connected to ref. level (ex. VCAREF=0.25xVCC);
  An output filter should be used to minimize switching noise;
  CAOUT used to gate Timer_A CCI1B, capturing tCM_discharge.

## Slide 8: Resistive Sensors Measurements (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Ratiometric conversion principle:
  Charge/Discharge timing for temperature measurement system:

## Slide 9: Resistive Sensors Measurements (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Slope resistance measurement considerations:
  Measurement as accurate as RREF;
  VCC independent;
  Resolution based on number of maximum counts;
  Precharge of CM impacts accuracy (although there are methods to avoid errors by precharge);
  Slope measurement time duration a function of RC;

## Slide 10: Voltage Measurements (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Comparator_A module’s application: Voltage measurement using single slope A/D conversion;
Relies on the charge/discharge of C:
  Capacitor charge: VSS < VM < VCAREF;
  Capacitor discharge: VCAREF < VM < VSS;
  Time capture to crossing using Timer_A (TACCR1);
    1st: Compare to VCAREF;
    2nd: Compare to VM.

## Slide 11: Voltage Measurements (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Voltage conversion and timing depends on:
  1 Measurement:
    VREF must be stable;
    RC tolerances influence measurements.
  2 Measurements: ;
    Same approach for discharge method.

## Slide 12: Voltage Measurements (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Slope voltage measurement considerations:
  The VCAREF selection should maximize VM range;
  Accuracy of result depends on VCC;
  Capacitor charge selection for minimum error time (7 time constant = 0.1% Error from VCC).