## Slide 1: Chapter 9 Data Acquisition Comparator_A
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Notes: <number>

## Slide 2: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Introduction to Comparator_A
Features
Voltage reference generator
Comparator_A interrupts
Comparator_A registers
Lab5D: Signal Acquisition
Quiz

## Slide 3: Introduction to Comparator_A (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Comparator_A module is primary designed to support:
  Low cost precision slope A/D conversions;
    Resistance measurement;
    Voltage measurement;
    Current measurement;
    Capacitance measurements..
    Requires few external components;
  Battery-voltage supervision;
  Monitoring of external analogue signals.
It is used on the FG4618 device (Experimenter’s board).

## Slide 4: Introduction to Comparator_A (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Comparator_A block diagram:

## Slide 5: Comparator_A Features
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Comparator_A features:
  Multiplexed inverting and non-inverting inputs;
  Software selectable low-pass filter (RC) for the output;
  Outputs:
    Timer_A capture input;
    Interrupt (one interrupt vector with enable): CAIFG;
    External: GPIO.
  Software control of the port input buffer;
  Selectable references, external or internal (reference voltage generator):
      VCAREF = 0.25 VCC;
      VCAREF = 0.5 VCC;
      VCAREF = ~0.55 V (diode);
  Comparator and reference generator can be powered down.

## Slide 6: Comparator_A components
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Comparator:
  Compares the analogue voltages at the (+) and (–) input terminals (CA0 and CA1 for a non-inverting topology);
  The comparator output:
    CAOUT = 1: CA0 > CA1;
    CAOUT = 0: CA0 < CA1 and CAON = 0 (switched off).
Analogue input switches (selected with P2CAx bits):
  Individually connect or disconnect the two comparator input terminals to associated port pins.
Output filter (CAF bit):
  Use the internal low pass filter to reduce errors (in accuracy and resolution) associated with comparator oscillation.

## Slide 7: Comparator_A interrupts
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
One interrupt flag, CAIFG, and one interrupt vector are associated with Comparator_A;
Condition for an interrupt:
  CAIFG = 1:
    Rising or falling edge at comparator output (CAIES bits);
    Interrupt request when CAIE = 1 and GIE = 1.
  CAIFG = 0:
    Interrupt request serviced;
    Reset by software.

## Slide 8: Comparator_A (1/2) Registers
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
CACTL1, Comparator_A Control Register 1
Bit |  | Description
7 | CAEX | Comparator_A exchange: CAEX = 1  Exchanges the comparator inputs and inverts the comparator output.
6 | CARSEL | Comparator_A reference: CAEX = 0: CAEX = 1: CARSEL = 0 VCAREF in + terminal VCAREF in - terminal CARSEL = 1 VCAREF in - terminal VCAREF in + terminal
5-4 | CAREFx | Comparator_A voltage reference: CAREF1 CAREF0 = 00  External (Internal reference off) CAREF1 CAREF0 = 01  VCAREF = 0.25 VCC CAREF1 CAREF0 = 10  VCAREF = 0.5 VCC CAREF1 CAREF0 = 11  VCAREF = 0.55 V (Diode reference)
3 | CAON | Comparator_A on when CAON = 1
2 | CAIES | Comparator_A interrupt edge: CAIES = 0  Rising edge CAIES = 1  Falling edge
1 | CAIE | Comparator_A interrupt enable when CAIE = 1
0 | CAIFG | The Comparator_A interrupt flag, CAIFG = 1 when an interrupt is pending

## Slide 9: Comparator_A (2/2) Registers
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
CACTL2, Comparator_A Control Register 2
CAPD, Comparator_A Port Disable Register
  The 8-bit CAPD register allows individual enable or disable of each P1.x pin buffer, when the corresponding CAPDx = 0 or CAPDx = 1 values respectively are configured.

## Slide 10: Lab5D: Voltage signal comparison
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Objective:
  With the Comparator_A module included in the MSP430FG4618 of the Experimenter´s board hardware development tool, perform a comparison of an external voltage signal with the internal reference.
Details:
  Like the previous exercise (Lab4), this one is composed of several sub-tasks.
  This laboratory has been developed for the Code Composer Essentials version 3 software development tool only.

## Slide 11: Lab5D: Voltage signal comparison
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Project files:
  C source files: Chapter 9 > Lab5 > Lab5D_student.c
  Solution file: Chapter 9 > Lab5 > Lab5D_solution.c
Overview:
  This laboratory analyses the operation of Comparator_A.
  A voltage is applied to one of the comparator inputs, generated either by the DAC12 or by another external source;
  Whenever the external voltage value is higher than the compare value internally generated, an interrupt is generated that switches the LED state.

## Slide 12: Lab5D: Voltage signal comparison
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  The resources used by the application are:
    DAC12;
    Comparator_A;
    Digital IO;
    Timer_A.

## Slide 13: Lab5D: Voltage signal comparison
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  The application starts by stopping the Watchdog Timer;
  Timer_A is configured to generate an interrupt once every 1 msec, with the output of the DAC12 updated in order to provide a ramp signal;
  The Comparator_A’s output is configured to be accessible at pin P6.6, which is available at the Header 4 pin 7;
  The signal applied to CA0 input is compared with 0.5xVcc internal reference voltage;
  Every time that a compare match occurs, an interrupt is requested and switches the state of LED1.

## Slide 14: Lab5D: Voltage signal comparison
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  Comparator_A configuration:
  Configure the registers in order to receive the external signal at the CA0 input and compare it with the internal reference 0.5xVcc;
  Enable the comparator with an interrupt triggered in a low-to-high transition of the comparator output.
  CACTL1 = _____________________;
  CACTL2 = _____________________;

## Slide 15: Lab5D: Voltage signal comparison
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  The verification of this laboratory experiment can be accomplished by connecting the output of the DAC12, available on Header 8 pin 7, to the Comparator_A’s input CA0, available on Header 4 pin 7;
  Monitor the signals wave form at the input of the Comparator_A input and output using an oscilloscope;
  LED1 switches state whenever the input voltage value is lower than the compare value.

## Slide 16: Lab5D: Voltage signal comparison
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Comparator_A configuration:
CACTL1 = CAON + CAREF_2 + CARSEL; // Enable comp,
// ref = 0.5*Vcc
CACTL2 = P2CA0; // Pin to CA0
MSP-EXP430FG4618 | SOLUTION
Using the MSP-EXP430FG4618 Development Tool and the MSP430FG4618 device, perform a voltage signal comparison with an internal reference. | 

## Slide 17: Quiz (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
22. Using the Comparator_A to measure resistive elements, its accuracy is limited by:
  (a) Precision of resistors, number of counts, capacitor precharge;
  (b) Precision of resistors, VCC stability, capacitor precharge;
  (c) RC tolerance, VCC stability, VREF stability;
  (d) None of above.
23. To use the Comparator_A with internal low pass filtering, the control register bit:
  (a) CAON must be reset;
  (b) CAF must be set;
  (c) CARSEL must be reset;
  (d) CAEX must be set.

## Slide 18: Quiz (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
24. To use the Comparator_A with an internal diode reference voltage at the positive terminal, configure the control register bits:
  (a) CAREFx = 2; CARSEL = 0; CAEX = 1;
  (b) CAREFx = 1; CARSEL = 1; CAEX = 1;
  (c) CAREFx = 3; CARSEL = 1; CAEX = 1;
  (d) CAREFx = 0; CARSEL = 0; CAEX = 0.

## Slide 19: Quiz (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Answers:
  22. (a) Precision of resistors, number of counts, capacitor precharge.
  23. (b) CAF must be set.
  24. (c) CAREFx = 3; CARSEL = 1; CAEX = 1.