## Slide 1: Chapter 9 Data Acquisition Operational Amplifiers
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Notes: <number>

## Slide 2: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Introduction to Operational Amplifiers (Op-Amps)
Internal Structure
Architectures of Operational Amplifiers
Registers
Configuration of Topologies
Quiz

## Slide 3: Introduction (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Some devices in the MSP430 family provide analogue signal amplification in the form of operational amplifiers;
The main op-amp characteristics are:
  Signal protection from interference (voltage level increase);
  Good signal transfer due to high impedance inputs and low impedance output;
  Improvement to signal precision by adjustment of the voltage level at the ADC input.
There are different types of op-amps:
      Single Supply;
      Dual Supply;
      CMOS or Bipolar or mixed;
      Rail-to-Rail In;
      Rail-to-Rail Out.

## Slide 4: Introduction (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
All op-amps (OAs) included in the MSP430 devices are Single Supply and CMOS;
The MSP430FG4618 has three op-amps;
The MSP430F2274 has two op-amps;
Main op-amp features:
  Selectable gain bandwidth: 500 kHz, 1.4 MHz, 2.2 MHz;
  Class AB output for mA range drive;
  Integrated charge pump for rail-to-rail input range and superior offset behaviour (FG only);
  User-configurable feedback and interconnects:
    Internal R ladder;
    Internally chainable (minimises external passive components);
    Internal connections to the ADC and DAC.

## Slide 5: Internal Structure (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The internal structure of each op-amp allows:
  Flexible feedback networking;
  Flexible modes (optimized current consumption and performance;
  User configurable as:
    General purpose;
    Unity gain buffer;
    Voltage comparator;
    Inverting programmable gain amplifier (PGA);
    Non-inverting programmable gain amplifier (PGA);
    Differential amplifier.

## Slide 6: Internal Structure (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Op-Amp internal structure:

## Slide 7: Internal Structure (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
An OA consists of:
    Two inputs:
      Inverting input, V1;
      Non inverting input, V2.
    Single output, V0:
      Represented by E0 = AVD × VD:
        E0: input differential signal, VD = V2 – V1;
        AVD: Open-loop differential gain (ideally: infinity).
    High input impedance, ZIN (ideally: infinity);
    Low output impedance, Z0 (ideally: zero);
    Input offset voltage, VIO: Output voltage is displaced from 0 V (ideally: zero);
    Null input currents, I1 and I2 (ideally: zero).

## Slide 8: Architecture of Operational Amplifiers (1/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Inverting topology:
    Resistor Rf is connected from the output V0 back to the inverting input, to control the gain of the OA with negative feedback;
    VIN applied to the inverting input;
      Gain of the inverting OA: AVD = –Rf / R1;
      Output has a 180º phase shift from the input.
    Note: The single supply circuitry shown is only applicable for negative input voltages, and input signal is loaded by R1.

## Slide 9: Operational Amplifiers architectures (2/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Non-inverting topology:
    Resistor Rf is connected from the output V0 back to the inverting input to control the gain of the OA with negative feedback;
    VIN applied to the non inverting input;
    Gain of the non-inverting OA: AVD = 1 + Rf / R1.

## Slide 10: Architecture of Operational Amplifiers (3/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Non-inverting topology (continued):
    Output in phase with the input;
    Buffer (isolation between the circuit and the charge);
    Power amplifier;
    Impedance transformer;
    Input impedance: 5105 to 11012 ;
    Suitable for amplifying signals with high ZIN.

## Slide 11: Architecture of Operational Amplifiers (4/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Unity gain buffer (voltage follower) topology:
    Non-inverting amplifier with Rf = 0 and R1 equal to infinity (Note: often used with Rf for better dynamic performance);
    AVD = 1 + Rf/R1 = 1 (unity gain amplifier);
    V0 = VIN.

## Slide 12: Architecture of Operational Amplifiers (5/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Differential topology:
    Inverting and non-inverting topologies combined;
    Output signal is the amplification of the difference between the two input signals:
      AVD = Rf/R1;
      V0 = AVD(V2 – V1);

## Slide 13: Architecture of Operational Amplifiers (6/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Differential topology:
    Common-Mode Rejection Ratio (CMRR):
      Common mode noise is the voltage picked up on the leads connecting the sensor to the amplifier may be 100 to 1000 times greater than the magnitude of the sensor signal itself;
      The CMRR of the OA ensures that any signal appearing on both inputs at the same time will be attenuated considerably at the output;
      CMRR [dB] = 20log10(AVD/ACM);
      where: ACM: Amplification for Common Mode;
      ACM = (R1xR3 – RfxR2) / [R1x(R2 + R3)].

## Slide 14: Architecture of Operational Amplifiers (7/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Two OpAmp Differential topology:
    AVD = R2/R1
    V0 = AVD(V2 – V1)

## Slide 15: Architecture of Operational Amplifiers (8/8)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Three OpAmp Differential topology:
    AVD = R2/R1
    V0 = AVD(V2 – V1)

## Slide 16: Registers (1/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
OAxCTL0, OpAmp Control Register 0

## Slide 17: Registers (2/2)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
OAxCTL1, OpAmp Control Register 1
Bit |  | Description
7-5 | OAFBRx | OAx feedback resistor: OAFBR2 OAFBR1 OAFBR0 = 000  (Gain): AVD = 1 OAFBR2 OAFBR1 OAFBR0 = 001  (Gain): AVD = 1.33 OAFBR2 OAFBR1 OAFBR0 = 010  (Gain): AVD = 2 OAFBR2 OAFBR1 OAFBR0 = 011  (Gain): AVD = 2.67 OAFBR2 OAFBR1 OAFBR0 = 100  (Gain): AVD = 4 OAFBR2 OAFBR1 OAFBR0 = 101  (Gain): AVD = 4.33 OAFBR2 OAFBR1 OAFBR0 = 110  (Gain): AVD = 8 OAFBR2 OAFBR1 OAFBR0 = 111  (Gain): AVD = 16
4-2 | OAFCx | OAx function control: OAFC2 OAFC1 OAFC0 = 000  General purpose OAFC2 OAFC1 OAFC0 = 001  Unity gain buffer OAFC2 OAFC1 OAFC0 = 010  Reserved OAFC2 OAFC1 OAFC0 = 011  Comparing Op-Amp OAFC2 OAFC1 OAFC0 = 100  Non-inverting PGA OAFC2 OAFC1 OAFC0 = 101  Reserved OAFC2 OAFC1 OAFC0 = 110  Inverting PGA OAFC2 OAFC1 OAFC0 = 111  Differential Op-Amp
0 | OARRIP | OA rail-to-rail input off: OARRIP = 0  OAx input signal range is rail-to-rail OARRIP = 1  OAx input signal range is limited

## Slide 18: Configuration of Topology (1/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Op-Amp (OA) module topologies configuration:
OAFCx bits | Op-Amp (OA) module topology
000 | General-purpose op-amp
001 | Unity gain buffer
010 | Reserved
011 | Voltage comparator
100 | Non-inverting programmable amplifier
101 | Reserved
110 | Inverting programmable amplifier
111 | Differential amplifier

## Slide 19: Configuration of Topology (2/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
General-purpose op-amp (OAFCx = 000):
  Closed loop configuration;
  Connection from output to inverting input;
  Requires external resistors;
  OAxCTL0 bits define the signal routing;
  OAx inputs are selected with the OAPx and OANx bits;
  OAx output is internally connected to the ADC12 input.

## Slide 20: Configuration of Topology (3/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Inverting amplifier topology (OAFCx = 110):
  Output voltage:
  Configuration of the OAxCTL1 register:
    Using internal resistors: AVD = -0.33 to AVD = -15;
    The OAx input signal range can be rail-to-rail or limited (OARRIP bit).

## Slide 21: Configuration of Topology (4/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Non-inverting amplifier topology (OAFCx = 100)
  Output voltage:
  Configuration of the OAxCTL1 register:
    Using internal resistors: AVD = 1 to AVD = 16;
    The OAx input signal range can be rail-to-rail or limited (OARRIP bit).

## Slide 22: Configuration of Topology (5/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Unity gain buffer (OAFCx = 001):
  Closed loop configuration;
  OAx output connected internally to RBOTTOM and –input OAx;
  Non-inverting input is available (OAPx bits);
  External connection for the inverting input is disabled;
  OAx output is internally connected to ADC12 input (OAxCTL0).

## Slide 23: Configuration of Topology (6/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Voltage comparator (OAFCx = 011):
  Open loop configuration;
  OAx output is isolated from R ladder;
  RTOP is connected to AVSS;
  RBOTTOM is connected to AVCC;
  OAxTAP signal connected to the input OAx: comparator with a programmable threshold voltage (OAFBRx bits);
  Non-inverting input is selected by the OAPx bits;
  Hysteresis can be added (external positive feedback resistor);
  The external connection for the inverting input is disabled;
  OAx output is internally connected to ADC12 input (OAxCTL0).

## Slide 24: Configuration of Topology (7/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Differential amplifier (OAFCx = 111):
  Internal routing of the OA signals: 2-OpAmp or 3-OpAmp.
  Two-OpAmp:
    OAx output connected to RTOP by routing through another OAx in the Inverting PGA mode.
    RBOTTOM is unconnected providing a unity gain buffer (combined with the remaining OAx to form the differential amplifier).
    The OAx output is internally connected to the ADC12 input channel as selected by the OAxCTL0 bits.

## Slide 25: Topologies Configuration (8/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Two OpAmp Differential amplifier (OAFCx = 111):
  Configuration of control registers:
  Configuration of gain:
Registers | Configuration
OA0CTL0 | 00 xx xx 00
OA0CTL1 | 00 01 11 0x
OA1CTL0 | 10 xx xx xx
OA1CTL1 | xx x1 10 0x
OA1 OAFBRx bits | Gain
000 | 0
001 | 0.33
010 | 2
011 | 2.67
100 | 3
101 | 4.33
110 | 7
111 | 15

## Slide 26: Configuration of Topology (9/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Two-OpAmp Differential amplifier (OAFCx = 111):

## Slide 27: Configuration of Topology (10/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Three-OpAmp Differential amplifier (OAFCx = 111):
  Configuration of control registers:
  Configuration of gain:
Registers | Configuration
OA0CTL0 | 00 xx xx 00
OA0CTL1 | xx x0 01 0x
OA1CTL0 | 00 xx xx 00
OA1CTL1 | 00 01 11 0x
OA2CTL0 | 11 11 xx xx
OA2CTL1 | xx x1 10 0x
OA0/OA2 OAFBRx bits | Gain
000 | 0
001 | 0.33
010 | 2
011 | 2.67
100 | 3
101 | 4.33
110 | 7
111 | 15

## Slide 28: Configuration of Topology (11/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Three-OpAmp Differential amplifier (OAFCx = 111):

## Slide 29: Quiz (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
4. Ideal operational amplifiers have:
  (a) Zero ZIN, infinite gain, zero ZO, infinite bandwidth and zero offset;
  (b) Infinite ZIN, infinite gain, zero ZO, infinite bandwidth and zero offset;
  (c) Infinite ZIN, zero gain, zero ZO, infinite bandwidth and zero offset;
  (d) Infinite ZIN, infinite gain, infinite ZO, zero bandwidth, and zero offset.
5. When Rf = 0 and R1 = infinity, an Op-Amp becomes:
  (a) An amplifier with gain equal to infinity;
  (b) An amplifier whose output voltage equals its input voltage (voltage follower);
  (c) All of above;
  (d) None of above.

## Slide 30: Quiz (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
6. When Op-Amp control register bits OAFCx = 4, its topology is configured for:
  (a) Unity gain buffer;
  (b) Comparing OpAmp;
  (c) Non-inverting PGA;
  (d) Differential OpAmp.
7. To set a gain of AVD = 8, the OAx feedback resistor Op-Amp control register bits, OAFBRx, must be configured as:
  (a) OAFBRx = 6;
  (b) OAFBRx = 3;
  (c) OAFBRx = 4;
  (d) OAFBRx = 7.

## Slide 31: Quiz (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
8. The internal connection of the OAx output to the A0 ADC12 input channel requires setting the OA control bit:
  (a) OARRIP;
  (b) OAADC0;
  (c) OAADC1;
  (d) None of above.

## Slide 32: Quiz (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Answers:
  4. (b) Infinite ZIN, infinite gain, zero ZO, infinite bandwidth and zero offset.
  5. (b) An amplifier whose output voltage equals its input voltage (voltage follower).
  6. (c) Non-inverting PGA.
  7. (a) OAFBRx = 6.
  8. (b) OAADC0.