## Slide 1: Chapter 9 Data Acquisition SD ADC
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Notes: <number>

## Slide 2: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Introduction to Sigma-Delta ADC :
  Delta modulator
  Digital filter
  Decimation digital filter
MSP430 SD16(A) – Sigma-Delta ADC
Lab5D: SD16 Signal Acquisition
Quiz

## Slide 3: Sigma-Delta ADC Introduction (1/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Sigma-Delta (SD) converter determines the digital word:
    By oversampling the input signal using sigma-delta modulation;
    Applying digital filtering;
    Reducing data rate by collecting modulator output bits (decimation).

## Slide 4: Sigma-Delta ADC Introduction (2/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Delta modulator:
  Quantizes the difference between the current analogue input signal and the average of the previous samples.
  Example: 1st order modulator (simplest form):
    Quantization (comparator): Output={1,0} if Input={+,-}
    Demodulator (integrator - 1 bit DAC): Output={,} if Input={1,0}.

## Slide 5: Sigma-Delta ADC Introduction (3/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Delta modulator:
  Density of “1’s" at the modulator OUT is proportional to IN signal:
    Increasing IN, the comparator generates a greater number of “1’s";
    Decreasing IN, the comparator generates a lesser number of “1’s".
  By summing the error voltage, the integrator acts as a:
    Lowpass filter for the input signal;
    Highpass filter for the quantization noise.

## Slide 6: Sigma-Delta ADC Introduction (4/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Delta modulator:
  Most quantization noise is pushed into higher frequencies;
  Oversampling changes noise distribution (but not total noise);
  Quantization noise limits the dynamic range of the ADC;
  Noise is the “round-off” error of analogue signal quantization.

## Slide 7: Sigma-Delta ADC Introduction (5/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Delta modulator:
  As the OSR (Over-Sampling Ratio) increases, the noise decreases (SNR increases);
  As the order of the modulator increases, the noise decreases.

## Slide 8: Sigma-Delta ADC Introduction (6/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Digital Filter:
  Averages the 1-bit data stream;
  Improves the analogue to digital conversion resolution;
  Removes quantization noise outside the band of interest;
  Determines signal bandwidth, settling time and stopband rejection.

## Slide 9: Sigma-Delta ADC Introduction (7/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Digital Filter:
  There are several types of digital filters:
    Finite Impulse Response (FIR) filter: output is dependent only on past and present values of the input;
    Sinc filter: Removes all frequency components above a given bandwidth, leaving the the low frequency components. It has linear phase;
    Infinite Impulse Response (IIR) filter: the output is dependent on past and present values of both the input and the output;
    Averaging, Moving average filter.

## Slide 10: Sigma-Delta ADC Introduction (8/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Digital Filter:
  SD converters: widely used lowpass filter: Sinc³ or Sinc5 types.

## Slide 11: Sigma-Delta ADC Introduction (9/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Digital Filter:
  Main advantage of Sinc filter: notch response. The notch position is directly related to the output data rate, allowing high frequency noise reduction and 60 Hz mains.

## Slide 12: Sigma-Delta ADC Introduction (10/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Digital Filter:
  The output of the digital filter will be a data stream:

## Slide 13: Sigma-Delta ADC Introduction (11/11)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Decimation Digital Filter:
  Decimation: Reduces the sampling rate down from the oversampling rate without losing information (eliminates redundant data);
  Using the Nyquist theorem (fsample > 2finput) and the oversampling at the delta modulator, the input signal can be reliably reconstructed without distortion.

## Slide 14: SD16(A)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
MSP430 SD16(A) – Sigma-Delta ADC:
  Introduction
  SD16_A features
  SD ADC core
  Analogue input range and PGA
  Voltage reference generator
  Analogue input pair selection
  Analogue input characteristics and setup
  Digital filter
  Output data format
  Conversion modes
  Integrated temperature sensor
  SD16_A interrupts
  Interrupt vector generator (SD16IV)
  SD16 registers

## Slide 15: SD16(A) (1/2) Introduction
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Applications MSP430 devices with up to 7 SD ADCs:
  Portable medical (F42xx and FG42xx);
  Energy metering (FE42x(A), F47xx, F471xx);
  Generic applications (F42x and F20x3).
SD16_A: eZ430-F2013 hardware development tool;
SD16_A supports:
  16-bit SD core;
  Reference generator;
  External analogue inputs;
  Internal VCC sense;
  Integrated temperature sensor.

## Slide 16: SD16(A) (2/2) Introduction
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
SD16_A block diagram:

## Slide 17: SD16(A) SD16_A Features
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
16-bit sigma-delta architecture;
Up to eight multiplexed differential analogue inputs per channel;
Software selectable on-chip reference voltage generation (1.2 V);
Software selectable internal or external reference;
Built-in temperature sensor;
Up to 1.1 MHz modulator input frequency;
Selectable low-power conversion mode.

## Slide 18: SD16(A) 16 bit SD ADC core
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The analogue-to-digital conversion is performed by a 1-bit second-order oversampling sigma-delta modulator;
A single-bit comparator within the modulator quantizes the input signal with the modulator frequency, fM;
The resulting 1-bit data stream is averaged by the digital decimation filter (comb type filter with selectable oversampling) for the conversion result;
The decimation filter has ratios of up to 1024. Additional filtering can be done in software.

## Slide 19: SD16(A) Analogue Input Range and PGA
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The full-scale (FS) input voltage range for each analogue input pair is dependent on the gain setting of the PGA (= 1, 2, 4, 8, 16 & 32x);
The maximum FS range is ±VFS:

## Slide 20: SD16(A) Voltage Reference Generator
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Voltage reference options:
  Internal reference (1.2 V): SD16REFON=1, SD16VMIDON=0;
  External reference: SD16REFON=0, SD16VMIDON=0;
  Internal refeference, with reference with buffered output: SD16REFON=1, SD16VMIDON=1;
To reduce noise it is recommended to connect an external 100-nF capacitor from VREF to AVSS.

## Slide 21: SD16(A) Analogue Input Pair Selection
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The SD16_A can convert up to 8 differential input pairs multiplexed into the PGA;
The available analogue input pairs are:
  A0-A4: External to the device;
  A5: Resistive divider to measure
  the supply voltage (AVCC/11);
  A6: Internal temperature sensor;
  A7: Offset shunt (used for calibration
  of SD16_A input PGA offset
  measurement).

## Slide 22: SD16(A) Analogue Input Characteristics and Setup
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Analogue input equivalent circuit for the eZ430-F2013:
Max. sampling frequency, fS:
PGA gain | CS
1 | 1.25 pF
2 | 2.5 pF
4 | 2.5 pF
8 | 5 pF
16 | 10 pF
32 | 10 pF

## Slide 23: SD16(A) Analogue Input Step Response
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Sinc3 comb digital filter needs 3 data-word periods to settle;
SD16INTDLY = 00h, conversion interrupt requests do not begin until the 4th conversion after a start condition.

## Slide 24: SD16(A) Digital Filter
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Processes the 1-bit data stream from the modulator using a Sinc3 comb digital filter;
Take into consideration that:
    Oversampling rate is given by: OSR = fM/fS;
    The first filter notch is at: fS = fM/OSR;
Modify the notch frequency adjustment with:
    SD16SSELx and SD16DIVx: Change fM;
    SD16OSRx and SD16XOSR bits: Change OSR.
Number of output bits depends on the OSR, DR and number format, ranging from 15 to 30 bits.

## Slide 25: SD16(A) Output Data Format
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Selected with SD16DF and SD16UNI bits:
  Two’s complement;
  Offset binary;
  Unipolar.
  SD16UNI = 0 SD16UNI = 0 SD16UNI = 1
  SD16DF = 0 SD16DF = 1 SD16DF = 0

## Slide 26: SD16(A) (1/2) Conversion modes
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Single conversion:
  The channel is converted once (SD16SNGL = 1);
  After conversion completion: SD16SC = 0;
  Clearing SD16SC before the conversion is completed:
    Immediately stops conversion of the channel;
    Powers down the channel;
    Turns off the corresponding digital filter;
    The value in SD16MEM0 can change.

## Slide 27: SD16(A) (2/2) Conversion modes
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Continuous conversion:
  The channel is converted continuously (SD16SNGL = 0);
  Starts when SD16SC = 1;
  Stops when SD16SC = 0 (cleared by software);
  Clearing SD16SC before the conversion is complete has the same effect as a single conversion.

## Slide 28: SD16(A) Integrated temperature sensor
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Configured when:
  Analogue input pair SD16INCHx = 110;
  SD16REFON = 1;
  SD16VMIDON = 1 (if is used an external reference for other analogue input pair).
The typical temperature sensor transfer function:
VSensor,typ = TCSensor (273 + T[ºC]) + VOffset, Sensor [mV]

## Slide 29: SD16(A) SD16_A interrupts
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Two interrupt sources for each ADC channel:
SD16 Interrupt Flag (SD16IFG):
  SD16IFG = 1: SD16MEM0 memory register is written with a conversion result;
  An interrupt request requires:
    Corresponding SD16IE = 1;
    GIE = 1.
SD16 Overflow Interrupt Flag (SD16OVIFG):
  SD16OVIFG = 1: conversion result is written to SD16MEM0 location before the previous conversion result was read.

## Slide 30: SD16(A) Interrupt vector generator (SD16IV)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Used to determine which enabled SD16_A interrupt source requested an interrupt;
Considerations:
    The highest priority enabled interrupt generates a number in the SD16IV register (evaluated or added to the program counter to automatically call the appropriate routine);
    Any access, read or write, of the SD16IV register has no effect on the SD16OVIFG or SD16IFG flags;
    SD16IFG flags are reset by reading the SD16MEM0 register or by clearing the flags in software;
    SD16OVIFG bits can only be reset by software.

## Slide 31: SD16(A) (1/5) Registers
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
SD16CTL, SD16_A Control Register

## Slide 32: SD16(A) (2/5) Registers
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
SD16CCTL0, SD16_A Control Register 0

## Slide 33: SD16(A) (3/5) Registers
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
SD16CCTL0, SD16_A Control Register 0

## Slide 34: SD16(A) (4/5) Registers
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
SD16INCTL0, SD16_A Input Control Register

## Slide 35: SD16(A) (5/5) Registers
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
SD16MEM0, SD16_A Conversion Memory Register
  The 16-bit SD16MEMx register stores the conversion results. Depending on the SD16LSBACC bit state, it holds the upper or lower 16 bits of the digital filter output.
SD16AE, SD16_A Analogue Input Enable Register
  8 bits SD16AE = 1 to enable the corresponding external analogue input (MSB: A7 to LSB: A0).
SD16IV, SD16_A Interrupt Vector Register
  The contents of bits 1 to 4 of the 16 bits SD16IV indicate the interrupt source. According to their priority:
    SD16IV = 002h  SD16MEMx overflow;
    SD16IV = 004h  SD16_A Interrupt.
    For SD16IV = 000h  No interrupt pending.
    From SD16IV = 006h to =010h (lowest) to interrupt source are reserved.

## Slide 36: Lab5C: SD Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Objective:
  With the SD16_A ADC module included in the eZ430-F2013 hardware development tool, develop a temperature data logger.
Details:
  Like the previous exercise (Lab4), this laboratory is composed of several sub-tasks;
  This laboratory has been developed for the Code Composer Essentials version 3 software development tool only.

## Slide 37: Lab5C: SD Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Project files:
  C source files: Chapter 9 > Lab5 > Lab5C_student.c
  Solution file: Chapter 9 > Lab5 > Lab5C_solution.c
Overview:
  This laboratory implements a temperature data logger using the hardware kit’s integrated temperature sensor;
  The device is configured to read the temperature once each minute for one hour;
  Each temperature’s (ºC) value is transferred to flash info memory segment B and C;
  When the microcontroller is not performing any task, it enters into low power mode.

## Slide 38: Lab5C: SD Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  The SD16_A module uses VREF+ = 1.2 V as the reference voltage;
  It is necessary to select channel 6 of the SD16_A to use the integrated temperature sensor as the input;
  Timer_A generates an interrupt once every second that starts conversion using SD16_A;
  At the end of conversion, an interrupt is requested by the converter and the temperature value is written to flash memory.

## Slide 39: Lab5C: SD Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  The voltage value is converted into temperature using the mathematical formula provided by the eZ430-F2013 data sheet;
  After transferring the value to the flash memory, the system returns to low power mode LPM3.
  The resources used by the application are:
      SD16_A;
      Timer_A;
      Ports I/O;
      Interrupts;
      Low power mode.

## Slide 40: Lab5C: SD Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  The application starts by stopping the Watchdog Timer;
  System tests for calibration constants in info memory segment A are made. The CPU execution will be trapped if it does not find this information;
  The digitally controller oscillator (DCO) is set to 1 MHz, providing a clock source for MCLK and SMCLK, while the Basic Clock System+ is configured to set ACLK to 1.5 kHz through the VLOCLK;
  Controller’s flash timing is derived from MCLK divided by 3, to comply with the device specifications.

## Slide 41: Lab5C: SD Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  Port P1.0 is configured as output and will blink the LED once each second;
  The SD16_A is configured to use the input channel corresponding to the on-chip temperature sensor (channel A6);
  The configuration includes activation of the internal reference voltage: VREF+ = 1.2 V and selection of SMCLK as the clock signal;
  The converter is configured to perform a single conversion in bipolar mode and offset binary format. At the end of conversion, an interrupt is requested.

## Slide 42: Lab5C: SD Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  The Timer_A is configured to generate an interrupt once every second;
  ACLK/8 is selected as the clock signal using VLOCLK as the clock source and will count up until the TACCR0 value (up mode) is reached;
  The system enters into low power mode, where it waits for an interrupt;
  Flash memory pointers and interrupt counters are initialized.

## Slide 43: Lab5C: SD Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  The Timer_A ISR increments the variable counter and when this variable reaches the value 60 (1 minute), the software start of conversion is requested;
  At the end of this ISR, the system returns to low power mode;
  When the SD16_A ends the conversion, an interrupt is requested:
    While variable min is less than 60, the temperature is written to flash memory. The memory pointer is increased by two (word);
    When min = 60, the system stops operation.

## Slide 44: Lab5C: SD Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  DCO configuration:
  Adjust the DCO frequency to 1 MHz by software using the calibrated DCOCTL and BCSCTL1 register settings stored in information memory segment A.
if (CALBC1_1MHZ == _____ || CALDCO_1MHZ == _____)
{
while(1); // If calibration constants erased
// do not load, trap CPU!!
}
DCOCTL = ___________________;

## Slide 45: Lab5C: SD Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  Basic Clock module+ configuration:
  Set MCLK and SMCLK to 1 MHz;
  Use the internal very low power VLOCLK source clock to ACLK/8 clock signal as the low frequency oscillator (12 kHz):
  BCSCTL1 = __________________;
  BCSCTL3 = __________________;

## Slide 46: Lab5C: SD Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  SD16_A configuration:
  The SD16_A’s input channel is the integrated temperature sensor (A6) and it uses the reference signal VREF+ = 1.2 V;
  The SD16_A clock source is SMCLK;
  Configure the SD16_A to perform a single conversion and enable its interrupts. What are the values to write to the configuration registers?
  SD16CTL = __________________;
  SD16CCTL0 = ________________;
  SD16INCTL0 = _______________;

## Slide 47: Lab5C: SD Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  Timer_A configuration:
  Configure Timer_A register to enable an interrupt once every second;
  Use the ACLK clock signal as the clock source;
  This timer is configured in up mode in order to count until the TAR value reaches the TACCR0 value.
  Configure the following registers:
  TACCTL0 = ___________________;
  TACCR0 = ____________________;
  TACTL = _____________________;

## Slide 48: Lab5C: SD Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Monitor the temperature variation for 1 hour:
  After compiling the project and start the debug session, before run the application put a breakpoint on the line of code with the _NOP() instruction;
  Go to breakpoint properties and set action to Write data to file;
  Name the file as Temp.dat and define the data format as integer.

## Slide 49: Lab5C: SD Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Monitor the temperature variation for 1 hour:
  The data starts at address 0x01040 with a length of 3C;
  Run the application and let the temperature data logger acquire the values for 1 hour;
  Use a heater or a fan to force temperature variations during the measuring period;
  When execution reaches the breakpoint, the file will be available in your file system. Construct a graph to plot the temperature variation with time obtained by the data logger.

## Slide 50: Lab5C: SD Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DCO configuration:
if (CALBC1_1MHZ == 0xFF || CALDCO_1MHZ == 0xFF)
{
while(1); // If calibration constants erased
// do not load, trap CPU!!
}
DCOCTL = CALDCO_1MHZ; // Set DCO to 1 MHz
eZ430-F2013 | SOLUTION
Develop a temperature data logger through the integrated temperature sensor using the eZ430-F2013 Development Tool. | 

## Slide 51: Lab5C: SD Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Basic Clock module+ configuration:
BCSCTL1 = DIVA_3; // ACLK = 1.5 kHz
BCSCTL3 = LFXT1S_2; // Set VLOCLK (12 kHz)
SD16_A configuration:
SD16CTL = SD16REFON + SD16SSEL_1; // 1.2V ref, SMCLK
SD16INCTL0 = SD16INCH_6; // Temp. sensor: A6+/-
SD16CCTL0 = SD16SNGL + SD16IE; // Single conversion,
// Enable interrupts

## Slide 52: Lab5C: SD Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Timer_A configuration:
TACCTL0 = CCIE; // TACCR0 interrupt enabled
TACCR0 = 1500; // this count corresponds to 1 sec
TACTL = TASSEL_1 | MC_1 | ID_0; // ACLK/1, Up mode: // the timer counts up to TACCR0.

## Slide 53: Quiz (1/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
18. A Sigma-Delta ADC has the advantages of:
  (a) High resolution and accuracy, low sample rate, low cost;
  (b) High resolution and stability, low power, low cost;
  (c) High resolution and stability, low power, moderate cost;
  (d) High bandwidth and accuracy, high sample rate, moderate cost.
19. The quantization noise of a Sigma-Delta ADC:
  (a) Limits the dynamic range;
  (b) Is actually the “round-off” error;
  (c) Is pushed into higher frequencies through oversampling;
  (d) All of above.

## Slide 54: Quiz (2/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
20. The SD16_A digital output configured as unipolar provides an input voltage:
  (a) [–VFSR VFSR] = [0000h FFFFh];
  (b) [–VFSR VFSR] = [8000h 7FFFh];
  (c) [–VFSR VFSR] = [0000h 8FFFh];
  (d) None of above.
21. The SD16_A control register bits that adjust the frequency of the digital notch filter are:
  (a) SD16SSELx and SD16DIVx;
  (b) SD16OSRx and SD16XOSRx;
  (c) All of above;
  (d) None of above.

## Slide 55: Quiz (3/3)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Answers:
  18. (c) High resolution and stability, low power, moderate cost.
  19. (d) All of above.
  20. (a) [–VFSR VFSR] = [0000h FFFFh].
  21. (c) All of above.