## Slide 1: Chapter 9 Data Acquisition SAR ADC
MSP430 Teaching Materials
Texas Instruments Incorporated
University of Beira Interior (PT)
Pedro Dinis Gaspar, António Espírito Santo, Bruno Ribeiro, Humberto Santos
University of Beira Interior, Electromechanical Engineering Department
www.msp430.ubi.pt
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Notes: <number>

## Slide 2: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Introduction to Successive Approximation Register (SAR) Analogue-to-Digital Converter (ADC)
ADC10
ADC12
Laboratory 5: Signal Acquisition
  Lab5A: SAR ADC10 conversion
  LAB5B: SAR ADC12 conversion
Quiz

## Slide 3: Introduction to SAR ADC (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Successive Approximation Register (SAR) converters are well-suited to general purpose applications and are used in a wide range signal interfacing applications:
  Data loggers;
  Temperature sensors;
  Bridge sensors (resistive e.g. strain gauges);
  General purpose.

## Slide 4: Introduction to SAR ADC (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
SAR block diagram:

## Slide 5: Introduction to SAR ADC (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
SAR concept:
  Determines the digital word by approximating the analogue input signal using an iterative process, as follows:
    Discharge the capacitor array to the comparator’s Voffset;
    Sample the input voltage (VS) and hold;
    Switch all of the capacitors in the array to VS;
    Switch the capacitors to charge the comparator's input;
    Initiate a binary search:
      Switch the MSB capacitor to VREF (ADC’s FS range):
        Divided 1:1 between it and the rest of the array;
        Input voltage to the comparator is - VS + VREF/2;
        VS > VREF/2  Comparator output: MSB = 1;
        VS < VREF/2  Comparator output: MSB = 0;
      Switch the other capacitors in a decreasing charge capacity order from 16C to C.

## Slide 6: Introduction to SAR ADC (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
SAR concept:

## Slide 7: ADC 10
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC10:
  Introduction
  Features
  10 bit ADC core
  Conversion clock
  Sample and conversion timing
  Conversion modes
  Data Transfer Controller (DTC)
  Integrated temperature sensor
  ADC10 interrupts
  Registers

## Slide 8: ADC10 (1/2) Description
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The ADC10 module of the MSP430F2274 supports fast 10-bit analogue-to-digital conversions;
The module contains:
      10-bit SAR core;
      Sample select control;
      Reference generator;
      Data transfer controller (DTC) for automatic conversion result handling (ADC samples conversion and storage without CPU intervention).

## Slide 9: ADC10 (2/2) Description
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC10 block diagram:

## Slide 10: ADC10 Features
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Greater than 200 ksps maximum conversion rate;
Monotonic 10-bit converter with no missing codes;
Sample-and-hold with programmable sample periods;
Conversion initiated by software or Timer_A;
Software on-chip reference voltage generation (1.5 V or 2.5 V)
Software selectable internal or external reference;
Eight external input channels;
Conversion channels for internal temperature sensor, VCC, and external references;
Selectable conversion clock source;
Single-channel, repeated single-channel, sequence, and repeated sequence conversion modes;
ADC core and reference voltage (powered down separately);
Data transfer controller (automatic storage of results).

## Slide 11: ADC10 10 bit ADC core
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
10 bit ADC core (enable with ADC10ON bit):
  Converts an analogue input to its 10-bit digital representation;
  Stores the result in the ADC10MEM register;
  The analogue conversion range is limited by the upper and lower limits: VR+ ; VR-
  The digital output (NADC) is:
      Full scale: NADC = 03FFh, when the input signal  VR+ -0.5LSB;
      Zero: NADC = 0000h, when the input signal  VR- + 0.5 LSB.
  Conversion results:
    Binary format:
    Two’s-complement format.

## Slide 12: ADC10 Conversion clock
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The ADC10CLK is used both as the conversion clock and to generate the sampling period;
Each available ADC10 source clock is selected using the ADC10SSELx bits:
  SMCLK;
  MCLK;
  ACLK;
  Internal oscillator ADC10OSC;
  Each clock source can be divided from 1-8 (ADC10DIVx bits).
The ADC10CLK must remain active until the end of a conversion.

## Slide 13: ADC10 Sample and conversion timing
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
An A/D conversion is initiated by the rising edge of SHI. The sources of SHI (SHSx bits selection) can be:
  ADC10SC bit;
  Timer_A Output Unit 1, Output Unit 0, or Output Unit 2.
The SHTx bits select the sample period, tsample, to be 4, 8, 16, or 64 ADC10CLK cycles:

## Slide 14: ADC10 (1/2) Conversion modes
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Conversion modes (selected by the CONSEQx bits):
  Single channel, single-conversion: A single conversion for the channel selected by INCHx bits is performed, with the result being stored in the ADC10MEM registers;
  Sequence of channels: One conversion in multiple channels, beginning with the channel selected by INCHx bits and decrementing to channel A0, looping through a specified number of ADC10MEM registers and stopping after the conversion of channel A0.

## Slide 15: ADC10 (2/2) Conversion modes
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Conversion modes (selected by the CONSEQx bits):
  Repeat single channel: A single channel selected by INCHx bits is converted repeatedly until stopped and the result is stored in the ADC10MEM register;
  Repeat sequence of-channels: Repeated conversions for multiple channels, beginning with the channel selected by INCHx bits and decrementing to channel A0. Each ADC result is written to ADC10MEM. The sequence ends after conversion of channel A0, and the next trigger signal re-starts the sequence.

## Slide 16: ADC10 (1/2) Data Transfer Controller (DTC)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DTC (ADC10DTC1  0):
  Automatically transfers the conversion results from ADC10MEM to other on-chip memory locations each time the ADC10 completes a conversion and loads the result to ADC10MEM.
Requires one CPU MCLK:
  If the CPU is active during this period, it will be halted to ensure the transfer is completed;
  Ensure that no active conversion or sequence is in progress (ADC10 busy) during DTC transfer initiation.

## Slide 17: ADC10 (2/2) Data Transfer Controller (DTC)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The Data Transfer Controller (DTC) can be configured for:
  One-Block Transfer Mode (ADC10TB = 0):
    The value n in ADC10DTC1 defines the total number of transfers for a block;
    First block address range
    {Start: ADC10SA; End: ADC10SA+2n–2};
  Two-Block Transfer Mode (ADC10TB = 1):
    The value n in ADC10DTC1 defines the number of transfers for one block;
    First block address range
    {Start: ADC10SA ; End: ADC10SA+2n–2};
    Second block address range:
    {Start: SA+2n ; End: SA+4n–2}.

## Slide 18: ADC10 Integrated temperature sensor
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Input channel selected as INCHx = 1010;
Transfer function relating the input voltage, VTemperature [V] to the temperature, T [ºC], is given by:
Considerations:
    The sampling period must be greater than 30 μs;
    Large offset error, must be calibrated;
    Automatically turns on the on-chip reference generator.

## Slide 19: ADC10 ADC10 interrupts
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
One interrupt and one interrupt vector are associated with the ADC10 function:
  When the DTC is not used (ADC10DTC1 = 0): ADC10IFG is set when conversion results are loaded into ADC10MEM;
  When DTC is used (ADC10DTC1 > 0): ADC10IFG is set when a block transfer completes and the internal transfer counter n = 0.
When ADC10IE = 1 and GIE = 1, the ADC10IFG flag generates an interrupt request.

## Slide 20: ADC10 (1/7) Registers
<number>
Copyright 2008 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC10CTL0, ADC10 Control Register 0 (high byte)
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8
SREFx |  |  | ADC10SHTx |  | ADC10SR | REFOUT | REFBURST
Bit |  | Description
15-13 | SREFx | Select voltage reference: VR+ VR− SREF2 SREF1 SREF0 = 000  VCC VSS SREF2 SREF1 SREF0 = 001  VREF+ VSS SREF2 SREF1 SREF0 = 010  VeREF+ VSS SREF2 SREF1 SREF0 = 011  Buffered VeREF+ VSS SREF2 SREF1 SREF0 = 100  VCC VREF−/VeREF− SREF2 SREF1 SREF0 = 101  VREF+ VREF−/VeREF− SREF2 SREF1 SREF0 = 110  VeREF+ VREF−/VeREF− SREF2 SREF1 SREF0 = 111  Buffered VeREF+ VREF−/VeREF−
12-11 | ADC10SHTx | ADC10 sample-and-hold time: ADC10SHT1 ADC10SHT0 = 00  4 x ADC10CLKs ADC10SHT1 ADC10SHT0 = 01  8 x ADC10CLKs ADC10SHT1 ADC10SHT0 = 10 16 x ADC10CLKs ADC10SHT1 ADC10SHT0 = 11  64 x ADC10CLKs
10 | ADC10SR | ADC10 sampling rate: ADC10SR = 0  Reference buffer supports up to ~200 ksps ADC10SR = 1  Reference buffer supports up to ~50 ksps
9 | REFOUT | Reference voltage output (pin VREF+): REFOUT = 0  Disable REFOUT = 1  Enable
8 | REFBURST | Controls the operation of the internal reference buffer: REFBURST = 0  Reference buffer on continuously allowing the reference voltage to be present outside the device continuously. REFBURST = 1  Reference buffer automatically disabled when the ADC10 is not actively converting, and automatically re-enabled when during sample-and-conversion.

## Slide 21: ADC10 (2/7) Registers
<number>
Copyright 2008 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC10CTL0, ADC10 Control Register 0 (low byte)
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
MSC | REF2_5V | REFON | ADC10ON | ADC10IE | ADC10IFG | ENC | ADC10SC
Bit |  | Description
7 | MSC | Multiple sample and conversion (Valid for sequence or repeated modes): MSC = 0  Requires a rising edge of the SHI signal to trigger each sample-and-conversion. MSC = 1  After the first rising edge of the SHI signal that triggers the sampling timer the further sample-and-conversions are performed automatically as soon as the prior conversion is completed
6 | REF2_5V | Reference-generator voltage select (REFON bit must also be set): REF2_5V = 0  Reference voltage = 1.5 V REF2_5V = 1  Reference voltage = 2.5 V
5 | REFON | Reference generator: REFON = 0  Reference generator disable REFON = 1  Reference generator enable
4 | ADC10ON | ADC10 on: ADC10ON = 0  ADC10 off ADC10ON = 1  ADC10 on
3 | ADC10IE | ADC10 interrupt enable ADC10IE = 0  Interrupt disabled ADC10IE = 1  Interrupt enabled
2 | ADC10IFG | ADC10 interrupt flag: ADC10IFG = 0  No interrupt pending (interrupt request is accepted, or it may be reset by software) ADC10IFG = 1  Interrupt pending (ADC10MEM is loaded with a conversion result or when a block of DTC transfers is completed)
1 | ENC | Enable conversion: ENC = 0  ADC10 disabled ENC = 1  ADC10 enabled
0 | ADC10SC | Start conversion: ADC10SC = 0  No sample-and-conversion start ADC10SC = 1  Start sample-and-conversion

## Slide 22: ADC10 (3/7) Registers
<number>
Copyright 2008 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC10CTL1, ADC10 Control Register 1 (high byte)
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8
INCHx |  |  |  | SHSx |  | ADC10DF | ISSH
Bit |  | Description
15–12 | INCHx | Input channel select: INCH3 INCH2 INCH1 INCH0 = 0000  A0 INCH3 INCH2 INCH1 INCH0 = 0001  A1 INCH3 INCH2 INCH1 INCH0 = 0010  A2 INCH3 INCH2 INCH1 INCH0 = 0011  A3 INCH3 INCH2 INCH1 INCH0 = 0100  A4 INCH3 INCH2 INCH1 INCH0 = 0101  A5 INCH3 INCH2 INCH1 INCH0 = 0110  A6 INCH3 INCH2 INCH1 INCH0 = 0111  A7 INCH3 INCH2 INCH1 INCH0 = 1000  VeREF+ INCH3 INCH2 INCH1 INCH0 = 1001  VREF−/VeREF− INCH3 INCH2 INCH1 INCH0 = 1010  Temperature sensor INCH3 INCH2 INCH1 INCH0 = 1011  (VCC – VSS)/2 INCH3 INCH2 INCH1 INCH0 = 1100  (VCC – VSS)/2 or A12* INCH3 INCH2 INCH1 INCH0 = 1101  (VCC – VSS)/2 or A13 * INCH3 INCH2 INCH1 INCH0 = 1110  (VCC – VSS)/2 or A14 * INCH3 INCH2 INCH1 INCH0 = 1111  (VCC – VSS)/2 or A15 * * on MSP430x22xx devices
11–10 | SHSx | Sample-and-hold source: SHS1 SHS0 = 00  bit ADC10SC SHS1 SHS0 = 01  TIMER_A Output Unit 1 SHS1 SHS0 = 10  TIMER_A Output Unit 0 SHS1 SHS0 = 11  TIMER_A Output Unit 2
9 | ADC10DF | ADC10 data format: ADC10DF = 0  Binary ADC10DF = 1  Two’s complement
8 | ISSH | Invert signal sample-and-hold ISSH = 0  The sample-input signal is not inverted ISSH = 1  The sample-input signal is inverted

## Slide 23: ADC10 (4/7) Registers
<number>
Copyright 2008 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC10CTL1, ADC10 Control Register 1 (low byte)
Bit |  | Description
7–5 | ADC10DIVx | ADC10 clock divider: ADC10DIV2 ADC10DIV1 ADC10DIV0 = 000  / 1 ADC10DIV2 ADC10DIV1 ADC10DIV0 = 001  / 2 ADC10DIV2 ADC10DIV1 ADC10DIV0 = 010  / 3 ADC10DIV2 ADC10DIV1 ADC10DIV0 = 011  / 4 ADC10DIV2 ADC10DIV1 ADC10DIV0 = 100  / 5 ADC10DIV2 ADC10DIV1 ADC10DIV0 = 101  / 6 ADC10DIV2 ADC10DIV1 ADC10DIV0 = 110  / 7 ADC10DIV2 ADC10DIV1 ADC10DIV0 = 111  / 8
4–3 | ADC10SSELx | ADC10 clock source: ADC10SSEL1 ADC10SSEL0 = 00  ADC10OSC ADC10SSEL1 ADC10SSEL0 = 01  ACLK ADC10SSEL1 ADC10SSEL0 = 10  MCLK ADC10SSEL1 ADC10SSEL0 = 11  SMCLK
2–1 | CONSEQx | Conversion sequence mode: CONSEQ1 CONSEQ0 = 00  Single-channel, single-conversion CONSEQ1 CONSEQ0 = 01  Sequence-of-channels CONSEQ1 CONSEQ0 = 10  Repeat-single-channel CONSEQ1 CONSEQ0 = 11  Repeat-sequence-of-channel
0 | ADC10BUSY | ADC10 busy: ADC10BUSY = 0  No operation is active ADC10BUSY = 1  Sequence, sample, or conversion is active
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
ADC10DIVx |  |  | ADC10SSELx |  | CONSEQx |  | ADC10BUSY

## Slide 24: ADC10 (5/7) Registers
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC10AE0, Analogue (Input) Enable Control Register 0
  Enables the analogue input of the ADC10: BIT0 => A0, BIT1 => A1, and so on.
ADC10AE1, Analogue (Input) Enable Control Register 1 (‘F2274)
  Additional analogue input enable control register. BIT4 => A12, BIT5 => A13, BIT6 => A14, and BIT7 => A15.
ADC10MEM, Conversion-Memory Register
  Loaded with the conversion results;
  Numerical result format:
    Binary: Bits 15-10 = 0. The results in the least significant 10 bits.
    2’s complement: The results in the most significant 10 bits. Bits 5-0 = 0.

## Slide 25: ADC10 (6/7) Registers
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC10DTC0, Data Transfer Control Register 0

## Slide 26: ADC10 (7/7) Registers
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC10DTC1, Data Transfer Control Register 1
  This 8-bit register defines the number of transfers for each block;
  ADC10DTC1 = 0  DTC is disabled;
  ADC10DTC1 = 01h−0FFh  Number of transfers per block.
ADC10SA, Start Address Register for Data Transfer
  This 16-bit register defines the ADC10 start address for the DTC. It uses only the 15 most significant bits. Bit 0 is always read as 0.

## Slide 27: Contents
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC12
  Description
  Features
  12 bit ADC core
  Similarities with ADC10
  Sample and conversion timing
  Conversion memory
  ADC12 interrupts
  ADC12 interrupt vector generator
  Registers

## Slide 28: ADC12 (1/2) Introduction
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The ADC12 module of the MSP430F2013 supports fast 12-bit analogue-to-digital conversions;
The module contains:
    12-bit SAR core;
    Sample select control;
    Reference current generator.

## Slide 29: ADC12 (2/2) Introduction
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC12 block diagram:

## Slide 30: ADC12 ADC12 Features
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
It has same basic features as the ADC10, with the following differences:
    Monotonic 12-bit converter with no missing codes;
    Interrupt vector register for fast decoding of 18 ADC interrupts;
    Registers for storage of 16 conversion results;
    No Data Transfer Controller (DTC);
    16 control registers ADC12MCTLx for free choice of channels on sequential modes;
    Can also convert some channels more than once in one loop (e.g. placing two measurements of the same voltage and one measurement of current in between to calculate power).

## Slide 31: ADC12 12 bit ADC core
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
12 bit ADC core (enable with ADC12ON bit):
  Converts an analogue input to its 12-bit digital representation;
  Stores the result in a ADC12MEM register.
  The conversion is limited by the upper and lower limits: VR+ ; VR-
  The digital output (NADC) is:
      Full scale: NADC = 0FFFh, when the input signal  VR+;
      Zero: NADC = 0000h, when the input signal  VR-.
  Conversion results:
    Binary format:
    Two’s-complement format.

## Slide 32: ADC12 Similarities to ADC10
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Conversion clock selection;
ADC12 inputs and multiplexer;
Analogue port selection (P6);
Voltage reference generator:
  For proper operation requires
  storage capacitors across
  VREF+ and AVSS.
Conversion modes;
Integrated temperature sensor.

## Slide 33: ADC12 (1/3) Sample and conversion timing
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
An A/D conversion is initiated on the rising edge of SHI. The source for SHI (SHSx bits selection) can be:
  ADC12SC bit;
  Timer_A Output Unit 1; Timer_B Output Unit 0, or ; Output Unit 1.
ADC12 timer trigger for reference settling:

## Slide 34: ADC12 (2/3) Sample and conversion timing
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Sample-timing methods:
  SHP = 0: Extended sample mode:
    SHI signal directly controls SAMPCON;
    Defines the length of the sample period tsample;
    SAMPCON = 1  sampling is active;
    High-to-Low SAMPCON transition  starts the conversion after synchronization with ADC12CLK.

## Slide 35: ADC12 (3/3) Sample and conversion timing
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Sample-timing methods:
  SHP = 1: Pulse mode:
    SHI signal triggers the sampling timer;
    SHT0x and SHT1x bits (ADC12CTL0) defines the SAMPCON sample period, tsample;
    The sampling timer keeps SAMPCON = 1 after synchronization with AD12CLK.

## Slide 36: ADC12 Conversion memory
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
16 ADC12MEMx conversion memory registers (configured by the associated ADC12MCTLx control register) to store conversion results.
Non-sequential conversion (single- or repeat-single-channel):
  CSTARTADDx define the first and single ADC12MCTLx for conversion.
Sequential conversion (sequence-of- or repeat-sequence-of-channels):
  A sequence is started by the command found in the ADC12MCTLx register pointed to by CSTARTADDx;
  The pointer is incremented automatically to the next ADC12MCTLx for the next conversion;
  After ADC12MCTL15 the next conversion is ADC12MCTL0;
  The sequence runs until an EOS bit signals that this command is the last conversion of the actual sequence;
  The 16 ADC12MCTLx registers can contain more than one sequence.

## Slide 37: ADC12 ADC12 interrupts
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
The ADC12 has 18 interrupt sources:
  ADC12IFG0-ADC12IFG15: ADC12IFGx bits are set when their corresponding ADC12MEMx memory register is loaded with a conversion result;
  ADC12OV, ADC12MEMx overflow: ADC12OV is set when a conversion result is written to any ADC12MEMx before its previous conversion result was read;
  ADC12TOV, ADC12 conversion time overflow: ADC12TOV is set when another sample-and-conversion is requested before the current conversion is completed.
The DMA is triggered after the conversion in single channel modes or after the completion of sequence−of−channel modes.

## Slide 38: ADC12 ADC12 Interrupt vector generator
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Interrupt vector register ADC12IV used to determine which enabled ADC12 interrupt source requested an interrupt.
Considerations:
    The highest priority enabled interrupt generates a number in the ADC12IV register (evaluated or added to the program counter to automatically call the appropriate routine);
    Any access, read or write, of the ADC12IV register automatically resets the ADC12OV or the ADC12TOV conditions, if either were the highest pending interrupt;
    ADC12IFGx bits are reset automatically by accessing their ADC12MEMx register or may be reset by software;
    If another interrupt is pending after servicing of an interrupt, another interrupt is generated.

## Slide 39: ADC12 (1/6) Registers
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC12CTL0, ADC12 Control Register 0 (high byte)

## Slide 40: ADC12 (2/6) Registers
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC12CTL0, ADC12 Control Register 0 (low byte)
  The bold bits have the same function as the ADC10. Refer to the ADC10 to see their description.

## Slide 41: ADC12 (3/6) Registers
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC12CTL1, ADC12 Control Register 1
  The bold bits have the same funciton as the ADC10. Refer to the ADC10 to see their description.

## Slide 42: ADC12 (4/6) Registers
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC12MEMx, Conversion-Memory Register
  Loaded with the conversion results. Bits 15-12 are always 0. The results are stored in the least significant 12 bits.
ADC12MCTLx, ADC12 Conversion Memory Control Registers

## Slide 43: ADC12 (5/6) Registers
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC12MCTLx, ADC12 Conversion Memory Control Registers
(INCHx depends on the device)
Bit |  | Description
7 | EOS | Indicates the last conversion in a sequence: EOS = 0  Not end of sequence EOS = 1  End of sequence
6-4 | SREFx | Select voltage reference: VR+ VR− SREF2 SREF1 SREF0 = 000  AVCC AVSS SREF2 SREF1 SREF0 = 001  VREF+ AVSS SREF2 SREF1 SREF0 = 010  VeREF+ AVSS SREF2 SREF1 SREF0 = 011  VeREF+ AVSS SREF2 SREF1 SREF0 = 100  AVCC VREF−/VeREF− SREF2 SREF1 SREF0 = 101  VREF+ VREF−/VeREF− SREF2 SREF1 SREF0 = 110  VeREF+ VREF−/VeREF− SREF2 SREF1 SREF0 = 111  VeREF+ VREF−/VeREF−
3-0 | INCHx | Input channel select: INCH3 INCH2 INCH1 INCH0 = 0000  A0 INCH3 INCH2 INCH1 INCH0 = 0001  A1 INCH3 INCH2 INCH1 INCH0 = 0010  A2 INCH3 INCH2 INCH1 INCH0 = 0011  A3 INCH3 INCH2 INCH1 INCH0 = 0100  A4 INCH3 INCH2 INCH1 INCH0 = 0101  A5 INCH3 INCH2 INCH1 INCH0 = 0110  A6 INCH3 INCH2 INCH1 INCH0 = 0111  A7 INCH3 INCH2 INCH1 INCH0 = 1000  VeREF+ INCH3 INCH2 INCH1 INCH0 = 1001  VREF−/VeREF− INCH3 INCH2 INCH1 INCH0 = 1010  Temperature sensor INCH3 INCH2 INCH1 INCH0 = 1011  (AVCC – AVSS)/2 INCH3 INCH2 INCH1 INCH0 = 1100  A12 INCH3 INCH2 INCH1 INCH0 = 1101  A13 INCH3 INCH2 INCH1 INCH0 = 1110  A14 INCH3 INCH2 INCH1 INCH0 = 1111  A15

## Slide 44: ADC12 (6/6) Registers
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC12IE, ADC12 Interrupt Enable Register
  This 16-bit register enables (ADC12IEx = 1) or disables (ADC12IEx = 0), the interrupt request for the ADC12IFGx bits.
ADC12IFG, ADC12 Interrupt Flag Register
  Each bit of this 16-bit register is set when the corresponding ADC12MEMx is loaded with a conversion result and reset if the corresponding ADC12MEMx is accessed by software.

## Slide 45: Laboratory 5: Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Objective:
  Two laboratories have been developed to make use of the SAR ADCs included in the different hardware development tools:
    Lab5A: SAR ADC10 conversion;
    Lab5B: SAR ADC12 conversion.
Details:
  Like the previous laboratory exercise (Lab4), this one is also composed of sub-tasks.
  This laboratory has been developed for the Code Composer Essentials version 3 software development tool only.

## Slide 46: Lab5A: SAR ADC10 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Project files:
  C source file: Chapter 9 > Lab5 > Lab5A_student.c
  Solution file: Chapter 9 > Lab5 > Lab5A_solution.c
Overview:
  This laboratory implements a temperature data logger using the hardware kit’s integrated temperature sensor;
  The device is configured to perform an acquisition once each minute for one hour;
  Each value of temperature (ºC) is transferred to flash info memory segment B and C;
  When all tasks have been completed, the MSP430 enters into low-power mode.

## Slide 47: Lab5A: SAR ADC10 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  The ADC10 module uses VREF+ = 1.5 V as the reference voltage;
  It is necessary to configure the ADC10 to use the integrated temperature sensor (A10) as the input;
  Timer_A generates an interrupt once each second that starts the conversion on the ADC10;
  At the end of conversion, an interrupt is requested by the converter and the temperature value is written to flash memory.

## Slide 48: Lab5A: SAR ADC10 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  The voltage value is converted into temperature using the mathematical formula provided in the ADC10 sub-section;
  After transferring the value to the flash memory, the system returns to low power mode LPM3.
  The resources used by the application are:
      ADC10;
      Timer_A;
      Ports I/O;
      Interrupts;
      Low power mode.

## Slide 49: Lab5A: SAR ADC10 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  The application starts by stopping the Watchdog Timer;
  System tests for calibration constants stored in info memory segment A. The CPU execution will be trapped if it does not find this information;
  DCO is set to 1 MHz, providing a clock source for MCLK and SMCLK while the Basic Clock System+ is configured to set ACLK to 1.5 kHz;
  Controller’s flash timing is obtained from MCLK divided by 3 to comply with the device specifications.

## Slide 50: Lab5A: SAR ADC10 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  Port P1.0 is configured as an output and will blink the LED once each second;
  The ADC10 is configured to use the input channel corresponding to the on-chip temperature sensor (channel A10);
  The configuration includes the activation of the internal reference voltage VREF+ = 1.5 V and the selection of ADC10OSC as clock signal;
  The converter is configured for single-channel single-conversion.

## Slide 51: Lab5A: SAR ADC10 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  At the end of conversion an interrupt is requested;
  The Timer_A is configured to generate an interrupt once each second;
  ACLK/8 is selected as the clock signal using the VLOCLK as clock source and it will count until it reaches the TACCR0 value (up mode);
  The system enters into low power mode waiting for an interrupt.

## Slide 52: Lab5A: SAR ADC10 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  Flash memory pointers and interrupt counters are initialized;
  The Timer_A ISR increments the variable counter and when this variable reaches the value 60 (1 minute), the software start of conversion is requested;
  At the end of this ISR, the system returns to LPM;
  When the ADC10 ends the conversion, an interrupt is requested:
    While variable min is lower than 60, the temperature is written to flash memory. The memory pointer is increased by two (word);
    When min = 60, the system stops operation.

## Slide 53: Lab5A: SAR ADC10 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  DCO configuration:
  Adjust the DCO frequency to 1 MHz by software using the calibrated DCOCTL and BCSCTL1 register settings stored in information memory segment A.
if (CALBC1_1MHZ == ________||CALDCO_1MHZ == ________)
{
while(1); // If calibration constants erased
// do not load, trap CPU!!
}
DCOCTL = ___________________;

## Slide 54: Lab5A: SAR ADC10 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  Basic Clock module+ configuration:
  Set MCLK and SMCLK to 1 MHz;
  Use the internal very low power VLOCLK source clock set to ACLK/8 clock signal as the low frequency oscillator (12 kHz):
  BCSCTL1 = __________________;
  BCSCTL3 = __________________;

## Slide 55: Lab5A: SAR ADC10 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  ADC10 configuration:
  The ADC10’s input channel is the integrated temperature sensor (A10) and it uses the reference signal VREF+ = 1.5 V;
  The ADC10 clock source is ADC10OSC using the clock signal ADC10CLK/4. Configure the ADC10 sample-and-hold time: 64xADC10CLKs, to perform a single-channel single-conversion and enable its interrupts. What is the value to write to the configuration register?
  ADC10CTL1 = ________________;
  ADC10CTL0 = ________________;

## Slide 56: Lab5A: SAR ADC10 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  Timer_A configuration:
  Configure Timer_A register to enable an interrupt once each second;
  Use the ACLK clock signal as the clock source;
  This timer is configured in up mode in order to count until the TAR value reaches the TACCR0 value.
  Configure the following registers:
  TACCTL0 = ___________________;
  TACCR0 = ____________________;
  TACTL = _____________________;

## Slide 57: Lab5A: SAR ADC10 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Monitor the temperature variation during 1 hour:
  After compiling the project, start the debug session and before running the application, put a breakpoint on the line of code with the _NOP() instruction;
  Go to breakpoint properties and set action to Write data to file;
  Name the file as Temp.dat and define the data format as integer;

## Slide 58: Lab5A: SAR ADC10 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  Monitor the temperature variation over 1 hour:
  The data starts at address 0x01040 with a length of 3C;
  Run the application and let the temperature data logger acquire values for 1 hour;
  Use a heater or a fan to force temperature variations during the measurement period;
  When execution reaches the breakpoint, the file will be available in your file system;
  Construct a graph to plot the temperature variation obtained by the data logger.

## Slide 59: Lab5A: SAR ADC10 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DCO configuration:
if (CALBC1_1MHZ == 0xFF || CALDCO_1MHZ == 0xFF)
{
while(1); // If calibration constants erased
// do not load, trap CPU!!
}
DCOCTL = CALDCO_1MHZ; // Set DCO to 1 MHz
eZ430-RF2500 | SOLUTION
Develop a temperature data logger through the integrated temperature sensor using the eZ430-RF2500 Development Tool. | 

## Slide 60: Lab5A: SAR ADC10 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Basic Clock module+ configuration:
BCSCTL1 = DIVA_3; // ACLK = 1.5 kHz
BCSCTL3 = LFXT1S_2; // Set VLOCLK (12 kHz)
ADC10 configuration:
ADC10CTL1 = INCH_10 | ADC10DIV_3;
// Temp Sensor:A10,
// ADC10CLK/4,
// ADC10 clock source: ADC10OSC,

## Slide 61: Lab5A: SAR ADC10 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC10 configuration:
ADC10CTL0=SREF_1|ADC10SHT_3|REFON|ADC10ON|ADC10IE;
// Internal reference voltage Vref+ = 1.5 V
// ADC10 sample-and-hold time: 64 x ADC10CLKs
// Reference-generator voltage = 1.5 V
// ADC10 on + ADC10 interrupt enable

## Slide 62: Lab5A: SAR ADC10 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Timer_A configuration:
TACTL0 = CCIE; // TACCR0 interrupt enabled
TACCR0 = 1500; // this count corresponds to 1 sec
TACTL = TASSEL_1 | MC_1 | ID_0;
// ACLK/1, up mode to TACCR0

## Slide 63: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Project files:
  C source file: Chapter 9 > Lab5 > Lab5B_student.c
  Solution file: Chapter 9 > Lab5 > Lab5B_solution.c
Summary:
  This laboratory explores the ADC12 and OA modules using the MSP-EXP430FG4618 kit (MSP430FG4618 device);
  The test voltage is generated by the DAC12 channel 0, available at DAC12_ODAT register;
  The analogue signal is conditioned by the OA module (amplitude change), configured as a non-inverting PGA;
  This signal is applied to ADC12 input to be converted. Compare the DAC12_ODAT and the ADC12MEM0 values.

## Slide 64: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  The DAC12 module uses the same internal reference voltage as the ADC12 module (VREF+ = 2.5 V);
  The OA module is configured as Non-inverting PGA with unity gain;
  The Non-inverting input is the DAC0 internal while the output is connected to internal/external A1 of the ADC12;
  The ADC12 sample-and-hold time is configured to be 64 ADC12CLK cycles;
  It performs a single-channel, single-conversion using ADC12OSC/1 as the clock source.

## Slide 65: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
A. Resources:
  The resources used by the application (following the signal modification steps) are:
    DAC12;
    OA;
    ADC12;
    Timer_A;
    Interrupts.

## Slide 66: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  The laboratory is organized as follows:
    Peripherals initialization phase, finishing with the MSP430 in LPM3;
    ISR phase, constituted by a Timer_A overflow service routine that triggers a new ADC12 conversion and is responsible for the end of conversion.

## Slide 67: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  The application starts by stopping the Watchdog Timer;
  The system clock is configured by the FLL+ at 4 MHz (128 x 32768 Hz);
  The DAC12 module is configured to generate a zero voltage (0V) at the output;
  It uses the ADC12 internal 2.5 V reference voltage;
  The output of the DAC12 is configured with 12-bit resolution in straight binary.

## Slide 68: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  DAC12 uses the full scale output with a medium speed/current;
  The OA module is configured as a non-inverting PGA, with the input signal (DAC0 internal) and rail-to-rail range;
  The output of the OA is connected to internal/external A1;
  The ADC12 is configured to perform single-channel (channel A1), single-conversion;
  The configuration includes the activation of the same internal reference voltage as the DAC12.

## Slide 69: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
B. Software application organization:
  The ADC12 clock source is ADC12OSC, with the sample-and-hold time set to 64 ADC12CLK cycles;
  The Timer_A is configured to use the ACLK as the clock source;
  It will count in continuous mode (TACCR0 counts up to 0FFFFh) and generate an interrupt to update the ADC12MEM;
  When the interrupt is serviced, the MSP430 enters into LPM3.

## Slide 70: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  ADC12 configuration:
  The ADC12 module is configured in order to have the following characteristics:
    Single-channel, single-conversion operation;
    Internal signal VREF+ (2.5 V) as reference voltage;
    Sample-and-hold time: 64 ADC12CLK cycles;
    The conversion result available on ADC12MEM0;
    Sample-and-hold clock source: defined by software.
    ADC12CTL1 = ________________;
ADC12CTL0 = ________________;

## Slide 71: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  ADC12 configuration:
  The ADC12 module operates with reference voltages:
    VR+ = VREF+ and VR- = AVSS.
  The channel selected to perform the analogue-to-digital conversion is channel A1. This channel is internally connected to the output of OA0.
  ADC12MCTL0 = _______________;

## Slide 72: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
C. System configuration:
  OA0 configuration:
  The OA module of the MSP430FG4168 has three operational amplifiers with wide utilization flexibility;
  Use OA0 in non-Inverting PGA mode with the configuration:
    Inverting input is connected to the DAC12 channel 0;
    The amplifier gain is configured as unity;
    The input is configured in rail-to-rail mode;
    The output is connected to channel A1.
  OA0CTL0 = __________________;
  OA0CTL1 = __________________;

## Slide 73: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  This laboratory uses the previous modules to construct an analogue signal chain.

## Slide 74: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  The input voltage Vin is in the range 0 V and 2.5 V, with a resolution:
  The Vin value is controller by the DAC12_0DATA register value;
  The output voltage Vo has the same characteristics of the input voltage, but with a multiply factor (gain) supplied by the OA.

## Slide 75: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  The OA gain is selectable through the OAFBR field in the OA0CTL1 register;
  The Vo conversion result is stored in the ADC12MEM0 register;
  Once the signal chain modules are configured in accordance with the previous steps, continue the experiment by completing the file Lab5b_student.c, compiling it and running it on the Experimenter’s board.

## Slide 76: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
  For the evaluation of the peripherals during this laboratory, set a breakpoint on the ADC12_ISR and perform the following operations:
    Configure the DAC12_0DATA register with the value 0xFF. With the aid of a voltmeter, measure the analogue input voltage A6 (DAC12 channel 0 output). The value should be in the region of 0.15 V;
    Measure the input voltage A1 (output of the OA0). The voltage value should be the same;

## Slide 77: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
D. Analysis of operation:
    Execute the code. Verify the conversion result of the ADC12. The value should be similar to the one in the DAC12_0DATA register;
    Double the amplifier gain (2x). Verify the voltage at A0. It should be the double of the input voltage A1 (output of the OA0) shown in step 2;
    Execute the code. Verify the conversion result of the ADC12. The value should be twice the value of the DAC12_0DATA register;
    Execute further modifications in order to evaluate the digital-to-analogue and analogue-to-digital conversion. Do not exceed the Vo maximum value (2.5 V).

## Slide 78: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
DAC12 configuration:
DAC12_0DAT = 0x00; // DAC_0 output 0V
DAC12_0CTL = DAC12IR | DAC12AMP_5 | DAC12ENC;
// DAC_0 -> P6.6, DAC_1 -> P6.7
// DAC reference Vref, 12 bits resolution
// Immediate load, DAC full scale output
// Medium speed/
// Straight binary
// Not grouped
MSP-EXP430FG4618 | SOLUTION
Using the MSP-EXP430FG4618 Development Tool, perform a signal acquisition of the output of the DAC12 using the integrated operational amplifiers for signal conditioning and ADC12 to convert the analogue signal to digital. | 

## Slide 79: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC12 configuration:
ADC12CTL0 |= SHT02|REF2_5V|REFON|ADC12ON|ENC|ADC12SC;
//SHT1x (Sample-and-hold time) = 0000b -> N/A
//SHT0x (Sample-and-hold time) = 0010b -> 64 ADC12CLK
//MSC (Multiple sample and conversion) = 0b -> N/A
//REF2_5V (Reference generator voltage) = 1b -> 2.5 V
//REFON (Reference generator on) = 1b -> Reference on
//ADC12ON (ADC12 on) = 1b -> ADC12 on
//ADC12OVIE (overflow-int. enable) = 0b -> disabled
//ADC12TOVIE (time-overflow int enable) = 0b -> disabled
//ENC (Enable conversion) = 0b -> enable configuration
//ADC12SC (Start conversion) = 1b -> Start conversion

## Slide 80: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC12 configuration:
ADC12CTL1 = CSTARTADD_0;
//CSTARTADDx (Conv. start address.) = 0000b -> ADC12MEM0
//SHSx (Sample-and-hold source) = 00b -> ADC12SC bit
//SHP (Sample-and-hold pulse-mode select) = 0b -> SAMPCON
// signal is sourced from the sample-input signal.
//ISSH (Invert signal S-H) = 0b -> not inverted.
//ADC12DIVx (ADC12 clock divider) = 000b -> /1
//ADC12SSELx (ADC12 clock source) = 00b -> ADC12OSC
//CONSEQx (Conversion sequence mode) = 00b -> Single-
//channel, single-conversion
//ADC12BUSY (ADC12 busy) = xb -> read only

## Slide 81: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
ADC12 configuration:
ADC12MCTL0 = INCH_1 | SREF_1;
//EOS (End of sequence) = 0b -> Not Used
//SREFx (Select ref.) = 001b -> VR+=VREF+/VR-=AVSS
//INCHx (Input channel select) = 0001b -> A1

## Slide 82: Lab5B: SAR ADC12 Signal Acquisition
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
OA0 configuration:
OA0CTL1 |= OAFC_4 | OAFBR_0;
//OAFBRx (feedback resistor) = 000b -> Tap 0 (G=1)
//OAFCx (OAx function) = 100b -> Non-inverting PGA
//OARRIP = 0b -> OAx input range is rail-to-rail
OA0CTL0 |= OAP_2 | OAPM_3 | OAADC1;
//OANx (Inverting input) = XXb -> not important
//OAPx (Non-inverting input) = 10b -> DAC0 internal
//OAPMx (Slew rate select) = 11b -> Fast
//OAADC1 (OA output) = 1b -> output connected to A1
//OAADC0 (OA output) = 0b -> output not connected A12

## Slide 83: Quiz (1/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
12. The SAR derives its name from a process that:
  (a) Successively compares the input analogue voltage to the output of a DAC that has a binary weighted input code for a capacitive SAR ADC;
  (b) Sums a series of binary-weighted currents;
  (c) Sums current from a ladder resistor network for a resistive SAR ADC;
  (d) Sums voltages from a resistor network.
13. A 12-bit SAR ADC is found in:
  (a) eZ430-F2013;
  (b) eZ430-RF2500;
  (c) Experimenter’s board;
  (d) All of above.

## Slide 84: Quiz (2/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
14. To configure ADC10 in the eZ430-F2013 to use the internal voltage generator, the control register bits:
  (a) REFOUT must be set;
  (b) REF2_5V must be reset;
  (c) REFON must be set;
  (d) REFBURST must be set.
15. For the MSP430FG4618 in the Experimenter’s board, when the SHP control register bit is set, the ADC12’s sample timing method is:
  (a) Extended sample mode;
  (b) Synchronization with ADC12CLK mode;
  (c) Pulse mode;
  (d) Fixed sample period length mode.

## Slide 85: Quiz (3/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
16. The ADC12 interrupt sources available are:
  (a) ADC12IFGx and ADC12OV;
  (b) ADC12TOV;
  (c) All of above;
  (d) None of above.
17. The configuration of the ADC12 input channel as internal temperature sensor requires the INCHx control bits defined as:
  (a) INCHx = 12;
  (b) INCHx = 9;
  (c) INCHx = 10;
  (d) None of above.

## Slide 86: Quiz (4/4)
<number>
Copyright 2009 Texas Instruments
All Rights Reserved
www.msp430.ubi.pt
Answers
  12. (a) Successively compares the input analogue voltage to the output of a DAC that has a binary weighted input code for a capacitive SAR ADC.
  13. (c) Experimenter’s board.
  14. (c) REFON must be set.
  15. (c) Pulse mode.
  16. (c) All of above.
  17. (c) INCHx = 10.