## Slide 1: Exam
IAX 0600 Digital Systems Design
Alexander Sudnitson
Tallinn University of Technology

## Slide 2: Dates
Labs (reports and defences) red line is a day before chosen date of exam.
1. |  |  |  | 22.05.2020 14:00 ICT-A2 | 
2. |  |  |  | 25.05.2020 14:00 ICT-A2 | 
3. |  |  |  | 04.06.2020 14:00 ICT-A2 | 
4. |  |  |  | 10.06.2020 14:00 ICT-A2 | 

## Slide 3: Data Types
What is meant by strong typing in VHDL and why is it useful?
What is the relationship between std_ulogic and std_logic? Under what condition(s) would each be preferred as the type of a signal in a design description?
What is a subtype? What is a base type? Can a signal that is of a subtype be assigned to a signal that is of the base type of the subtype? Can a signal that is of a base type be assigned to a signal that is of a subtype of the base type? Under what condition will these kinds of assignments cause an error during a simulation?
What are the two composite types in VHDL and what are their similarities and differences?

## Slide 4: Data Types
Given the following declarations:
signal a, b : std_logic_vector (3 downto 0);
signal p, q : std_logic_vector (7 downto 0);
Give the value of the signal after the following assignments:
a <= (2 => '1', 1 => '0', 0 => '0', 3 => '1’);
p <= (7|5|3 => '1', others => '0’);
b <= (others => '0’);
q <= (6 downto 4 => '0', others => '1');

## Slide 5: Data Types
a
b
en
Write three state buffer VHDL description
What means predefined data type.
Give definition of type Boolean.
Write context clause to use unsigned and signed types.
Give definition of type Boolean.
Conversion between Std_logic_vector, Unsigned and Signed (give an example)
BIT versus STD_LOGIC

## Slide 6: Data Types
Given the following declarations:
constant m : unsigned := "1101";
constant p : signed := "1101";
constant i : integer := 145;
constant r : integer := —31;
constant q : integer := 19;
For the following assignment statements give the type, number of elements, and value of the target signal:
f <= to_unsigned(i, 8);
g <= to_signed(r,8);
h <= std_logic_vector(to_unsigned(q, 5));
j <= to_integer(m); k <= to_integer(p);

## Slide 7: Coding styles
What coding styles do you know?
Which coding styles describe a behavior of the system?
Suppose, we would like to evaluate Boolean expression (that equivalent to aXORb)
c = a and not b or not a and b
Write correct VHDL assignment signal assignment statement using AND, OR, NOT operators
c <=
What kinds of concurrent signal assignment statements do you know?
Write VHDL description of such multiplexor

## Slide 8: Coding styles
process (a, b)
begin
y <= a and b ;
end process;
For given process write equivalent process using WAIT ON statement.
Write two requirements for a process to synthesize a combinational system
a
b
g_bar
y0
y1
y2
y3
Write a VHDL description of 2-to-4 decoder using a case statement
Signals g_bar, y0, y1, y2, y3 are asserted when they are equal to '0'
Signals versus Variables
How to avoid unwonted latches

## Slide 9: Coding styles
Positional and named association in a component instantiation statement
(give an example)
Two forms for a component instantiation statement
Give structural description using direct component instantiation and positional association
Give structural description using indirect component instantiation and named association
AND
OR
AND
a
b
c
d
m
k
y
AND
i1
i2
o
OR
i1
i2
o
Compiled design entities (with names AND and OR)

## Slide 10: Sequential Systems and FSMs
Latch versus flip-flop
Explicit and implicit description of memory elements
Give VHDL description of this latch
Give VHDL description of D latch with asynchronous set and clear inputs

## Slide 11: Sequential Systems and FSMs
Positive-edge-triggered D flip flop
Give expressions for a positive clock-edge condition
Give VHDL description of positive-edge-triggered D flip flop
Give VHDL description D flip-flop with asynchronous set and clear inputs
Give VHDL description D flip-flop with synchronous set and clear inputs